## Slide 1: Neutral Particle Spectrometer (NPS) + Compact Photon Source with Longitudinal & Transverse Polarized NH2
Hall C Winter Meeting
Charles Hyde, Hall C Meeting, 28–29 Jan 2019
Experiment | Exp # | Beam | Target | PAC Days | Rating
π0 SIDIS | E12-13-007 |  | L H2 | 26 | A–
DVCS and Exclusive π0 | E12-13-010 |  | L H2 | 53 = (26)+27 | A
Wide Angle Compton Scattering (WACS) | E12-14-003 |  | L H2 | 18 | A–
Wide Angle Exclusive p0 photoproduction | E12-14-005 |  | L H2 | (18) | B
Initial State Helicity Correlation in WACS | E12-14-006 | CPS: |  | 31 | B
ALL & ALS Polarization Observables in WACS at large s, t, and u | C12-17-008 | CPS: |  | 46 | A–
Timelike Compton Scattering (TCS) off a Transversely Polarized Proton | C12-18-005 | CPS: | []T | 35 | C2
Experiment | Exp # | Beam | Target | PAC Days | Rating
π0 SIDIS | E12-13-007 |  | L H2 | 26 | A–
DVCS and Exclusive π0 | E12-13-010 |  | L H2 | 53 = (26)+27 | A
Wide Angle Compton Scattering (WACS) | E12-14-003 |  | L H2 | 18 | A–
Wide Angle Exclusive p0 photoproduction | E12-14-005 |  | L H2 | (18) | B
Initial State Helicity Correlation in WACS | E12-14-006 |  |  | 31 | B
ALL & ALS Polarization Observables in WACS at large s, t, and u | C12-17-008 |  |  | 46 | A–
Timelike Compton Scattering (TCS) off a Transversely Polarized Proton | C12-18-005 |  |  | 35 | C2

## Slide 2: NPS Layout on SHMS Carriage
DVCS H(e,e’ g)p, Deep H(e,e’ p0)p
e– to HMS
PbWO4 g-
WACS H(g, g p), Wide angle H(g, p0p)
Proton to HMS

## Slide 3: Sweep Magnet replaces SHMS Horizontal Bender
Looking upstream
  Vertical bend ~0.3 Tm
1cm steel septum between 0-field beam pipe and g-aperture (at smallest angle setting)
Ready for power, cooling
Magnetic field mapper constructed at ODU

## Slide 4: PbWO4 Crystal Procurement 2x2x20 cm3
SICCAS (China): 460 received, 160 failed specs, returned for replacement. Additional 52 below spec to be used at edges.
SICCAS: Contract to be signed for 400 more
Crytur (Czech Republic): 100 received, OK
Crytur: 250 crystals on order delivery ≤ October 2019
  Supply limited by PANDA order
  Raw material reserve exhausted

## Slide 5: PMTs from HyCal, New Active bases
Gain stabilization at high rates by amplifier fed from last stage of HV divider.
PMT base assembly: Ohio U.
Prototype assembly: IPN-Orsay

## Slide 6: Calorimeter Assembly
Carbon fiber alveoli cantilever crystals in place
Signal cables to 250 MHz FADC
Translation cards
Translation cards
HV
LED Ribbon
Temperature controlled box for crystals

## Slide 7: Calorimeter Servicing
Access to remove any individual PMT+Base module without disassembly
Module disassembles from calo with a single screw
LED fiber
Signal + HV ribbon jumper

## Slide 8: Compact Photon Source for Polarized Targets
Self-contained radiator, forward collimator, & electron dump
Pure photon beam on NH3
  Longer polarization lifetime
  Higher gp luminosity
  Transverse polarization
Dipole magnet, central Cu absorber/dump, W powder and borated plastic radiation absorber.
CPS concept Jlab Internal Review Committee 2018. Feasible and ready for detailed design

## Slide 9: WACS Polarization Observables
UVA n NH3 target
  100° longitudinal aperture
  38° transverse aperture
ALL = KLL
  Except when it doesn’t.
  Free elementary quark (diluted by polarization)
Kroll, Miller = handbag models (different off-shell)
K-V = SCET

## Slide 10: Timelike Compton Scattering
Access to E(x,t) Compton Formfactor with transversely polarized target.
Quark Orbital Angular Momentum
TCS
BH
11 GeV Kinematic Coverage
DVCS
TCS
DVCS
TCS

## Slide 11: NPS
Equipment will be ready for beam before 2022
Rich physics program
Join us!
https://wiki.jlab.org/cuawiki/index.php/Main_Page
Tanja Horn, coordinator

## Slide 13: Magnet Mapper
ODU graduate student Mitch Kerver at the controls
Hall Probe recording now added