## Slide 1: Computing at PANDA
15.2.2018 Tobias Stockmanns
The PandaRoot Simulation and Analysis Framework

## Slide 2: Computing at PANDA
Computing at PANDA coveres three areas:
  Online Computing
    Processing of the raw data of the experiment
    Goal: Selection of data to keep for detailed analysis
    Speed  Precision
  Offline Computing
    Processing of stored experimental data
    Goal: Physics result
    Precision
  Simulation
    Simulation of experiment

## Slide 3: Processing Stages
Sim
Digi
Local Reco
Global Reco
Event Building
Analysis
Paper
sim

## Slide 4: Processing Stages
PANDA
FPGA
Sim
Digi
Local Reco
Global Reco
Event Building
Event Selection
Analysis
Storage
Paper
online
sim

## Slide 5: Processing Stages
PANDA
FPGA
Sim
Digi
Local Reco
Global Reco
Event Building
Event Selection
Analysis
Storage
Paper
Raw Data
online
offline
sim
Calibration Alignment

## Slide 6: Processing Stages
PANDA
FPGA
Sim
Digi
Local Reco
Global Reco
Event Building
Event Selection
Analysis
Storage
Paper
Raw Data
online
offline
sim
Calibration Alignment
PandaRoot

## Slide 7: PandaRoot

## Slide 8: FairRoot
Structure
. . .
Topology Editor
Parameter/ Condition Management
DDS
(Dynamic Deployment)
Testing
FairMQ
Geometry
Magnetic Field
Event Generators
FairRoot
Detector Response
ALFA
AliceO2
http://alice-o2.web.cern.ch/
BNMRoot
http://mpd.jinr.ru
MPDRoot
http://mpd.jinr.ru
EnsarRoot
http://igfae.usc.es/satnurse/ensarroot.html
ExpertRoot
http://er.jinr.ru/
ATTPCRootv2
https://github.com/ATTPC/ATTPCROOTv2
R3BRoot
https://www.gsi.de/r3b
PandaRoot
https://panda.gsi.de/
CbmRoot
https://fair-center.eu/for-users/experiments/cbm.html
FairShip
http://ship.web.cern.ch/ship/
Software Stack
Boost
Network
(ZeroMQ, nanomsg, OFI libfabric)
CMake
Simulation Engines
VGM
. . .
Serialization
(Protocol Buffers, msgpack, FlatBuffers, ROOT)
ROOT
Google Test
SofiaRoot
AsyEosRoot
see: R. Karabowicz Saturday 11:00

## Slide 9: Event Generators
Event Generators
Signal
Background
PGun
EvtGen
EMFF
DPM
UrQMD
FTF
Pythia
GiBuu
BoxGen
FlatGen

## Slide 10: Particle Propagator
Usage of Virtual Monte Carlo allows seamless change of propagation engine
Same geometry description in propagation and reconstruction of events by using the same geometry engine from root
Virtual MC
Geant3
Geant4

## Slide 11: Geometry description

## Slide 12: Geometry description
Magnets
MVD
STT
GEM
DIRC + SciTil
EMC

## Slide 13: Geometry description
Magnets
MVD
STT
GEM
DIRC + SciTil
EMC

## Slide 14: Magnetic Field

## Slide 15: Digitization
Translates ideal detector data into realistic data stream
  3D space points into channel number
  Deposited energy into ADC values
  Adding noise and inefficiencies
  Charge sharing between neighboring detector elements
  Dead times and electronics properties
Data should look like as coming from the final experiment
Simulated EMC waveform
Avalanche Simulation in MDT

## Slide 16: Reconstruction - I
Local reconstruction for each sub-detector
  Translation from detector data into physical parameters (from channel number to space point, ADC to energy)
  Calibration
  Cluster formation
  Reconstruction algorithms
  Various different algorithms implemented for each sub-detectors
  Compared with test beam data
  PandaRoot used to reconstruct test beam data

## Slide 17: Detector Processing Example

## Slide 18: Reconstruction - II
Global reconstruction
  Combining different sub-detectors
  Tracking
  PID
  Event building

## Slide 19
Tracking

## Slide 20: Tracking
Event Simulation

## Slide 21: Tracking

## Slide 22: Simulated Events
STT
~ 4200 straws
Dense packaging
Isochrones (2D)
Up to 250 ns drift time
< 150 µm resolution
No start time
 4D tracking needed
Time series of MVD and STT detector signals in PANDA (view along beam axis)
MVD
4 barrel layers
6 disks
3D space points
< 30 µm point resolution
< 10 ns time resolution
risochr
Straw Tube
STT
MVD

## Slide 23: Tracking Procedure
Full track reconstruction happens in various steps:
  Group the hits which belong to the same track
  Fast evaluation of the track parameters
  Precise fitting of the track parameters
  Propagate track parameters to the point where they are needed
  pattern recognition / track finding
  pre-fit
  Kalman fit
  propagation / extrapolation

## Slide 24: Offline Barrel Tracking
Local pattern recognition in STT and MVD
Correlation of STT and MVD tracklets
Extrapolation to GEM
Kalman Filter
MVD
STT

## Slide 25: Forward Tracking
Cellular Automaton
  Build short track segments
  Connect according to track model
  Collect segments into track candidates
  Select best track candidates
Cellular Automaton
97 % track finding efficiency

## Slide 26: Tracking: Global Fit
Prefit Track
Kalman Filter
(GENFIT)
Detector Hits
Track Follower
(GEANE)
same geometry for simulation and track following
Energy loss
Not homogeneous magnetic field
Different detector hits
planar hits – MVD/GEM
tube + drift time – STT/FTS
barrel
forward

## Slide 27: Tracking - offline
Track finding and fitting working in Central and Forward Spectrometer
Kalman filter used as second stage developed by TUM (GenFit 1 + 2)
Efficiency above 90 % (for beam above 3 GeV/c)
Momentum resolution between 1% and 5% depending on momentum
For p(pbar) < 3 GeV/c
B = 1T
p resolution doubles
low p efficiency increases
For online tracking
see: T. Stockmanns Saturday 11:30

## Slide 28
Particle Identification

## Slide 29: Geometry description
MVD dE/dx
STT dE/dx
DIRC Cherenkov
SciTil TOF
EMC ShowerShape
Muon #layers, #hits
RICH Cherenkov
FTOF TOF

## Slide 30: Particle Identification
EMC
MVD
STT
DIRC
DISC
MDT
Implemented PDFs for many detectors (Bayes)

## Slide 31: PID
If many detectors/alogirhtms contribute to PID
Probability that a given track with parameters x corresponds to particle type h
k = MVD dE/dx, DRC C…
Global Likelihood
Bayes Theorem

## Slide 32: Machine Learning for PID
Artifitial Neural Network
Boosted Decision Tree
Work in progress
More about ML:
R. Kliemt Saturday 08:30

## Slide 33
Time-Based Simulation

## Slide 34: Time-Based Simulation
Signal and background-events very similar  no hardware trigger possible
Quasi continuous beam with maximum interaction rate of 20 MHz  Poisson distribution
Raw data rate of 200 GByte/s
Reduction of 1000 needed for permanent storage O(PByte/year)  Online Event Filte

## Slide 35: Time-Based Simulation
Single Event

## Slide 36: Time-Based Simulation
20 MHz overlap

## Slide 37: Time-Based Reconstruction
MVD
STT
Event 1
Event 2
Event 3
Activities on the central tracker MVD + STT + GEM + SciTil + EMC
EMC
Work in progress
see: T. Stockmanns Saturday 11:30

## Slide 38
Panda Analysis

## Slide 39: Analysis Tools
Reconstruction
Vertex Fit
PndAnalysis
Kinematic Fit
DecayTree Fit
QA Tools
PWA

## Slide 40: Analysis Tools
Rho
Reconstruction
Vertex Fit
PndAnalysis
Kinematic Fit
DecayTree Fit
QA Tools
PWA

## Slide 41: Analysis Framework
Rho
  Small framework to handle particle candidates
  Combinatorics, lists and selectors
  Smart n-tuple: RhoTuple
PndAnalysis
  Providing Rho with reconstructed data and basic particle lists
  PID selections on PndPidProbability
  Propagation interface to GEANE
  MC-Truth access & decay chain MC-Matching
Rho and PndAnalysis

## Slide 42: Analysis Tools
Vertexing
  POCA finder
  RhoKalmanVtxFitter: fast
  RhoKinVtxFitter: precise
Particle Fitters
Kinematic Fits
  Rho4CFits
  RhoKinFitter:  Mass, 4C (P3, E)
Tree Fits
  Iterative mechanism
  DecayTreeFitter fits complete decay tree at once

## Slide 43: Analysis Framework
QaTools
  Employs smart n-tuples (RhoTuple) as root trees
  Many automated functions to fill them (p4, daughters, mc, pid, ...)
  Common nomenclature for fast command line analysis
QuickAnalysis
  Automated scripts to get large n-tuples by a few settings for: combinatorics, fits and selections
  Usually enough to make all desired plots!
  FastSim implementation allows results from one macro
Supporting Tools
see: K. Götzen Saturday 9:00

## Slide 44: Analysis example
Rho package
  Combine hits
  Fit with constraints
  Apply cuts

## Slide 46: PandaRoot Example Macros

## Slide 47: PandaRoot Infrastructure
Code Repository: pandaatfair.githost.io
  Issue Tracker, Constant Integration for each commit
Nightly builds and tests
Dashboard: https://cdash.gsi.de/index.php?project=PandaRoot
Wiki page: panda-wiki.de/foswiki/bin/view/Computing/PandaRoot
Forums: forum.gsi.de & Slack: pandaroot.slack.com
Bi-weekly online metings: Thursdays 10-11

## Slide 48: Computing Infrastructure

## Slide 49: Online Data Taking
DETECTORS
MASS STORAGE
80GB/s ‐ 200GB/s
1/1000 reduction factor
80MB/s ‐ 200MB/s
Max Interaction rate
20MHz
FPGA
CPU GPU
ASIC

## Slide 50: Connection to Green Cube
3500 optical fibers for CBM
500 optical fibers for PANDA
4 empty tubes
(10Gb/s fiber)
PANDA 2 X 310 GB/s
GreenCube
Panda
Maximum data rate from Panda data concentrators:
200 GB/s

## Slide 51: Design of Distributed Computing
Tier 0
  Prompt reconstruction
  Permanent storage of ALL data
  Calibration
  Reprocessing
  Simulation ?
Tier 1
  Reprocessing
  Calibration ?
  Simulation
  Permanent storage of part of the data
  Analysis ?
Tier 2
  Analysis
  Taking data from close Tier 1
  Small simulation jobs
50k cores (6 months)
70k cores (12 months)

## Slide 52: Summary
Computing at PANDA is challenging
  Overlapping events in time
  Many different sub-detectors
  Two different magnetic fields
  Reconstruction of low momentum particles
  Online reconstruction
PandaRoot / FairRoot software well developed (but still some holes open)
Online reconstruction still an open issue
  Which algorithm to use at which hardware?
  Change to FairMQ