## Slide 1: Online Computing at PANDA
15.2.2018 Tobias Stockmanns

## Slide 2: Boundary Conditions
Two magnets
4 tracking systems
7 PID detectors
4 calorimeters
Time difference between two events
No time structure in beam
Up to 20 MHz interaction rate
Up to 200 GByte/s raw data
Online tracking and event selection
< 10 tracks / event
Mainly p, π, K, e, µ 𝛾, N

## Slide 3: Online Data Taking
DETECTORS
MASS STORAGE
80GB/s ‐ 200GB/s
1/1000 reduction factor
80MB/s ‐ 200MB/s
Max Interaction rate
20MHz

## Slide 4: Online Data Taking
DETECTORS
MASS STORAGE
Fully digitized data Time-stamp for event building
Sub-detector specific Local processing
Burst of 1.6 µs with all detector Data sorted by time-stamp
Event building
Tracking + PID
Selection
ASIC/FPGA
FPGA
FPGA Compute Nodes
FPGA CPU
GPU

## Slide 5: Online Data Taking
Intelligent Front-End
Time distribution system
Data concetrators
EMC Readout Scheme
Burst-building network
Online Computing

## Slide 6: Online Data Taking
ATCA
Xilinx Ultrascale 60
16 GByte DDR4
Compute Node v4
4 xTCA mezzanine cards
1 RTM

## Slide 7: Connection to Green Cube
3500 optical fibers for CBM
500 optical fibers for PANDA
4 empty tubes
(10Gb/s fiber)
PANDA 2 X 310 GB/s
GreenCube
Panda
Maximum data rate from Panda data concentrators:
200 GB/s

## Slide 8: Online Tracking

## Slide 9: Online Tracking
Find and fit tracks with the production speed at Panda up to 20 MHz
Alternative hardware:
  FPGA:
    Helix tracking algorithm
  GPGPU:
    Cellular automaton
    Hough transformation
    Triplet finder
    Riemann transformation
    Direct switch in PandaRoot between CPU and GPU
Work in progress

## Slide 10: Simulated Events
STT
~ 4000 straws
Dense packaging
< 150 µm resolution
Isochrones
250 ns drift time
2D space point
No start time
Time series of MVD and STT detector signals in PANDA (view along beam axis)
MVD
4 barrel layers
6 disks
Mixed pixels / strips
3D space points
< 30 µm point resolution
< 10 ns time resolution
risochr
Straw Tube
STT
MVD

## Slide 11: Triplet Finder
Find 2 out of 3 combinations of hits in pivot layers and primary vertex
Calculate circle
Add hits in other layers by distance to circle
Straight line fit for z-component
Select track candidates by number of hits
x
+ Simple algorithm
+ No fitting needed
- No isochrone information
- Limited on primary tracks
Optimized for GPUs together with Nvidia Application Lab
Marius Mertens(FZJ), Andrew Adinetz(FZJ), Andreas Herten(FZJ)

## Slide 12: Triplet Finder
Non-bunched: packages of single events send
Bunched: Fixed time bunch with many events

## Slide 13: Cell Track Finder
Find (unambiguous) neighbours with hits  generates tracklets
Find connections between tracklets
Fit connected tracklets and take best matching one (Circle fit via Riemann Surface)
Add the ambiguous hits
Correct for isochrones
Straight line fit for z-component
+ All hits processed at once
+ Primary and secondary tracks
+ Generall clustering algorithm
o Isochrone information in an additional stage
- Only suitable for STT
Optimized for GPU
1/10 7/15
1/10 7/15
1/10 7/15
1/10 7/15
1/10 7/15
Jette Schumann (FZJ), Walter Anderson (Uppsala), Jenny Regina (Uppsala)

## Slide 14: Cell Track Finder
Version | Runtime per event | Ratio of CPU Time
CPU | 4.56 ms | 100 %
GPU (algorithm) | 0.575 ms | 12.08 %
GPU (+ event) | 0.045 ms | 0.94 %
Process neighbourhood relations (EvaluateState & EvaluateMultiStates)
Processing time per event incl. data transfer
t [ms]

## Slide 15: Circle Hough
Calculate for all hits all circles through origin which are tangent to isochrone
Fill x, y coordinate of circle center into histogram
Find peaks
Straight line fit for z-component
+ All hits in parallel
+ Isochrone information naturally in
+ Works for STT and MVD
- Limited on primary tracks
Andreas Herten (FZJ),
Ludovico Bianchi (FZJ)

## Slide 16: Pair Circle Hough

## Slide 17: Circle Hough

## Slide 18: Pair Circle Hough

## Slide 19: Track Finding on FPGA
Road Finding
Circle Fitting
Straight Line Fitting
Tube_ID
Layer_ID
x
y
xc, yc, R
E2 = ∑(xi2 + yi2 + a xi+ b yi + c)2 (1/di)2
E2 = ∑(Φi + kzi + Φ0)2 (1/di)2
+ Hits processed sequentially
+ Isochrone information used
+ T0 extraction possible
- Only suitable for STT
Optimized for FPGA
Yutie Liang (JLU Giessen)

## Slide 20: Track Finding on FPGA
T0 determination
T0 shifted by:
-50 ns:
-20 ns:
10 ns:
20 ns:
Extracted T0:
-47.0±4.0 ns
-19.8±2.1 ns
9.4±2.5 ns
19.0±2.3 ns
T0 shift = Ʃdi /N / const (N: number of hits
di: signed distance of circle to track)

## Slide 21: Performance
Efficiency > 90 %
σpt : ~ 3.2% σpz : ~ 4.2% .
7 μs/event (6 tracks)
Tracking strategy in case of missing t0
new

## Slide 22: FairMQ
Multi processing

## Slide 23: Test of FairMQ with Real Data
| Tobias Stockmanns
Parallel readout of 4 pixel detectors
Readout done by 4 FPGA boards sending their data to two PCs
On the PC bitstream converted into raw data
Raw data send via FairMQ to a FileSink

## Slide 24: Idea
Use MQ to completely process TB data online
Processing steps:
  Convert raw data into Digis
  Sort by time stamp
  Build “event”
  Find cluster
  Convert Digis into Hits
  Combine data stream of all four ASICs
  Build global event
  Find Tracks
  Fit Tracks
4 x Single FE

## Slide 25: Single Front-End
Raw Data Sampler
Raw to Digi
Dupli-cator
Distri-butor
Sorter
Sorter
Sorter
Merger
File Sink
Online
Digi to Hit
TB Data
Online
File handling
Data handling
Online monitoring
Data processing

## Slide 26: Distributor
Chart: Position in data stream

## Slide 27: Data after sorting
Chart: Position iin data stream

## Slide 28: Multiple Front-Ends
Raw Data Sampler
Raw to Digi
Dupli-cator
Distri-butor
Sorter
Sorter
Sorter
Merger
File Sink
Online
Digi to Hit
TB Data
Raw Data Sampler
Raw to Digi
Dupli-cator
Distri-butor
Sorter
Sorter
Sorter
Merger
File Sink
Online
Digi to Hit
TB Data
Raw Data Sampler
Raw to Digi
Dupli-cator
Distri-butor
Sorter
Sorter
Sorter
Merger
File Sink
Online
Digi to Hit
TB Data
Raw Data Sampler
Raw to Digi
Dupli-cator
Distri-butor
Sorter
Sorter
Sorter
Merger
File Sink
Online
Digi to Hit
TB Data
Event Builder
Track Finder/Fitter
File
Sink
Online
Online

## Slide 29: Event Builder
FE 1
FE 2
FE 3
FE 4
Data of each FE sorted in time
Time Stamps

## Slide 30: Event Builder
FE 1
FE 2
FE 3
FE 4
Take first in stack

## Slide 31: Event Builder
x
FE 1
FE 2
FE 3
FE 4
Take first in stack
Take earliest

## Slide 32: Event Builder
x
x
FE 1
FE 2
FE 3
FE 4
Take first in stack
Take earliest
Search for matching hits

## Slide 33: Event Builder
x
x
FE 1
FE 2
FE 3
FE 4
Take first in stack
Take earliest
Search for matching hits
Write out those in one event

## Slide 34: Event Builder
FE 1
FE 2
FE 3
FE 4
Fill empty positions with next hits

## Slide 35: Event Builder
FE 1
FE 2
FE 3
FE 4
Fill empty positions with next hits
Repeat selection

## Slide 36: Event Builder
FE 1
FE 2
FE 3
FE 4
Fill empty positions with next hits
Repeat selection

## Slide 37: Online Monitoring
running on 6 PC
  4 for each FE
  1 for tracking
  1 for control

## Slide 38: Online Monitoring
Running on 6 PC
  4 for each FE
  1 for tracking
  1 for control
Hitmap
Cluster finder

## Slide 39: Online Monitoring
Event builder
Track fitter
Track
finder

## Slide 40: Parallelization of Event Builder

## Slide 41
Time-Based Simulation

## Slide 42: Event Structure and Detector Response
Slow detector
.
.
.
time
ev 1
ev 2
ev 3
= detector hits from different events
Event 1
Event 2
Event 3
Wanted data structure
Data structure in Root

## Slide 43: Idea
3 Stage approach:
  Each event gets an event time generated after the simulation stage
  In the digitization stage a buffer is introduced which keeps the data beyond an event boundary
  In the reconstruction stage data is not retrieved event-by-event but based on time information

## Slide 44: Event Mixing and Time Association
Back-ground
Signal 1
Signal n
MC Files:
Digiti zation
MC file does not know anything about time structure
Time structure is calculated at the beginning of digitization
Many different signal files can be added to one background file
Event 102: time 10230.1 ns
…
Event 0: time 50.3 ns
Event 1: time 72.4 ns
…

## Slide 45: FairWriteoutBuffer
Special buffer to store detector digis between events
Stores data as long as it can influence later events (Active Time)
Modifies the data if a detector element is hit a second time (pile-up)
If time of new event is after Active Time the data is written to file
Result is a randomized data stream for further processing
Mimics realistic detector response
U
Uthr
t
Active Time
Time Stamp
Preamplifier with threshold

## Slide 46: Digi Data Randomized
Digi Data Stream
Digi Index
Same color = same event

## Slide 47: Digi Data Randomized
TimeStamp of Digi vs Index
Digi Index
Time Stamp [ns]

## Slide 48: Sorting Data - FairRingSorter
0-Element Pointer
Number of storage cells given by the spread of the time stamps within the data stream
Width of one storage cell given by time resolution of detector
Storage Pointer
position calculated numerically from time stamp
If a storage position is calculated which would override old data, the old data is saved to disk and the storage cell is freed

## Slide 49: Digi Data Sorted
Digi Data Stream
Digi Index
Same color = same event

## Slide 50: Digi Data Sorted
Digi Index
Time Stamp [ns]
TimeStamp of Digi vs Index after sorting

## Slide 51: Reading Back Data
Two different methods exists
FairRootManager::GetData(BranchName, Functor, Parameter);
FairRootManager::GetData(BranchName, StartFunctor, StartParam, StopFunctor, StopParam);
GetData with one functor/parameter runs always forward in time
  Data is only read once
GetData with two sets of functor/parameter is able to get data within a time window
  Data can be extracted many times

## Slide 52: Reading Back Data
Different algorithms available to extract data:
  All data up to a given time
  All data in a time window
  All data between timegaps of a certain size
Other algorithms can be (easily) implemented

## Slide 53: Examples
GEM Digis – Event separation by time gap
MC Truth
Packages
DIRC Pile-Up
GEM tracking eff. for
p > 1 GeV/c:
Event based: ~ 95%
Time based: ~ 87%
Event based
Time based
GEM track reconstruction
Chart: Merged events for different clock frequencies of MVD
40 MHz | 129 | 104 | 59 | 32 | 19 | 6 | 9 | 8 | 4 | 1 | 2 | 0 | 0 | 0 | 2
50 MHz | 193 | 127 | 66 | 30 | 13 | 9 | 8 | 1 | 2 | 1 | 1 | 1 | 0 | 0 | 0
80 MHz | 352 | 158 | 57 | 19 | 5 | 5 | 3 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0
155 MHz | 608 | 132 | 25 | 10 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
p [GeV/c]
time [ns]
R. Dzygadlo
R. Karabowicz
R. Karabowicz

## Slide 54: Summary
Online reconstruction of PANDA data is THE challenge in PANDA computing
Some work has been done especially in tracking but no complete picture exists
Try to stay open to new developments and new types of hardware
FairMQ looks as a very useful tool for parallelizing the processing
More tests and more work is needed.

## Slide 55: Backup

## Slide 56: Time-Based Simulation
Single Event

## Slide 57: Time-Based Simulation
20 MHz overlap

## Slide 58: Time-Based Reconstruction
MVD
STT
Event 1
Event 2
Event 3
Activities on the central tracker MVD + STT + GEM + SciTil + EMC
EMC
Work in progress

## Slide 59: Summary
Tracking in PANDA challenging
Several different algorithms exists in different states of maturity
No best candidate obvious
Common test environment finished
Next steps:
  Finalize the algorithms
  Test all on common data sample
  Chain or combine algorithms
  Machine Learning as alternative?

## Slide 60: Online Track Finding
Circle Hough

## Slide 61: Online Track Finding
Circle Hough

## Slide 62: Online Track Finding
Circle Hough

## Slide 63: Online Track Finding
Circle Hough

## Slide 64: Online Track Finding
Circle Hough

## Slide 65: Online Track Finding
Circle Hough

## Slide 66: Online Track Finding
Circle Hough

## Slide 67: Online Track Finding
Circle Hough

## Slide 68: Online Track Finding
Circle Hough

## Slide 69: Online Track Finding
Circle Hough

## Slide 70: Online Track Finding
Circle Hough

## Slide 71: DPM Example 2

## Slide 72: DPM Example 2

## Slide 73: DPM Example 2

## Slide 74: DPM Example 2

## Slide 75
Tracking Algorithm -- Road Finding
Hit
Hit
Hit
Hit
Hit
Hit
Hit
Hit
Hit
Hit
Hit
Tube_ID
Layer_ID
Hit: Seg_ID (3 bits) + LayerID (5 bits) + Tube_ID (6 bits) + Arrival time
1: Start from inner layer
2: Attach neighbour hit to tracklet layer by layer
Boundary between two segments.
Number of neighbor:
4 in axial layer; 6 in stereo layer

## Slide 76
Known : xi , yi , di
Question: To determine a circle,
x2 + y2 + ax + by + c = 0
Method: Minimize the equation
E2 = ∑(xi2 + yi2 + a xi+ b yi + c)2 (1/di)2
Sx = ∑xi …
Sxx = ∑xixi …
Sxxx = ∑xixixi …
Tracking Algorithm -- helix parameters calculation
1) Circle para.
2) Track quality.
x
y
xc, yc, R

## Slide 77
Pz reconstruction
1: The radius, the position of the helix center in the XY plane are determined.
2: Φ = kZ + Φ0
z
y
x
One cylinder the helix lies in.
Based on Pt determined before
One straw tube
Track need to be tangent to the crossing ellipse.
Crossing points
(ellipse)
Gianluigi Boca and Panda Collaboration, Panda STT TDR, 2012

## Slide 78
Known : zi , Φ i , di
Question: To determine a line,
Φ + kz + Φ0= 0
Method: Minimize E2 = ∑(Φi + kzi + Φ0)2 (1/di)2
Pz reconstruction

## Slide 79
Extract T0 from Tracking
T0 shifted by:
-50 ns:
-20 ns:
10 ns:
20 ns:
Extracted T0:
-47.0±4.0 ns
-19.8±2.1 ns
9.4±2.5 ns
19.0±2.3 ns
T0 shift = Ʃdi /N / const (N: number of hits
di: signed distance of circle to track)

## Slide 80
20 MHz
1600 ns revolution time
400 ns gap
TMean between 2 events: 50 ns
Drift time: ~200 ns
Event Structure -- pile-up
Event pile-up

## Slide 81
Tracking Strategy with experimental data -- 20 MHz
Hits are sorted according to their arrival time.
In case of T0 provided:
Start from T0  Collect hits in 220 ns window 
Run tracking algorithm  Assign track to right event
In case of T0 not provided:
Do tracking and T0 extraction at the same time

## Slide 82
Tracking Strategy with experimental data -- Phase I
Hits are sorted according to their arrival time.
In case of T0 provided:
Start from T0  Collect hits in 220 ns window 
Run tracking algorithm  Assign track to right event
In case of T0 not provided:
Take the earliest time of a segment of hit as T0 .  do one more iteration to optimize.

## Slide 83
83
8.4
35.9
114.1
128.2
139.0
148.3
T0 (ns) : MC Input Iter_2
9.0
0.0
#0 T0 = 9.0 ns
#1 T0 = 35.7 ns
#1 T0 = 95.3 ns
8.4
35.9
114.1
128.2
139.0
148.3
T0 (ns) : MC Input Iter_2
9.0
0.0
37.2
9.4
#0 T0 = 37.2 ns
#1 T0 = 9.4 ns
#1 T0 = 98.3 ns
8.4
35.9
114.1
128.2
139.0
148.3
T0 (ns) : MC Input Iter_2
9.0
0.0
37.2
114.5
9.4
38.2
#0 T0 = 38.2 ns
#1 T0 = 114.5 ns
#1 T0 = 115.3 ns
#1 T0 = 128.0 ns
8.4
35.9
114.1
128.2
139.0
148.3
T0 (ns) : MC Input Iter_2
0.0
37.2
114.5
140.9
116.6
9.0
9.4
38.2
#1 T0 = 116.8 ns
#1 T0 = 116.6 ns
#1 T0 = 119.0 ns
#1 T0 = 140.9 ns
8.4
35.9
114.1
128.2
139.0
148.3
T0 (ns) : MC Input Iter_2
0.0
37.2
115.3
9.0
9.4
38.2
114.5
140.9
141.1
150.9
8.4
35.9
114.1

## Slide 84
PC as data source and receiver.
Ethernet.
Optical link
FPGA
FIFO
Tracking algorithm
Ethernet via
Optical Link
Setup and Test
FIFO

## Slide 85
Block diagram of algorithm in VHDL

## Slide 86
Performance at FPGA
For one event with 100 hits (6 tracks): 7 μs
Hit reading
Road finder
Pt extraction
Pz extraction
(100 cc)
(50 cc X 6)
(120 cc X 2 X 6)
(60 cc X 2 X 6)

## Slide 87
Tracking at FPGA
Data flow: Hit information at PC  FPGA, extract helix para.  PC
PC is used to draw hits and helix in the plot. The helix parameters come from FPGA.

## Slide 88
Performance test

## Slide 89
The Latency