## Slide 1: Design Options for the JLEIC Large Aperture IR Quadrupoles
GianLuca Sabbi
Lawrence Berkeley National Laboratory
JLEIC Spring Collaboration Meeting 2019
April 1-3, 2019

## Slide 2
Layout and Parameters (V. Morozov)
Quadrupole Element | Magnetic length [m] | Inner radius [cm] | Outer Radius [cm] | Good Field Radius [cm] | Field Gradient Normal / Skew [T/m] | G x Rinner [T]
iQDS1a | 2.25 | 9.2 | 23.1 | 4 | -37.2 / -1.23 | 3.4
iQDS1b | 2.25 | 12.3 | 31.0 | 4 | -37.2 / 0.0 | 4.6
iQDS2 | 4.5 | 17.7 | 44.4 | 4 | 26.0 / 0.0 | 4.6
200 GeV/c protons
10 GeV/c electrons

## Slide 3: IR Quadrupole Design References
RHIC (130 mm, 48 T/m, 4.5K)
LHC MQXC (120 mm, 118 T/m, 1.9K)
HL-LHC MQXF (150 mm, 143 T/m, 1.9K)
LHC MQXA (70 mm, 205 T/m, 1.9K)
Nb3Sn
LHC MQXB (70 mm, 205 T/m, 1.9K)
AHF-2 (634 mm, 10.1 T/m, 1.9K)
Note: diameters refer to the coil winding

## Slide 4
Cos(nq) Coil Layout
The cos(nq) coil layout with keystone Rutherford cable has dominated the accelerator applications to date
The extension to iQDS1a appears to be relatively straightforward (although aperture is significantly larger than in design references)
Combination of very large aperture, gradient, and limited radial/axial space budget in iQDS1b/2 may require a modified approach

## Slide 5
A Preliminary Design for iQDS1a
Goals:
Perform a first-pass magnetic analysis and optimization
Obtain a preliminary design and performance parameters: cable and coil geometry, operating current, margin to quench, fringe field, magnetic length and field quality
Iterate as needed, get feedback to/from AP
Coil and yoke geometry:
Single layer coil with 15 mm width
Two coil blocks (one wedge) for control of geometric harmonics
Inner coil radius at 9.19 cm (increase ~8 mm for inner vessel)
Radial space reserved for collars: 23 mm
Outer yoke radius 23.1 cm (decrease ~6 mm for outer vessel)
Superconductor and cable:
NbTi superconductor at 4.5K
MQXC inner cable (same as LHC dipole inner cable)
Alternative options: MQXC outer cable (same as LHC dipole outer cable, LHC arc quadrupole); MQXB inner cable

## Slide 6
Design and Performance Parameters
Operating Parameters (2D) | Unit | Value
Current | kA | 9.5
Field Gradient | T/m | 38.0
Peak field in the coil (*) | T | 4.3
Lorentz force (azimuthal) | MN | 0.38
Coil stress (azimuthal) | MPa | 25
Superconducting strand | Unit | Value
Strand diameter | mm | 1.065
Critical current density (*) | kA/mm2 | 2.85
Copper/non-copper ratio |  | 1.65
Cable and coil geometry | Unit | Value
Number of strands |  | 28
Cable width | mm | 15.1
Cable thickness (min) | mm | 1.736
Cable thickness (max) | mm | 2.064
Number of turns (B1+B2) |  | 17+6
(*) 5T, 4.2K
(*) Includes strand self-field

## Slide 7
Short Sample and Margin to Quench
Short sample parameters (*) | Unit | Value
Current | kA | 14.9
Peak field | T | 6.75
Gradient | T/m | 59.6
Margins to quench (*) | Unit | Value
Operating point on the load line | % | 63.7
Fraction of critical current at Iop | % | 32.4
Temperature margin at Iop | K | 1.85
(*) based on a linear extrapolation of the peak field load line

## Slide 8
Fringe Field at the electron beamline
B along a 90 degree arc at R=240 mm
Magnetic field (By) along the x-axis
At the operating gradient, the iron yoke thickness at the magnetic mid-plane is sufficient to return all the magnetic flux
Fringe field field outside yoke is below 0.002 T at the magnetic mid-plane, and further decreasing to < 0.001 T at the pole
Note however that this case does not include radial space for He vessel/beam pipe and yoke geometry optimization to control saturation
By (y=0) detail outside the iron yoke
< 0.002 T
mm
mm
mm
deg

## Slide 9
Field Quality (2D)
Field quality optimization carried out and reported at 60 mm radius (~2/3 of aperture)
Good field radius required by beam is 40 mm: significant benefit for higher orders
Harmonics at nominal current can be optimized to << 1 “unit” (10-4 of quadrupole)
However, b6 saturation is several units (R=60 mm) in the absence of yoke optimization
Yoke optimization for saturation control will increase the fringe field: is it needed?
Random errors calculated for radial/azimuthal block displacements with ±100 mm range
Persistent current and ramp rate effects not yet analyzed – generally dominated by dipoles
9.5 kA
Saturation effect on b6 (R=60 mm)
Saturated region
Non-saturated region
Random errors (1 sigma) for 100 mm block displacements
2x16 independent variables

## Slide 10
Field Quality (3D)
Large negative contribution to b6, b10 in the ends
  Due to conductor blocks lifting away from the mid-plane as they turn around the pole
b6: -280 units peak, or -43.3 units integrated over a magnetic length (straight section equivalent) of 406.3 mm
b10: -30 units peak, or -3.1 units integrated over 406.3 mm
Integral can be corrected by body-end compensation or by end optimization – with different advantages and disadvantages
Need AP evaluation and feedback for different options
+b6, +b10

## Slide 11
Coil End Optimization
Negative b6, b10 due to turns lifting away from the mid-plane can be compensated by increasing the length of straight section for these turns. Here we increase the straight section length of the entire lower block to avoid introducing additional spacers
b6: Dz (B1)= 53 mm results in two peaks of ± 250 units which integrate to essentially zero
Additional spacers would be required to compensate b10, or to further lower the b6/b10 peaks
Spacers are also effective to control the peak field in the ends (iron needs to cover entire length to avoid a large fringe field) but will increase the magnet length requirements
+53 mm
+53 mm

## Slide 12
Magnet Length Requirements
Longitudinal space budget is one of the main challenges for the JLEIC IRs
Requires a global optimization to meet both AP requirements and technology constraints:
  Selection of operating parameters, coil design, acceptable fringe field, field quality (with implications on corrector needs), end mechanical support, leads and splices, integration of cold mass in cryostat and integration of different magnets/beamlines
A first-pass evaluation of the preliminary design will be useful to determine next steps
  Main question: do we need to increase the central gradient (with potential implications for coil design, operating temperature/margins, fringe field, forces etc.) to decrease length
Longitudinal efficiency:
Baseline (compact) end:
Coil half-length in the model: 450 mm
Magnetic length: 406.3 mm
With additional spacer:
Physical length +53 mm
Magnetic length + 44.6 mm
Requires a 17 mm increase of total coil length (both ends) to achieve the same magnetic length

## Slide 13
iQDS1b preliminary analysis
(*) Includes strand self-field
Margins to quench (*) | Unit | Value
Operating point on the load line | % | 72.2
Temperature margin at Iop | K | 1.48
(*) based on 2D peak field
Main features:
Same gradient with increase aperture
Double-layer coil with 30 mm total width
MQXC cable with lower (1/2) keystone angle
One wedge in each layer (probably not required)
Radial space for “collars”: 25 mm
Radial space for He vessel: 8mm + 8 mm
Operating Parameters (2D) | Unit | Value
Current | kA | 7.1
Copper current density | kA/mm2 | 0.46
Field Gradient | T/m | 36.7
Field at coil radius (GxRin) | T | 4.9
Peak field in the coil (2D) (*) | T | 5.67
Lorentz force (Fq 1 octant) | MN/m | 1.12
Coil and iron yoke geometry | Unit | Value
Inner coil radius | cm | 13.1
Outer yoke radius | cm | 30.2
Number of turns (L1, L2) |  | 33, 35
B [T]

## Slide 14
iQDS2 preliminary analysis
Operating Parameters (2D) | Unit | Value
Current | kA | 6.5
Copper current density | kA/mm2 | 0.42
Field Gradient | T/m | 26.2
Field at coil radius (GxRin) | T | 4.85
Peak (2D) coil field (*) | T | 5.86
Lorentz force (Fq 1 octant) | MN/m | 1.49
Coil and iron yoke geometry | Unit | Value
Inner coil radius | cm | 18.5
Inner yoke radius | cm | 24.5
Outer yoke radius | cm | 43.4
Number of turns (L1, L2) |  | 46, 49
Margins to quench (*) | Unit | Value
Operating point on the load line | % | 72.7
Temperature margin at Iop | K | 1.46
Main features:
Double-layer coil with 30 mm total width
MQXC cable with lower (1/2) keystone angle
One wedge in each layer (probably not required)
Radial space for “collars”: 30 mm
Radial space for He vessel: 8mm + 10 mm
(*) Includes strand self-field
(*) based on 2D peak field

## Slide 15
Advanced Hydrotest Facility at LANL
50 GeV synchrotron
Firing site 2

## Slide 16
AHF Final Focus System Parameters
Case 1 and Case 2 Quadrupole Requirements
AHF Large Bore Quadrupole Focusing System Parameters
Case 2 coil geometry and operating field
Reference: J. Schultz et al., IEEE TASC Vol. 13,
No. 2, June 2013, pp.1343
G x Rpipe= 2.5 T ; G x Rcoil = 3.3 T

## Slide 17
AHF-2 Cable and Coil Design at MIT
2-layer cos(2q) layout
Rutherford cable in Cu channel
Raised saddle end
3 spacers in each layer
SSC strand and cable
Dummy turns in outer layer

## Slide 18
AHF-2 Mechanical Design at MIT
Design approach and main components:
The mechanical design is based on a 30 mm thick welded stainless steel shell directly surrounding the coil which provides preload and support against the Lorentz forces
The (warm) iron yoke is not part of the mechanical support structure
The pre-load level is selected to prevent separation at the coil-pole interface up to full field
A Titanium pole is required to increase pre-load at cool-down and decrease the warm pre-load
Cable is encased in a copper channel is to cope with the high pre-load and Lorentz forces/stresses
Results of mechanical analysis:
Stresses for Ti pole are within material limits
Warm pre-loaded stage is the most critical
Comments/next steps:
New approach to address the specific design challenges, but outside established experience
Many questions: need to study in more detail, and discuss with MIT colleagues who may provide additional insights or experimental information
Range:
140-260 MPa
Compute stress in cable conduit after pre-load (with Ti pole)

## Slide 19
Shell-based structure option
The LBNL shell-based structure has replaced the traditional collars in high field/force/stress magnets
Based on an aluminum shell over iron yoke
Assembly preload provided by water-pressurized bladders and interference keys
Significant pre-load increase at cool-down due to differential thermal contraction
Main elements of the mechanical structure:
Shell-Yoke sub-assembly
  Aluminum shell
  Iron yoke
Coil-pack subassembly
  Nb3Sn Coils
  Aluminum Collars
  Load pads
Master Key assembly
  Slots for pressurized bladders
  Load keys, alignment keys
Axial rods for longitudinal pre-load
HL-LHC (MQXF) IR Quadrupole
Note however that radial space requirements for shell and bladder assembly features will further constrain the yoke optimization relative to a traditional collar-based structure

## Slide 20
Shell structure test results
Demonstrated performance in the range of interest: force and stress levels, fine control of pre-load, low pre-load at warm, large diameter (fabrication and test)
TQS quadrupole (LBNL/LARP)
FRESCA2 dipole (CERN)

## Slide 21
AHF-2 Design Study at Fermilab
Design drivers and approach:
Traditional shell type coil will suffer from stress accumulation at the mid-plane and conductor displacements during excitation
Split in mechanically decoupled blocks, for stress management and individual positioning and support
NbTi and Nb3Sn options considered
Active shielding of fringe field
Reference: V. Kashikhin et al., PAC 2003

## Slide 22
iQDS1b fringe field
B along a 90 degree arc at R=310 mm
Magnetic field (By) [T] along the x-axis
By (y=0) detail outside the iron yoke
Fringe field is ~0.25 T
Evaluate correction options
Integrate the design of electron and ion quadrupoles and beamlines

## Slide 23
iQDS2 Fringe Field
Fringe field is 0.1-0.15 T
Evaluate correction options
Integrate the design of electron and ion quadrupoles and beamlines
B along a 90 degree arc at R=240 mm
Magnetic field (By) along the x-axis
By (y=0) detail outside the iron yoke

## Slide 24: Summary
A preliminary analysis of the JELIC large aperture IR quadrupoles was performed
Parameters of first quadrupole (iQDS1a) are within established technology envelopes
  Design can be based on traditional cos2q approach: superconducting wire and cable, NbTi coil fabrication and collar-based mechanical support
  Initial parameters were provided and can be used as a starting point for further optimization (e.g. cable dimensions, operating current, collar thickness etc.)
  Field quality estimates were provided including 2D random errors, saturation effects, 3D end harmonics, and correction options
  Main issue is longitudinal space budget and optimization
  iQDS1a would be a good candidate for preliminary AP feedback on field quality and a detailed engineering exercise to establish longitudinal requirements for coil ends/transitions, current leads and splices, axial mechanical support, cooling, He contsinment and cryostat design. Results will be also useful for other magnets
The second and third quadrupoles (iQDS1b and iQDS2) require a significant extrapolation from past experience due to a combination of aperture, field gradient, radial and longitudinal space constraints
  Initial work should focus on conceptual design studies and selection of promising approach for conductor, cable, coil fabrication and mechanical structure
  Prototype fabrication and test will be required to validate the proposed design
Current radial allowances do not include any radiation shielding in the bore

## Slide 25: Additional slides

## Slide 26
iQDS1a with reduced radial envelope
In order to provide radial space for the inner and outer LHe containment and beam pipe, the inner coil radius is increased by 8 mm and the outer yoke radius is decreased by 6 mm
No change in cable parameters (15.1 mm width)
Added two turns in B1 and adjusted angles
Radial space for collars: 20 mm (-3 mm)
Margin on the load line decreases by 4.2%
Lorentz force and stress increases by ~24%
Operating Parameters (2D) | Unit | Value
Current | kA | 9.9
Field Gradient | T/m | 37.6
Peak field in the coil (*) | T | 4.63
Lorentz force (azimuthal) | MN | 0.47
Coil stress (azimuthal) | MPa | 31.1
Coil and iron yoke geometry | Unit | Value
Inner coil radius | cm | 10.0
Outer yoke radius | cm | 22.5
Number of turns (B1+B2) |  | 19+6
(*) Includes strand self-field
Margins to quench (*) | Unit | Value
Operating point on the load line | % | 67.9
Fraction of critical current at Iop | % | 36.7
Temperature margin at Iop | K | 1.65
(*) based on a linear extrapolation of the peak field load line
B [T]

## Slide 27
Fringe field at the electron beamline
Fringe field is 0.02-0.04 T
Expect further increase if yoke is optimized for low saturation
Evaluate correction needs and options:
Passive correction e.g. with iron surrounding the electron beamline
Active correction by tuning the design of the electron quadrupoles, or with a small dipole coil
B along a 90 degree arc at R=240 mm
Magnetic field (By) along the x-axis
By (y=0) detail outside the iron yoke