## Slide 1
SNS PPU Cryomodule Vacuum Vessel
Matt Marchlik
SNS PPU CRYOMODULE FDR
SNS PPU Cryomodule Vacuum Vessel
Matt Marchlik

## Slide 2: Outline
Requirements
Design
Procurement
Response to PDR Recommendations and Comments
Remaining Tasks
Summary

## Slide 3: Requirements
Vacuum Vessel will be ASME stamped vessels with a MAWP of 25 PSIG
Design pressures of 30 PSIG internal and 15 PSIA external
Interface with all necessary subsystems

## Slide 4: Requirements
Agreement between the labs defined in detail in “SNS PPU Cryomodule Pressure & Vacuum Systems” Power Point slides, by Gary Cheng, dated November 6, 2018
  To meet ORNL requirements
    The End Can vacuum shell and Vacuum Vessel will be ASME stamped vessels with a MAWP of 25 PSIG
    Design pressures of 30 psig internal and 15 psia external
  To meet JLab requirements
    Vacuum vessels will be designed and built to the intent of the ASME BPVC pressure vessel code
    Comply with JLAB’s ES&H Manual Chapter 6151
  FPC Vacuum top hats and bellows will be designed to the ASME BPVC but treated as JLab Category II vacuum components
    Consistent with the SNS HB Prototype and allows JLab to make the top hat bellows closure weld

## Slide 5: Design
The existing SNS drawings will be used for unchanged components
JLab drawings have been created to capture any changes from the original design.
This section primarily highlights any design changes

## Slide 6: Design - Vacuum Vessel Weldment
Weldment
304 SS
Comprised of the welded bodies that make up the pressure boundary and items welded to the boundary
Only the vendor, a ASME BPVC code shop, may weld to the pressure boundary.

## Slide 7: Design - Vacuum Vessel Weldment
End Flanges
Stiffener Rings
x5
JT Valve Port
Supply End
Can Port
Return End
Can Port
Lock Down Weld Pads
x24
Supply End
Can Mount Pad
Return End
Can Mount Pad
FPC Exhaust
Manifold Ports
x4
Air Side FPC Ext.
Mounts
X4 sets
FPC Exhaust Manifold Support Weld Pads

## Slide 8: Design - Vacuum Vessel Weldment
FPC Ports
x4
Instrumentation Ports
x4
Pressure Manifold Port
Vessel Restraint Brackets
x4
ISO250-K Ports x10
Interface Panel Weld Pads

## Slide 9: Design - Vacuum Vessel Assembly
End flanges x2
Parallel plate PRV
x2
Blanks
x7
Weldment
Tie downs
x24
Coupler top hats
x4
FPC Exhaust
Manifold Port Supports
x3
Port for burst disk
In CM Assembly

## Slide 10: Design - Vacuum Vessel Assembly
Interface Panel
Mounts
X4

## Slide 11: Design – End Flange Weld
The configuration matches sketch (4a) of fig.2-4 of ASME BPVC VIII-I
Radially and longitudinally self-fixturing to assist in arriving at desired tolerances
Internal circumferential weld contraction should have less impact on flange flatness than other configuration
Unchanged since PDR
(4a)
Flange flatness, location and perpendicularity to shell axis is GD&T controlled on the weldment drawing

## Slide 12: Design – Vessel End Can Ports
Originally, the return end can port of the vacuum vessel had a significantly smaller ID than that of the end can elbow
The vacuum vessel port ID has been opened up to match that of the return end can elbow
More clearance between pipes and walls
SEC has plenty of clearance
Increased vessel port
7.80 in ID
Original vessel port
6.36 in ID

## Slide 13: Design – End Can Mounting
Set screws have been added since PDR. After alignment, they are inserted to pocket face prior to welding in order to minimize weld contraction
Mounting pads are considered weld pads, do not make up the pressure boundary. Welded by JLAB during assembly
Mounting Pad
Support Mount
End Can Support Arm
Set Screws

## Slide 14: Design – End Flange Reinforcement
Unchanged since PDR
The warm to cold beam line modification outlined by K. Wilson & J. Henry requires the opening in the end flange to increase.
The new opening of 6.1 in and reinforcement was shown to be acceptable per ASME BPVC VIII-I, UG-39
Reinforcement

## Slide 15: Design – Beamline to Vessel Flange
Unchanged since PDR
There were 20 bolts making up the beamline to vacuum vessel end flange joint
Verified bolt number with calculation per BPVC VIII-I
The number of bolts has been reduced to 12
20 bolts
12 bolts

## Slide 16: Design – Beamline to Vessel Flange
Slots
+/- 5 degree rotation
Gate Valve
Rotatable CF
At the Clean Room Assembly level, the warm to cold bellows is connected to the gate valve
Rotatable CF flange at the gate valve end is utilized to accomplish the desired bellows clocking
The through holes in the end flange have been slotted to allow +/- 5 degree of misalignment to ensure studs pass through the flange

## Slide 17: Design – Warm to Cold Transitional Bellows
Original SNS Bellows
CRM9005040-0008
Successfully shipped in the past
Current Bellows
104210300-M8U-8200-A101
Analysis performed for comparison and to verify that the shorter bellows response to shipping is acceptable

## Slide 18: Design – Warm to Cold Transitional Bellows
5 g longitudinal
Max stress = 8 ksi
PDR D&MR Report Recommendation 5: Verify that the dynamic response of the warm to cold transitional joint intercept flange is not detrimental to the bellows during shipping
Transportation Load Analysis
Conservatively eliminated thermal straps
Assumed convolution geometry
4 g vertical load
Max stress = 5 ksi
* Yield = 31 ksi

## Slide 19: Design – Warm to Cold Transitional Bellows
Modal Analysis
The new bellows are shorter than the original
Mode search range: 0 – 100 Hz
Analyzed with no straps and with straps from .005” - .1”
Compared old design at mode 5 for comparison
Results
Mode 5 (longitudinal oscillation of intercept): only mode found that was not inherent to strap geometry
Original design contains longer bellows, frequency shifted down as expected
Avoids air ride trailer frequency of 1.5 – 2 Hz.
Avoids the shipping frame’s spring rate frequency of 4, 6 and 8 Hz.
Avoids 60 Hz
PDR D&MR Report Recommendation 5: Verify that the dynamic response of the warm to cold transitional joint intercept flange is not detrimental to the bellows during shipping

## Slide 20: Design – Relief Path
PDR D&MR Report Comment 10: Verify that the relief valve flow paths between the outer magnetic shielding and the vacuum vessel are adequate
23 in2
A =
Burst Disk
Opening
7 in2
The parallel plate relief flanges had a small hole, 3” ID, through the center. This is has been increased to the original 6” ID flange. Reduces chance of obstruction from MLI or other debris
The parallel plate will need to open ~.37” to equal 7in2 area of burst disk
The flow area between the outer mag shield and vac vessel is much larger at 23 in2
6 in
(28 in2)

## Slide 21: Design – End Can/Vessel Leak Checking
PDR D&MR Report Comment 4: Consider leak testing the end can to vacuum vessel connections prior to making the pipe welds
An end can extension cap inserted over the end can piping was considered
The cold mass assembly is too close to the end can piping to fit any type of cap
The vacuum vessel and end cans will be leak tested individually. Procedural controls will ensure the flanges are protected from damage from the time between initial leak test and installation. The flanges will be examined before making the vacuum vessel to end can connections.
  This is deemed an acceptable risk. The probability level of flange damage is considered to be low

## Slide 22: Procurement
Vessel weldment along with corresponding flanges will be fabricated by an ASME BPVC “code shop”
SOW (104210800-M8U-8200-A001-SOW) is approved
SOW reflects details found in the existing SNS and JLab SOW
The parallel plate relief valves will be purchased separately, are not considered part of the vacuum vessel assembly
The FPC top hats will be purchased separately
The first and last vessel will arrive with all flanges necessary for leak testing

## Slide 23: Summary
Vessel design is in good shape, > 90% complete
Vessel interfaces with other subsystems have been verified
Drawings, quantity of 21, for any design changes have been completed
Drawings have been through preliminary checking. They are in final checking/approval
Necessary calculations for proposed changes are complete. Will be turned into analysis notes and approved
SOW is written and approved
All PDR D&MRR comments and suggestions have been addressed and are considered closed

## Slide 24: Backups
PDR response table
End flange calculations
Beamline to Vacuum Bolt Number and Flange Stress Calculation
Warm to cold transition bellows dynamic loading and Modal analysis notes

## Slide 25: D&MRR Comment/Recommendation Response
D&MRR Comment/ Recommendation | Description | Response/Status
* Informal/verbal, not in D&MRR | Add weld pads to the vessel for bracket mounts. Eliminates need for weld repair to pressure boundary if fragile brackets are damaged. Slides 9 & 10 | Incorporated weld pads with tapped holes. Brackets now connect to weld pads through use of hardware instead of welding. CLOSED
Recommendation 5 | Verify that the dynamic response of the warm to cold transitional joint intercept flange is not detrimental to the bellows during shipping. Slide 19 | FEA performed. Stresses in the bellows were found to be negligible. Bellows restraint is not required for shipping. CLOSED
Comment 3 | To the extent possible, perform finite element analysis on simplified assembly models of the cryomodule Slide 20 | Modal analysis performed on the warm to cold transitional bellows. Detrimental frequencies avoided. CLOSED
Comment 10 | Verify that the relief valve flow paths between the outer magnetic shielding and the vacuum vessel are adequate Slide 21 | The flow areas are substantially larger than the areas of the valves themselves, adequate flow path is present CLOSED
Comment 4 | Consider leak testing the end can to vacuum vessel connections prior to making the pipe welds Slide 22 | Is not feasible. The risk is deemed an acceptable risk. The probability level of flange damage is considered to be low. CLOSED

## Slide 26: Backups
End Flange Calculations

## Slide 27: Backups – End Flange Calcs

## Slide 28: Backups – End Flange Reinforcement/Max Opening Calc

## Slide 29: Backups – End Flange Reinforcement/Max Opening Calc

## Slide 30: Backups – End Flange Reinforcement/Max Opening Calc

## Slide 31: Backups – End Flange Reinforcement/Max Opening Calc

## Slide 32: Backups – End Flange Reinforcement/Max Opening Calc

## Slide 33: Backups – End Flange Reinforcement/Max Opening Calc

## Slide 34: Backups
Beamline to Vacuum Bolt Number and Flange Stress Calculation

## Slide 35: Backups

## Slide 36: Backups

## Slide 37: Backups

## Slide 38: Backups

## Slide 39: Backups
Warm to cold transition bellows
dynamic loading and modal analysis notes

## Slide 40
BELLOWS DESIGN
SS CUFFS
SS BELLOWS
Cu INTERCEPT BLOCK

## Slide 41
TRANSPORT LOADING
4 g transverse acceleration loading
One analysis of .008” thick bellows
Fixed supports at each cuff end
Thermal straps not included
.008” Thick Bellows
Deflection of .007”
Stress only 5.4 ksi. Allowable is 20 ksi

## Slide 42
MODAL ANALYSIS
Modes search range of 0 – 100 Hz
Since the stiffness and behavior of braided thermal straps is very difficult to model in FEA, analyses were performed with varying thermal strap thickness in an attempt to establish a relation of mode shift to strap thickness
The original CRM bellows was analyzed as well for comparison

## Slide 43
MODAL ANALYSIS
Only one mode was found in the search range that was not strap geometry dependent
The found mode, named Mode 5, can be described as a longitudinal oscillation of the Cu intercept block

## Slide 44
MODAL ANALYSIS
As expected, the thicker bellows drives the mode higher
The original CRM bellows were found to have modes at the lowest frequency due to their longer length that the other two bellows
The graph below shows the mode behavior, with two data sets for bellows thickness and varying strap thickness

## Slide 45
ANALYSIS - SUMMARY
The newly designed PPU warm to cold bellows will survive the transport loading according to the analysis results
The modal results show that the new bellows design geometry avoids the air ride frequency of 1.5-2 Hz, the shipping frame’s spring frequency of 4, 6.5 and 8 Hz, and the 60 Hz frequency induced from AC powered equipment