## Slide 1: SNS PPU CRYOMODULE FDR
SNS PPU Cryomodule Instrumentation
Peter Owen

## Slide 2: Outline
Instrumentation Overview
Changes for PPU
Updates since PDR
  Response to Recommendations & Comments Items
SOW & Procurement Plan

## Slide 3: Instrumentation Overview
Cernox temperature sensors
Field Probe cable
Heaters
Liquid level probes
Instrumentation port flanges
Vacuum vessel pressure sensors
Helium circuit pressure transducers*
FPC instrumentation*
*Final parts provided by SNS

## Slide 4: Cernox Temperature Sensors - Cavity
Cernox Temperature Sensors (38 per CM)
  CX-1050-CU-HT-1.4L
  All mounted external to helium circuits
  Cavity, helium vessel & FPC (6 per, 24 total)
    Helium Vessel (low and high), FPC Flange, Beam Pipe, FPC 1/3 from end (x2)
    Sensors through J2 feedthroughs on instrumentation ports (slide 9)
Beam Pipe
FPC flange
FPC body (x2)
He Vessel High
He Vessel Low

## Slide 5: Cernox Temperature Sensors – End Cans
Cernox Temperature Sensors (38 per CM)
  Surge Tank (2 total)
    Surge tank sensors through J23 feedthroughs on instrumentation port #1 (slide 9)
  End Cans (12 total)
    Supply End Can (shield inlet) x 2
    Return End Can (HX HP inlet & outlet, HX LP inlet & outlet, shield outlet) x2
    10 Pin CF feedthroughs on end can top plates
Shield
exit
HX LP inlet
HX LP outlet
HX HP outlet
HX HP inlet
(2) 10 pin feedthroughs on CF
Surge tank
Shield
supply
(1) 6 pin feedthrough on CF

## Slide 6: Field Probe Cable
SNS provides the field probe with the cavities
Will use original SNS design for cable
  72 inches long, CRM9007000-1059
  SOW CRM9007000-1059 exists but need to remove reference to HOM cables
  Type N connector at warm end on instrumentation port (J6)
Gore Phaseflex cable
  0XN01R010720
FP cable through J6 feedthroughs on instrumentation ports (slide 9)
FP Cable heat sink
on thermal shield

## Slide 7: Heaters
One 100 watt heater in each helium vessel
  Kapton foil type heater mounted on G10 plate
Two heaters through each 8 pin cryogenic feedthrough
  Between cavities 1&2, and 3&4
Through J1 feedthrough on instrumentation ports (slide 9)
Cavity 1 Heater
8 pin feedthrough for two heaters between cavities

## Slide 8: Liquid Level Probes
Two liquid level probes in helium vessel #1
Single 8 pin cryogenic feedthrough on helium vessel exit
Single 10 pin feedthrough on top of vacuum vessel near return end flange
8 pin feedthrough in return header
Liquid Level Probes
Mini CF port for 10 pin feedthrough

## Slide 9: Instrumentation Flange
One instrumentation port per cavity/helium vessel
Port #1
Port #2
Port #3
Port #4
Field Probe (Type N)
Port 1 only, Surge tank CERNOX diodes, 6 pin feedthrough on mini CF
Ports 2-4 blank flange
Cavity/helium vessel & FPC CERNOX
diodes
19 pin feedthrough
Heater, Tuner motor and limit switches
19 Pin feedthrough
J2
J1
J23
J6

## Slide 10: Instrumentation Feedthrough
Liquid He Level
J8
Vacuum Pressure Gages
Port #5
(1) 6 pin feedthrough on CF
(2) 10 pin feedthroughs on CF

## Slide 11: Vacuum Vessel Pressure Sensors
Cold Cathode Gauge (2)
Convectron Gauge (1)
Isolation and pump out valve
Mounted to NW 40 flange on vacuum vessel
All JLAB supplied
Ref. P&ID
R8U-8200-P001r0
Port 5 (NW 40)
Pressure manifold at SNS

## Slide 12: Pressure Transducers
Three on end cans (supplied and installed at SNS)
  High and low pressure for primary circuit
  Surge tank pressure
30/30 dial gauge and mounts for transducers (Supplied and installed by JLab)
Typical sub atmospheric pressure transducer manifold
Isolation valve
30/30 dial gauge
Low and high pressure transducer with VCR connectors
Pump out port with VCR
Surge tank Honeywell transducer with VCR adaptor
a b c c a d

## Slide 13: FPC Instrumentation
All supplied by SNS
Additional instrumentation installed at SNS on air side components
Cold Cathode
Gauge (x2)
Electron Probe
Thermocouple
on exit cooling tube
Heater assembly (x2)
Thermocouple (x2) and thermal
switch
Window for Arc Detector

## Slide 14: FPC Instrumentation Panel
Support for FPC instrumentation connectors
Plate and connectors - Jlab
Sensors and wire - SNS
CRM-900-1000-000

## Slide 15: Changes for PPU
Changes relative to the HB spare module
Will use all Cernox temperature sensors, radiation durability (CX-1050-CU-HT-1.4L)
Added threaded mounts for the temperature sensors on the helium vessel, mechanical mounts for the end can
Eliminated the HOM connections on the four instrumentation ports
Changed one port to a mini-CF connection for the surge tank temperature sensors on Port 1
  Ports 2-4 will have a blank flange

## Slide 16: Updates since PDR
Researched current vendors and part numbers
Updated drawings with current schematics and part numbers
  CM Wiring Diagram
    104212000-M8U-8200-A001
  End Can Wiring Diagram
    104212000-M8U-8200-A002
  SNS High Beta Cryomodule Instrumentation & Control Interface Table updated
    104210200-M8U-8200-A007
Instrumentation drawings are either signed off, or final checking

## Slide 17: Updates since PDR
From the PDR Review in February

## Slide 18: SOW and Procurement Plan
Create a SOW for Field Probe Cable (CRM9000000-1028)
  Same as previous SOW, remove mention of HOM cables
  Test FP cable with cryocycling
Begin writing requisitions for instrumentation when funds are available
  Many items sole-source eg. Cernox - Lakeshore

## Slide 19
powen@jlab.org
Peter Owen
Instrumentation Overview
Changes for PPU
Updates since PDR
SOW & Procurement Plan

## Slide 20
Backup Slides

## Slide 21: CERNOX Temperature Sensors – Overview
Location | # CERNOX
Cavity (6 per) | 24
Surge Tank | 2
Supply End Can | 2
Return End Can | 10
Total | 38