## Slide 1: RadCon Overview for LERF Isotope Test
Keith Welch
RadCon Manager
September 26, 2019

## Slide 2: Outline
Controls for prompt radiation
  Shielding
  Monitoring
Controls for residual dose rates
  General requirements
  Target access/retrieval
  Estimated dose rates
Packaging and Shipping
  Transfer/packaging
  Package dose rates and classification

## Slide 3: Controls for Prompt Radiation
Shield design goals
  Maintain dose rates outside structural shielding at levels below RCA (0.05 mrem/h)
  Minimize damage/activation to components in vault
  Allow for relatively quick access to target
Shielding designated “medium” project
  Reviewed by RadCon/SCMB
  Shield is not Credited Control
Shielding

## Slide 4: Controls for Prompt Radiation
Shielding modeled with FLUKA
  Simplified geometry with 13” steel and 8” water
  Dimensionally accurate with respect to gallery above
Shielding

## Slide 5: Controls for Prompt Radiation
Dose rate at 5 kW 40 MeV
Shielding
Side View
Gallery floor
Vault ceiling
Gallery dose rate: ~ 0.02 mrem/h
Agrees well with semi-empirical calculations
Dose rate in vault at 1 meter:
~ 250 rem/h
Good for several hundred hours operation with negligible impact

## Slide 6: Controls for Prompt Radiation
RF Gallery
LERF CARMs
  Part of certified PSS
  Probes positioned appropriate for source
Surveys during run
  RSAD specifies RCD presence required to commence production run
RF gallery to be conservatively posted as RCA in target region
Monitoring

## Slide 7: Controls for Prompt Radiation
Air Monitoring
  Continuous sampling from vault using AMS-4
    Standard monitoring system used in CEBAF
  EPICS archiving
Monitoring
  RSAD threshold for operations hold point (standard practice)
  Significant activity not expected, but measurement will validate

## Slide 8: Controls for Residual Radiation
Rear shield block retracts to provide access to target
Radiator remains in place upstream within hutch
Target Access/Retrieval
Extended tool for retrieving target
Moveable shadow shield planned
Extraction procedure to be captured in RWP, rehearsed
  Target placed immediately in transport pig, hutch closed
  Pig moved to low-background area
  Gamma spec performed
  Packaging for shipment

## Slide 9: Controls for Residual Radiation
General Requirements
RWP will guide all activities
  All entries to the vault after the run has started require RCT survey/escort
  At least 8 hours decay required prior to opening shield
  Radiation levels outside shield expected < 2 mrem/h after decay
  All surfaces internal to shield will be considered contaminated
  All steps for target removal, transfer, counting and packaging to be rehearsed in full detail, procedure included in RWP

## Slide 10: Controls for Residual Radiation
Estimating Residual Dose Rates
FLUKA model used for assessing activation and residual dose rate
Beam

## Slide 11: Controls for Residual Radiation
Estimating Residual Dose Rates
30 cm dose rate at target ~ 400 mrem/h
Actual work area dose rate ~ 100 mrem/h
Beam

## Slide 12: Controls for Residual Radiation
ALARA practices for target extraction
Portable shadow shield
Target
Pig on cart
Shield design gives clear access to target
Target removal should take less than 2 minutes
Shadow shield to be evaluated during 1 kW run
RWP development underway
Detailed rehearsals to occur when installation complete
Preliminary estimate for dose during removal < 50 person-mrem

## Slide 13: Packaging and Shipping
  Dose rate from target/crucible
Once removed from hutch, crucible has 30 cm dose rate ~ 180 mrem/h
Crucible moved to southwest vault for counting/packaging
Counting configuration for unshielded count will require about 3 meter distance
Canberra ISOCS system used for analysis
Contamination control protocols invoked for all handling of crucible
May be able to count in pig

## Slide 14: Packaging and Shipping
  Package Details
DOT Spec 7A Type A
Certified for liquids
Acceptable for quantities expected for 5 kW runs
Loading sequence is video recorded for reference
Will be shipped exclusive use
Excl. use not required for 1 kW, but speeds up delivery
JLab maintains DOT hazardous materials shipping registration
Registered for FedEx Custom Critical

## Slide 15: Packaging and Shipping
  Activity Estimates and dose rate on package
Nuclide | Quantity (mCi) | DR @ Crucible surf | DR @ Pig surf | DR @ Can surf | DR @ Box surf
Cu 64 | 55 | 4400 | 165 | 75 | 16
Cu 67 | 10 | 250 | 0.05 | - | -
Ga 67 | 350 | 17500 | 70 | 25 | 6
Ga 72 | 4 | 4000 | 680 | 240 | 50
Zn 69m | 4 | 520 | 15 | 6 | 1.5
Totals | 423 | 26670 | 930 | 346 | 75
Pig
Crucible
Box
Ga-72 dose rate per mCi
Values above for 5 kW exposure and 24-hour decay
Dose rate expected to be no more than about half the values above for 1 kW and 10 hour decay
“Transport Index” expected ~1-2
  Requires “Yellow III” label
Exclusive use not required

## Slide 16: Extra Slides

## Slide 17: Extra Slides
2017 irradiation post-run survey

## Slide 18: Extra Slides
2017 irradiation post-run survey