## Slide 1
Clock/Control for Streaming Readout
William Gu & Ben Raydo
Streaming Readout VI
May 2020, CNU_virtual
1. Clock Control requirement
2. JLAB Trg/Clk/Sync/Busy overview
3. Existing studies
4. Proposed Clock/Control system
5. Feasibility studies
6. Summary

## Slide 2
1. Clock Control Requirement
Clock jitter: ~ps for ADC measurement;
Clock Time Interval Error : ~ps for TDC measurement, hit coincidence between different parts of the detector;
Phase aligned slower clocks derived from the fast system clock;
Correct (synchronized) time_zero for streaming data time stamp;
Calibration ‘events’ (detector, electronics, and timestamp etc.)
……
ADC: jitter, neighboring clocks
TDC: TIE, absolute time measurement;
jitter, if a reference exists (the width measurement)

## Slide 3
2. JLAB 12GeV Trg/Clk/Sync/Busy overview
~60
Trigger etc. (16-bit @62.5MHz)
Clock (250MHz)
Sync (Manchester Encoded)
FiberMeas(Manchester Encoded)
FiberMeas
Not_used
Not_used
Acknowledgements/Busy
TS/TD/TI_master
TI (front end)
QSFP optic transceiver
MTP Fiber assignment (8/12):
TS
SD
TD (up to 16)
TI
FronEnd Readout electronics
Same clock for the system;
Frontend electronics is Synced to one clock period (4 ns);
Delay adjustment on TI to compensate for the fiber delays;
Clock jitter: several ps;
Clock TIE: source dependent only;
Board setup/control: VME
(TS) Trigger
Supervisor
(TD) Trigger
Distribution
(TI) Trigger
Interface
Front End
TDC/ADC
Signal Distribution
VXS backplane
Signal Distribution
VXS backplane
MTP fibers

## Slide 4
3. Existing Studies
3.1 Clock recovery from SerDes
  Xilinx MGT recovered clock: jitter ~ps, but TIE ~ 100ps.
  Good enough for ADC, but not for TDC
A typical clock recovery circuit
3.2 White Rabbit Network
  Based on Etherment PTP, and Sync Ethernet (1 Gbe)
  Jitter ~ps, but TIE is sub_ns
  Clock is limited to 10MHz, and 125 MHz
3.3 CERN lpGBT
  Radiation tolerant (TID and SEU)
  But it is optimized for 40 MHz clock, and TIE ~10s ps

## Slide 5
4. Proposed Clock/Control system:
CCM
Clock
Control
Status
CCD
CCD
CCD
CCN
CCN
CCN
CCN
CCN
CCM: Clock_Control_Master
  -- control encoding, status decoding.
  The interface for machine clock source, Data acquisition, detector control and monitor, Front end electronics. The CCM may be a PCIe card sitting in the DAQ computer, or it may be built in on the CCD with an Ethernet connection to the DAQ computer
CCD: Clock_Control_Distribution
  The clock/control fanout, and status/busy accumulation. Each CCD may have some CCM functions for the subsystem test; The CCD can be chained for expandability.
CCN: Clock_Control_Node
  -- control decoding, status encoding.
  The clock/control interface to the front end electronics.
  It will be a mezz. card with the decoded control, clock, data, monitoring, and the required power to/from the carrier board (or it can be built-in on the carrier board, where a standard QSFP connector is required)
4.1 Dedicated CLOCK distribution tree using QSFP connectors
Data Acquisition

## Slide 6
Gigabit Ethernet for CCD/CCN (slow control)
Clock
Sync FiberMeas (fast control)
FiberMeas / FrontEnd Status (fast control)
Up stream
Computer / CCM / CCD_output
Down stream
Detector / CCN / CCD_input
QSFP signal assignment:
It is not expensive (Commercial !) and relatively compact:
  QSFP multimode optic transceiver $40 (~100 meters),
  Single-mode optic transceiver: $200 (~km),
  short Copper cables <$50 (~meters)
4.2 QSFP signal assignment
Gigabit Ethernet for CCD/CCN (slow control)
Tx1
Tx4
Tx3
Tx2
Rx1
Rx4
Rx3
Rx2
Tx1
Tx4
Tx3
Tx2
Rx4
Rx1
Rx2
Rx3
DataLink
DataLink
DataLink or Frontend status
Gigabit Ethernet (Slow control)
Sync etc. (Fast control)
DataLink
Clock/Status etc.
QSFP, 4 Rx 4 Tx

## Slide 7
4.3 PCB diagrams
CCM
CCN
Ext. Clock
Osc. Clock
PCI express
GBE
FPGA
Clock mux/fanOut
QSFP
+3V_in
Sync.
Reset status Data clock etc.
FPGA
Zynq
Clock synth.
QSFP
QSFP
FPGA
External IO
On-board
Photoshopped PCB
Photoshopped PCB
Sync etc./Fast control
DataLink
Gigabit Ethernet/Slow control
Clock/Status etc.
Ext.
controls

## Slide 8
4.3 PCB diagram
CCD
Osc. Clock
1/10 GBE
FPGA
Clock mux/fanOut
QSFP_’out’
QSFP_’in’
QSFP_’out’
QSFP_’out’
QSFP_’out’
GBE switch_chip
(or FPGA builtin)
Power supply
QSFP28
DAQ
Photoshopped PCB
Clock/Status etc.
Sync etc./Fast control
DataLink
Gigabit Ethernet/Slow control
Data
Control
Status

## Slide 9
4.4.1 Clock distribution (fan out tree)
4.4 Clock/Control working model
LVPEL/LVDS/optic distribution: minimum added jitter (< 1ps)
Super low jitter buffers readily available
Any frequency clock (to match with the accelerator) (> optic transceiver frequency requirement)
Lower frequency clock phase deterministic synthesizers with optional jitter cleaner: SI534x, AD9510, etc
 ~ps jitter, common clock is easily achievable
4.4.2 Slow control /asynchronous control (GBE)
The slow control is through the GBE network asynchronously. Each CCN and CCD will have a unique (16-bit) setting (MAC, also possible for a local network IP). No other buses (e.g. VME) are needed. The GBE can reprogram the CCN/CCD remotely;
The status can be accessed through the GBE network, and the dedicated links.

## Slide 10
4.4 Clock/Control distribution working model
The fast controls ( e.g. RESET ) are coded at the system clock rate, then Manchester encoded, and the control commands are generated on the minimum multiple of the front end clock periods, and distributed synchronously.
 The slower clocks on the CCN are phase aligned across the system
The CCN (and the CCD input QSFP) can initiate Fiber delay measurement by signal loopback. The measurement results can be used to compensate the delays of the synchronization commands. The requirement on the fiber latency measurement precision is half of the transmitted clock period.
4.4.3 Fast control /Clock synchronous control
Fiber latency measurement
Fast control
Delay/decoding
CCD
Synchronous fast controls
CCN#1
CCN#2
CCN#3
Time_0
Fast control
commands
Fast control
commands
CCN

## Slide 11
4.4.4 How to deal with data overflow
4.4 Clock/Control distribution working model
Option#1: using the BUSY feedback
  When the computer readout can not catch up with the data input, it can send a PAUSE fast control signal to the front end to stop the data streaming;
  Meanwhile, the front end can also send a PAUSE_REQUEST by asserting the BUSY signal indicating that the front end buffer is about to overflow.
Option#2: Automatic data drop
  The front end can drop all the data in a certain time interval (for example 100 us) if the front end can not stream the data out promptly.
  The daq computer can also drop certain time intervals, if the computer can not process them, or the data is too late.
  Because all the front end data has time stamp, and the data should be formatted in certain time buckets (100 us for example). (This also means that the front end will send ‘no data’, or empty bucket, with this time stamp to indicate no data is dropped by front end). The event recorder can keep track the data lost (either dropped by the front end or dropped by the data processor).
Both options will be designed as the option#1 is more efficient if the data loss is frequent, and option#2 is more efficient if the data loss is occasional.

## Slide 12
4.5 not just Clock/Control distribution
The CCD can also be served as the data collection board.
    The CCN (or its carrier board) serves as a front end data collection board ( >= 10 gbps ). The zero-suppression should be performed, (timestamp and BUSY are needed)
    The CCD merge the data and sends them directly to a commercial card inside the DAQ computer (for example: Xilinx VCU1525 (shown here), or Xilinx AI board VCK190 (will be available).
    The data can be processed by the online computers, or the commercial FPGA (Acceleration, or AI) boards;
CCD
CCD
CCD
CCN
CCN
CCN
CCN
CCN
~10 gbps
~100 gbps

## Slide 13
4.6 Where is the software (CODA)
DAQ server
CCM
CCD
CCD
CCD
CCN
CCN
CCN
CCN
CCN
DAQ server
VCU1525
100 GBE
DAQ server
VCU1525
100 GBE
DAQ server
VCU1525
100 GBE
DAQ server
VCU1525
100 GBE
100 GBE switch
1 GBE / 10GBE switch
Sub_system/test
QSFP28
100 GBE
1/10 GBE
Clock/Control QSFP
~10 gbps
~100 gbps
Sub_system/test

## Slide 14
4.6 Where is the software (CODA)
CONFIG: define the participating (hardware) components; CCM supplies the stable system clock. Only slow controls in this step
  reset Downloaded, Running, and Run_ended; set Configured or Error.
StartRun: Time_0 set, streaming data flows (either full streaming data, or timestamped data). Only fast controls in this step
  reset Run_ended ; set Running or Error.
Download: set up the hardware components, ready for fast controls; set up the software components; ready for data;
  reset Running, and Run_ended; set Downloaded or Error.
EndRun: data generation stops, and the downstream finish the data processing
  set Run_ended or Error.
Reset: Run sequence interrupt, it is always available.
  reset Configured, Downloaded, Running, Run_ended, and Error
Configured
Running
Downloaded
Initialized
Run ended
Error

## Slide 15
5. Feasibility studies:
5.1 FADC  VTP
5.2 VETROC  Xilinx KCU116:
QSFP: VETROC (Streaming TDC)  Xilinx KCU1500: 20 Gbps with 8b/10b encoding,
limited by the Artix-7 capability;
KCU1500  host PC: > 5 Gbyte/s with PCIe3x8;
The VTP can ‘be’ a carrier board (hosting the CCN), and generate data at >= 10 gbps
The VTP can also ‘be’ a data concentrator board, collects 16 inputs and pass the data at >= 40 gbps

## Slide 16
5.3 CC Test board:
A new version of the PCI express Trigger Interface (TIpcie) board is being prototyped. It can be used to test the proposed QSFP fiber assignments, to test the CCM, CCD, and CCN distribution tree, and data readout.
FPGA based high resolution absolute timing measurement (64-channel TDC)
also:

## Slide 17
5.3 CC Test board:
Test board configurations
CCM: PCIeQSFP
CCN: QSFPCarrierBoard
CCD: QSFPQSFP distribution
CCD: Data Concentrator (2xQSFPPCIe)
CCN: Data Acquisition (TDCQSFP)
CCD: DAQ, feeding data to computer

## Slide 18
6. Summary:
The Clock Control for streaming readout is feasible
  The dedicated clock distribution tree is easier, flexible and cost manageable;
  The SYNC can be accomplished with the fiber length measurement, and delay compensation;
  The distribution system is Ethernet controlled, does not depend on a crate (VME)
Thank You
But, depends on the radiation in the EIC, we may have to adapt the lpGBT, or other rad hard components
The Data acquisition for streaming readout
  The Front end FPGAs do the zero suppression
  Extra processing in the Xilinx (AI) board, not just the computers