## Slide 1: CLARA: Data-Stream Processing Framework
Framework for streaming readout
V. Gyurjyan for JLAB EPSCI Group

## Slide 2: Outline
Problem statement and possible solutions
  Hardware diversification
  Parallelization
  Streaming
Micro-services architecture
  Micro-service vs monolith
Flow based programming paradigm
  Reactive communication
CLARA: reactive data-stream processing framework that implements micro-services architecture and FBP
Summary

## Slide 3: Problem we face
Chart: Global Digital Data
| Y2010 | Y2011 | Y2012 | Y2013 | Y2014 | Y2015 | Y2016 | Y2017 | Y2018 | Y2019 | Y2020
Scientific | 0.7 | 0.945 | 1.155 | 1.435 | 1.785 | 2.7685 | 3.675 | 4.9 | 6.3 | 9.1 | 12.6
NonScientific | 1.3 | 1.755 | 2.145 | 2.665 | 3.315 | 5.1415 | 6.825 | 9.1 | 11.7 | 16.9 | 23.4
Experiment | Conditions | Event Rate | Data Rate | Comments
Moller | Production/ integrated mode | 1920Hz | 130MB/s | Can be handled with the traditional DAQ.
EIC | L=1034 cm-2s-1 | 450-550Hz Not included background noise rates. | 20-25GB/s not included vertex tracker that will generate ~240GB/s | ~10Kz/mb, track multiplicity = ~5 JLAB EIC detector design will have millions of channels. Only non-vertex detectors combined will have ~1M channels plus vertex detector: estimated 20-50M channels. In total ~1000 ROC’s. Control nightmare (starting stopping a run). Streaming readout has less control requirements.
TIDIS |  | rTPC hit rates enormous (~800KHz/pad) | 4GB/s | How to match up super Bigbyte detected electrons with rTPC detected spectator protons is a big question. Conventional triggered DAQ will be challenged.
SoLID | 30 sector GEM |  | 30GB/s | 30 separate DAQ’s each 1GB/s? How to combine GEM readout with other detectors? Handling GEM hits sharing adjacent sectors.
CLAS12 | Phase 2 | 100KHz | 5-7GB/s | 

## Slide 4: CPU based architecture limitations
MIPS/clock speed plateau
Squeezing more cores per
chip becomes difficult
A Roadmap for HEP Software and Computing R&D for the 2020s. HEP Software Foundation, Feb. 2018
“Frameworks face the challenge of handling the massive parallelism and heterogeneity that will be present in future computing facilities, including multi-core and many-core systems, GPUs, Tensor Processing Units (TPUs), and tiered memory systems, each integrated with storage and high-speed network interconnections.”

## Slide 5: The Scale-Cube
Scale by splitting similar things , Y-axis
such as events. Multi-threading
Scale by cloning things. X-axis
Multi-processing
Scale by splitting independent things, Z-axis
Functional decomposition
The Art of Scalability. by Martin L. Abbott and Michael T. Fisher. ISBN-13: 978-0134032801
Horizontal scaling
Vertical scaling or multi-treading
Micro-services

## Slide 6: Why decomposition into independent modules
Smaller and independent code bases. Reinforce a maximum independence and isolation of functional components.
Fault tolerant
Overall micro-services based application evolves much faster
No other dependencies other than data (loose coupling) can run on heterogeneous hardware and software infrastructures.
Relatively easy evolution, due to
  Requirement changes
  Environment changes
  Errors or security breaches
  New equipment added or removed
  Improvements to the system
Encourages contribution and inclusion of new technologies

## Slide 7: Micro-services vs Monolithic architecture
Presentation
Logic
Data
Pros
Strong coupling, network independent
Full control of your application
Cons
No agility for isolating, compartmentalizing and decoupling data processing functionalities, suitable to run on diverse hardware/software infrastructures
No agility for rapid development or scalability
Pros
Technology independent
Fast iterations
Small teams
Fault isolation
Scalable
Cons
Complexity networking (distributed system)
Requires administration and real-time orchestration

## Slide 8: FBP paradigm and reactive programming
S1
S2
S1: Proactive, responsible for change in S2
S2: Passive, unaware of the dependency
S1
S2
S1: Broadcasts it’s own result
S2: Subscribes S1 change events and changes itself
Passive programming
Reactive programming
Enables event driven stream processing
Subscriber/Consumer
Publisher/Producer
t2
t0
t1
Feedback to control backpressure
Flow based programming paradigm assumes reactive programming
Notes: express a problem in terms of transforms on streams of data

## Slide 9: CLARA Framework
Reactive, data-stream processing framework that implements micro-services architecture and FBP
Provides service abstraction (data processing station) to present user algorithm (engine) as an independent service.
Defines service communication channel (data-stream pipe) outside of the user engine.
Stream-unit level workflow management system and API
Defines streaming transient-data structure
Supports C++, JAVA, Python languages
http://claraweb.jlab.org
CLARA: A Contemporary Approach to Physics Data Processing, 2011, J. Phys.: Conf. Ser. 331 032013 doi:10.1088/1742-6596/331/3/032013
Development of A Clara Service for Neutron Reconstruction, 2011, APS: 2011APS..DNP.EA024C
Component Based Dataflow Processing Framework, 2015, IEEE DOI: 10.1109/BigData.2015.7363971, ISBN: 978 1-4799-9926-2
Earth Science Data Fusion with Event Building Approach, 2015, IEEE DOI: 10.1109/BigData.2015.7363972, ISBN: 978 1-4799-9926-2
CLARA: The CLAS12 Reconstruction and Analysis framework, 2016, J. Phys.: Conf. Ser. 762 012009 doi:10.1088/1742-6596/762/1/012009
Publications
V. Gyurjyan, S. Mancilla, R. Oyarzun, S. Paul, A. Rodrigues
Design: 2009
Betta release and first application: 2010
3 master theses
Authors and chronology
Rewards
Research Opportunities in Space and Earth Sciences (ROSES) 2015
Funding for 3 years by the NASA's Earth Science Technology Office (ESTO) and the Advanced Information Systems Technology (AIST) Program.
NAIADS Project ID: AIST-14-0014.
SRB Project ID:LARC-14-0014-2
Users
Documentation

## Slide 10: Basic components and a user code interface
Data Processing Station
Data-Stream Pipe
Orchestrator
Data Processing Station
Data processing Engine
Data Processing Micro-Service
https://claraweb.jlab.org/clara/docs/quickstart/java.html
Engine Tutorials
https://claraweb.jlab.org/clara/docs/quickstart/cpp.html
https://claraweb.jlab.org/clara/docs/quickstart/python.html
Single Interface

## Slide 11: Data Processing Station
Multi-threading
Configuration
Communication
0MQ
POSIX-SHM
In-memory Data Grid (IDG)
Runtime Environment
C++
JAVA
Python
https://github.com/JeffersonLab/clara-java.git
Language Bindings
https://github.com/JeffersonLab/clara-cpp.git
https://github.com/JeffersonLab/clara-python.git
Chart: CLAS12 Reconstruction Application Vertical Scaling
Chart: Amdahl's Law Curve Fit
configuration:
io-services:
writer:
compression: 2
services:
MAGFIELDS:
magfieldSolenoidMap: Symm_solenoid_r601_phi1_z1201_13June2018.dat
magfieldTorusMap: Full_torus_r251_phi181_z251_08May2018.dat
variation: rga_fall2018
DCHB:
variation: rga_fall2018
dcGeometryVariation: rga_fall2018
dcT2DFunc: "Polynomial"
DCTB:
variation: rga_fall2018
dcGeometryVariation: rga_fall2018
EC:
variation: rga_fall2018
mime-types: - binary/data-hipo
Chart: 
| msec(5038) | Hz(5038) | msec(4013) | Hz(4013)
farm19 | 6.78 | 147.5 | 5.8 | 172.4
farm18 | 9.73 | 102.8 | 9.51 | 105.2
farm16 | 13.2 | 75.8 | 12.17 | 82.2
farm14 | 20.67 | 48.4 | 19.89 | 50.3
2020-05-08 11:48:30.940: Benchmark results:2020-05-08 11:48:30.941:
average event time = 0.14 ms2020-05-08 11:48:30.943: MAGFIELDS 2000 events total time = 0.02 s average event time = 0.01 ms2020-05-08 11:48:30.945: FTCAL 2000 events total time = 0.26 s average event time = 0.13 ms2020-05-08 11:48:30.946: FTHODO 2000 events total time = 0.29 s average event time = 0.15 ms2020-05-08 11:48:30.948: FTEB 2000 events total time = 0.13 s average event time = 0.06 ms2020-05-08 11:48:30.949: DCHB 2000 events total time = 1126.76 s average event time = 563.38 ms2020-05-08 11:48:30.951: FTOFHB 2000 events total time = 3.93 s average event time = 1.96 ms2020-05-08 11:48:30.952: EC 2000 events total time = 1.87 s average event time = 0.94 ms2020-05-08 11:48:30.953: CVT 2000 events total time = 150.14 s average event time = 75.07 ms2020-05-08 11:48:30.955: CTOF 2000 events total time = 4.75 s average event time = 2.37 ms2020-05-08 11:48:30.956: CND 2000 events total time = 1.49 s average event time = 0.74 ms2020-05-08 11:48:30.957: BAND 2000 events total time = 0.02 s average event time = 0.01 ms2020-05-08 11:48:30.959: HTCC 2000 events total time = 0.11 s average event time = 0.05 ms2020-05-08 11:48:30.960: LTCC 2000 events total time = 0.05 s average event time = 0.03 ms2020-05-08 11:48:30.961: EBHB 2000 events total time = 1.60 s average event time = 0.80 ms2020-05-08 11:48:30.963: DCTB 2000 events total time = 988.61 s average event time = 494.30 ms2020-05-08 11:48:30.964: FTOFTB 2000 events total time = 3.98 s average event time = 1.99 ms2020-05-08 11:48:30.965: EBTB 2000 events total time = 2.86 s average event time = 1.43 ms2020-05-08 11:48:30.966: RICH 2000 events total time = 2.15 s average event time = 1.07 ms2020-05-08 11:48:30.967: WRITER 2000 events total time = 7.09 s average event time = 3.55 ms2020-05-08 11:48:30.968: TOTAL 2000 events total time = 2296.38 s average event time = 1148.19 ms

## Slide 12: Data Stream Pipe
https://github.com/JeffersonLab/xmsg-java.git
Language Bindings
https://github.com/JeffersonLab/xmsg-cpp.git
https://github.com/JeffersonLab/xmsg-python.git
req
rep
OMQ / POSIX_SHM / IDG
Transient Stream Unit
Google ProtoBuf
Meta-data
Serialization
Encryption

## Slide 13: Workflow orchestrator
Orchestrator
Hardware Optimizations
Service Registration/Discovery
Data-Set Handling
and Distribution
Farm (batch or cloud) Interface
Application Deployment
and Execution
Application Monitoring,
Real-time Benchmarking
Command-Line Interface
Exception Logging and Reporting

## Slide 14: CLAS12 Data Processing Applications
MAGF
FCAL
FTHODO
FTEB
DCHB
FTOFHB
EC
CVT
EBTB
FTOFTB
DCTB
EBHB
LTCC
HTCC
BAND
CND
CDG
Data Quality Assurance
Event Reconstruction Application
J/
Data Provisioning
Physics Analysis Application
Data Acquisition System

## Slide 15: Heterogeneous data-stream processing (LDRD-2018)
Detector reconstruction services (DRS)
Cluster, segment finder
Road finder
Detector 1
Sector 1
SIS
SIS
SIS
SIS
VTP
Stream interface services (SIS)
Runs on FPGA
0 suppression
Electronic noise removal
Flash ADCs/TDCs
VXI Crate
Detector N
Sector N
ERS 1
EP
DRS X
DSTP
ERS N
ANAS 1
ANAS 2
ANAS N
Detector reconstruction services (DRS)
Full detector reconstruction
Calibration, alignment
Kalman filter
Note: some DRS services might run on GPGPU/TPU
Event persistency
Raw data
Some detectors might need
other detector’s data to
complete their reconstruction.
Event reconstruction services
DST persistency
Reconstructed data
Analysis services
Note: FPGA based CLARA service’s code base (C++) will be deployed in CPU first for
verification and quality control, and only after will be deployed into FPGAs.
To use existing hardware in a streaming mode data must be reduced while streaming.
DRS
DRS
SRS
Sector reconstruction services (SRS)
Geometry matching
Partial software trigger
SSP
EBS
EB service (GT) or CODA (triggered)
VXS

## Slide 16: Hall-B VTP Test-setup 2
FADC
Clara Test Implementation
Hall B VTP Test 2
(emulates multi-stream system: stream/FADC)
FADC
FADC
VTP
CSS
SRO10
CSS
CSS
CSS
CSS
CSS
CSS
CSS
CSS
CSS
CSA
CSA
CSA
CSP
CER
10Gb/sec
Stream Source
Stream Aggregator
Event Recorder
Stream Processor

## Slide 17: Summary
To address scientific data 3V expansion we need to design frameworks capable of leveraging data streams, as well as massive parallelism and heterogeneity of feature computing facilities.
CLARA is a mature data stream processing framework that utilizes micro-services architecture and flow-based programming paradigm, currently in production-use at JLAB and NASA Langley.
CLARA together with JANA are being tested on the Hall-B SRO test-setup 2 for evaluation, and setting up a foundation for an integrated data processing framework for future experiments at home and elsewhere.
Thank you

## Slide 18
Backups

## Slide 19: Structure
FE
Service Layer
Orchestration Layer
Registration
DPE
SC
SC
DPE
SC
SC
DPE
SC
SC
DPE
SC
SC
gateway
security
Local Registration
Local Registration
Local Registration
Local Registration
Meta-Data
Data
ZeroMQ(xMsg)
in-Memory Data-Grid
POSIX Shared Memory (FIPC)

## Slide 20: Event Reconstruction Application (sub-event level parallelization)
FCAL
FTHODO
FTEB
DCHB
FTOFTB
EC
CVT
EBTB
CTOFTB
DCTB
EBHB
LTCC
HTCC
RICH
CND
MAGF
FTOFHB

## Slide 21: Heterogeneous deployment algorithm
FCAL 0.08ms
FTEB 0.05ms
FHOD 0.05ms
DCHB 34.05ms
DCTB 63.7ms
FTOF 1.16ms
EBTB 0.38ms
EC 0.75ms
EBHB 0.37ms
LTCC 0.05ms
HTCC 0.14ms
CTOF 0.19ms
Processing Node/DPE
Clara
Monitor
Server
InfluxDB
service
Grafana
DB
claraweb.jlab.org
JSON data-format
Binary/HIPO
DST
Remote
Client
Histogram
Analyzer
Archiver
DB
RS
0.07ms
WS
0.25ms
FCAL HS/TLS
FHOD HS/TLS
FTEB HS/TLS
DC HS/TLS
CTOF HS/TLS
EC HS/TLS
HTCC HS/TLS
LTCC HS/TLS
EB HS/TLS
Monitor Node/DPE
Filter
TLS
DST
Data
DST
WS
DST Node/DPE/process
CLARA micro-service
Can be deployed as a separate process or
a thread within a process. Multi-threaded
CLARA transient data-stream
Message passing through pub-sub middleware. No dependencies between micro-services.
FCAL 0.08ms
FTEB 0.05ms
FHOD 0.05ms
DCHB 34.05ms
DCTB 63.7ms
FTOF 1.16ms
EBTB 0.38ms
EC 0.75ms
EBHB 0.37ms
LTCC 0.05ms
HTCC 0.14ms
CTOF 0.19ms
Processing Node/DPE
Clara
Monitor
Server
InfluxDB
service
Grafana
DB
claraweb.jlab.org
JSON data-format
Binary/HIPO
DST
Remote
Client
Histogram
Analyzer
Archiver
DB
RS
0.07ms
WS
0.25ms
FCAL HS/TLS
FHOD HS/TLS
FTEB HS/TLS
DC HS/TLS
CTOF HS/TLS
EC HS/TLS
HTCC HS/TLS
LTCC HS/TLS
EB HS/TLS
Monitor Node/DPE
Filter
TLS
DST
Data
DST
WS
DST Node/DPE/process
CLARA micro-service
Can be deployed as a separate process or
a thread within a process. Multi-threaded
CLARA transient data-stream
Message passing through pub-sub middleware. No dependencies between micro-services.
FCAL 0.08ms
FTEB 0.05ms
FHOD 0.05ms
DCHB 34.05ms
DCTB 63.7ms
FTOF 1.16ms
EBTB 0.38ms
EC 0.75ms
EBHB 0.37ms
LTCC 0.05ms
HTCC 0.14ms
CTOF 0.19ms
Processing Node/DPE
Clara
Monitor
Server
InfluxDB
service
Grafana
DB
claraweb.jlab.org
JSON data-format
Binary/HIPO
DST
Remote
Client
Histogram
Analyzer
Archiver
DB
RS
0.07ms
WS
0.25ms
FCAL HS/TLS
FHOD HS/TLS
FTEB HS/TLS
DC HS/TLS
CTOF HS/TLS
EC HS/TLS
HTCC HS/TLS
LTCC HS/TLS
EB HS/TLS
Monitor Node/DPE
Filter
TLS
DST
Data
DST
WS
DST Node/DPE/process
CLARA micro-service
Can be deployed as a separate process or
a thread within a process. Multi-threaded
CLARA transient data-stream
Message passing through pub-sub middleware. No dependencies between micro-services.
FCAL 0.08ms
FTEB 0.05ms
FHOD 0.05ms
DCHB 34.05ms
DCTB 63.7ms
FTOF 1.16ms
EBTB 0.38ms
EC 0.75ms
EBHB 0.37ms
LTCC 0.05ms
HTCC 0.14ms
CTOF 0.19ms
Processing Node/DPE
Clara
Monitor
Server
InfluxDB
service
Grafana
DB
claraweb.jlab.org
JSON data-format
Binary/HIPO
DST
Remote
Client
Histogram
Analyzer
Archiver
DB
RS
0.07ms
WS
0.25ms
FCAL HS/TLS
FHOD HS/TLS
FTEB HS/TLS
DC HS/TLS
CTOF HS/TLS
EC HS/TLS
HTCC HS/TLS
LTCC HS/TLS
EB HS/TLS
Monitor Node/DPE
Filter
TLS
DST
Data
DST
WS
DST Node/DPE/process
CLARA micro-service
Can be deployed as a separate process or
a thread within a process. Multi-threaded
CLARA transient data-stream
Message passing through pub-sub middleware. No dependencies between micro-services.
In-Process SHM
Farm Node
Java-DPE
In-Memory Data-Grid
FTOF
DCHBc
EC
C++-DPE
DCHBg
Pg=
Pc=

## Slide 22: Data-quantum size and GPU occupancy
FCAL 0.08ms
FTEB 0.05ms
FHOD 0.05ms
DCHB 34.05ms
DCTB 63.7ms
FTOF 1.16ms
EBTB 0.38ms
EC 0.75ms
EBHB 0.37ms
LTCC 0.05ms
HTCC 0.14ms
CTOF 0.19ms
Processing Node/DPE
Clara
Monitor
Server
InfluxDB
service
Grafana
DB
claraweb.jlab.org
JSON data-format
Binary/HIPO
DST
Remote
Client
Histogram
Analyzer
Archiver
DB
RS
0.07ms
WS
0.25ms
FCAL HS/TLS
FHOD HS/TLS
FTEB HS/TLS
DC HS/TLS
CTOF HS/TLS
EC HS/TLS
HTCC HS/TLS
LTCC HS/TLS
EB HS/TLS
Monitor Node/DPE
Filter
TLS
DST
Data
DST
WS
DST Node/DPE/process
CLARA micro-service
Can be deployed as a separate process or
a thread within a process. Multi-threaded
CLARA transient data-stream
Message passing through pub-sub middleware. No dependencies between micro-services.
FCAL 0.08ms
FTEB 0.05ms
FHOD 0.05ms
DCHB 34.05ms
DCTB 63.7ms
FTOF 1.16ms
EBTB 0.38ms
EC 0.75ms
EBHB 0.37ms
LTCC 0.05ms
HTCC 0.14ms
CTOF 0.19ms
Processing Node/DPE
Clara
Monitor
Server
InfluxDB
service
Grafana
DB
claraweb.jlab.org
JSON data-format
Binary/HIPO
DST
Remote
Client
Histogram
Analyzer
Archiver
DB
RS
0.07ms
WS
0.25ms
FCAL HS/TLS
FHOD HS/TLS
FTEB HS/TLS
DC HS/TLS
CTOF HS/TLS
EC HS/TLS
HTCC HS/TLS
LTCC HS/TLS
EB HS/TLS
Monitor Node/DPE
Filter
TLS
DST
Data
DST
WS
DST Node/DPE/process
CLARA micro-service
Can be deployed as a separate process or
a thread within a process. Multi-threaded
CLARA transient data-stream
Message passing through pub-sub middleware. No dependencies between micro-services.
FCAL 0.08ms
FTEB 0.05ms
FHOD 0.05ms
DCHB 34.05ms
DCTB 63.7ms
FTOF 1.16ms
EBTB 0.38ms
EC 0.75ms
EBHB 0.37ms
LTCC 0.05ms
HTCC 0.14ms
CTOF 0.19ms
Processing Node/DPE
Clara
Monitor
Server
InfluxDB
service
Grafana
DB
claraweb.jlab.org
JSON data-format
Binary/HIPO
DST
Remote
Client
Histogram
Analyzer
Archiver
DB
RS
0.07ms
WS
0.25ms
FCAL HS/TLS
FHOD HS/TLS
FTEB HS/TLS
DC HS/TLS
CTOF HS/TLS
EC HS/TLS
HTCC HS/TLS
LTCC HS/TLS
EB HS/TLS
Monitor Node/DPE
Filter
TLS
DST
Data
DST
WS
DST Node/DPE/process
CLARA micro-service
Can be deployed as a separate process or
a thread within a process. Multi-threaded
CLARA transient data-stream
Message passing through pub-sub middleware. No dependencies between micro-services.
FCAL 0.08ms
FTEB 0.05ms
FHOD 0.05ms
DCHB 34.05ms
DCTB 63.7ms
FTOF 1.16ms
EBTB 0.38ms
EC 0.75ms
EBHB 0.37ms
LTCC 0.05ms
HTCC 0.14ms
CTOF 0.19ms
Processing Node/DPE
Clara
Monitor
Server
InfluxDB
service
Grafana
DB
claraweb.jlab.org
JSON data-format
Binary/HIPO
DST
Remote
Client
Histogram
Analyzer
Archiver
DB
RS
0.07ms
WS
0.25ms
FCAL HS/TLS
FHOD HS/TLS
FTEB HS/TLS
DC HS/TLS
CTOF HS/TLS
EC HS/TLS
HTCC HS/TLS
LTCC HS/TLS
EB HS/TLS
Monitor Node/DPE
Filter
TLS
DST
Data
DST
WS
DST Node/DPE/process
CLARA micro-service
Can be deployed as a separate process or
a thread within a process. Multi-threaded
CLARA transient data-stream
Message passing through pub-sub middleware. No dependencies between micro-services.
In-Process SHM
Farm Node
Java-DPE
In-Memory Data-Grid
FTOF
EC
C++-DPE
DCHBg
set data-quantum size

## Slide 23: Data-processing chain per NUMA
FCAL 0.08ms
FTEB 0.05ms
FHOD 0.05ms
DCHB 34.05ms
DCTB 63.7ms
FTOF 1.16ms
EBTB 0.38ms
EC 0.75ms
EBHB 0.37ms
LTCC 0.05ms
HTCC 0.14ms
CTOF 0.19ms
Processing Node/DPE
Clara
Monitor
Server
InfluxDB
service
Grafana
DB
claraweb.jlab.org
JSON data-format
Binary/HIPO
DST
Remote
Client
Histogram
Analyzer
Archiver
DB
RS
0.07ms
WS
0.25ms
FCAL HS/TLS
FHOD HS/TLS
FTEB HS/TLS
DC HS/TLS
CTOF HS/TLS
EC HS/TLS
HTCC HS/TLS
LTCC HS/TLS
EB HS/TLS
Monitor Node/DPE
Filter
TLS
DST
Data
DST
WS
DST Node/DPE/process
CLARA micro-service
Can be deployed as a separate process or
a thread within a process. Multi-threaded
CLARA transient data-stream
Message passing through pub-sub middleware. No dependencies between micro-services.
FCAL 0.08ms
FTEB 0.05ms
FHOD 0.05ms
DCHB 34.05ms
DCTB 63.7ms
FTOF 1.16ms
EBTB 0.38ms
EC 0.75ms
EBHB 0.37ms
LTCC 0.05ms
HTCC 0.14ms
CTOF 0.19ms
Processing Node/DPE
Clara
Monitor
Server
InfluxDB
service
Grafana
DB
claraweb.jlab.org
JSON data-format
Binary/HIPO
DST
Remote
Client
Histogram
Analyzer
Archiver
DB
RS
0.07ms
WS
0.25ms
FCAL HS/TLS
FHOD HS/TLS
FTEB HS/TLS
DC HS/TLS
CTOF HS/TLS
EC HS/TLS
HTCC HS/TLS
LTCC HS/TLS
EB HS/TLS
Monitor Node/DPE
Filter
TLS
DST
Data
DST
WS
DST Node/DPE/process
CLARA micro-service
Can be deployed as a separate process or
a thread within a process. Multi-threaded
CLARA transient data-stream
Message passing through pub-sub middleware. No dependencies between micro-services.
FCAL 0.08ms
FTEB 0.05ms
FHOD 0.05ms
DCHB 34.05ms
DCTB 63.7ms
FTOF 1.16ms
EBTB 0.38ms
EC 0.75ms
EBHB 0.37ms
LTCC 0.05ms
HTCC 0.14ms
CTOF 0.19ms
Processing Node/DPE
Clara
Monitor
Server
InfluxDB
service
Grafana
DB
claraweb.jlab.org
JSON data-format
Binary/HIPO
DST
Remote
Client
Histogram
Analyzer
Archiver
DB
RS
0.07ms
WS
0.25ms
FCAL HS/TLS
FHOD HS/TLS
FTEB HS/TLS
DC HS/TLS
CTOF HS/TLS
EC HS/TLS
HTCC HS/TLS
LTCC HS/TLS
EB HS/TLS
Monitor Node/DPE
Filter
TLS
DST
Data
DST
WS
DST Node/DPE/process
CLARA micro-service
Can be deployed as a separate process or
a thread within a process. Multi-threaded
CLARA transient data-stream
Message passing through pub-sub middleware. No dependencies between micro-services.
FCAL 0.08ms
FTEB 0.05ms
FHOD 0.05ms
DCHB 34.05ms
DCTB 63.7ms
FTOF 1.16ms
EBTB 0.38ms
EC 0.75ms
EBHB 0.37ms
LTCC 0.05ms
HTCC 0.14ms
CTOF 0.19ms
Processing Node/DPE
Clara
Monitor
Server
InfluxDB
service
Grafana
DB
claraweb.jlab.org
JSON data-format
Binary/HIPO
DST
Remote
Client
Histogram
Analyzer
Archiver
DB
RS
0.07ms
WS
0.25ms
FCAL HS/TLS
FHOD HS/TLS
FTEB HS/TLS
DC HS/TLS
CTOF HS/TLS
EC HS/TLS
HTCC HS/TLS
LTCC HS/TLS
EB HS/TLS
Monitor Node/DPE
Filter
TLS
DST
Data
DST
WS
DST Node/DPE/process
CLARA micro-service
Can be deployed as a separate process or
a thread within a process. Multi-threaded
CLARA transient data-stream
Message passing through pub-sub middleware. No dependencies between micro-services.
In-Process SHM
Farm Node
Java-DPE
Start DPE pined to a NUMA socket.
In-Process SHM
NUMA 1
Back pressure control
NUMA 0
Java-DPE

## Slide 24: Results
Chart: Rate vs. Threads for a Single NUMA Socket CLAS12 Reconstruction Application: v. 5.9.0, Data File: clas_004013.hipo, NUMA 0
Xeon E5-2687A | 1.9797 | 3.9162 | 5.8281 | 7.7481 | 9.6022 | 11.5181 | 13.6768 | 16.1005 | 17.8742 | 20.3735 | 22.4215 | 24.4339 | 27.1003 | 29.3485 | 32.9815 | 32.345 | 34.1763 | 32.6904 | 35.2195 | 35.0508 | 36.3725 | 37.9651 | 37.0737 | 36.1272 | 35.9324 | 39.3649 | 39.9574 | 38.6001 | 40.7056 | 39.7562 | 41.6204 | 40.8942
Xeon Gold 6148 | 3.0201 | 5.9691 | 8.6705 | 11.4775 | 14.2032 | 16.8473 | 19.7837 | 22.748 | 25.3443 | 25.8933 | 27.0856 | 28.1188 | 28.7191 | 30.3183 | 31.2891 | 31.8539 | 32.8623 | 33.415 | 34.188 | 34.2153
Chart: 
| 1.0 | 2.0 | 3.0 | 4.0 | 5.0 | 6.0 | 7.0 | 8.0 | 9.0 | 10.0 | 11.0 | 12.0 | 13.0 | 14.0 | 15.0 | 16.0 | 17.0 | 18.0 | 19.0 | 20.0
 | 3.4491 | 6.9865 | 10.3835 | 13.8179 | 17.327 | 20.8478 | 24.2307 | 27.5533 | 30.8674 | 33.9866 | 36.9094 | 40.4476 | 43.4657 | 46.49 | 49.2368 | 52.2739 | 54.9149 | 58.0271 | 60.8643 | 63.7484
 | 1.9797 | 3.9162 | 5.8281 | 7.7481 | 9.6022 | 11.5181 | 13.6768 | 16.1005 | 17.8742 | 20.3735 | 22.4215 | 24.4339 | 27.1003 | 29.3485 | 32.9815 | 32.345 | 34.1763 | 32.6904 | 35.2195 | 35.0508
 | 3.0201 | 5.9691 | 8.6705 | 11.4775 | 14.2032 | 16.8473 | 19.7837 | 22.748 | 25.3443 | 25.8933 | 27.0856 | 28.1188 | 28.7191 | 30.3183 | 31.2891 | 31.8539 | 32.8623 | 33.415 | 34.188 | 34.2153
AMD EPYC 7502 : 1.5MHz, 128/128, NUMA-2
Xeon E-2687A: 2.6GHz, 32/32, NUMA-2
Xeon Gold 6148: 2.4GHz, 40/40, NUMA-4
NUMA socket physical core limit for each node
Chart: CLAS12 Reconstruction Application Vertical Scaling
Chart: CLAS12 Reconstruction Application Vertical Scaling Amdahl's Law Curve Fit
99.5% parallel efficiency over physical cores