## Slide 1: Science Networks
Eli Dart, Network Engineer
ESnet Science Engagement
Lawrence Berkeley National Laboratory
NUG User Facilities SIG
Berkeley, CA
June 24, 2020

## Slide 2: Outline
Science Networks – structure and relationship to the rest of the Internet
Key elements of high performance data transfer
Data transfer at HPC facilities
Data portals – past, present, and future

## Slide 3: What Is A Science Network?
Moving data between facilities happens via the network
  (unless you’re shipping disks…)
  What does “via the network” actually mean?
  What is “the network” anyway?
Most of us are familiar with the notion of an ISP
  Internet access at home (Netflix, etc.)
  Data for phones (Facebook, maps, Google, etc.)
  This is “the Internet” that most people see
Science networks interconnect scientific sites
  HPC facilities
  Particle accelerators (LHC, light sources, …)
  Data portals
Science networks use the same protocols as the rest of the Internet
  They are also connected to the rest of the Internet

## Slide 4: The Internet
The Internet is composed of a large number of individual networks
  Each is run by some entity for its own reasons
    Google
    US Department of Defense
    Ford Motor Company
    US Department of Energy
    AT&T
    Many many many many many more….
  Each network connects to other networks for its own reasons
In general, networks are more valuable when connected to each other
  But remember – this connectivity happens for selfish reasons
  Not all networks are the same – each exists for its own reasons

## Slide 5: Selected networks and their missions
Notes: Blue-toned networks are science networks

## Slide 6: Selected networks and their missions
Notes: Blue-toned networks are science networks

## Slide 7: Notes about different networks
The previous diagram is a drastic simplification
  http://www.caida.org/research/topology/as_core_network/2015/
Key points:
  All networks exist for a specific reason
    Some networks provide connectivity between networks
    Some networks primarily serve their own users
    Some networks provide services to users who access them via different networks (e.g. Google)
  These lines are blurry, but it’s a useful way to think about it
Network mission influences engineering, policy, reliability, etc.
  Not all networks are built the same way
  Not all networks can support all use models
  Science networks have a different traffic profile than commercial networks

## Slide 8: Science Networks Are Built For Science
Commodity networks often throttle high-speed flows
  What does a multi-gigabit traffic spike mean?
  Commodity: another DoS attack - this should be stopped!
  R&E: another scientist doing normal things - this is core mission!
Commodity networks often have packet loss
  This is bad, as we’ll see in a minute
Common theme: R&E networks are engineered to support science while commodity networks are not
  This shouldn’t surprise anyone - high speed science is what we’ve been doing for years

## Slide 9: Effective Use Of Science Networks – Science DMZ
Networks are an essential part of data-intensive science
  Connect data sources to data analysis
  Connect collaborators to each other
  Enable machine-consumable interfaces to data and analysis resources (e.g. portals), automation, scale
Performance is critical
  Exponential data growth
  Constant human factors
  Data movement and data analysis must keep up
Effective use of wide area (long-haul) networks by scientists has historically been difficult
© 2014, Energy Sciences Network
Notes: Human factors – attention span, ability to manage complexity – these are constant
There is a huge amount of promise in data-intensive science. Effective use of networks can help realize those benefits.
The Science DMZ model helps address the difficulties scientists often experience with using networks.

## Slide 10: The Central Role of the Network
The very structure of modern science assumes science networks exist: high performance, feature rich, global scope
What is “The Network” anyway?
  “The Network” is the set of devices and applications involved in the use of a remote resource
    This is not about supercomputer interconnects
    This is about data flow from experiment to analysis, between facilities, etc.
  User interfaces for “The Network” – portal, data transfer tool, workflow engine
  Therefore, servers and applications must also be considered
What is important? Ordered list:
  Correctness
  Consistency
  Performance
© 2014, Energy Sciences Network
Notes: Networks are key. However, the user interface runs on systems at the edges.
The ordered list of important items is derived from the users of the network:
1) If a tool doesn’t behave correctly, the tool is broken – get another tool
2) If the tool doesn’t behave consistently, I can’t organize my life
3) Among the tools that behave correctly and consistently, choose the tool with the required performance that is easiest to use

## Slide 11: Performance At Different Data Scales
This table available at:
http://fasterdata.es.net/fasterdata-home/requirements-and-expectations/
© 2014, Energy Sciences Network
Notes: This succinctly describes what the end to end data path must achieve – network, hosts, storage, application
Green: <= 100Mbps Throughput (almost all domestic locations can do this) – less than Fast Ethernet!
Black: 100Mbps to 10Gbps Throughput (most major research institutions can do this, if its running clean)
Blue 10Gbps to 100Gbps Throughput (emerging at major locations)
Orange > 100Gbps Throughput (future for many)
Note: 1TB/hour and 100TB/week fit easily within 10G of throughput

## Slide 12: TCP – Ubiquitous and Fragile
Networks provide connectivity between hosts – how do hosts see the network?
  From an application’s perspective, the interface to “the other end” is a socket
  Communication is between applications – mostly over TCP
TCP – the fragile workhorse
  TCP is (for very good reasons) timid – packet loss is interpreted as congestion
  Packet loss in conjunction with latency is a performance killer
  Like it or not, TCP is used for the vast majority of data transfer applications (more than 95% of ESnet traffic is TCP)
© 2014, Energy Sciences Network
Notes: The application sees the network as a socket.
The socket interface does not provide path diagnostics or other troubleshooting information.
TCP behaves as it does because of measures taken in the 1980s to fix the congestion collapse of the Internet
TCP makes a promise to the application – TCP will get the data to the other end, or TCP will return an error. TCP makes no promises about performance.

## Slide 13: A small amount of packet loss makes a huge difference in TCP performance
Metro Area
Local
(LAN)
Regional
Continental
International
Measured (TCP Reno)
Measured (HTCP)
Theoretical (TCP Reno)
Measured (no loss)
With loss, high performance beyond metro distances is essentially impossible
© 2014, Energy Sciences Network
Notes: This is an annotated version of the plot from the Science DMZ paper
Beyond your metro area, zero loss is essentially required for high performance
Where are your collaborators? Where are your users?
When global collaboration is the norm, nobody can afford to be a local-only resource

## Slide 14: Working With TCP In Practice
Far easier to support TCP than to fix TCP
  People have been trying to fix TCP for years – only some success
    RFC1323
    Buffer autotuning
  Like it or not we’re stuck with TCP in the general case
Pragmatically speaking, we must accommodate TCP
  Sufficient bandwidth to avoid congestion
  Zero packet loss
  Verifiable infrastructure
    Networks are complex
    Must be able to locate problems quickly
    Small footprint is a huge win – small number of devices so that problem isolation is tractable
© 2014, Energy Sciences Network
Notes: Do not underestimate the value of three TCP improvements:
RFC1323 (window scaling)
Kernel autotuning
Improved congestion algorithms
However, loss + latency is still a performance killer.
TCP must be accommodated – this is our job as engineers and architects

## Slide 15: Putting A Solution Together
Effective support for TCP-based data transfer
  Design for correct, consistent, high-performance operation
  Design for ease of troubleshooting
Easy adoption is critical
  Large laboratories and universities have extensive IT deployments
  Drastic change is prohibitively difficult
Cybersecurity – defensible without compromising performance
Borrow ideas from traditional network security
  Traditional DMZ
    Separate enclave at network perimeter (“Demilitarized Zone”)
    Specific location for external-facing services
    Clean separation from internal network
  Do the same thing for science – Science DMZ
© 2014, Energy Sciences Network
Notes: In order to accommodate TCP, we need a pragmatic engineering solution that:
Addresses the needs
Is implementable given financial, policy, and cultural constraints
Can be defended – we cannot ignore security

## Slide 16
Dedicated Systems for Data Transfer
Network Architecture
Performance Testing & Measurement
  Data Transfer Node
High performance
Configured specifically for data transfer
Proper tools
Science DMZ
Dedicated network location for high-speed data resources
Appropriate security
Easy to deploy - no need to redesign the whole network
perfSONAR
Enables fault isolation
Verify correct operation
Widely deployed in ESnet and other networks, as well as sites and facilities
The Science DMZ Design Pattern
© 2014, Energy Sciences Network
Notes: The Science DMZ design pattern is a set of composable ideas, including:
The architectural element itself – the Science DMZ enclave
Appropriate security that does not impact performance
Dedicated systems – Data Transfer Nodes
perfSONAR
The elements of the Science DMZ can be combined in a variety of ways depending on the need

## Slide 17: Abstract or Prototype Deployment
Add-on to existing network infrastructure
  All that is required is a port on the border router
  Small footprint, pre-production commitment
Easy to experiment with components and technologies
  DTN prototyping
  perfSONAR testing
Limited scope makes security policy exceptions easy
  Only allow traffic from partners
  Add-on to production infrastructure – lower risk
© 2014, Energy Sciences Network

## Slide 18: Science DMZ Design Pattern (Abstract)
© 2014, Energy Sciences Network
Notes: This is an abstract cartoon – nobody’s network looks exactly like this
The diagram has no management LAN, no terminal servers, etc.
However, this is the minimum network diagram that shows the essential Science DMZ components:
Science DMZ enclave
DTN
perfSONAR (in the WAN, at the border, in the Science DMZ)
Security policy controls

## Slide 19: Local And Wide Area Data Flows
© 2014, Energy Sciences Network
Notes: The green data path is susceptible to TCP performance problems stemming from packet loss combined with long distances
The red data path is very low latency – loss matters much less here (though too much loss will still cause problems)
Remember the throughput vs. latency graph

## Slide 20: Supercomputer Center Deployment
High-performance networking is assumed in this environment
  Data flows between systems, between systems and storage, wide area, etc.
  Global filesystem often ties resources together
    Portions of this may not run over Ethernet (e.g. IB)
    Implications for Data Transfer Nodes
“Science DMZ” may not look like a discrete entity here
  By the time you get through interconnecting all the resources, you end up with most of the network in the Science DMZ
  This is as it should be – the point is appropriate deployment of tools, configuration, policy control, etc.
Office networks can look like an afterthought, but they aren’t
  Deployed with appropriate security controls
  Office infrastructure need not be sized for science traffic
© 2014, Energy Sciences Network

## Slide 21: Supercomputer Center
© 2014, Energy Sciences Network
Notes: Applying the Science DMZ design patterns to a supercomputer center
Note global filesystem – avoids double-copy workflow between DTNs and compute resources
DTNs are not part of major computational resource, and so are not entangled with its config
Science DMZ does not look discrete – however, the elements are here
Firewall appropriately placed
Security for major resources and DTNs implemented in network core
PerfSONAR for performance assurance

## Slide 22: Supercomputer Center Data Path
© 2014, Energy Sciences Network
Notes: DTNs are not part of major computational resource, and so are not entangled with its config
They are part of the filesystem – the DTNs are the external interface to the filesystem.

## Slide 23: The Petascale DTN Project
Built on top of the Science DMZ model
Effort to improve data transfer performance between the DOE ASCR HPC facilities at ANL, LBNL, and ORNL, and also NCSA.
  Multiple current and future science projects need to transfer data between HPC facilities
  Performance goal is 15 gigabits per second (equivalent to 1PB/week)
  Realize performance goal for routine Globus transfers without special tuning
Reference data set is 4.4TB of cosmology simulation data

## Slide 24: DTN Cluster Performance – HPC Facilities

## Slide 25: Science Data Portals
Large repositories of scientific data
  Climate data
  Sky surveys (astronomy, cosmology)
  Many others
  Data search, browsing, access
Many scientific data portals were designed 15+ years ago
  Single-web-server design
  Data browse/search, data access, user awareness all in a single system
  All the data goes through the portal server
    In many cases by design
    E.g. embargo before publication (enforce access control)

## Slide 26: Legacy Portal Design
Very difficult to improve performance without architectural change
  Software components all tangled together
  Difficult to put the whole portal in a Science DMZ because of security
  Even if you could put it in a DMZ, many components aren’t scalable
What does architectural change mean?
Notes: Legacy portal model:
Web server with filesystem-level access to data store
CGI, perl/python, database, etc. for portal logic all run on the web server
Evolved in place over 15-ish years
Need to work smarter not harder – re-think the architecture

## Slide 27: Architectural Examination of Data Portals
Common data portal functions (most portals have these)
  Search/query/discovery
  Data download method for data access
  GUI for browsing by humans
  API for machine access – ideally incorporates search/query + download
Performance pain is primarily in the data handling piece
  Rapid increase in data scale eclipsed legacy software stack capabilities
  Portal servers often stuck in enterprise network
Can we “disassemble” the portal and put the pieces back together better?
  Use Science DMZ as a platform for the data piece
  Avoid placing complex software in the Science DMZ
Notes: Back to data portals now – how can we take the traditional data portal apart and optimize the pieces for scalability and for deployment in a Science DMZ?

## Slide 28: Legacy Portal Design
Notes: So, how do we fix this?
Borrow ideas from commercial Internet - CDNs

## Slide 29: Next-Generation Portal Leverages Science DMZ
Notes: Portal logic still runs in the enterprise network.
However, instead of handing out pointers to data objects stored within the portal server, the portal hands out pointers to data objects stored on the big filesystem and accessible via the DTNs.

## Slide 30: Put The Data On Dedicated Infrastructure
We have separated the data handling from the portal logic
Portal is still its normal self, but enhanced
  Portal GUI, database, search, etc. all function as they did before
  Query returns pointers to data objects in the Science DMZ
  Portal is now freed from ties to the data servers (run it on Amazon if you want!)
Data handling is separate, and scalable
  High-performance DTNs in the Science DMZ
  Scale as much as you need to without modifying the portal software
Notes: Key point – the portal hands users references to data objects stored elsewhere. Because those data objects are tied to a name (the Globus endpoint in this case, but it could be any tool), the infrastructure behind that name can be scaled as much as it needs to be scaled….all without touching the portal code.
Large-scale computing facilities can now handle the big data objects, and the portal just needs to refer back to the appropriate service running at the computing facility.

## Slide 31: Data Portal Implications
Portals hold a lot of valuable data
  Observations (sky surveys, satellite data, genomes, etc.)
  Many have been in place for years
Most are inadequate to support large-scale analysis
  Legacy search/query interfaces
  Legacy access protocols/tools
  This is in the process of changing
The technology exists to radically improve the utility of data portals
  What should the performance expectation be?
  HPC facilities can do 1PB/week – if data portals could do this…

## Slide 32: NCAR RDA Performance to DOE HPC Facilities
1.5TB data set
1121 files

## Slide 33: Summary
Science networks are engineered to support data-intensive science
  Related to and connected to the rest of the Internet, but different
Science DMZ model effectively connects data infrastructure to networks
  If you need to send your sysadmin to me, feel free
Globus at HPC facilities makes terascale to petascale data transfers possible
Huge opportunity in upgrading data portals to use Science DMZ, DTNs, advanced tools (e.g. Globus)
  Make large data repositories available for analysis at HPC facilities

## Slide 34: In conclusion – ESnet’s vision:
    Scientific progress will be completely unconstrained by the physical location of instruments, people, computational resources, or data.

## Slide 35: Links and Lists
  ESnet fasterdata knowledge base
    http://fasterdata.es.net/
  Science DMZ paper
    http://www.es.net/assets/pubs_presos/sc13sciDMZ-final.pdf
  Science DMZ email list
    Send mail to sympa@lists.lbl.gov with subject "subscribe esnet-sciencedmz”
  perfSONAR
    http://fasterdata.es.net/performance-testing/perfsonar/
    http://www.perfsonar.net
  Globus
    https://www.globus.org/
© 2015, Energy Sciences Network

## Slide 36: Thanks!
Eli Dart
Energy Sciences Network (ESnet)
Lawrence Berkeley National Laboratory
http://my.es.net/
http://www.es.net/
http://fasterdata.es.net/