## Slide 1: BigBite shower and preshower current status
Arun Tadepalli – Jefferson Lab
Bogdan Wojtsekhowski – Jefferson Lab
Eric Fuchey – University of Connecticut
Mark Jones – Jefferson Lab

## Slide 2: BigBite spectrometer
Major upgrade to 6 GeV version of BigBite
  4 GEM chambers
    INFN
  GRINCH Cerenkov
    W&M
  1 GEM chamber
    UVa
  Preshower
  Scintillator plane
    Glasgow
  Shower
  Will be the electron arm

## Slide 3: Purpose of shower and preshower
27 layers of blocks
7 blocks per each layer
Shower and preshower will be the trigger for all these experiments
Lot of changes made since the last collaboration meeting
Figure credit: Nandhu

## Slide 4
Before de-cabling and disassembling preshower

## Slide 5: Right side removed
Honeycomb sheet
Mu metal sheet
Rubber sheets
Timing hodoscopes
*left-right convention when looking downstream

## Slide 6: Left side removed

## Slide 7: Current status
Blocks were cleaned, tested and painted (the square side that is opposite to the PMT)
Albert has been working on wrapping up the blocks
Needs to be installed and cabling needs to be re-attached
DAQ cables need to be attached
Cosmic commissioning needs to be done

## Slide 8: Work on shower
Replaced the inefficient shower blocks with more efficient shower blocks
Installed alternating layers of thick and thin mu-metal sheets in between different layers and on the side
Re-attached the PMT bases

## Slide 9: Shower status and plan
Replaced (previously adjusted) top layers of inefficient shower blocks with good preshower blocks
The HV bases for the shower have been installed

## Slide 10: Shower status
100 m long BNC cables for shower completed
Next step is to start cabling up the front end shower electronics
Install the cosmic counter on top of the shower

## Slide 11: List of remaining tasks - shower
Ask Hall C technicians for help with making whatever cables we need
Attach the cables for the updated trigger logic from the patch panels
Check for any light leaks
Make sure that all the cable connectors are intact
Cosmic counter connected but HV connection need to be labeled and identified in the software
Check if the cables are connected properly
Make sure the current on the HV bases are ok by turning on one layer at a time and observing the base current. Make sure that they are mapped correctly by checking the signals from the DAQ side
Check the shape of the amplitude distribution from each module
Take data at different high voltage settings
Perform gain matching studies for the shower (Mark’s code) and make sure that the 𝛂 value is satisfactory
Make documentation

## Slide 12: List of remaining tasks - preshower
Install the magnetic shield items (blue plate, smaller plate and spacers)
Make inlet for gas flow for each preshower block housing
Move preshower blocks from EEL building
Install the preshower modules in place (rubber piece goes at the bottom*)
Install the red u-channel and cable support angle bar
Attach the cables
Steps are identical as mentioned in the previous slide (steps 1 - 11)

## Slide 13: DAQ for shower and preshower
Switch to CODA 3 ( B. Moffit)
Setup TS and TD in VXS crate ( B. Moffit, A. Camsonne, M. Jones)
  Setup fast clear for the FASTBUS ADC/TDC
    Need to run optical fiber from TD to FASTBUS TI. Fiber carries the readout signal and crate busy signal
    Fast clear ECL cable from TS to FASTBUS back plane card
    ADC Gate/TDC stop cable from TS to FASTBUS back plane card
Pedestal readout with pulser trigger to test system (E. Fuchey, A. Tadepalli, M Jones)
Cosmic data for shower (E. Fuchey, A. Tadepalli, M Jones)
  Use shower sum of two layers as the trigger.
Cosmic data for preshower (E. Fuchey, A. Tadepalli, M Jones)
  Use separate scintillator paddles as trigger

## Slide 14
Thank you

## Slide 15
2018/08/13
15
Global scheme: BB Ecal and trigger logic + preliminary timing
Patch panel somewhere?
NB: #?? in gray corresponds to item number on item liste table
(1)
(2)
#11
#1
#13
#14
#15
#12
#16
#17
#18
#19
#2
#4
#3
#4
#5
#6
#7
#10
#20
#8 (1)
#8 (2)
#8 (3)
#21
#22
#9
#23
#25
#24
If Δt3-4 <250 ns (to be measured), we can use 500 ns cables to delay ADC.
Notes: 7/14/20
15
15