## Slide 1
HPS DAQ updates
Sergey Boyarinov
JLAB
Nov 18, 2020

## Slide 2: HPS DAQ & Trigger Requirements
20kHz event rate
100MB/s data rate
>95% livetime
Achieved event rate 27kHz

## Slide 3: HPS DAQ/Trigger Front-End Electronics
3 VXS crates, 2 servers, 1 ATCA crate, 7 Readout Controllers

## Slide 4: HPS DAQ Status
- Calorimeter Readout: 442 channels of 12bit 250MHz Flash ADCs
- Hodoscope Readout: 32 channels of 12bit 250MHz Flash ADCs
CPU/VTP/TS/SD/TD trigger and signal distribution boards
3 VXS crates
2 servers with TIpcie cards for SVT readout
SVT readout (front-end and ATCA blades)
Back-end computing and software is CLAS12 facility: network, computing, DAQ software, data monitoring, messaging system, realtime database

## Slide 5: Main development for future run
Two new TIpci boards were received from production and currently under testing
TIpci was tested in servers where old version failed, and it works now, servers recognize it as standard PCI device
Library being developed
More boards will be produced, then we will be able to send one to SLAC
SVT readout have to be adjusted using new TIpci boards

## Slide 6
Better PCIe compatibility:
Xilinx UltraScale+ FPGA: xcku3p
PCIexpress from gen1x1 (low power) to gen3x8 (high bandwidth)
More like a VME TI:
TI fiber#1, fiber#5
40-pin IO to the second front panel
  8 outputs + 1 clock output; (LVDS, 3 optional ECL)
  10 inputs + 1 clock input; (any diff. level)
More potentials:
Another 64 LVDS connection to the FPGA:
  64-channel FPGA based TDC
USBC connector on the front panel
  +5V in for standalone operation
Two prototypes under testing, more boards are ordered
New TIpcie module

## Slide 7: DAQ Status
All hardware and software on JLAB side is ready to run any time, except new TIpci boards
SVT part is removed
Integration with SVT DAQ has to be repeated again because of new TIpcie module, it has to be discussed and planned (test setup at SLAC)
If SVT readout performance improved we can increase overall DAQ performance (without SVT, DAQ can run >30kHz)