## Slide 1: SBS DAQ
February 17th 2021
Alexandre Camsonne
SBS collaboration meeting

## Slide 2: Outline
Overview
Bigbite
  Shower
  GRINCH
  Hodoscope
  GEM
Superbigbite
  HCAL
  Recoil polarimeter
  CDet
LHRS
Floor plan
Cabling
Network
Timeline

## Slide 3: First SBS run group
GEn-RP
  HCAL
  BigBite
  RP
nTPE
WAPP
GMn
  HCAL
  BigBite

## Slide 4: SBS DAQ subsystems and manpower
BigBite
  Shower : Mark, Arun
  Hodoscope : Rachel, Ralph
  GEM
    INFN : Evaristo, Ezekiel
    UVA : Kondo, Anruda, Thir
    BigBite : Holly, Xinzhan
HCal : Scott, Juan Carlos
Gen RP
  Scintillators : Brad
  UVA GEMs : Kondo, Anruda, Thir
LHRS : Bob, Maria
Helicity : Paul, Bob
Beamline : David, Bob, Paul
DAQ : Alexandre Camsonne, Bryan Moffit, Ben Raydo

## Slide 5: SBS configuration GMn/Gen/Gen RP
 |  | Channels | Modules | Nb modules | On-hand | Ordered | Installed | Needed
BigBite | Shower | 189 | FADC | 12 | 1 | 2 | 0 | 
 | Preshower | 54 | FADC | 4 | 0 | 4 | 0 | 
 | Scintillator | 180 | V1190 | 2 | 2 |  | 2 | 
 |  | 64 | V792 | 4 | 2 |  | 2 | 
 | Cerenkov | 550 | VETROC | 6 | 6 |  | 6 | 
 |  |  | V792 | 4 | 4 |  | 4 | 
 | GEM INFN | 14000 | MPD | 23 | 23 |  | 7 | 
 | GEM UVA | 113000 | MPD | 77 | 77 |  | 0 | 
BigBen |  |  |  |  |  |  |  | 
 | HCAL | 288 | FADC | 19 | 18 |  | 18 | 
 |  |  | F1 | 5 | 5 |  | 5 | 
 | CDet | 2520 | VETROC | 13 |  | 13 |  | 
HRS |  |  |  |  |  |  |  | 
 | S2m | 32 | FADC | 2 | 2 |  | 2 | 
 | S0/Cerenkov | 12 | FADC | 1 | 1 |  | 1 | 
 | PRL | 68 | FADC | 4 | 4 |  | 0 | 
 | A1 | 22 | FADC | 2 | 2 |  | 2 | 
 | VDC | 1536 | 1877 | 16 | 16 |  | 16 | 
 | BPM/Raster | 12 | FADC | 1 | 1 |  | 1 | 
RP |  |  |  |  |  |  |  | 
 | Proton Large Angle | 96 | FADC | 6 | 4 |  | 0 | 
 | Active analyzer | 32 | FADC | 2 | 0 |  | 0 | 
 |  |  | TDC | 1 |  |  | 0 | 

## Slide 6: New trigger rates GMn
Gen/RP

## Slide 7: HCAL rates
GEN-RP coincidence : 1.25 MHz x 10 KHz x 50 ns = 625 Hz

## Slide 8: GMn data rates
 |  |  |  | Trigger rate : | 5000 |  |  |  |  |  |  | 
Column1 | Column2 | Column3 | Column4 | Column5 | Column6 | Column7 | Column8 | Column9 | Column10 | Column11 | Column12 | Column13
 | Rate per cm2 | Rate per plane | hits in 325 ns | occupancy | strip hits | XY | 6 samples | bytes | Rate MB/s |  | Rate | Rate MB/s
1 | 65 | 390 | 126.75 | 20% | 443.625 | 887.25 | 5323.5 | 21298 | 106.49 |  | 1.06E+08 | 106.49
2 | 80 | 480 | 156 | 24% | 546 | 1092 | 6552 | 26208 | 131.04 |  | 1.31E+08 | 131.04
3 | 85 | 1020 | 331.5 | 34% | 1160.25 | 2320.5 | 13923 | 55692 | 278.46 |  | 2.78E+08 | 278.46
4 | 85 | 1020 | 331.5 | 34% | 1160.25 | 2320.5 | 13923 | 55692 | 278.46 |  | 2.78E+08 | 278.46
5 | 85 | 1020 | 331.5 | 34% | 1160.25 | 2320.5 | 13923 | 55692 | 278.46 |  | 2.78E+08 | 278.46
 |  |  |  |  |  |  |  |  |  |  |  | 1,072.91
Samples | 20 |  |  |  |  |  |  |  |  |  |  | 
FADC |  | Event size |  |  |  |  |  |  |  |  |  | 
 | 288 | 13968 | 69.84 |  |  |  |  |  |  |  |  | 
 |  | Total | 1142.75 |  |  |  |  |  |  |  |  | 
5 KHz single arm gives 1.1 GB/s if SSP give factor 3 reduction around 300 MB/s but need to be checked

## Slide 9: Data rates Gen RP BigBite
Coincidence trigger rate expected 625 Hz
Bigbite rate : about 311 MB/s expect factor of 3 reduction from SSP about 100 MB/s
1 VXS crate with VTP readout 1.25 GB/s

## Slide 10: Data rates Gen RP polarimeter GEMS
About 300 MB/s so 100 MB/s after online reduction
Total GEM data rate about 200 MB/s , 2 VXS crates total bandwidth 2.5 GB/s , computer wth 40gigE adapter

## Slide 11: Requirement summary
Max 5 KHz trigger rate for GMn
Max 2 KHz trigger rate for Gen-RP at 30 % GEM occupancy
1 GB/s data rate

## Slide 12: Shower
243 channels lead glass
FADC readout : 10 FADC from electronics group + 6 Glasgow FADC ordered
VXS received
SoLID crate for testing with 4 FADC and VTP
Need add TDC for sums : F1
Fastbus testing with cosmics
CODA3 setup complete
Started looking at FADC preshower on FADC
To do :
  Install other FADC
  Setup with TS
  Setup FADC trigger ( optional )

## Slide 13: Bigbite DAQ ( non GEM) Full inventory
 |  | Type | Channels | Model | Number | On-hand | Ordered | Installed | Needed
BigBite | Shower | VXS |  |  | 1 | 1 |  | 1 | 
 |  | CPU |  |  | 1 | 1 |  | 1 | 
 |  | TI |  |  | 1 | 1 |  | 1 | 
 |  | SD |  |  | 1 | 1 |  | 1 | 
 |  | VTP |  |  | 1 | 1 |  | 1 | 
 |  | FADC | 243 | FADC | 12 | 1 | 6 | 0 | 9
 | Scintillator | VME64X |  |  | 1 | 1 |  | 1 | 
 |  | CPU |  |  | 1 | 1 |  | 1 | 
 |  | TI |  |  | 1 | 1 |  | 1 | 
 |  | TDC | 180 | V1190 | 2 | 2 |  | 2 | 
 |  | ADC | 64 | V792 | 4 | 2 |  | 2 | 
 |  | Clock dist |  |  | 1 | 0 |  |  | 
 | GRINCH | VXS |  |  | 1 | 1 |  | 1 | 
 |  | CPU |  |  | 1 | 1 |  | 1 | 
 |  | TI |  |  | 1 | 1 |  | 1 | 
 |  | SD |  |  | 1 | 1 |  | 1 | 
 |  | TDC | 550 | VETROC | 6 | 6 |  | 6 | 
 |  | ADC | 64 | V792 | 4 | 4 |  | 4 | 

## Slide 14: Bigbite trigger and timing

## Slide 15: L1 logic for non pipelined electronics
Scheme for GEp5, replace ECAL by BB shower
Fast L1A
Fast clear if no L2, he L2 is accepted trigger by TS
For Fastbus ADC / TDC , V792

## Slide 16: FADC inventory
FADC list |  |  |  |  | 
 |  |  |  |  | Compton
 |  | 1 | ACDI-814 HALLA |  | HCAL
 |  | 2 | B21595_25R ACC |  | HCAL
 |  | 3 | ACDI-807 HALLA |  | HCAL
 |  | 4 | ACDI-412 PHY |  | HCAL
 |  | 5 | ACDI-407 PHY |  | HCAL
 |  | 6 | ACDI-806 HALLA |  | HCAL
 |  | 7 | ACDI-823 HALLA |  | HCAL
 |  | 8 | ACDI-809 HALLA |  | HCAL
 |  | 9 | ACDI-812 HALLA |  | HCAL
 |  | 10 | ACDI-420 PHY |  | HCAL
 |  | 11 | ACDI-818 HALLA |  | HCAL
 |  | 12 | ACDI-820 HALLA |  | HCAL
 |  | 13 | ACDI-821 HALLA |  | HCAL
 |  | 14 | ACDI-813 HALLA |  | HCAL
 |  | 15 | ACDI-822 HALLA |  | HCAL
 |  | 16 | ACDI-824 HALLA |  | HCAL
 |  | 17 | ACDI-864 HALLA |  | HCAL
 |  | 18 | ACDI-863 HALLA |  | HCAL
 |  | 19 | ACDI-811-HALL-A |  | HCAL
 |  | 20 | ACDI-817-HALL-A |  | HCAL sum
LHRS |  | 19 | ACDI-762 PHY |  | S2ML
 |  | 20 | ACDI-786 PHY |  | S2MR
 |  | 21 | ACDI-201 HALL A |  | Gas Cerenkov S0
 |  | 22 | ACDI-783 PHY |  | A1
 |  | 23 | ACDI-748 PHY |  | Raster/BPM
 |  | 24 | ACDI-794 PHY |  | PRL
 |  | 25 | ACDI-819-HALL-A |  | PRL
 |  | 26 | ACDI-807-HALL-A |  | PRL
 |  | 27 | ACDI-862-HALL-A |  | PRL
SBS |  | 28 | ACDI-237-HALL-A |  | Raster BPM
 |  | 29 | ACDI-211-HALLA |  | Hall C
 |  | 16 |  |  | 

## Slide 17: Grinch
550 channels with NINO
VXS crate, TI and SD
6 VETROC readout
CODA3 upgrade complete

## Slide 18: Hodoscope
180 channels scintillator readout with NINO
CAEN TDC V1190
1 VME64X crate with TI
2 V792 ADC for calibration
CODA3 upgrade complete
Data taking on going
To do :
  Fast clear with TS
  Add FADCs if available
V792 in high background : either use Fastbus or FADC

## Slide 19: HCAL
288 channels
FADC readout : 16 + 2 FADC
5 F1 TDCs
CODA3 setup
Taking cosmics and LED
Need setup DAC
Digital trigger ( optional )

## Slide 20: Recoil polarimeter
96 + 32 channels
FADC readout
Crate will be installed in Bigbite weldment

## Slide 21: CDet
2520 channels
MAPMT readout and NINO readout
Fastbus for testing
VETROC ordered
VXS ordered
Starting CODA3 setup and testing VETROC

## Slide 22: GEM
UVA clean room
  Taking cosmics using VME readout
  CODA3 setup
  Optical readout set up but not in use
  Issue of low efficiency in some module being investigated
INFN clean room
  Taking cosmics using VME readout
  Optical readout set up but not in use
  Instabilities issues solved with hardware replacement and increase of low voltage
  Starting using CODA3

## Slide 23: GEM continued

## Slide 24: GEM continued

## Slide 25: GEM continued
BB GEM setup
  1 VME crate
  1 VXS crate with SSP TI and SD
  GEM readout being setup on tedbbdaq
  Space in TEDF being cleaned up for GEM layer installation in BigBite in December
  3 VXS crate on site
  Optical to VXS adapter ordered : 80 MPDs per VXS crate
  Need 3 VTPs
  16 Optical to VXS adapter : 400 $ x 16 = 6400 $

## Slide 26: GEM

## Slide 27: GEM

## Slide 28: GEM timeline
Zero-suppression and common mode suppression ongoing
Debugging INFN, UVA chambers
VTP readout testing : end of April
GEM move and cabling in Hall A
High rate test around May

## Slide 29: MPD
Issue of noise on optical link
Need (small redesign of board)
Nilanga ordering 5 MPDs, will order 3 for SOLID

## Slide 30: LHRS
S0 2PMTs : FADC
S2m 16 PMTs : FADC
PRL 68 channels : FADC
768 VDC channels : 3 Fastbus
Upgrading to CODA3, intel CPU and new TI
Need fiber trunk for TI fiber installed

## Slide 31: Cable list
https://docs.google.com/spreadsheets/d/1gPhDCgyxigeVbjGXxMINClUUzg42ZZZJy8PBZF-zLAc/edit?usp=sharing

## Slide 32: Cable and rack layout from Eric
RP crate
Network

## Slide 33: Bigbite weldment cable trays

## Slide 34: Network upgrade
Install new router and fibers in March
10 gigE available in Hall A, 40 gigE to DAQ computer
Need buy install fibers to SBS weldment

## Slide 35: Timeline
TS setup End of February
Network upgrade March
Move to Hall A April
Cabling SBS helicity crates / BPM / scalers
Stand alone DAQs running May
Test high rate data May

## Slide 36: Purchases
Required
  TI fibers installation for HRS
  3 VTP for GEMs = 3 x 10K$
  FADCs
Useful / practical
  Router SBS weldment 10 K$
  GEM VME readout / firmware update
    6 TI = 6 x 3K$ = 18 K$
    6 VME CPU = 6 x 3K$ = 18 K$

## Slide 37: Documentation
No special safety documentation, included in other detectors
Wiki documentation for test stands
  https://hallaweb.jlab.org/wiki/index.php/SBS_DAQ_meetings
  https://hallaweb.jlab.org/wiki/index.php/SBS_DAQ:_GEM_EEL_Cleanroom_setup
  https://hallaweb.jlab.org/wiki/index.php/SBS_DAQ:_GEM_TEDF_BigBite_setup
Need to finalize documentation of Hall data taking after move in Hall A in May

## Slide 38: Conclusion
Most hardware on hand
FADC for hodoscope and Grinch would be nice but shower has priority ( Shortage of Hall A FADCs )
All systems taking data now
Network upgrade and VTP readout gives headroom for rate
Some items to be ordered
  3 VTP = 30 K$
  Optical to VXS adapter = 6.4 K$
  TI fiber installation ~ 10 K$
  GEM VME readout : 36 K$