## Slide 1
CORE: wiki and RHIC/AGS presentation highlights
CORE meeting, June 14, 2021

## Slide 2
CORE wiki is up!
The CORE wiki is public, but hosted at JLab, so a JLab account is needed for editing.
  Off-site access is straightforward
  Instructions for registering are on the wiki page.
The wiki has direct links for editing subscription details for all CORE mailing lists.

## Slide 3
K0 ID
Ks  p+p- decays (ct = 2.68 cm) can be measured in the outer part of the tracker
  Ks with all momenta can be measured, but the efficiency will drop with momentum.
  p/p+ ID in the DIRC will distinguish Ks  p+p- from L  pp-.
The Belle II KL-m (KLM) system
KL will be detected in the KLM/Hcal, which will provide a precise angular measurement
  pT for a single neutral hadron can be obtained from pT balance
  For a single neutral hadron, n/KL ID can be obtained from hermeticity and baryon conservation (target baryons stay near the beam)
Tracker optimization

## Slide 4
4𝜋 EMcal
Both the endcap and barrel could be projective
The small-angle EMcal could be SciGlass.
PWO (1-2%) for electron hemisphere: (up to 2p, h < 0 coverage)
W-Shashlyk (6%?) for hadron hemisphere: (h > 0 coverage)
Projective modules in the barrel
Non-projective modules in the endcap
Photons from DVCS on 4He (YR)
DVCS on nuclei:
  A high-resolution EMcal in the electron hemisphere makes it possible to reconstruct the t-distribution from the DVCS photon

## Slide 5
e/𝜋 identification in the electron hemisphere
For the EIC, a clean identification of the scattered electron is essential.
The barrel region poses the greatest challenge and requires the best electron ID.
CORE addresses this issue by extending the PWO EMcal coverage up to h < 0 (or possibly -0.5)
Additional e/p suppression (at least 1:10 up to 1.2 GeV) is also provided by the DIRC.
Q2 > 1 &
y < 0.95
to the right of orange line
B. Schmookler
h = -ln(tan(q/2))

## Slide 6
Thank you!

## Slide 7
CORE systems
inner CORE in Geant (fun4all)
B. Schmookler
New 2.5 T solenoid (2.5 m long, 1 m inner radius)
Tracking: central all-Si tracker (eRD25) and h-endcap GEM tracker (eRD6)
EMcal (eRD1): PWO for h < 0 and W-Shashlyk for h > 0
Cherenkov PID (eRD14): DIRC (50 cm radius) in barrel and dual-radiator RICH in h-endcap
TOF: LGADs in e-endcap (eRD29) and a simple TOF behind the dRICH
Hcal / KL-m (KLM) detector integrated with the magnetic flux return
dRICH photosensors

## Slide 8
CORE solenoid
The CORE solenoid is 2.5 m long with a 1 m inner radius
CORE is compatible with any field in the 2 - 4 T range
2.5 T is the current baseline option
B. Schmookler
solenoid | field (T) | volume (m3) | 2020 cost (M$)
EIC-IP6 | 3 | 29 | 21
CORE | 3 | 7.8 | 8.5
CORE | 2.5 | 7.8 | 6.6
CORE | 2 | 7.8 | 4.8
cost (2020 M$) = 1.8 x 0.458 x (stored energy)0.7
M. A. Green and S. J. St. Lorant, Adv. Cryo. Eng. 39
Excellent projectivity for the field in the dual-radiator RICH.
A 1 m inner radius leaves 50 cm between the DIRC and solenoid
The field at the DIRC photosensors is less than 2 T, enabling use of MCP-PMTs:
  best performance and low technical risk

## Slide 9
CORE solenoid in opera – 2.6 T on axis at IP
CORE in opera
Field on iron surfaces
Field in the dual-radiator RICH (dRICH)
Transverse field along the line-of-sight from the IP in the dRICH
Paul Brindza