## Slide 1: The new ALICE Data Acquisition system (O2/FLP) for LHC Run 3
Vasco Barroso, Barthélémy von Haller, Konstantinos Alexopoulos, Martin Boulais, Sylvain Chapeland, Filippo Costa, Roberto Divia, Ulrich Fuchs, Claire Guyot, Jik Huijberts, Piotr Konopka, Iosif-Charles Legrand, Teo Mrnjavac, George Raduta, Adam Wegrzynek, Pierre Vande Vyvre on behalf of the ALICE O2/FLP project

## Slide 2: Outline
ALICE Upgrade
ALICE O2/FLP portfolio
First operational experience

## Slide 3: ALICE Upgrade

## Slide 4: ALICE Upgrade
An overview
ALICE upgrades during the LHC Long Shutdown 2
Online Offline (O2) system
new computing facility
on line tracking & data compression
50kHz PbPb event rate

## Slide 5: ALICE Upgrade
O2 computing system
First Level Processors
Detector
HI run 3.5 TB/s
Storage
Event Processing Nodes
HI run 130 GB/s
9000 links
488 readout cards
HI run 900 GB/s

## Slide 6: ALICE Upgrade
O2 computing software
Guiding principles:
  Clean-sheet design
  Leverage existing 3rd party tools

## Slide 7: ALICE O2/FLP portfolio

## Slide 8: Detector readout
Readout cards
CRU
LHCb PCIe40
Intel Arria 10
PCIe Gen 3
472 cards
CRORC
ALICE Run 2 legacy
Xilinx VIRTEX6
PCIe Gen 2
16 cards

## Slide 9: Detector readout
Servers: the FLPs (First Level Processors)
Dell PowerEdge R740
Up to 3 CRUs
96 GB RAM
2x Xeon Silver 4210 (10 cores) (1)
202 servers
(1) A few nodes with 2x Xeon Gold 6230 (20 cores)

## Slide 10: Detector readout
Software
Readout
ReadoutCard
Data readout process
Launched on each FLP
Written in C++
Writte in C++ (python bindings)
High level interface for accessing and controlling the readout cards
Uses Portable Driver Architecture (PDA)
CHEP 2023 talk Thu 14:15
S. Chapeland, Commissioning of the ALICE readout software for LHC Run 3

## Slide 11: Quality Control
QC Framework
QC GUI
Sample, process, merge, check, aggregate, store
Covers both online and offline worlds
Written in C++
Web-based: Javascript, nodejs
Visualize and interact with QC objects
Uses JSROOT
CHEP 2023 talk Tue 12:00
P. Konopka, The ALICE Data Quality Control

## Slide 12: Experiment Control System
AliECS
AliECS GUI
Direct control of the tasks running in FLP and QC nodes
Overall orchestration of ALICE data taking activities
Written in Go
Web-based: Javascript, nodejs
Deploy/shutdown tasks, start/stop runs
CHEP 2023 poster Tue 15:30
T. Mrnjavac, The ALICE Experiment Control System in LHC Run 3

## Slide 13: Operational Services
Monitoring, Logging, Configuration, Bookkeeping
Monitoring
Modular stack: telegraf + Kafka + Influxdb + Grafana
C++ library to inject metrics from O2 tasks
Logging
InfoLogger in-house tool for application logs
ELK (Elastic, Logstash, Kibana) stack for system logs

## Slide 14: Operational Services
Monitoring, Logging, Configuration, Bookkeeping
Configuration
C++ library to access config from O2 tasks
Consul for key/value store, service discovery
Bookkeeping
Web-based: Javascript, nodejs, mariadb, gRPC
Electronic logbook
CHEP 2023 poster Tue 15:30
G. Raduta, Bookkeeping, a new logbook system for ALICE
CHEP 2023 talk Tue 15:00
G. Raduta, Security Models for ALICE Online Web-Based Applications

## Slide 15: First operational experience

## Slide 16: First operational experience
Data rates limits
Aggregated
1.24 TB/s
Per FLP
650 GB/s design value
12.5 GB/s line rate
network
10-11 GB/s
8.6 GB/s design value
11 GB/s
10 GB/s

## Slide 17: First operational experience
Run types
SYNTHETIC
Replay of MC data
1-1200 GB/s readout
COSMICS
Commissioning
85 GB/s readout
PHYSICS p-p
pp collisions at 500 kHz
500 GB/s readout
PHYSICS Pb-Pb (1)
130 GB/s storage
PbPb collisions at 50 kHz
2 GB/s storage
No writing to storage
30 GB/s storage
900 GB/s readout
(1) expected

## Slide 18: First operational experience
Data taking efficiency
Chart: Data Taking Efficiency
| Q1 | Q2 | Q3 | Q4
2022 | 0.2 | 0.5 | 0.8 | 0.9
2023 | 0.5 | 0.9

## Slide 19: Key takeaways
ALICE has a brand new DAQ system
Extensive portfolio with mixture of in-house and 3rd party tools
Excellent initial performance, quite promising for Run 3

## Slide 20: Backup

## Slide 21: ALICE Upgrade
An overview
Time Projection Chamber (TPC)
New readout chambers using GEM technology
New electronics for continuous readout (SAMPA)
MUON ARM
New electronics for Muon Chambers (SAMPA)
New electronics for Muon Trigger
New Trigger Detectors (FIT)
New Central Trigger Processor (CTP)
TOF, TRD new readout electronics
PHOS, EMCAL, CPV, HMPID
improvement of readout rate with existing electronics
Common Projects:
Common Readout Unit (CRU) for all detectors (PCI card)
SAMPA common FE chip for TPC and Muon arm
ALICE upgrades during the LHC Long Shutdown 2
Online Offline (O2) system
new computing facility
on line tracking & data compression
50kHz PbPb event rate
New Inner Tracking System (ITS)
improved pointing precision
less material -> thinnest tracker at the LHC
Muon Forward Tracker (MFT)
new Si tracker
Improved MUON pointing precision

## Slide 22: ALICE Upgrade
O2 computing system
New computing system
Read-out the data of all interactions
Compress these data intelligently by online reconstruction
One common online-offline computing system: O2
Baseline correction and zero suppression
Data volume reduction.
No event discarded.
Average compression factor 4
Unmodified raw data of all interactions shipped from detector to online farm in triggerless continuous mode
Asynchronous (hours) event reconstruction with final calibration
HI run 3.5 TByte/s
Data Storage
1 year of compressed data
90 GByte/s
Tier 0, Tiers 1 and
Analysis Facilities
20 GByte/s
Data volume reduction by online tracking. Only reconstructed data to data storage.
Average compression factor 7
900 GByte/s
130 GByte/s
Requirements
LHC min bias Pb-Pb at 50 kHz
Rare physics processes with very small signal over background ratio
Triggering techniques very inefficient if not impossible
50 kHz > TPC inherent rate Support for continuous read-out
Detector Electronics
9000 GBTs links
200 First-Level Processors
Hw acc: FPGAs
IB network
350 Event Processing nodes
Hw acc: GPUs
Switching Network
Write 130 GB/s
Read 75 GB/s
Capacity: 120 PB

## Slide 23: Deployment
FLP Suite
Set of Ansible roles
In house-tool as wrapper
Deployment in production via gitlab pipeline
40-50 min for a full provisioning of all tools
Set of CI tests including run start/stop via GUI