## Slide 1: ATLAS LAr Calorimeter Commissioning for LHC Run-3
Marin FURUKAWA
The University of Tokyo
on behalf of the ATLAS LAr Collaboration
CHEP2023

## Slide 2: ATLAS Liquid Argon (LAr) Calorimeter
EMEC
(electromagnetic)
HEC
(hadronic)
Fcal
(electromagnetic & hadronic)
Measure the momentum of electrons, photon, and hadron jets.
Sampling Calorimeter Lead, copper, and tungsten as absorber material.
Liquid argon as active material.
Around 200,000 channels, EM Barrel has 4 layers, the others have 1〜4 layers depending on the regions.
The information is provided to the 1st level of the ATLAS trigger (L1 Trigger).
EM Barrel
(electromagnetic)
A-side
C-side
Presampler(PS)
Front
Back
▲Layer structure
▲LAr Calorimeter
Middle

## Slide 3
New trigger system have been installed during Long Shutdown 2 (LS2).
Under the final commissioning using Run 3 data to use as the trigger in 2023
Talk theme: Commissioning status of newly installed trigger system for LHC Run-3
LS3 and
HL-LHC
Installation
Now
Commissioning
LHC-Plan
Today’s talk
Trigger upgrade HW installation
Run 3
Run 2
LS 2

## Slide 4: Current status
Beam entered from C side to A side
Beam
Single beam Splash run is done
on 28th Mar. 2023
before having a collision
Main readout works well.

## Slide 5: Trigger readout upgrade for luminosity increase
In LHC-Run3, luminosity and pileup increased more than Run2, while ATLAS L1 Trigger keep at 20 kHz for electron and photon.
Increasing the momentum threshold for an increase in background events can miss the target signal event.
Trigger system is upgraded
Readout unit changed to 10 times finer Super cell (SC).
Whole of system replaced from analogue to digital.
▲Readout unit during Run2
SC achieves efficient object identification!
It maintains triggering efficiency
without raising the threshold.
Hadron jet
EM shower
▲Readout unit during Run3
Threshold
▲Efficiency of lowest unprescaled single EM trigger
(with legacy system)
(with digital system)
Not fully raised

## Slide 6: LAr Calorimeter Trigger System
Front-End
Back-End
L1
Trigger
Legacy
trigger system
New digital trigger system
Digitizer
Processor
124 Digitizer Boards
Digitized with 40 MHz clock,
ADC is sent in 12 bit.
Signals summed up by SC unit
(in total 34,048 SCs)
10 m
40 Tbps
Pulse from calorimeter is around 600 ns long.
200k channels
(BC at 40 MHz)
31 Processor ATCA Blades
4 AMCs (LATOME) per blade.
Signals
Main readout for analysis
Amplitude
Time [ns]
70m
25.2 Tbps
Mezzanine
114 Baseplanes on crates.
Path to the Digitizer

## Slide 7: Firmware for digital processing
Input: 5.12 GHz/fiber in total 40 fibers
Output: 11.2 GHz/fiber in total 40 fibers
Data is formed to be sent to the next stage.
The frequency is reduced to 240 MHz for easier handling in the main module.
8 SC × 16 bit ＝128 bit is sent as 1 frame to Input stage
by 320 MHz.
Momentum reconstruction
Transvers momentum magnitude and injected timing are reconstructed by “Optimal Filter”, one of the FIR computation in real-time at fixed latency 125 ns.
Bunch Crossing (BC) identification
Identify from which BC the particle came from and use its information to trigger.
+Saturation detection
Proportional to momentum
LATOME
(Intel Arria-10 FPGA)
In total 116 FPGAs
Digitizer
L1 Trigger
FPGA resource occupancy is large
92% of Logic unit
95% memory We have managed to avoid any timing violation!
Main module
*Approximately 8200 fibers.

## Slide 8: Timing Alignment for BC identification
Each digitized point is associated with BCID.
1BC
(LHC clock)
0
1
2 …
… 6
7
8 …
BCID = 7
Simple toy simulation
Amplitude
All of 4458 fibers have been scanned and fixed taking latency into account.
Injected timing is calculated for all points and the momentum and BCID that timing is 0 ns is sent to the later stage.
Important!
Matching the BCID of the LHC with the BCID assigned to each data point.

## Slide 9: Run 3 collision data after the Timing Alignment
Injected timing distribution
Data of SCs in good condition and not affected by FW configuration error are shown.
Hadronic section
EM Barrel
Momentum comparison (DT vs main readout)
5%
95%
EM Barrel
Digital triggers reach 95% more quickly and rate is lower.
In case no FW or HW errors, the digital trigger perform well as expected.
EM section will be used as main from this month.
No discrepancy

## Slide 10: Supercells status
Issue of the digitizer board, pulse shape, or the parameter to reconstruct momentum.
A board for calibration system was out of order since Apr. 2022
→ All fixed in early 2023
More than 99 % of SCs are working in good condition and no spots of malfunctioning now!
Signal caught in LAr Calorimeter
Beam splash on 28 Mar. 2023

## Slide 11: Summary
ATLAS LAr Digital Trigger system has been introduced as Phase-I upgrade.
10 times higher granularity (Supercell) to use EM shower shape to suppress multi-jet background for EM triggers.
High speed and high density digital processing system is introduced!
  More than 8200 fast links with 116 FPGAs in total.
  Momentum and timing calibration has been established.
  → 99% Super Cells are functional.
  EM trigger performance is good.
  (close to expected in Technical Design Report)
  → EM digital trigger will be used as main from this month.
LAr Calorimeter main readout is performing well
as in Run-2.

## Slide 12: Back up

## Slide 13
Inner
Outer

## Slide 14: Trigger by Shower shape
(1)
(2)
(3)
The SC with the highest incident momentum in the Middle layer is the centre.
Mean Front layer
means range for summing
←3×2 SCs
←7×2 SCs
Ratio of deposited across Front, Middle and Back to injected into one Back layer.
Spread of 𝐸_𝑇 of 3 2 SCs of Middle layer
▼Distribution of each parameter by z→ee electrons and hadron jets in

## Slide 15: Supercells status
Masked SC: Issue of LTDB, pulse shape, or the parameter to reconstruct momentum.
A board for calibration system was out of order since Apr. 2022
→ replaced with new one (early 2023)
More than 99 % of SCs are working in good condition and no spots of malfunctioning now.

## Slide 16: Baseline correction
Optimal Filter
Bipolar pulse have zero integral value with time. → Large amounts of pileups cancel each other out.
At the ends of successive BCs, the amount of pileup is not sufficient so that base line is shifted.
Pile up
Summed pulse
……
empty
Filled bunch
Bunch structure
Pulse
Baseline shift

## Slide 17
Relative difference between and

## Slide 18: Momentum comparison