## Slide 1: JUNO Offline Software for Data Processing and Analysis
Ziyan Deng, Wenxing Fang, Xingtao Huang, Teng Li, Weidong Li, Tao Lin, Zhengyun You, Jiaheng Zou
on behalf of the JUNO offline software team
May 8-12 , 2023
1

## Slide 2: Contents
JUNO Experiment
JUNO Software (JUNOSW)
    Framework
    Event Data Model
    Geometry Management System
    Event Display Tools
    Database System
    Analysis Framework
    Data Processing and Analysis Chain
Summary

## Slide 3: Jiangmen Underground Neutrino Observatory (JUNO)
JUNO is a multiple-purpose neutrino experiment currently under construction in southern China
  Large fiducial volume: 20 kton liquid scintillator detector
  Excellent energy resolution :3% energy resolution at 1MeV
  Rich physics programs:
  Reactor neutrinos: Mass Hierarchy and precision measurement of oscillation parameters
  ﻿﻿Supernova neutrinos
  ﻿﻿Geoneutrinos
  ﻿﻿Solar neutrinos
  ﻿﻿Atmospheric neutrinos
  Status:
    Finished civil construction in Dec. 2021
    Detector assembling goes smoothly now
    Expected to start data taking in 2024
“JUNO physics and detector”, Progress in Particle and
Nuclear Physics, Volume 123, March 2022, 103927

## Slide 4: JUNO Software (JUNOSW)
Data processing and analysis of neutrino experiments is different from the one of the collider experiments, i.e. reactor neutrino is detected with the Inverse Beta Decay (IBD)
  M.C. production: Event splitting and mixing -> one neutrino event splits a prompt
  and a delayed event -> complicate relations
  Physics analysis : time and vertex coincidence between the
  prompt and delayed events -> event buffering
  Large data volume and rare signal: 2 PB/year * 20 years; only ~60 reactor neutrinos per day
JUNOSW (originally called as JUNO offline) has been developed based on NuWa ( the offline software of the Daya Bay experiment) from scratch since 2012.
  Core Software: Framework, Event Data Model, Geometry Management, Database System, Analysis Framework
  Applications: simulation, calibration, reconstruction and analysis
  Modern management technologies: C++17, python3, cmake, gitlab (https://code.ihep.ac.cn/JUNO/offline/junosw)
“Modern Software Development for JUNO offline software” by Tao Lin on May 9

## Slide 5: SNiPER Framework
SNiPER (Software for Non-Collider Physics Experiment) : a general-purpose software framework
  Light weighted: only dependent on Boost.Python
  Highly modularized and extensible
  Originally developed for JUNO, but also adopted by several experiments: LHAASO, STCF, HERD, nEXO, etc.
  Key components
  Algorithm: an unit of event data proceeding
  Service: an unit for common functions that can be called by users, anywhere when necessary.
  Task: a lightweight application manager to assemble specific algorithms, service as well as sub-tasks.
  Data Buffer: a central place in memory for holding and sharing multiple events
J. H. Zou et al 2015 J. Phys.: Conf. Ser. 664 072053

## Slide 6: SNiPER Framework
SNiPER (Software for Non-Collider Physics Experiment) : a general-purpose software framework
  Light weighted: only dependent on Boost.Python
  Highly modularized and extensible
  Originally developed for JUNO, but also adopted by several experiments: LHAASO, STCF, HERD, nEXO, etc.
  Key components
  Algorithm: an unit of event data proceeding
  Service: an unit for common functions that can be called by users, anywhere when necessary.
  Task: a lightweight application manager to assemble specific algorithms, service as well as sub-tasks.
  Data Buffer: a central place in memory for holding and sharing multiple events
J. H. Zou et al 2015 J. Phys.: Conf. Ser. 664 072053

## Slide 7: SNiPER Framework
SNiPER (Software for Non-Collider Physics Experiment) : a general-purpose software framework
  Light weighted: only dependent on Boost.Python
  Highly modularized and extensible
  Originally developed for JUNO, but also adopted by several experiments: LHAASO, STCF, HERD, nEXO, etc.
  Key components
  Algorithm: an unit of event data proceeding
  Service: an unit for common functions that can be called by users, anywhere when necessary.
  Task: a lightweight application manager to assemble specific algorithms, service as well as sub-tasks.
  Data Buffer: a central place in memory for holding and sharing multiple events
J. H. Zou et al 2015 J. Phys.: Conf. Ser. 664 072053

## Slide 8: SNiPER Framework
SNiPER (Software for Non-Collider Physics Experiment) : a general-purpose software framework
  Light weighted: only dependent on Boost.Python
  Highly modularized and extensible
  Originally developed for JUNO, but also adopted by several experiments: LHAASO, STCF, HERD, nEXO, etc.
  Key components
  Algorithm: an unit of event data proceeding
  Service: an unit for common functions that can be called by users, anywhere when necessary.
  Task: a lightweight application manager to assemble specific algorithms, service as well as sub-tasks.
  Data Buffer: a central place in memory for holding and sharing multiple events
J. H. Zou et al 2015 J. Phys.: Conf. Ser. 664 072053

## Slide 9: Multi-threaded SNiPER (MT.SNiPER)
MT.SNiPER supports concurrent task of event processing based on the TBB
  A thread-safe Global Buffer is designed and implemented with a ring and configurable capacity and cordon
  All events in the Global Buffer are sorted by their time stamps
  Allow the dedicated Input Task, Worker Task, Output Task to put, take, and popup events at the same time in different threads
  Events are concurrently processed in different Worker Tasks
The multi-threaded simulation and reconstruction have
been working very well
J.H. Zou et al., J. Phys. Conf. Ser. 1085, 032009 (2018)
T. Lin et al., EPJ Web of Conferences 214, 02008 (2019)

## Slide 10
Event Data Model
Event Data Model (EDM) defining event objects for different processing stages and correlations between different event objects takes very important roles on the whole data processing and analysis
JUNO EDM is based on ROOT and takes advantage of its intrinsic powerful functions, persistency, IO streamer, scheme evolutions, run time type Information etc.
T. Li et al., J. Phys. Conf. Ser. 762 (2016) 012001
T. Li et al., Chinese Physics C 41(6): 066201
  All EDM classes are derived from TObject
  Two layer design (Header and Event) of EDM classes are adopted to speed up event selection
    The Header holds light-weighted features (tag) of events while the Event holds heavy data
    A smart references (SmartRef) based on GUUID is developed to build correlations between Header and Event
    SmartRef also provides a lazy-loading mechanism to dramatically reduce I/O burden

## Slide 11
Event Data Model
EvtNavigator is developed to serve as the catalogue for EDM objects
  EvtNavigator also uses SmartRef to correlate EDM objects
  A event-index mechanism based on Global UUID is implemented to facilitate cross-file correlation analysis
  Provide the way to trace the MC truth of readouts at the event/particle/hit level with the help of external associations

## Slide 12
Event Data Model
EvtNavigator is developed to serve as the catalogue for EDM objects
  EvtNavigator also uses SmartRef to correlate EDM objects
  A event-index mechanism based on Global UUID is implemented to facilitate cross-file correlation analysis
  Provide the way to trace the MC truth of readouts at the event/particle/hit level with the help of external associations

## Slide 13
Event Data Model
EvtNavigator is developed to serve as the catalogue for EDM objects
  EvtNavigator also uses SmartRef to correlate EDM objects
  A event-index mechanism based on Global UUID is implemented to facilitate cross-file correlation analysis
  Provide the way to trace the MC truth of readouts at the event/particle/hit level with the help of external associations

## Slide 14
Geometry Management System (GMS)
GMS is developed to provide a consistent and detailed detector description for different applications
  Input from single source of geometry data : currently from ROOT file, plan to read from DB
  Export from Geant4 detector construction into GDML/ROOT TGeo file format
  Perform automatic conversion with Files – Geant4 – GDML – ROOT – Applications with different services
    Parameter Service
    RecGeom Service
K. J. Li et al., NIM A 908 (2018) 43–48
  Geometry information depending on different level of request
  Some information not supported by GDML can be retrieved from Parameter Services
    Optical Surface
    Matrixes

## Slide 15: Event Display
Unity based Event Display: ELAINA (Event Live Animation with unIty for Neutrino Analysis)
Root based Event Display: SERENA (Software for Event display with Root Eve in Neutrino Analysis)
J. Zhu et al., JINST 14 (2019) 01, T01007

## Slide 16: Database System
OfflineDB is developed to unify management of Conditions Data and Parameter data
  Two types of data are stored in Payloads in their suitable formats and deployed in CVMFS
  Meta data are managed with DB tables: Payload, IOV, Version, Tag and GlobalTag
  A GlobalTag combines the tag of Conditions data and Parameter data
  Three backups are implemented to meet different applications
    MySQL for quickly testing of database
    Frontier+Squid for massive data production
    SQLite for online event classification (OEC)
X.T. Huang et al., EPJ Web of Conferences 245, 04030 (2020)

## Slide 17: Analysis Software Framework
  Challenges of data analysis
  Time correlation analysis (a prompt signal and a delayed signal within varying time window)
  Rare signals (1kHz event rate, but only ~60 reactor neutrinos per day)
  Developed analysis software framework with an Indexing Technique
  The Indexed Analysis Data (IAD) consists of two parts:
    A pointer to the associated Event Summary Data (ESD)
    A collection of key reconstructed variables needed by the analysis
  Analysis work flow
  Step1: perform event pre-selection within the IAD stream based on its key variables
  Step2: navigate back to the associated ESD and perform further selection in the ESD stream
  Time correlation analysis could be applied in both steps

## Slide 18: Analysis Software Framework
  Multi-threading in Analysis
  One data input thread reads IAD blocks and puts them in the global buffer
  Multiple worker threads
    get IAD blocks from global buffer and convert them to a collection of IAD event objects
    perform two-level event selections and run analysis algorithms
  One or two data output threads
    write skimmed IAD event objects into a file
    write Data Summary Type (DST) objects into another file
Input thread
Worker
Worker
Worker
Data flow of multi-threading

## Slide 19: Integration of machine learning-trained models
  A python based datastore is developed for data sharing between C++ and Python
  Popular ML libraries are integrated into JUNOSW in C++ for inference with three solutions:
  Python API for SNiPER Algorithm in python
  Native C/C++ APIs: TensorFlow, PyTorch
  Open standard for ML: ONNX + ONNX Runtime (C++)
Trained Models
Python APIs
PyData Store
Native C++ APIs
ONNX Models
ONNX Runtime C++ APIs
SNiPER C++
Algorithms
SNiPER Python
Algorithms
T. Lin et al., Integration of machine learning-trained models into JUNO's offline software, ACAT2022

## Slide 20: Data Processing and Analysis Chain
  MCHITS (Monte-Carlo Simulated Hits Data)
  In ROOT format, contains GenEvt, SimEvt
  RAW (Raw Data from DAQ and OEC)
  In byte-stream format. Also contains the OEC result.
  RTRAW (ROOT RAW)
  In ROOT format (with EvtNavigator).
  Sorted; contains ElecEvt, TrigEvt, OecEvt; may contain GenEvt and SimEvt for simulated data.
  ESD (Event Summary Data)
  In ROOT format (with EvtNavigator), contains CalibEvt, RecEvt
  DST (Data Summary Type)
  Contains information of physical events, Flexible definition and file format, Does not contain relationships
  IAD (Indexed Analysis Data) (Auxiliary data)
  Contains the address to the RAW/ESD and the necessary physics variables
RAW
Data
ESD
IAD
Physics generators
+ Geant4 Simulation
Trigger + OEC
Independent Reconstruction
or
Joint Reconstruction
MCHITS
RTRAW
Format conversion from byte-stream to ROOT
Event Mixing
+ Digitization
Simulation
DST

## Slide 21: Summary
The JUNO offline software (JUNOSW) has been developed with modern technologies to meet the specific requirements of JUNO experiment and other non-collider experiments
  Data processing framework, SNiPER, supports buffering and management of multiple events, event splitting and mixing, TBB-based multi-threading, and integration of machine learning etc.
  ROOT based event data model to character data representations at different processing stages and complicated relationships between them.
  Unified detector geometry management system to support multiple applications including simulation, calibration, reconstruction and detector visualization.
  Unified database system to manage the conditions data and parameter data
  Event index based correlation analysis framework to support selection of sparse physics events from the large volume of data.
The JUNO data processing and analysis chain was completed and has been used by several rounds of M.C. data challenge on either local computing clusters or the distributed computing infrastructure.

## Slide 22: Thanks for your attention!