## Slide 1: On Estimating Gradients of Discrete Stochastic Programs for Detector Design Optimization
CHEP 2023
Lukas Heinrich, TUM Michael Kagan SLAC

## Slide 2: Differentiable Programming
A major enabler of large-scale Machine Learning:
Ability to compute gradients of numeric programs
To deal with hyper-planes in a 14-dimensional space, visualize a 3D space and say 'fourteen' to yourself very loudly.
                -G. Hinton
Program
Program

## Slide 3: Gradients Beyond ML
Differentiable Matrix Elements
2203.00057
Interest in applying DP to programs that are not NNs:
powerful method to combined physics + ML
Differentiable Inference
Differentiable Proton Structure
Differentiable Accelerator Simulation
Differentiable Calabi-Yau Manifolds
1907.05075
10.21105/joss.02823
2211.12520
2211.09077

## Slide 4: Emerging Usecase: Design Optimization
One of the most consequential high-dim. optimizations:
find a good detector design
before
after
arXiv:2002.04632 […, MK, …]
arxiv:2202.00728

## Slide 5: A Requirement:
For a gradient-based design optimization, one needs both: a differentiable simulation and reco/analysis
Simulation
Design Parameters
Analysis / Objective
Events
Theory
Design Rating

## Slide 6: A Small Problem
To first order, most of simulation is stochastic branching, while most of analysis is iterative clustering with many discrete choices
Simulation
Analysis
Data
HEP: fundamentally incompatible with differentiable programming?

## Slide 7: Not necessarily
The gradients we need are gradients of expectation values over probability distributions & observables with discrete aspects
discrete data
probability density
non-differentiable evaluation function
In many cases, the expectation value is differentiable (just not via standard automatic differentiation)

## Slide 8: Simple Examples
Discrete Jumps
Smooth Expectation Value

## Slide 9: Differentiating Expectation Values
The best known algorithm for gradient estimation is used a lot in Reinforcement Learning - score function estimation
HEP Simulator: discrete processe
Atari Games discrete actions
requires tracking probabilities (and their gradients) while running code → probabilistic programming

## Slide 10: Differentiating Expectation Values
More recently, renewed interest in approaches based on “smoothed pertubation analysis”
Extend fwd-mode AD to discrete-stochastic environments
Dual Numbers in Standard AD
Quadruplets in Stochastic AD
arxiv: 2210.08572

## Slide 11: Key Questions in HEP
Gradients Estimation in Stochastic Programs can suffer from very high variance → unstable optimization
HEP is in an interesting corner:
a lot of tiny stochastic steps
branching processes, many independently, variable-length processes
Standard AD
e.g. naive score function
Q: Will these methods work in a HEP setting?

## Slide 12: Example Application
Material Distribution
Shower
Radial Hit Distribution
We consider a simplified material- induced particle shower
High Density: E-loss and splitting Low Density: linear propagation
Design Parameter: Radial Distance of Material
Design Goal: Shower Depth

## Slide 13: Example Application
Material Distribution
Shower
Radial Hit Distribution

## Slide 14: Optimizing Material Distribution
At least for this toy model, optimizing material for hits properties works
Objective: Mean Hit Radius → 2.0
Loss Function
Gradient Estimate
Evaluated Parameters
We do see noisy gradients, but: as long as direction is OK (in expectation), minimization works
initial
final

## Slide 15: Comparison
Both score function and Stochastic AD gradient estimates massively reduce variance and optimization is possible

## Slide 16: A fun experiment:
Alternatively: 20 free-floating blocks of detectors.
x
y
x
z
Self-assembly into a circular shell to contain showers

## Slide 17: Next Steps & Outlook
Takeaway message: The presence of discrete stochastic randomness makes differentiable programming difficult …
But not impossible. With appropriate techniques, we can differentiate the seemingly undifferentiable But, may require integration of more complex programming constructs than just AD.