## Slide 1: ML for Transition Radiation Detector
Yulia Furletova ( and eRD22 team )
A.I Town Hall, 26 July 2021

## Slide 2
High resolution tracker and particle ID detector
Low material budget detector (tracker)
GEM based TRD:
TR radiator in the front of each chamber ( radiator thickness ~5-10cm )
Xenon-based gas mixture ( TRD uses a heavy gas for efficient absorption of X-rays)
Increased drift region up to 2-3 cm (for the same reason).
Number of layers depends on needs: Single layer could provide e/pi rejection at level of 10 with a reasonable electron efficiency (85-95%).
Transition Radiation detector concept
Radiator
Drift region
electron
pion
TR
photon
Primary
dE/dx
clusters
Readout
Xe gas mixture
pion
electron
Transition radiation is produced by a charged particles when they cross the interface of two media of different dielectric constants
the probability to emit one TR photon per boundary is of order ~1/137. Therefore multilayer dielectric radiators are used to increase the transition radiation yield, typically few hundreds of mylar foils.
TR in X-ray region is extremely forward peaked within an angle of 1/γ
Energy of TR photons are in X-ray region ( 2 - 40 keV )
Total TR Energy ETR is proportional to the γ factor of the charged particle

## Slide 3
e, ~3 GeV
dE/dx of Pions
dE/dx of electrons
dE/dx of electrons + TR
Energy deposition (dE/dx + TR) vs drift distance
Only e produce TR photons (E>1GeV)
Pions only start to produce TR at E > 100-150 GeV

## Slide 4
Used different methods/programs (JETNET, Root based-TMVA, etc) for cross-check.
Cluster counting method ( Time, Amplitude, number of clusters )
4
4
4
Machine learning technique

## Slide 5
Radiators Tests : Fleece
Beautiful response, High TR-yield, soft and hard TR photon’s spectrum
Aerogel:
No TR yield is seen
e, ~3 GeV
e, ~3 GeV

## Slide 6
Electron identification (e/hadron separation)
J/Ψ, φ
Br (J/->e+e- ) ~6%
Br (J/->+- ) ~6%
J/ identification
b
c
W
e
Br (B->e++XC ) ~10%
Heavy quark tagging
Br (D->e+X ) ~16%
Exotic spectroscopy (pentaquarks, tetraquarks, XYZ)
Other BSM physics
b
e
е’’
Ivan Vitev
Multi-leptons
VM production
Heavy photon

## Slide 7
Jefferson Lab:
  Fernando Barbosa
  Cody Dickover
  Yulia Furletova
  Sergey Furletov
  Lubomir Pentchev
  Chris Stanislav
  Beni Zihlmann
University of Virginia
  Kondo Gnanvo
  Nilanga K. Liyanage
Temple University
  Matt Posik
  Bernd Surrow
Old Dominion University
  Lee Belfore
eRD22 team:
Many thanks to the Hall-D and GlueX teams!
( in particular Eugene Chudakov and Tim Whitlatch)
A new Transition Radiation detector based on GEM technology
https://doi.org/10.1016/j.nima.2019.162356

## Slide 8: Backup

## Slide 9
9
Different TR-radiators.
We continue to search and test different types of radiators
Goal: to find low material budget, but high TR-yield radiators
The TR-energy spectrum is very important
(minimum of self-absorption)
Single module (X/X0) :
Radiator ( 10cm) ~ 1.5 % X0 for fleece ( could go down with mylar foils )
Xenon gas (2.0 cm) ~ 0.1% X0
Triple GEM with readout at active area ~ 0.7% X0
( could go down to 0.4%, see current eRD6 )

## Slide 10
GEMTRD performance
Few runs with the fleece radiator 9 cm and 15 cm
Data points are in a good agreement with MC predictions
For e/ data point : compared data at the different locations: pair-spectrometer (e-beam only) vs Glue-X setup ( mainly hadrons) .
Need to validate this point at the Fermilab with e and pion test beams.
Thickness [cm]

## Slide 11: Readout
Current setup: preamplifiers (GAS2 ASIC chip) with shaping times of∼10-12ns.
The flash ADC has a sampling rate of 125 MHz and 12 bit resolution but provides only pipe-lined triggered readout ( price ~50$/channel)
Current setup
80ns (Sampa) shaping time
~ 40ns shaping time
~ 20ns shaping time
Shaping time:
For TRD applications not only raising time is important, but also full width (tails, return to baseline )
In Xe – high density clusters ( ionization density)

## Slide 12: Readout
a preamplifier (GAS2 ASIC chip) with shaping times of∼10-12ns.
The flash ADC has a sampling rate of 125 MHz and 12 bit resolution but provides only pipe-lined triggered readout ( price ~50$/channel)
Sampling frequency:
Current setup
125MHz
62.5 MHz
31.25 MHz
15.6 MHz

## Slide 13
GEANT4: electron and pion comparison
Soft TR-photons:
absorbs near entrance window, therefore have large drift time
sensitive to dead volumes, like Xe-gap, cathode material.
Increase of radiator thickness does not lead to increase of number of soft-photons ( radiator self-absorption)
Hard TR-photons:
Depending on energy of TR-photons, could escape detection (depends on detection length)
Increase of radiator leads to increase of hard TR-spectra.
Separation/ Identification of TR-clusters and dE/dx clusters
radiator