## Slide 1: Core @ 3 Tesla with Hcal and coil mods
Paul Brindza, ODU
August 17, 2021

## Slide 2: CORE magnet update
Modify iron on Hcal end
Revise coil from a simple single coil solenoid to a three coil solenoid with the same exterior dimensions
Current density is 2880 amps/cm^2
Model uses 50 % iron density to simulate presence of detectors within
Model CORE is axi-symmetric
CORE is not symmetric about z=0 so investigate axial forces

## Slide 3: Revised CORE Hcal end @ 3 Tesla

## Slide 4: CORE Bz on axis -500 to 500 cm

## Slide 5: CORE Hcal mod projectivity( 0-250 Y, 0- 300 Z) Note the iron change made larger angles accessible Pr1 thru Pr7 match previous range

## Slide 6: Bz inside solenoid

## Slide 7: Some comments
Core is not symmetric along Z and one should expect some coil forces as a result
Trying to passively compensate by manipulating the content of the calorimeters may be possible
A better, lower risk solution would be to subdivide the solenoid coil so we have some adjustability
The original single coil was 10 by 250 cm centered.
This proposal is a center coil 10 by 230 cm and two flanking coils 10 by 10 cm with the capability to be powered independently.

## Slide 8: 3 coil CORE model

## Slide 9: Bz on axis for 3 coil core

## Slide 10: Comments on coil forces
The Bz field causes an outward radial force that amounts to a pressure on the coil and coil case, is symmetric and the coil case must support this pressure.
The Br field causes axial forces and in the presence of asymmetric iron can result in a net axial or de-centering force.
The average field in coil 1 is near zero and the result is less than the overall accuracy of the calculation ~ 1.5 %
The difference between the average field of coil 2 and coil 3 is small and about equal to the calculation accuracy
The product of current density, coil area and length for coil 1 is 47E6 and for coils 1 & 2 it is 2E6 amps-meters
Small field asymmetries result in significant forces if real

## Slide 11: By field in the middle of the coils(may cause axial force)

## Slide 12: Force case all coils same current ( 2880 amps/cm^2)
 | Average Br field | J*A*L ( amp meters) | force | 
Coil 1 | -0.0015 Tesla | -47.87 E 6 | -73,717 Nt | 
Coil 2 | -1.9579 Tesla | - 2.081E 6 | - 4.075E6 Nt | 
Coil 3 | +1.9759 Tesla | -2.081 E6 | + 4.112E6 Nt | 
net |  |  | -36,324 Nt | - 8,166 #

## Slide 13: Force case coil 2 has 20 amps/cm^2 less than coils 1 and 3
 | Average Br field | J*A*L ( amp meters) | force | 
Coil 1 | -0.0021 Tesla | -47.87 E 6 | -98,353 Nt | 
Coil 2 | -2.085 Tesla | - 2.067E 6 | - 4.309 E6 Nt | 
Coil 3 | +2.124 Tesla | -2.081 E6 | + 4.421 E6 Nt | 
net |  |  | + 13,151 Nt | +2,956 #

## Slide 14: Br in iron- note most Br is at coil ends

## Slide 15: B mag on Iron surface Bmax is 1.41 Tesla

## Slide 16: Bmag exterior of iron, Bmax ~ 1.1 Tesla

## Slide 17: Field in Hcal

## Slide 18: Field in Ecal

## Slide 19: Field magnitude in DIRC

## Slide 20: Bz in DIRC

## Slide 21: Br in DIRC

## Slide 22: Summary on CORE 3 T magnet
This looks OK to me.
Make suggestions
New Field grid file available