## Slide 1: Technical solutions for CEBAF upgrade, towards - Positrons experimental capability - 22 GeV energy upgrade program
Presented to the JLab Staff Scientist Meeting on NSAC LRP
Andrei A. Seryi Associate Director for Accelerator Operations and R&D
Newport News, Virginia August 19, 2022

## Slide 2: Energy upgrade foundation
CEBAF – separate arc for each different energy
EMMA (Electron Model for Multiple Applications) –demonstrated that orbits can be compacted to within 10 mm in radius over an electron momentum range of 12–18 MeV/c
Acceleration in the linear non-scaling fixed-field alternating-gradient accelerator EMMA, S. Machida, et al., Nature Physics volume 8, pages 243–247 (2012)

## Slide 3: Energy upgrade foundation
CEBAF – separate arc for each different energy
CBETA (Cornell-Brookhaven energy recovery linac Test Accelerator) – the fixed-field alternating-gradient optical system used for the return loop successfully transported electron bunches of 42, 78, 114, and 150 MeV in a common vacuum chamber
CBETA: First Multipass Superconducting Linear Accelerator with Energy Recovery, A. Bartnik, et al., Phys.Rev.Lett. 125 (2020) 4, 044803
EMMA & CBETA FFA approach: we can increase number of passes through CEBAF linac without the need to increase the number of arcs

## Slide 4: The FFA@CEBAF Collaboration
†
Positrons @CEBAF Collaboration
Alex Bogacz, JLab
Alicia Hofler, JLab
Amy Sy, JLab
Andriy Ushakov, IJCLab-Orsay
Carlos Hernandez-Garcia, JLab
Cristhian Valerio, Univ. of Sinoloa
Dennis Turner, JLab
  Ryan Richards, Univ. of Virginia
  Sami Habet, IJCLab-Orsay
  Stephen Brooks, BNL
  Joe Grames, JLab
  Val Kolstrum, Xelera
  Yuhong Zhang, JLab
  Yves Roblin, JLab
  Eric Voutier, IJCLab-Orsay
  Fanglei Lin, ORNL
  Jay Benesch, JLab
  Karl Smolenski, Xelera
  Larry Cardman, JLab
  Reza Kazimi, JLab
  Ryan Bodenstein
Joe and Eric continue to fan and feed and push things along
Alex Bogacz is leading the energy upgrade design efforts

## Slide 5: Accelerator expertise and CEBAF upgrade foundations
CEBAF upgrade will significantly benefit from JLAB world-leading expertise in many areas:
  Recirculating accelerators
  Energy Recovery Linacs (ERL)
  Superconducting RF (SRF)
  Polarized electron sources, etc.
CEBAF upgrade is benefitting from experience of collaborating teams, BNL, Cornell, ORNL, IJCLab-Orsay:
  Fixed Field Alternative gradient optics (FFA)
  Permanent magnets FFA
  CBETA operations experience
  ILC positron production design, etc.

## Slide 6: CEBAF upgrade, assumptions  design focus
Polarized positrons capability
  Near term, about five years from now, 12 GeV, multi-hall
Energy upgrade experimental program
  22-24 GeV, a decade from now, multi-hall
    Can have an intermediate stage of 17 GeV
    No positrons required in 22 GeV era
Modern and advanced design approach
  Non-scaling FFA demonstrated at EMMA (Daresbury, UK) and CBETA (Cornell)
  Fixed field suitable for permanent magnets – energy efficiency
  Collaborative efforts with BNL, ORNL and Cornell experts
Maximizing the overall affordability
  Uncoupled stages, build up on the previous stage, make each stage affordable
  Maximally re-use resources (space, buildings, hardware) already available

## Slide 7: Energy upgrade to 22 GeV, big picture
Hardware needed:
  Replace an arc per side with new FFA permanent magnet arc
    (One or two pair of arcs considered)
    (Options for 22 GeV or 24 GeV)
  Add ~650MeV injector (e.g. one-pass-recirculation-based compact injector)
    This mean a shielded vault of ~70x10m

## Slide 8: Polarized e+, big picture
Hardware needed:
  High current polarized e- source
  A cryomodule to accelerate e-
  An e+ target-source and collection system
  A cryomodule to accelerate e+
Scheme courtesy Joe Grames. See also JLAB UO’22 talk by Matt Poelker
10
90-110
90-110
Polarized positrons generation
e-
e-
e+ source/collection
e-
e+
e+ @ 123
Cryomodule ~C100
Cryomodule ~C100
Space requirements for e+ source are similar to what is needed for ~600 MeV injector for 22 GeV program
Most of hardware from e+ stage can be re-used in the 22 GeV program – synergy with energy upgrade

## Slide 9: Several options were considered, e.g. … :
New underground vault
…however, the most cost-effective is the one which re-uses an existing shielded facility

## Slide 10
LERF is used for e+ development, while tunnel is constructed. Once connected – start e+ program. Then reconfigure LERF as 650 MeV injector and start 22 GeV program
Option 2c: new cut-and-cover tunnel between LERF and E Arcs
New tunnel, with slope from LERF to tunnel level
A new beamline from East arc, along the ceiling of South Linac, and along the West arc, can bring ~120 MeV positrons, or 650 MeV electrons, into the standard injection point at the beginning of the North Linac
2a
2b
Options 2a and 2b assumed connecting the new tunnel to one of the existing stabs. They both have some disadvantages and they were put aside in the process of design optimization with our conventional construction experts
2c

## Slide 11: Tunnel to East Arc
Conventional Facilities construction experts assessment and design optimization
  Options 2a and 2b assessed
  Option 2c suggested and evaluated
  Feasibility confirmed
Rough cost estimates for hardware are in the process
Drawings courtesy Joel Dolbeck

## Slide 12: Accelerator Physics Details of CEBAF Energy Upgrade
Materials courtesy of Alex Bogacz, Accelerator Physics Group, CASA
Feasibility study for FFA* racetracks in the existing CEBAF tunnel to reach the top energy of about 22-24 GeV
*FFA (Fixed Field Alternating-Gradient)

## Slide 13: CEBAF FFA Upgrade – ‘Option 1 under Study’
  Starting with 12 GeV CEBAF as a baseline
  NO new SRF (1.1 GeV per linac)
  New 650 MeV recirculating injector
  Remove the highest recirculation pass (Arc 9 & A) and replace them with two FFA arcs including time-of-flight chicanes
  Recirculate 4 + 6 times to get to about 22 GeV
Novel permanent magnet technology used for power and cost savings
Pass Arithmetic: 5 -1 + 6 = 10
TOF
TOF
650 MeV

## Slide 14: CEBAF FFA Upgrade – ‘Option 2 under Study’
  Starting with 12 GeV CEBAF as a baseline
  NO new SRF (1.1 GeV per linac)
  New 650 MeV recirculating injector
  Remove the highest recirculation pass (Arc 9 & A) and replace them with two FFA arcs including time-of-flight chicanes
  Recirculate 4 + 4 times to get to about 18 GeV
Novel permanent magnet technology used for power and cost savings
Pass Arithmetic: 5 -1 + 4 + 3 = 11
TOF
TOF
TOF
TOF
  Install a second pair of FFA arcs ‘on the floor’ below Arc 9 & A
  Recirculate 3 times to get to about 24 GeV
650 MeV

## Slide 15: FFA CEBAF with -like Arcs

## Slide 16: Compact FFA FODO Cell – How Does it Work?
Large momentum acceptance FFA cell, configured with combined function magnets capable of transporting multiple energy beams through the same string of permanent magnets (six beams with energies spanning a factor of two)
1 T
50 T/m
1 T
50 T/m
magnets: from 38cm2 to 78cm2
BD
BF
BD
BF
BD
BD
Closely spaced orbits for all six beams (~ 1 cm)
Extremally low dispersion (a few mm) in a combined function lattice
Self similar beta functions for different energy beams

## Slide 17: Multi-Bunch Dynamics in FFA Arc
Stephen Brooks
BNL

## Slide 18: Injector Upgrade - 650 MeV Recirculating Injector
With the present 123 MeV injector, the difference in the first and final pass energies in the North Linac is too large (1:175) to effectively control the beam.
650 MeV recirculating injector (3-pass) based on LERF will allow a manageable difference in energies (1:33)
LERF is used for e+ development, while tunnel is constructed. Once connected – start e+ program. Then reconfigure LERF as 650 MeV injector and start 22 GeV program
Option 2c: new cut-and-cover tunnel between LERF and E Arcs
A new beamline from East arc, along the ceiling of South Linac, and along the West arc, can bring ~120 MeV positrons, or 650 MeV electrons, into the standard injection point at the beginning of the North Linac

## Slide 19: Recirculating Injector Based on LERF (3-pass)
C-75
C-75
C-75
436 MeV
10 MeV + 3 × 3 × 71 MeV = 650 MeV
10 MeV

## Slide 20: Recirculating Injector Based on LERF (3-pass)
C-75
C-75
C-75
10 MeV + 3 × 3 × 71 MeV = 650 MeV
New arc
New arc
650 MeV

## Slide 21: 123 MeV e+ injector for 12 GeV positrons
#6 – SRF accelerate e+ to 123 MeV
#4 - Produce e+ accelerate to 50-70 MeV
#2 - SRF accelerate >100 MeV
#1B – CEBAF style polarized e- injector 10 MeV
#1A – FEL style compact e- injector 10 MeV
#3 – Extract e- to target
#7 – Transport e+ at 123 MeV to exit LERF
#5 – Injector e+ to linac
The e+ and E+ configs in LERF are compatible, and most of hardware re-used

## Slide 22: Energy Loss, Emittance Dilution (4-pass CEBAF)
  Doubling the energy, while staying within current CEBAF footprint, makes the synchrotron radiation effects of paramount importance.
  Quantum nature of a ‘recoil’ effect on electrons due to photon emission makes significant impact on both the transverse and longitudinal beam dynamics, leading to cumulative emittance growth (transverse and longitudinal).
Energy loss
Emittance dilution
Natural energy spread

## Slide 23: Energy loss, Emittance Dilution (Option 1: 6-pass FFAs)
6 passes
Synchrotron radiation mitigation in FFAs
  High fill factor (88% space filled with bends) increases significantly the bend radius, r.
  By virtue of extremally small dispersion and betas, the horizontal emittance dispersion, <H>, is highly suppressed (factor of 50 lower then in a conventional CEBAF arc lattice).

## Slide 24: Energy loss, Emittance Dilution (Option 2: 7-pass FFAs)
4 passes
3 passes
Synchrotron radiation mitigation in FFAs
  High fill factor (88% space filled with bends) increases significantly the bend radius, r.
  By virtue of extremally small dispersion and betas, the horizontal emittance dispersion, <H>, is highly suppressed (factor of 50 lower then in a conventional CEBAF arc lattice).

## Slide 25: Accelerator Design Summary
Present Baseline (1.1 GeV per linac):
  650 MeV Recirculating Injector (additional three C-75 cryomodules)
  Recirculate 4 passes with the current CEBAF plus:
    Option 1: Additional 6 passes via a single FFA: 10.4 – 22.8 GeV
    Option 2: Additional 7 (4 + 3) passes via two FFAs: 10.4 – 17.9 GeV and 19 – 24.6 GeV
Adiabatic FFA arcs configured with compact FODO cells
  Beta and dispersion matching to the linacs through cell-by-cell variation (length, bend)
  Open mid-plane permanent magnet design: B-field ≤ 1 T, Gradient ≤ 47 T/m
Synchrotron Radiation impact on beam quality (Option 1):
  Net transverse emittance dilution (normalized): 60 mm mrad
  Net natural energy spread: 2×10-3
  Net synchrotron radiated energy: 1 GeV
Engineering analysis and cost estimations – are in progress
  Will be ready in time for LRP submission
at 22 GeV, b = 20 m → s = 150 microns

## Slide 26: Summary on the path towards 22-24 GeV CEBAF era
Modern design, energy efficient, cost-effective approach
Strong collaborative design team – BNL, ORNL, Cornell, JLAB
  Enthusiasm and inspiration
Staged approach allow gradual realization:
Start e+ capability in about five years
  Design to be synergic with the energy upgrade, to maximize overall affordability
In about a decade, implement FFA 22-24 GeV upgrade (one or two stages)
Positrons upgrade:
Source in LERF
New tunnel to East arc
Beamline E-Arc to NL
Energy upgrade to 18GeV
Pair of FFA arcs
Injector in LERF
Beamlines to halls upgrade
Energy upgrade to 24GeV
Second pair of FFA arcs

## Slide 27
Thanks for your attention!