## Slide 1: Polarized Ion Sources at BNL
September 26, 2023
D. Raparia, G. Atoian, E. Beebe, S. Ikeda, T. Kanesue, S. Kondrashev, J. Maxwell, R. Milner, M. Musgrave, M. Okamura, A.A. Poblaguev, J. Ritter, A. Sukhanov, S. Trabochi, A. Zelenski
SPIN 2023

## Slide 2: Outlines
Introduction
Polarized proton source , OPPIS
- Upgrades
- OPPIS components
- Performance
Development of Polarized 3He++ source
- 3He++ Source based on EBIS
- Gas purification system
- 3He Gas Cell
- Spin Rotator Chicane
- 6 MeV Polarimeter
Conclusion

## Slide 3: Overview of the BNL Hadron Complex
Uniquely flexible and only hadron collider in US for exploration of QCD phase diagram and proton spin
Injectors also used for application programs: - Linac/BLIP for isotope production - Booster/NSRL for space radiation studies
- Tandem for industrial/academic users
R&D for future facilities and application sources, pol. beams, …

## Slide 4: Polarization Facilities at RHIC
EBIS

## Slide 5
OPPIS (Optically Pumped Polarized Ion Source) Since 2000, H- ion source has been upgraded several times to higher intensity and polarization.
Prior to Run-13(2013), the ECR-type source was used to generate the primary proton beam. The ECR-source was originally developed to operate on DC current and placed inside a super conductive solenoid (SCS).
In 2013, the ECR-source was replaced with a high-brightness source “Fast Atomic Beam Source” (FABS) operating in a pulsed mode. The FABS-source improved source parameters such as beam current density, angular divergence and stability.
In 2022, We reduced the LEBT portion of the beam line by about 5feet, modify polarization part of OPPIS (He-cell, Rb-cell and Na-cell) and the extractor-transformer system.
Optically Pumped Polarized Proton Source

## Slide 6
LEBT (35 keV) Upgrade with 3 Sources
OPPIS
Magnetron S-2
Magnetron S-1
To RFG
The Low Energy Beam Transport (LEBT) lines combine three beams. The first line is the polarized OPPIS beam-line, and the second and third lines are the high-intensity unpolarized beam lines.
The LEBT line has been modified twice; the first modification was the addition of another high-intensity unpolarized H-beam line and the second modification was the reduction of the transport line of the OPPIS line by more than 5 feet).
Laser
Room
Magnetron S-1,2
High intensity
BLIP, NSRL
130 mA, 1000 𝝻 s
6.67 Hz
OPPIS
RHIC, NSRL
500 𝝻A, 500 𝝻 s
0.15 -1 HZ
RFQ
Slits for energy discrimination
Chopper
Switching Magnet (50 ms)

## Slide 7: OPPIS

## Slide 8: OPPIS Layout
OPPIS produces 3-5 mA Polarized H- ion pulse current
81-84% polarization @200 MeV , 0.5 mA

## Slide 9
He-cell
Rb-cell
SC-solenoid
Sona-transition with 3 corr. coils in it
Na-jet
&
Solenoid
H0
H-
9
Production of circular polarized tunable wavelength (~795nm) laser beam
Polarization of the outer electron of Rb-atom by a laser
Production of electron spin polarized hydrogen atoms by capture electron from Rb
Polarization transfer from electron to proton by “Sona-transition” technique
Ionization of hydrogen atoms by capture of second electron in Na-jet for acceleration
Polarized light
Polarized electron
Polarized proton
(Quarks? Gluons ? Sea quarks?
Ionization of hydrogen atom at He-cell.
H0*
H+
H0*
Polarization Transfer Technique

## Slide 10: Polarization Dilution due H0
Ionize
H0
7keV
40%
Rb-cell
60%
He-cell
H2-cell
Neutralize
In FABS-source
Inside of the SCS
Ionizer & Extractor
H-39keV
0.72%
Accelerate
32keV
3%
H-
7keV
Na-jet
8%
Decelerate, ΔE=4.0keV
He-cell
70%
2%
Na-jet
>90%
Ionize
Extr.
Accelerate
32keV
Extr.
Ionize
H0
7keV
H+
7keV
H+
7keV
H+
3keV
Neutralize
H0
3keV
H-
3keV
H-
35keV
Dilution of polarization (0.72/3 =0.24) can be reduced by the energy separation of the H- beam (~25-30 times) to 0.24/25~ 0.01

## Slide 11: Fast Atomic Beam Source

## Slide 12: He-Ionizer Cell with 3-grid Energy Separation System
Two functions of the new He-cell with pulsed valve:
Ionization of the injected neutral beam
Deceleration of the ionized part of the beam to separate from the no-ionized part
He-valve
Operating in high magnetic field ~1-3T
He-pulsed
valve
3-grid beam
Deceleration system
He-cell

## Slide 13: Optically –Pumped Rb- vapor Cell

## Slide 14: 4-Grid Sperical Ion Optical System

## Slide 15: Sodium –Jet Ionizer Cell

## Slide 16: H- Beam Acceleration to 35 keV

## Slide 17
Total: 0.85 - 0.90
P = EH2 ∙ PRb∙ S ∙ BRG∙ ELS∙ EES ∙ ESona∙ Eion ~ 85-90%
Depolarization Factors
Depol. factor |  | Process | Estimate
1 | EH0 | Dilution due H0 part of the beam (LEBT) | 0.99 - 0.99
2 | PRb | Rb-optical pumping (Laser system) | 0.99 - 0.99
3 | S | Rb polarization spatial distribution (Collimators) | 0.97 - 0.98
4 | BRG | Proton neutralization in residual gas (Vacuum) | 0.98 - 0.99
5 | ELS | Depolarization due to spin-orbital interaction | 0.98 - 0.98
6 | EES | Dilution due to incomplete energy separation not polarized component of the beam (LEBT) | 0.98 - 0.99
7 | ESona | Sona-transition efficiency (Adjustment) | 0.96 - 0.98
8 | Eion | Incomplete hyperfine interaction breaking in the ionizer magnetic field | 0.98 - 0.99
Notes: 17

## Slide 18: H- Current at 200 MeV-1.05 mA

## Slide 19
OPPIS
LINAC
Booster
AGS
RHIC
2.2∙1011 p/bunch, P ~65%
6.3∙1011(maximum 40∙1011) polarized H- /pulse.
3.6∙1011 polarized H- /pulse at 200 MeV, P=80-82%
2.5∙1011 protons /pulse at 2.3 GeV
200 uA X300us
Scraping in Booster
Polarized beams in RHIC
~2∙1011 p/bunch, P~60-65% at 100GeV
P ~ 50% at 250 GeV
Notes: 19

## Slide 20
Beam Intensity in 2023 @ 200 MeV: 420𝝻A ( ~7*10^11)

## Slide 21
Beam Performance
𝞵A
ECR

## Slide 22: Polarized 3He++ Source development
U. S. Department of Energy
Office of Science | Nuclear Physics FY 2018
Research and Development for Next Generation Nuclear Physics Accelerator Facilities
… A doubly polarized electron-ion collider (EIC) is the best way to examine the internal structure of the proton and neutron. The technology to accelerate polarized proton beams has been well established at RHIC. However, studying the structure of the neutron requires the acceleration of polarized 3He++, which carries ~90% of its polarization in the neutron, and to match the unprecedented statistical precision an EIC will provide, it is indispensable to have high precision measurements of the hadron beam polarization. For this reason, development of a polarized 3He ion beam has been identified as an R&D priority by the EIC Advisory Committee in 2009 and the Office of Nuclear Physics Community Review in 2017.
In 2003 A. Zelenski, J. Alessi proposed a production polarized 3He++ beam in EBIS.
(A. Zelenski, J. Alessi, “Proposal of production of polarized 3He++ beam in EBIS” , ICFA Beam Dynamics Newsletter 30, p.39, (2003)
Polarized 3He++ source is a part of the ongoing EBIS upgrade project.
The development of the polarized 3He ion source is being done as a collaboration between BNL and Massachusetts Institute of Technology (MIT).

## Slide 23
Polarized 3He++ beam can be accelerated in the AGS and RHIC using existing “Siberian snakes

## Slide 24: Requirements to the 3He++ Source at BNL
Intensity ~ 5∙1011 3He++ ions in 20 us pulse ~10.0 mA-peak current
Maximum polarization > 80%
Compatibility with the operational EBIS for heavy ion physics.
Spin flip for every source pulse in the beam transport line.

## Slide 25
Principle of EBIS Operation
Radial trapping of ions by the space charge of the electron beam.
Axial trapping by applied electrostatic potentials at ends of trap.
The total charge of ions extracted per pulse is ~ (0.5 – 0.8) x ( number electrons in the trap ~1.0∙1012 )
Ion output per pulse is proportional to the trap length and electron current.
Ion charge state increases with increasing confinement time.
Output current pulse is independent of species or charge state!
10A, 10-20 keV
Notes: 25

## Slide 26
Ions | He - U
Q / m | ≥1/6
Current | > 1.5 emA (20 s)
Pulse length | 10-40 s
Rep rate | 5 Hz
Output energy | 2 MeV / u
Time to switch species | 1 second
EBIS Preinjector (2 MeV/u)
EBIS
RFQ
IH LINAC
BEAM TRANSPORT LINE
BIG BEND
BOOSTER
EBIS
RFQ
IH LINAC
LION
HCIS2
HCIS1
TOF

## Slide 27: EBIS is an Accumulator and Charge State Multiplier with a widely programmable output pulse width and is capable of working with Internal gas Injection.
Typically operation is with ion injection from external sources:
Fast injection: Laser Ion Source (LION) , ~100’s uA – 1mA , 10-200 us
Slow injection: HCIS, 1-10’s uA, 10-40 ms
Widely variable extraction pulse width 5uS to greater than 50ms
Booster/AGS/Rhic injection typically 5-40 us (High Intensity)
Pure Beams (low contamination by unwanted ion species)
High utilization of relatively low charge capacity
Lower space charge beam transport to RFQ
Above: Au Time-of-Flight Spectrum
(Reflex mode – channeltron EM)
Max peak is Au32+
Au pulse (all charge states)
With external Au1+ ion injection:
ChC Magenta3.5mA, 1 mA/div, 10 µs/div
ChD Blue: 70nC , 20uVs/div
Without external ion injection
Ch2 Green: 0.2mA, 1 mA/div, 10 µs/div
ChB Red: 1nC , 10uVs/div
Note very low background contamination characteristic of EBIS

## Slide 28
EBIS beams run to date on RHIC EBIS
D, 3He2+, 4He1+,2+, Li3+, C5+,6+, O7+, Ne5+, Al5+, Si11+,12+, Ar11+, Ca14+, Ti18+, Fe20+,24+, Cu11+, Kr18+, 90Zr15+, 96Zr16+, Nb16+, Xe27+, Ta38+, 184W31+, Au32+, Pb34+, 232Th39+, U39+
1 second switching between species (2, or more), alternating
<30 second switching among almost any 10, if loaded into external sources

## Slide 29: Challenges and Key Development for the Extended EBIS
Pumping Ultra-High Vacuum Regions
  -Custom heated linear high capacity NEG
Early work with injection of 3He into EBIS showed that it would be difficult to polarize the 3He gas external to the EBIS and then transport the gas into the EBIS for ionization to 3He++, while maintaining both high intensity and maintaining polarization.
The concept of an in-bore gas / high field polarization cell has been developed. This necessitates the development of a highly efficient gas injection system and led to the development of a hybrid vacuum system using both conventional internal drift tubes and a new modular “external” drift tube system to accommodate placement of the gas reservoir and polarization equipment.
3He Polarization for EBIS
  -Gas Purification, and pulsed valve
  developments
  - Development of the fast valve

## Slide 30: Production of Polarized 3He++ in EBIS
3He polarization by optical pumping and metastability-exchange technique inside the EBIS in high (5.0T) magnetic field. No polarization losses in 3He+ state.
EBIS is used for efficient ionization and accumulation of polarized 3He++ ions to the full capacity of about (2.5-5.0)∙1011 , 3He++ ions.
Notes: 30

## Slide 31: Extended EBIS for 3He++
The polarized 3He ion source will be mounted on the Solenoid-1.
The atoms of the 3He gas will be polarized by Metastability Exchange Optical Pumping (MEOP) technique and
After injected through a fast pulse valve in the ion trap region of the EBIS.
There the 3He ions will be trapped and bred to the 3He++ state.

## Slide 32: EEBIS
In the test Lab
At the site

## Slide 33: Polarized 3He++ Source Development
3He optical pumping polarization in the high magnetic field.
3He purification and filling system for the “open” cell configuration.
3He injection valve development
Spin rotator and 3He-4He polarimeter development in 6.0 MeV beam line.

## Slide 34: Optical Pumping and Probe Lasers Layout
Pumping laser
Probe laser, Toptica, DL-100, diode laser
Detector
WS6-200
wavemeter
Pumping laser-Keopsys 10 W 1083 nm- fiber laser

## Slide 35
Circular polarized
Laser light at 1083 nm

## Slide 36
Holder 3He-cell with filling and injection valves inside the EBIS SC Solenoid-1
Procedure to polarize the 3He gas at high magnetic field:
Prepare the 3He gas for polarization by the purification system; Valve1-open/ Valve2-close
Polarize the 3He gas inside the glass-cell by a MEOP technique; Valve1-close/ Valve2-close
Continually control the polarization of the injected 3He gas by using the Optical Probe polarimeter;
Inject a polarized 3He portions into drift tube (beam line) through the pulsed valve ( ~2-3*1012 atoms/pulse); Valve1-close/ Valve2-open
Ionize the polarized atoms of 3He by electron beam (~10 A).
3He-cell
3He Filling Valve1
3He Injection pulse Valve2
HV isolator
Drift tube (20-40 kV)
e-beam ~10A
To the purification system
Rf –discharge

## Slide 37: 3He-gas purification and filling system
Modified Cryo-pump for 3He
purification and storage
Vessel filled with charcoal granules
The pump also absorbs quite a significant amount of 3He gas (of about 100 scc).
The absorbed gas is released by the pump vessel heating ~20K.
This provides gas storage and supply for 3He-cell operation at the optimal pressure value (3-5 Torr).

## Slide 38: 3He Contamination Monitoring
The hydrogen Balmer-alpha line intesty at 656 nm is strongly reduced <0.4%
Relative to the 668 nm 3He line after 10 hours of RF discharge with the
isolation valve closed

## Slide 39: Gas Cell with pump out manifold and external drift tube connections

## Slide 40
“Electro-magnetic”, [IxB] valve operation principle
Lorentz (Laplace) force moves the flexible conducting plate in the high (~ 3-5 T) magnetic field.
For I=10 A, L=5 cm, F=2.5 N. Current pulse duration ~100-500 us
B
F
I
Pulsed valve for
Un-polarized gas
Injection to the EBIS
Fast Pulsing Gas Valve
A prototype valve test at 2.5 T , a gas flow of 2.10^12 atom/pulse
was measured at 12 A. Also test for consecutive pulse 4 ms apart
producing 10^13 atoms/cycle.

## Slide 41: Pulsed 3He Valve Operation in 2.0T Solenoid.
Pulsed current width (𝝻 s)
4∙1011 3He
Atoms per/pulse
1000 𝝻 s

## Slide 42
Polarization Measurements by the Probe Laser Absorption
Closed cell
Open cell
89% polarization in. sealed
3He cell at 3 Torr pressure
Polarization build-up time .
0-4 min: Valve open
5-27 min: valve closed
29 min: laser off and valve opened
(3 Torr valve closed)

## Slide 43: 3He++ Spin-Rotator in the at 6.0 MeV Beam Energy
After acceleration by EBIS LINAC, the polarized 3He++ beam will have an energy of 6MeV with a longitudinal spin direction.
The longitudinal polarization of beam is at first rotated to transverse direction using the 21.5 deg bending magnet (Dipole-1) and after
The Spin- solenoid will change the spin direction to the vertical . It is a pulsed solenoid with reversible field to enable spin-flip on an EBIS pulse-by-pulse basis.
Vertically polarized beam will return to the straight HEBT line by the system of dipole magnets (2,3,4).
The polarimeter will install in the straight section after the Dipole-3 magnet. With a spin-flip, we can measure polarization of the beam with a standard configuration of left/right symmetric Si-strip detectors).
1
2
3
4

## Slide 44: Spin Rotator -Chicane

## Slide 45: 3He-4He scattering polarimeter at 5.3 MeV beam energy
By a measuring, the spin correlated asymmetry of 3He (beam ions) scattering on the 4He (gas target) to determine the polarization of 3He beam.
The asymmetry could be found from the number of detected scattered particles in left/right (L/R) detectors depending on the beam spin ():
and ,
where is the beam polarization, - analyzing power and
- statistical accuracy.
Analyzing power in 3He-4He elastic scattering at 5.4 MeV beam energy and 79° - angle is close to 100%.

## Slide 46
Control Module
Connect port
Polarimeter Control Module
With the beam we plan to study:
Kinematics of elastic 3He-4He scattering;
energy distribution of the 3He-4He pair;
energy and time resolution;
electronics and DAQ;
data collection and analysis of events;
controlling and monitoring the detectors;
vacuum control system;
communication system;
…
We have prepared a complete detector with the requirement geometry, measured the energy range and is ready for installation in the EBIS beam line.
Setup of 6 MeV polarimeter
12-ch End-Off electronics
Chamber-1
Valve-1
Gauge-1
Beam dump (FC)
Gauge-2
Gauge-3
Valve-2
Turbo pump
Chamber-2
Target (He4) filling system
Scroll pump

## Slide 47
Summary
Polarized H-
OPPIS reliably (>95%) providing polarized H- ions for RHIC
OPPIS has gone though couple of successful upgrade and is ready for next run.
Polarized 3He++
Polarized 3He++ production is important part of the ongoing extended EBIS “upgrade" project.
High polarization of He was achieved in the "open" cell in the high magnetic field. This is a significant step forward to achieve its goals.
A new technique of 3He purification system (based on cryo-pumping) was developed to meet the strict requirements for high polarization.
A new type of pulsed electromagnetic valve was developed for 3He injection into the drift tube. This new valve will improve the efficiency and reliability of the injection process.
Design of gas cell is progressing well; first cell will be finish by end of this year
In addition, the spin rotator chicane will be tested with unpolarized 3He by the end of this year. This is a critical step in developing the full functionality of 3He source.
Notes: 47