## Slide 1: A research program to measure the lifetime of spin polarized nuclei in magnetically confined fusion plasmas
W.W. (Bill) Heidbrink1, L.R. Baylor2, M. Büscher3,4, R.W. Engels3,5, C.B. Forest6, A.V. Garcia1, M. Gryaznevich7, G.W. Miller8, A.M. Sandorfi8, X. Wei9, X. Zheng8
1University of California, Irvine
2Oak Ridge National Laboratory
3Forschungsszentrum Jülich
4Heinrich-Heine Universität Düsseldorf
5GSI Helmholtzzentrum für Schwerionenforschung 6University of Wisconsin, Madison
7Tokamak Energy, Milton, UK
8University of Virginia
9Jefferson Lab
The DIII-D Tokamak in San Diego

## Slide 2: Spin polarized fuel relaxes the requirements for fusion energy
D-T fusion cross-section is increased by 50% when the spins of both nuclei are polarized along the magnetic field1
Due to self-heating, >50% increase in fusion power with no additional requirement on plasma confinement2
Depolarization mechanisms are theoretically weak in the core,1 but the polarization lifetime has never been measured
Polarized fuel is now available in sufficient quantities for experimental tests2
[1] R.M. Kulsrud et al., Nucl. Fusion 26 (1986) 1443.
[2] L. Baylor et al., Nucl. Fusion 63 (2023) 076009
Notes: Cite PRO

## Slide 3: Outline
Fusion in contemporary magnetic fusion experiments
Spin polarized fuel
Depolarization mechanisms
Planned & desired experiments
Notes: Cite PRO

## Slide 4: Three fusion reactions are often measured in fusion experiments
Deuterium is usually the main ion species
Many fusion reaction products are unconfined in a moderate-size tokamak
Heidbrink et al., Nucl. Fusion 23 (1983) 917
Notes: Cite PRO

## Slide 5: Many experiments are heated by neutral beams
Inject ~ 80 keV D neutrals
Beam ions take O(0.1 s) to thermalize
Routinely measure 2.45 MeV neutrons from d(d,n)3He
Notes: Cite PRO

## Slide 6: Some experiments are fueled by pellets that ablate & ionize in the plasma
Pellet injector above DIII-D
Inject frozen D pellets
Inject ”shell pellets” with gas inside
Typical “particle confinement time” is O(0.1 s)
Electron density
L. Baylor et al., Phys. Plasmas 7 (2000) 1878
Notes: Cite PRO

## Slide 7: Distinguish between thermal & super-thermal distribution functions
Most of the plasma is thermal with ion temperatures Ti of a few keV
Neutral beams produce non-thermal, anisotropic populations with O(100 keV) energies
Beam-plasma
Typical D distribution function f
Notes: Cite PRO

## Slide 8: Use D-3He as a proxy for D-T
Fusion products:
14.7 MeV proton
3.6 MeV alpha
Mirror reaction virtually identical at O(100 keV) energies
L. Baylor et al., Nucl. Fusion 63 (2023) 076009
Notes: Cite PRO

## Slide 9
Relative reactant energies of ~100 keV are needed for a D-3He experiment
Semilog scale
cross section
relative speed

## Slide 10: For adequate count rate, require either 100 keV fast ions or Ti > 10 keV
Thermonuclear
Semilog scale
Beam-plasma
Beam-Plasma reactions
Thermonuclear reactions
Semilog scale
means averaged over distribution functions

## Slide 11: Must use relative measurements of the differential cross section to measure the polarization accurately*
*A.V. Garcia et al., Nucl. Fusion 63 (2023) 026030
D-3He “emissivity” is
(the “reaction rate” is the integral of the emissivity over the volume)
Magnetic fusion plasmas are not very reproducible
The deuterium density is known to ~ 10% accuracy
The helium density is known to ~10% accuracy
The ion temperature is known to 5-10% accuracy  large uncertainty in
 Uncertainty in reaction rate > effect of polarization
Notes: TODO: Not sure how to make this flow

## Slide 12: Use relative measurements of the differential cross section to measure polarization
Differential cross section depends upon the tritium (or 3He) polarization & the vector and tensor D polarizations, and
50% increase in if both maximally polarized (PT = = 1)
No change in total cross section if only one is polarized
[If only one polarized] must be
isotropic
The relative change in emitted perp/parallel fusion-product signal is sensitive to polarization
Persistence of polarized signal  lifetime measurement
angle of emitted fusion product relative to
L. Baylor et al., Nucl. Fusion 63 (2023) 076009
Notes: TODO: Not sure how to make this flow

## Slide 13: Outline
Fusion: Use D-3He differential cross section to test 50% enhancement in D-T cross section
Spin Polarized Fuel
Depolarization Mechanisms
Possible experiments
Notes: Cite PRO

## Slide 14: Deliver deuterium as a solid 7Li-D pellet*
Use dynamic nuclear polarization to transfer spin polarization from electrons to nuclei to align the D spins.
Electrons are aligned in a strong B field at low temperature
Microwaves drive a hyperfine transition that transfers spins to D nuclei.
Use lithium to avoid high Z contamination of the plasma
Use 7Li to avoid background fusion reactions
Spin transfer occurs on multi-hour timescale
Need cryogenic (<4K) pellet gas gun to interface with polarizer
Target: &
~ 1020 D nuclei
Xiangdong Wei, Wed. 11:30
*L. Baylor et al., Nucl. Fusion 63 (2023) 076009
Cryostat for e-beam bombardment of LiD pellets
Notes: Cite PRO

## Slide 15: Deliver 3He as a shell pellet*
Hybrid spin-exchange optical pumping polarizes the 3He at high temperature
Polarized fuel is transferred to a glow-discharge polymer (GDP) capsule
Relaxation time is 3 days at 77K
MRI images of 3He permeating a GDP capsule
0 8.5 min
Target: @ 25 atm
~1019 3He nuclei
*L. Baylor et al., Nucl. Fusion 63 (2023) 076009
Photograph of amber GDP pellet
Notes: Cite PRO

## Slide 16: An intense polarized neutral beam is desirable
Schematic of test apparatus
Injected neutrals
Solenoid defines
Measure polarization
Large gradient aligns nuclei
Sona-like transition
In neutral frame, rapidly changing is an RF wave at precession frequency that provides radio-wave pumping within the Zeeman splitting
Hope to test at Tokamak Energy
Target: O(1019) polarized D or 3He nuclei per second
Polarized beams would:
simplify DIII-D experiments
enable experiments on small flexible devices
Faatz, Today 15:00
Kannis, Tuesday 9:00
Ciullo, Tuesday 12:00
Notes: Cite PRO

## Slide 17: Outline
Fusion
Spin Polarized Fuel: Exists in quantities sufficient for a DIII-D experiment
Depolarization Mechanisms
Possible experiments
Notes: Cite PRO

## Slide 18: Two mechanisms can cause depolarization: resonances at the precession frequency & hyperfine interactions
Deuterium precession frequency is 0.43
3He precession frequency is 2.13
Hyperfine interactions with bound electrons also a depolarization mechanism.
proton cyclotron frequency
Nuclei in a hot plasma are fully ionized, so this mechanism is irrelevant
Notes: Cite PRO

## Slide 19
Fluid (MHD) instabilities
Decreasing Spatial Scale; increasing frequency
A fusion plasma is filled with waves—won’t they depolarize the nuclei?
Fast-ion driven instabilities
Thermal-gradient driven instabilities
Coulomb collisions
In detailed calculations*, Kulsrud et al argue that depolarization lifetimes are long but are they right?
*R.M. Kulsrud et al., Nucl. Fusion 26 (1986) 1443.

## Slide 20: Magnetic moment conservation is a cornerstone of plasma theory
The adiabatic invariant is conserved as long as:
gyroradius
A very successful plasma theory, “gyrokinetics,” assumes conservation
The particle orbit and polarization (Bloch) equations are nearly identical:
 if is conserved, the polarization should be too!
Notes: Cite PRO

## Slide 21: Experiments can assess most depolarization mechanisms
Inhomogeneous static magnetic fields during injection
  Immerse flight tube in a O(0.1) T field to preserve polarization [1]
  Gradients too long to cause depolarization [1]
Hyperfine interactions during ionization
  Neutral ground state has no interaction
  Few % loss for 3He [1]
Binary Coulomb collisions
  Spin-spin, spin-orbit and quadrupole moment interactions predicted negligible [2]
Electromagnetic waves
  Most instabilities too low in frequency
  Waves near problematic
Wall interactions
  High depolarization rates at metal walls [3]
Limited by particle confinement time
[1] L. Baylor et al., Nucl. Fusion 63 (2023) 076009.
[2] R.M. Kulsrud et al., Nucl. Fusion 26 (1986) 1443.
[3] Greenside, Journal of Vacuum Science & Technology A 2, 619 (1984).
Notes: TODO: Animate the bottom

## Slide 22: Outline
Fusion
Spin Polarized Fuel:
Depolarization Mechanisms can be tested in existing facilities
Possible experiments
Notes: Cite PRO

## Slide 23: Use relative measurements of emitted 3.6 MeV alphas & 14.7 MeV protons to infer polarization*
Projected orbits
Ideal thermonuclear case
Complication: changes along escaping orbit
Adequate accuracy despite:
counting statistics
realistic polarization fractions
orbit uncertainties
uncertainty in emissivity profile
*A.V. Garcia et al., Nucl. Fusion 63 (2023) 026030
Notes: Cite PRO

## Slide 24: Planned experimental scenarios on DIII-D
1) Ti > 10 keV thermonuclear with H beams and LiD & 3He pellets.
2) Beam-plasma with unpolarized 3He neutral beam and LiD pellets.
Scenario
Large sensitivity
Special operating conditions; very hard plasma to make
Weaker sensitivity
Special operating condition; adequate count rate easy
3) Beam-plasma with unpolarized D neutral beam and LiD pellets.
D-D Sensitivity unknown
D beam injection routine; adequate count rate easy
4) Thermonuclear with LiD pellets.
D-D Sensitivity unknown
Easy operational regime; adequate count rate
Notes: Cite PRO

## Slide 25: With intense polarized beams and/or D-D differential cross sections experiments on many other facilities become feasible
Polarized D injection w/ polarized 3He pellet in Tokamak Energy’s ST40
Polarized D and 3He injection into WHAM
D-D experiment on the Madison Symmetric Torus

## Slide 26: Conclusions & Opportunities
Fusion: Use D-3He differential cross section to test 50% enhancement in D-T cross section
Spin Polarized Fuel: JLab and UVa are preparing LiD and 3He pellets for injection into DIII-D
Depolarization Mechanisms can be tested in existing devices
DIII-D polarization lifetime measurements are anticipated in ~ 5 years
3
Opportunities
Provide ~ 1 Amp polarized neutral beam
Polarization dependence of D-D differential cross sections at ”low” energy
1) “Polarized Fusion and Potential in situ Tests of
Fuel Polarization Survival in a Tokamak Plasma,”
L. Baylor, A. Deur, N. Eidietis, W.W. Heidbrink, G.L. Jackson, J. Liu, M.M. Lowry, G.W. Miller, D. Pace, A.M. Sandorfi, S.P. Smith, S. Tafti, K. Wei, X. Wei and X. Zheng, Nucl. Fusion 63 (2023) 076009.
2) “Conceptual design of DIII-D experiments to
diagnose the lifetime of spin polarized fuel”
A.V. Garcia, W.W. Heidbrink and A.M. Sandorfi, Nucl. Fusion 63 (2023) 026030.
Notes: Cite PRO

## Slide 27: Backup

## Slide 28: Backup

## Slide 29: What about a reactor?
Q: (70% D) * (65% 3He) only increases the cross section by 23%. Is it worth it?
1 Kannis (2021) Chem. Phys. Lett.
Q: Is the added complexity of polarization practical?
A: High flux laser driven polarization techniques1 should achieve 100% D and T polarization
2 Abdou (1986) Fusion Technology.
& Polarization
Notes: Cite PRO

## Slide 30: A beam-target D-D experiment is attractive but …
Use unpolarized D beam; tensor polarized D pellet
Cross section is larger at low energy than for D-3He
3.0 MeV protons have nearly the same orbits as 3.6 MeV alphas
Can also measure energy shift in silicon detectors
No theoretical expression available for the effect of polarization!
However, there probably is some effect--the unpolarized cross section is anisotropic
If we measure an effect of polarization, we can measure how long it persists!

## Slide 31
The polarization lifetime can be accurately determined*
*Garcia (2022).
Thermonuclear Scenario
Simulated data assume 0.40 s lifetime
Inferred lifetimes are

## Slide 32
Complication #2: Pellets not deposited in core
Use shell pellet with 3He payload
3He deposited around
[1] Hollmann AIP Conference (2009).
Izzo
Deuterium ice pellet mostly deposits at
Must rely on inward transport to take fuel to core

## Slide 33
Use gamma-ray detector for an independent measurement of the total reaction rate
The D-3He reaction produces gammas at 16.9 MeV and 15.4 MeV with a branching ratio of approximately 4.5 x 10-5
Different polarization dependence than main branch*
Wide solid angle detector needed for adequate counting rate
Kiptily, PPCF (2006)
*Garcia (2022)

## Slide 34: Measure the pitch, energy & poloidal distribution to diagnose reaction anisotropy
Relative changes in escaping CFP pitch, poloidal/axial position, and energy all sensitive to changes in
Energy at a silicon diode2
Multiple poloidal locations
ψ
Pitch at a FILD1
[1] Zweben, Nucl. Fusion (1989)
Pitch =
[2] Heidbrink, Nucl. Fusion (1984)
Notes: 1. , while the reaction rate is not

## Slide 35: Inject pellets with spin polarized nuclei
Prepare polarized D pellet
Prepare polarized 3He pellet (for thermonuclear experiment)
How long will the fuel stay polarized?
Preserve polarization during injection
1L. Baylor et al.
If using only one pellet: use D pellet and 3He fast ions
Two pellets requires a hot thermonuclear plasma
Notes: Cite PRO

## Slide 36: Direct detection of polarization (like in NMR) is attractive but seems very challenging