## Slide 1: Ce+BAF : Positron Injector for CEBAF 12 GeV
Joe Grames
  12 GeV e+ Capability
  R&D Topics
  Participation, Logistics, Timeline

## Slide 2: Expands 12 GeV capability with e+
Build two new injectors…
  10 mA polarized e- injector
  100 kW positron target
Two beam sources for CEBAF
  Retains original 4-hall polarized e- injector
  Adds new pair (e-/e+) and limited pol e- injector
Prioritizes
  Multi-hall capability (alt. is <4 halls)
  cw operation (alt. is pulsed <100% DF)
Timeline
  Ce+BAF capability happens after Moller
  Demonstration of e+ beams happens before this
Production of Highly Polarized Positrons Using Polarized Electrons at MeV Energies, D. Abbott et al., Phys. Rev. Lett. 116 (2016) 214801

## Slide 3: An electron/positron injector vault is required for 12 GeV e+ and 22 GeV e-
Existing FEL + long beam line
123 MeV e+ for 12 GeV CEBAF
650 MeV e- for Energy Upgrade
Green option is presently more cost effective and provides options for staging positron and energy upgrade

## Slide 4: PEPPo II : Polarized e+ Prototype Experiment
4
Next, we want to build a scalable polarized positron injector at LERF to demonstrate beam
  300 kV polarized gun + Wien filter, demonstrate > 1kC lifetime at milliamp current
  Build up the SRF e- injector 50 – 100 MeV
  Ramp up efforts for high power target 50 – 100 kW, e+ collection and compression
  Complete start-to-end concept in FY23

## Slide 5: Electron Injector (selected R&D)
LERF photo-gun will likely need to operate at a voltage greater than the CEBAF 200 kV Upgrade Gun.
  studies are evaluating new ceramic/receptacle >350 kV
  vacuum must be in the 10-12 Torr range (like CEBAF)
  and no Field Emission (like CEBAF)
July 2022 (unpublished) results of collaboration between Old Dominion University, Brookhaven National Lab and Jefferson Lab
Carlos Hernandez-Garcia
Matt Poelker

## Slide 6: Positron Injector (selected R&D)
Positron injector at LERF is a composite of systems,
  ”source” is integrated set of technologies; high power target, high field solenoid, RF capture
  CW operation will be unique, developing strategy for collection – capture - compression
PhD work of S. Habet (U. Paris)
SuperKEKB
Pulsed e+
Source

## Slide 7: Positron Target Development (selected R&D)
Building up team of target experts to study various target materials & geometries
  prototype/proof-of-principle (3-4 kW)
  full power design (17-20 kW)
Water pipe
Cu frame
Beam axis
  Rotating W target in a Cu frame cooled with RT water
Thermal Cycle
Heating Phase
Silviu Covrig
Andriy Ushakov

## Slide 8: US-Japan Cooperation – e-/e+ Injectors (planned DOE HEP 3-year)
  400 kV Polarized Electron Source
    Design and fabrication of commercial insulator (KEK/Kyocera) and (JLAB/MPF)
    Assembly and operational HV cathode test (JLAB) with large area electrode for improved space charge limit and photocathode lifetime
    Electrostatic modeling and design of compatible Wien Filter (JLAB)
  Positron Target Concept Development
    Liquid Xe target (SLAC), CFD thermodynamics calculations (KEK, JLAB) and evaluation of spin polarization (JLAB)
    Design and fabrication of 15 kW fixed target prototype (JLAB)
  Solid Target Fatigue Studies
    Beam irradiation (MAMI/JLAB, KEK) and thermal cycling (JLAB, KEK) of W-Cu and W crystal and alloys
    Target material evaluation of composition at PETRA light source (JLAB) and Old Dominion University Nanoprobe (JLAB)
  Positron Collection Technology
    Design and fabrication of e+ capture cavity (SLAC)
    Evaluation of pulsed flux concentrator vs. dc solenoid (KEK, JLAB)
  Electron and Positron Injector Beam Dynamics
    Simultaneous transports of low and high intensity bunch charges (KEK)
    Modeling and simulation of tunable polarized positron injector for CEBAF 12 GeV (JLAB)
KEK – Yoshinori Enomoto
SLAC – Spencer Gessner
JLAB – Joe Grames
Carlos Hernandez-Garcia
Gabriel Palacios-Serrano
Reza Kazimi Alicia Hofler
Sami Habet
Andriy Ushakov
Silviu Covrig
Sandeesh Gopinath
Andriy Ushakov
Md Mamun
Probir Ghoshal

## Slide 9: GaInSn Liquid Metal e+ Target (pending DOE SBIR Phase 1 proposal)
Material GaInSn PbBi
Composition 67Ga 20.5In 12.5Sn vol% 44.5Pb 55.5Bi at%
Melting Point -19 to 10.5 oC 123.5 oC
Vapor Pressure <E-08 Torr@500 oC 7.5E-09 Torr@250 oC
Density 6.44 g/cm3@ 20 oC 10.44 g/cm3
Radiation Length Xo 1.470 cm 0.606 cm
Thermal Conductivity 16.6 W/m-K 10.89 W/m-K (130 oC)
Dynamic viscosity 2.4E-3 Pa-s 3.3E-3Pa-s
Val Kolstroun
Karl Smolenski
Joe Conway

## Slide 10: Polarized Electrons, Positrons, and Polarimetry (P3E @ STRONG 2020)
Purpose : pushing further intensity frontiers of polarized electron sources, the intensity frontier of low energy polarized positron sources, and the precision frontier of electron polarimetry
Hydro-Møller polarimeter for on-line polarimetry at 100 MeV at P2@MESA
Mainz University
Application of the PEPPo technique to hadronic physics accelerator
IJClab
Jlab
Hamburg University
Mainz University
Development of high quantum
effciency and long live-time photocathodes
Jlab

## Slide 11: Polarized Electrons, Positrons, and Polarimetry (P3E @ STRONG 2020)
With a >400 C lifetime we could operate at 3 mA for about 3 days
Josh Yoskowitz, Joe Grames, Geoff Krafft
Sami Habet, Andriy Ushakov et al.
Niklaus Berger et al.
Design of a positron injector for CE+BAF
Evaluation of positron production targets
Development of HV-MAPS pixel detectors
(2x2 cm2)

## Slide 12: 2022 LDRD – degraded electrons (A. Sy, CASA)
Goals: evaluate CEBAF acceptance and compare to simulation; evaluate machine limits on positron beam size and current; transport positrons through parts of the CEBAF injector
How? Build a bypass beamline in the CEBAF injector to degrade electron beams through multiple scattering in thin target foils
  Phase space range between nominal CEBAF parameters and positron distribution posited in JLAB-TN-21-043
In FY23, we will design the bypass beamline and procure components
Beamline concept at 5D line in CEBAF injector
Quarter cryomodule
5D Dipole
Dipole
Dipole
Dipole
Target
Collimators
…
To CEBAF
e- beam with large emittance and momentum spread
Amy Sy
Yes Roblin
Dennis Turner
Cristhian Valerio
Victor Lizarraga

## Slide 13: Opportunities for participation
Areas where we have people working, but welcome participation…
  Beam optics (Yves, Dennis)
  Polarized electron source (Carlos, Gabriel)
  Electron injector design & modeling (Reza, Alicia, Max)
  Accelerating cavities (SRF, RF)
  Positron injector design (Andriy, Sami)
  High field solenoid magnets (Probir)
  Positron target development (Silviu, Andriy, Eric+, Val+)
  Spin rotator design (Fanglei)
Areas where I think we benefit from growing participation…
  Radiation shielding calculations & modeling
  Electron and positron polarimetry
  Materials calculations and evaluation (targets and collimators)
  Your new idea or interest

## Slide 14: Logistics and Timeline
Participation
  Completely new suggestion, folded into the R&D plan, or…
  Teaming up with an existing senior topical PI
    Scientist, Engineer, Post-doc, Technician
    Grad student plus an involved supervisor
2023 Goals
  February 1 – define 5 year milestones for LERF e+ development and CEBAF integration
  Produce a start-to-end conceptual design and technical report
    April 1 – IPAC’23 contributions status of R&D development
    June 1 – distribute outline and writing assignments
    September 1 – first drafts due at +3 months
    December 1 – final material due at +6 months