## Slide 1: Hpernuclear DAQ
Alexandre Camsonne
March 3rd 2023

## Slide 2: Outline
Experiment overview
Channel count
Overview pipelined electronics
Trigger overview
To do
Conclusion

## Slide 5: Channel count

## Slide 6
Level 1 & Trigger Distribution
Up to 128 front-end crates
CPU
VXS-Crate
Global Trigger Crate
Trigger Distribution Crate
trigger decisions
L1 Subsystem Data Streams (hits & energy)
Clock, Trigger, Sync, & Busy
Fiber Optic
Data Links
Front-End Crates
VME Readout to Gigabit Ethernet
TI
SSP
SSP
SSP
SSP
SSP
SSP
SD
VTP
SSP
SSP
SSP
SSP
SSP
SSP
CPU
VXS-Crate
TS
TD
TD
TD
TD
TD
TD
TD
TD
TD
TD
TD
TD
SD

## Slide 7
VXS (VITA 41 standard)
VME64x + high speed
serial fabric on J0
VXS Backplane Physical Layout:
Crate Level Use:
  VME64x used for event readout
  VXS: Low jitter clock & trigger distribution
  VXS: Gigabit serial transmission for L1 data streams to switch slot for processing
Crate Level – Signal Distribution
VXS Based, 20 Slot Redundant Star Backplane
VME64x backplane w/VXS (VITA 41 Standard) provides standard with high speed serial extension (new J0 connector)
18 Payload slots w/VME64x, 2 Switch slots
Each payload slot has 8 high speed capable links (10Gbps each) to both switch slots

## Slide 8
Splitter
QDC
Discriminator
Delay line
TDC
to primitive
trigger logic
detector
signal
detector
signal
FADC250
to smart
trigger logic
Existing System:
New System:
Capturing the Pulses…
(for timing >500ps)
Expensive, bulky delay cable
dispersive & attenuates
multiple modules for
time & energy
Non-pipelined electronics guarantee dead-time
(conversion time)
Very limited channel resolution used in trigger
Time, energy, trigger output in 1 module
CLAS TOF has >150,000ft delay line!
Pipelined sampling, readout, & trigger -> no dead-time
Digitization retains original signal integrity
Long pipeline allow more time for complex triggers
Gate

## Slide 9
Front-End Electronics: fADC250
Used in existing 6GeV program:
  Hall A BigBite
  Upgraded Hall A Moller Polarimeter
16 Channel 12bit, 250Msps Flash ADC
8µs raw sample pipeline, >300kHz sustained trigger rate (bursts @ ~15MHz)
Post-processing in customizable firmware to extract time, charge, and other parameters minimizing event size
Module supports 2eSST VME transfers at 200MB/s transfer rate
Large event block sizes (>100) to minimize CPU interrupt handling
VXS P0/J0 outputs 5Gbps L1 data stream (hit patterns & board sum)
JLab-FADC250:

## Slide 10: Channel count
FADC = 88 + 42 +48 +116 = 294 channels = 19 FADCs = 2 VXS crates
V1190 = 2268 channels = 18 V1190 = 1 VME64X crate
TOF = 204 channels = 7 V1290 = 8 F1 = 3 VETROC
If not running with SBS or NPS most likely enough FADCs
Can use HMS electronics
BPM rasters : 2 FADC

## Slide 11: Data rates
Rough estimates
  HKS = 1 MHz
  HES = 1 MHz
  Coincidence = 1MHz x 1 MHz x 20 ns = 2 KHz
Plan for up to 20 KHz desirable
Using CODA3 and event blocking should be doable ( similar to CLAS12) will be tested during NPS
Need to evaluate detector occupancies
If useful can record full FADC waveforms
Example scintillator SoLID beam test

## Slide 12: Trigger
FADC
VTP
VTP
FADC
FADC
FADC
TI
TI
HKS
HES
TI
V1190
Can program VTP for coincidences between scintillators
If use VETROC instead of V1190 could add Drift Chamber to trigger
VETROC
VETROC
VETROC
VETROC

## Slide 13: Additionnal electronics
Beamline info
  Target BPM
  Raster
  1C12 BPM cabling

## Slide 14: To do / Testing
Bench testing and testing with detector VETROC
Setup FADC trigger with VTP
Setup testing in ESB

## Slide 15: Additionnal detectors
MCP PMTs
MRPC
Would need dedicated new electronics

## Slide 16: Conclusion
HKS and HES
  FADC = 88 + 42 +48 +116 = 294 channels = 19 FADCs = 2 VXS crates
  V1190 = 2268 channels = 18 V1190 = 1 VME64X crate
  TOF = 204 channels = 7 V1290 = 8 F1 = 3 VETROC
  Could use HMS/NPS/SBS hardware
CODA3 with event blocking should allow 20 kHz trigger rate
Digital trigger using FADC and VTP
If use VETROC instead of V1190 can include in L1 trigger ( High res TOF and Drift Chamber )

## Slide 17: Backup

## Slide 18: CLAS12 Trigger
Detector | Can be in trigger? | Will be in trigger? | Trigger Algorithm
ECAL/PCAL | Yes | Yes | U/V/W Clustering
DC | Yes | Yes | Segment Position/Angle Finding
CTOF/FTOF | Yes | Yes | Hit based
HTCC/LTCC | Yes | Yes | Hit based
FT | Yes | Yes | 3x3 Clustering
CND | Yes | No | N/A
SVT | Yes | No | N/A
RICH | Yes | No | N/A
MicroMegas | No | No | N/A
CLAS12 triggering will support geometric matching (e.g. drift chamber segment points to clusters, etc…)

## Slide 19: Drift Chamber Segment Finder Example
sweeps angle and wire offset:
valid segments are binned into common angle, VHDL file w/equations auto-generated:

## Slide 20: Drift Chamber Segment Finding Trigger
Scope like interface on GTP allows real-time display of found segments by trigger logic
  Cosmic event shown where only 1 segment was the trigger condition
x14 DCRB
70Gbps
(DC Hits)
GTP:
prototype VXS concentrator card
Receives all DC hits from DCRB
Searches for track segments and reports position/angle to next trigger stage
VTP (mentioned later in talk) with be used in CLAS12