## Slide 1: C100 Transition to Operations

## Slide 2: C100 Zone Overview
The 10 new C100 cryomodules were each designed to deliver a minimum of 100 MeV of acceleration to the electron beam per pass. The Cathode Power Supply (CPS) and High Power Amplifier (HPA) have been redesigned to generate required power for producing the accelerating fields in the superconducting RF cavities. Higher gradients and narrower bandwidth along with Lorentz force detuning and increased microphonic sensitivity were formidable obstacles to realizing cavity RF field stability. In order to meet cavity field phase and amplitude specifications for physics quality beam, a new RF Low Level Control system utilizing the precision of digital signal processing was designed and manufactured. Infrastructure upgrades such as increased capacity for the Cryogenic Helium Liquefier plant and Low Conductivity Water cooling system, site power, master oscillator and service building environmental controls all contributed to the successful commissioning of the C100 cryomodules for the 12 GeV era.

## Slide 3: In a perfect world…
  1 Button Operation
  No trips
  = NO PROBLEMS!
  Unfortunately…

## Slide 4: The Reality
12 GeV
R100
C50
C100
1-3
C25
C100
4-10
5 “Flavors” of cryomodules, each with their own operational characteristics
+ the additional pleasure of contending with construction/heavy equipment,
jets flying by, traffic, thunderstorms, doors slamming, etc…
“With greater power comes… more trips” – Clyde Mounts

## Slide 5: C100 Transition Aids

## Slide 6: What’s been done so far?
Tuners over fiber modification
Heater distribution to all 8 cavities
1 button Cold Start recovery script
  Automatically find POFF and TDOFF values
1 button cavity/zone recovery script
Master Reset
EDM screens suite tailored for C100/R100
Burt save/restore
And a ton of “under the hood” refinements…

## Slide 7: Recovering a C100 Zone
From the RF Captain screen
1. Push “R”
Bar should turn green
2. Push “1”
Boxes should turn green
3. Push “RF On”
The cavity boxes will
automatically cycle
through SEL, GDR,
Gradient Ramp,
RF fully on
That was easy!™

## Slide 8: Recovering a C100 Zone
From the RF Combo
That was easy!™
1. Push
2. Push
3. Watch the arrows
until all the cavities
are to “Ena Ramp”.
“Done” will display
when the script
completes.

## Slide 9: For Robust Operations - Administrative
Documentation
  System owner’s manual
Operator training - Technical staff training
  OJT (ongoing)
  Formal Low Level Classes (development in process)
EPICS/hlapps diagnostics tools development (all in process)
  Gradient Management
  All Cavity Status
  Fault Counter/Viewer
  Ring Buffer Waveform Viewer/Analysis tools
Engineering staff control room presence/availability
Integration of lessons learned during real-time operations
Keep in mind that the RF System relies on other systems to perform within specifications -
  Familiarity with support system characteristics and status is invaluable for determining root causes of RF faults and performance issues not directly attributable to RF HW/SW deficiencies
  Meetings are currently taking place between EESRF/SRF, and EESRF/Cryo to discuss performance issues and develop plans to mitigate problems

## Slide 10: For Robust Operations - Design/Hardware
Diagnostics tools development
  First fault capture
  Ring buffers
  Trigger on FSD
  CPS/HPA fault firmware diagnostics
Spares availability
PZT integration (C100 1-3)
Refine control system algorithms
  Tuners
  Loop gains/parameters
  Recovery speed tweaks
Individual heater control
  Test plans for understanding performance anomalies are in development
System failure management process development
  Removing a cavity(ies) from service - bypass
1 button zone burt save/restore function

## Slide 11: Questions?