## Slide 1: HyperCT: Hyperspectral Neutron Computed Tomography
Shimin Tang, Ph.D (tangs@ornl.gov)
PI: Hassina Bilheux
Materials Engineering Group, Neutron Scattering Division
Oak Ridge National Laboratory

## Slide 2: Neutrons interact uniquely with matters
Neutron
X-ray
https://www.psi.ch/en/niag/what-is-neutron-imaging
Non-destructive
High penetration depth
Sensitive to light elements (H, Li, etc.)
Isotopic contrast

## Slide 3: Continuous and Pulsed Neutron Sources
Continuous Source (reactor)
Pulsed Source (spallation source)
Source
Source
Continuous stream of neutrons with a mixture of multiple wavelength
Pulses of neutrons
Detector
Detector
: Neutrons leave the source
: Neutrons arrive at the detector
Time-stamping neutrons = capability to calculate their wavelength
One radiograph
Up to 3000 radiographs (low signal-to-noise)
Wavelength or energy dependent = hyperspectral

## Slide 4: Hyperspectral Feature
Two-dimensional TOF neutron radiograph
Bragg-edges
Incident neutron (I0)
Transmitted neutron (I1)
Transmitted neutron (I2)
Extract crystallographic information from the Bragg-edge spectrum
“Hyperspectral”
(Lambert-Beer Law)
Depends on the crystallite size along the beam direction
E. Fermi, W. Sturm, R. Sachs. The transmission of slow neutrons through microcrystalline materials, Physical Review 71 (1947) 589.

## Slide 5: Hyperspectral Neutron CT
Data Acquisition
Sample
Pulsed Neutron Beam
Slit System
Neutron Source
CT Reconstruction Algorithm
Sinogram
MCP detector

## Slide 6
Hyperspectral Neutron CT has longer measurement time
*svmbir, 2020, SVMBIR Development Team, Super-Voxel Model Based Iterative Reconstruction (SVMBIR), Software library available from https://github.com/cabouman/svmbir
ADARA archives raw data
ADARA triggers auto reduction
SNS analysis server
Detector
Sample
Neutron CT reconstruction
Start/Stop
Instrument scientists / Users
After one-day measurement
After 5-day measurement
Acquisition starts with new scan angle and pCharge
Radiography
Script monitors reduced data
API serves new scan angles to EPICS
Scan Angles
AI-based system
* courtesy of George Nelson

## Slide 7
Find the longer dimension
Keep diversity
Projection angles that are aligned with longest edges of the object of interest are important.
: scalar weight controlling the level of diversity
: the angle to be selected, be the intermediate reconstruction from = {}.
Optimized Sample-Shape Adaptive Angle Selection via Reconstruction Understanding*
*Shimin Tang, Yang, Diyu, Singanallur V. Venkatakrishnan, Mohammad SN Chowdhury, Yuxuan Zhang, Hassina Z. Bilheux, Gregery T. Buzzard, and Charles A. Bouman. "An Edge Alignment-based Orientation Selection Method for Neutron Tomography." arXiv preprint arXiv:2212.00647 (2022).

## Slide 8
Edge alignment from data fitting
1
2
: input image slice
: edge image slice
:
Linearized edge image
Cost Function
Normalized angle spacing cost function w.r.t. view angles.
Red mark shows the values of existing view angles.
Notes:             Obtain edge image with Canny Edge Detection algorithm
            Obtain linearized edge image with Probabilistic Hough Transform
            For each rotate to angle 𝜃 in ,a segment is extended to cover all rows and count the number of overlapping pixels on the edge image
            Obtain edge image with Canny Edge Detection algorithm
            Obtain linearized edge image 𝐿 with Probabilistic Hough Transform
            For each rotate to angle 𝜃 in 𝐿,a segment 𝑙_𝑖 is extended to cover all rows and count the number of overlapping pixels on the edge image

## Slide 9: Obtain better reconstruction with less scans
Reference image
Recon with angle selection
Proposed algorithm
Golden-angle
NRMSE Plot
Better quality
* Courtesy of Yuxuan Zhang

## Slide 10
Subjectively assign the quality scores
Data Augmentation
3D CNN model
CNN based streaming neutron computed tomography (nCT) reconstruction quality evaluation

## Slide 11
The comprehensive streaming-quality index (1-5)  stopping reference
Streaming Time-Line
Streaming nCT quantity quality index (QI)
Single Reconstruction Score
Subsequent Improvement Index
6 hours
12 hours
18 hours
24 hours
30 hours
36 hours
42 hours
48 hours
52 hours
Notes: User can set

## Slide 12: AI-based Autonomous Neutron Imaging System
The autonomous system consists of (1) Artificial Intelligence (AI) based 3D reconstruction quality assessment and (2) Automatic subsequent angle selection.
Commands
Reconstruction
Decision Making
AI Quality Evaluation
AI Reconstruction Quality Score
Reconstruction Improvement
Quality Index
Stop
Angle Selection
Recon. Edge Detection
Edge Alignment Angle Selection
Continue
Next Angle

## Slide 13: First completely autonomous neutron experiment at ORNL
Start
Acquisition starts with new scan angle and pCharge
ADARA archives raw data
ADARA triggers auto reduction
SNS analysis server
Script monitors reduced data and triggers
AI-driven HSnCT system
AI-driven HSnCT system
@ Edge Node
Stop
Continue
CT Reconstruction
(SVMBIR*)
AI Quality Evaluation
Propose Next Scan Angle
Making Decision
API serves new scan angles to EPICS
New Angle
Radiography
Reduced Data
Reconstruction
Goniometers
Detector
Sample
Users can access the reconstructed data and change criteria setting via ThinLinc
*A. C. Kak and M. Slaney, Principles of computerized tomographic imaging. SIAM, 2001.
Automatically stopped after ~27 projection angles, which is ~10 times faster than a naïve scan*.

## Slide 14: Unique Contrast Mechanisms for Biomaterials
Bone/metal implant interfaces
  Bone porosity/both growth
  Strain of implant on bone
  Bone/implant behavior under stress
Application portfolio is immense:
  orthopedic (joint implants, cements, fillers, scaffolds), cardiovascular (stents), dental restorative materials (composites, cements)
Cancer in bones
At ORNL, we have both conventional neutron imaging (MARS@HFIR) and hyperspectral neutron imaging (VENUS@SNS)
*Rat femur with titanium implant. (A) Photograph of a representative rat femur. (B) 3D rendered volume of rat femur obtained from nCT. (C) Diagonal slice showing the titanium rod inside the femur. Red arrows show the trabecular bone. The scale bars are presented by the x and y axes, respectively.
*Bilheux HZ, Cekanova M, Warren JM, Meagher MJ, Ross RD, Bilheux JC, Venkatakrishnan S, Lin JYY, Zhang Y, Pearson MR, Stringfellow E. Neutron Radiography and Computed Tomography of Biological Systems at the Oak Ridge National Laboratory's High Flux Isotope Reactor. J Vis Exp. 2021 May 7;(171). doi: 10.3791/61688. PMID: 34028436.

## Slide 15: Takeaways
Neutron images have unique contrast mechanisms for biomaterials
Upcoming VENUS (Hyperspctral) will bring more wavelength-relative details
AI-based autonomous imaging system reduced the HyperCT’s time costing
ORNL will provide the advanced neutron imaging studies via 3-Source Strategy (Details can find in poster)
HFIR
MARS enables real-time 3D tomography of objects
SNS (Aug. 2023)
VENUS will leverage time-of-flight capabilities of the pulsed-beam accelerator for unique insights via Bragg-edge imaging
STS (2033)
The high volume of specialized cold neutrons at STS will enable kinetic measurements

## Slide 16: Acknowledgement
A portion of this research used resources at the High Flux Isotope Reactor and Spallation Neutron Source, DOE Office of Science User Facilities operated by the Oak Ridge National Laboratory. Oak Ridge National Laboratory is managed by UT-Battelle, LLC, for the U.S. DOE under contract DE- AC05-00OR22725.

## Slide 17: Our team (present and past contributors)
Aaron Hanks, Amy Jones, Amy Byrd, John Cristy, Molly , Ian Turnbull, Matthew Balafas, Tim Lessard, Ryan Mangus, Bill McHargue, Harley Skorpenske, Mary-Ellen Donnelly, Dave Conner, Jean Bilheux, Mark Lyttle, Tena Graben-Galyon, Steve Chae, Wendy Cain, Scott Helus, Matt Kyte, Franz Gallmeier, Irina Popova, Wei Lu, Thomas Huegle, Georg Ehlers, Bogdan Vacaliuc, Greg Guyotte, Alex Koldys, Rich Crompton, Matt Bedynek, Steven Mellard, Saul Kaminskas, Bino Vasquez, Robert Marrs, Jerry Stockton, Christ Stone, Rob Knudson, Bhargavi Krishna, George Rennich, Scott Keener, Andre Parizzi, Randy Williams, Patrick Thornton, Xiaosong Gang, Yuxuan Zhang, Erik Stringfellow, Jamie Molaison, Steve Hicks, Richard Ibberson, Tommy Thomasson, Venkat Venkatakrishnan, Shimin Tang, Su-Ann , Natalie Hogan, Mariano Ruiz-Rodriguez, and my apologies for the names I forgot to list.

## Slide 18
VENUS
MARS

## Slide 19
Cost Function
measures the angular distance between and .
Normalized angle spacing cost function w.r.t. view angles.
Red mark shows the values of existing view angles.

## Slide 20
NR
Medulla
Capsule
Fat in the renal sinus
Renal Pelvis
Cortex
A
MRI
C
D
X-CT
B
NR
*Neutron radiograph of feline metastatic breast cancer in lungs. (A) Photograph, (B) H&E stained section, (C) neutron radiograp in grey scale, and (D) neutron radiograph in color scale of 2-mm thick feline metastatic breast cancer in lungs. Grey and color scale bars represent neutron transmission in scale 0-100% .
HFIR | MARS (CG-1D)
*M. Cekanova, R. Donnell, H. Bilheux and J. -C. Bilheux, "Neutron imaging: Detection of cancer using animal model," Proceedings of the 2014 Biomedical Sciences and Engineering Conference, Oak Ridge, TN, USA, 2014, pp. 1-4, doi: 10.1109/BSEC.2014.6867752.
Notes: Hydrogen nuclei scatter cold neutrons stronger than any other atomic nuclei; therefore hydrogen is a primary contributor to neutron contrast in biological specimens.
The limitations of neutron imaging for biological samples have been overcome by the introduction of digital CCD cameras, increased spatial resolution (100μm) and increased neutron flux (1×107 neutrons/cm2/s).

## Slide 21: Neutron Computed Tomography of Human Cadaver Teeth
First human teeth were measured at CG-1D (IPTS-23792) December 24-25, 2019. Neutrons may shed some light into the mineralization levels of tissues surrounding metal restoration. This research is done in collaboration with Dr. F.L. Esteban Florez at the Univ. of Oklahoma.
40 s radiograph of 3 extracted cadaver teeth (left) and respective photographs (right). The two bottom teeth have TiO2 implants.
Anxiously waiting for SNS|VENUS we can measure the residual strain on the bone due to the implant.

## Slide 22
Two subsequent reconstructions are compared to each other using the normalized mean square error (NRMSE) and the structural similarity index measure (SSIM) algorithms.
Improvement index defined as: ()
Subsequent reconstructions comparison
NRMSE
SSIM
Better quality
Better quality
Higher scaled score
Notes: extracts the point wise statistics of local normalized luminance signals and measures image naturalness (or lack there of) based on measured deviations from a natural image model

## Slide 23
Rat femur with titanium implant. (A) Photograph of a representative rat femur. (B) 3D rendered volume of rat femur obtained from nCT. (C) Diagonal slice showing the titanium rod inside the femur. Red arrows show the trabecular bone. The scale bars are presented by the x and y axes, respectively.
Neutron computed tomography and slices through the plant root/soil system. (A) Photograph of plant sample. (B) 3D rendered volume from neutron computed tomography of the plant showing the stem above ground, and the soil system with water (in red). (C) and (D) are cuts through the sample angled to show the stem and roots in the soil (red arrows). Darker blue areas in the soil indicate the presence of water
Rat femur with titanium implant. (A) Photograph of a representative rat femur. (B) 3D rendered volume of rat femur obtained from nCT. (C) Diagonal slice showing the titanium rod inside the femur. Red arrows show the trabecular bone. The scale bars are presented by the x and y axes, respectively.

## Slide 24: VENUS
VENUS is an imaging beamline that can measure unique materials properties based on their crystalline structures and isotopic content using two techniques:
    Bragg-edge imaging – quantitative interpretation of total cross-section provides crystalline structure characterization (cold neutrons ~ meV)
    Resonance imaging – isotopic-sensitive spatially-resolved spectroscopy technique (epithermal neutrons ~ eV)
VENUS can also penetrate thicker samples using:
    Epithermal imaging – higher energy neutrons provide higher penetration through thick samples (epithermal neutrons ~ eV)
We are developing hyperspectral reconstruction algorithms using machine learning algorithms (due to low signal-to-noise ratio)
An AI-based Autonomous Neutron Imaging System is under developing also.