## Slide 1: Accelerator System - Reliability
System reliability is an important consideration for any system that is critical to the success of an organization. By understanding the factors that affect reliability and taking steps to improve it, organizations can reduce the risk of system failures and improve the uptime of their critical systems.
O. Garza
    Primary Systems
Beam Dumps
Beam Transport
Control Systems
Cryogenic Systems
Diagnostics
Facilities
Gun/Laser
Information Systems
Magnet Systems
Operations
Others
Radio Frequency Systems (RF)
Radiation Controls
Safety Systems
Vacuum Systems

## Slide 2: Examples of Primary Sub-System DT Categories
Beam Dumps
  Stationary Dumps - Insertable Dumps – etc.
  Beam Transport
    Optics - Beam Loss - Beam Instability – Orbit – Config. Change – etc.
    Control Systems
      IOCs – CAMAC Crates – Reboot Switches – etc.
Cryogenic Systems
  CHL1 – CHL2 – Linacs – ESR – etc.
Diagnostics
  Harps – Viewers – BPMs – etc.
Facilities
  AC Distribution – Chiller Loop – Fire Protection – etc.
Gun/Laser
  Laser Table – Gun HV – Laser RF – etc.
Information Systems
  Low Level Applications – Network – UNIX Apps – File Servers – etc.

## Slide 3: Examples of Primary Sub-System DT Categories
Magnet Systems
  Box Supplies – Trim Racks – Dipoles – Quads – Shunts – etc.
Operations
  Operations Personnel – Operator Staffing – Operator Training – Operator Error – etc.
Others
  Weather – Unknown/Missing – Hall Downtime – etc.
Radio Frequency Systems (RF)
  Cryo-modules – RF Cavities – RF Separators – MO System – etc.
Radiation Controls
  Radiation Monitors/PSS Interlocked – etc.
Safety Systems
  Access Controls – FSD – Beam Stoppers – ION Chambers – MPS BLM – etc.
Vacuum Systems
  Beam Valves – Ion Pumps SRF – Ion Pumps EE – SRF Insulating Vacuum – Turbo Pumps – Beamline Instrumentation - etc.

## Slide 4: Annual Availability for Beam Transport
Chart: 
| 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023
Beam Transport | 92.9 | 86.9 | 92.6 | 92.2 | 97.9 | 94.2 | 91.5
Chart: DT - Beam Transport
| 2017-Run | 2018-Run | 2018-Run | 2019-Run | 2020-Run | 2020-Run | 2021-Run | 2022-Run | 2023-Run
Optics | 0 | 190 | 26 | 165 | 11 | 3 | 2 | 20 | 11
Beam Loss | 15 | 55 | 15 | 39 | 52 | 27 | 35 | 170 | 28
Beam Instability | 3 | 34 | 20 | 25 | 9 | 8 | 3 | 35 | 20
Orbit | 14 | 7 | 9 | 26 | 7 | 7 | 8 | 21 | 35
Beam Quality Check | 1 | 4 | 16 | 39 | 8 | 9 | 5 | 22 | 12

## Slide 5: Annual Availability for Controls
Chart: Overall Control Systems
| 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023
Controls | 99.2 | 99.6 | 99.8 | 99.8 | 99.4 | 99.8 | 99.8
Chart: DT - Controls
| 2017-Run | 2018-Run | 2018-Run | 2019-Run | 2020-Run | 2020-Run | 2021-Run | 2022-Run | 2023-Run
IOCs | 3.6 | 11.5 | 12.5 | 19 | 4.5 | 0 | 19 | 15 | 7.5
CAMAC | 3 | 1.5 | 1 | 0 | 0 | 0 | 0 | 2 | 0.75

## Slide 6: Annual Availability for RF Systems
Chart: Overall RF Systems
| 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023
RF | 95.8 | 96.5 | 98.8 | 98.2 | 98.4 | 98.5 | 98.1
Chart: DT - RF Systems
| 2017 | 2018 | 2018 | 2019 | 2020 | 2020 | 2021 | 2022 | 2023
Cryomodules | 40 | 38 | 80 | 75 | 43 | 62 | 65 | 150 | 45
RF Cavities | 25 | 16 | 35 | 38 | 27 | 34 | 80 | 95 | 50
RF Separators | 56 | 7 | 35 | 49 | 11 | 25 | 32 | 25 | 13
Warm RF | 12 | 6 | 4 | 4 | 20 | 2 | 4 | 38 | 2
MO System | 0 | 7 | 2 | 1 | 2 | 1 | 2 | 0 | 1

## Slide 7: Annual Availability for Vacuum Systems
Chart: Overall Vacuum Systems
| 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023
Vacuum | 99.7 | 99.8 | 99.6 | 99.6 | 99.7 | 99.8 | 99.6
Chart: DT - Vacuum Systems
| 2017-Run | 2018-Run | 2018-Run | 2019-Run | 2020-Run | 2020-Run | 2021-Run | 2022-Run | 2023-Run
Beamm Valves | 0 | 1.2 | 8.5 | 55 | 7 | 2 | 17 | 7.5 | 1
Ion Pumps -SRF | 1.5 | 0.1 | 3.2 | 3 | 0 | 25 | 1 | 8.1 | 0
Ion Pumps | 0 | 2.1 | 4 | 11 | 13 | 5 | 1 | 8.1 | 1
Fast Valves | 0 | 0.6 | 2 | 36 | 0 | 0 | 0 | 0 | 0
SRF Insulating Vac | 0 | 2.2 | 0 | 1 | 3 | 0 | 0 | 2.5 | 13
Waveguide SRF | 2 | 0.9 | 0 | 0.5 | 0 | 0.2 | 1 | 4.5 | 0

## Slide 8: Annual Availability for Safety Systems
Chart: DT - Safety Systems
| 2017-Run | 2018-Run | 2018-Run | 2019-Run | 2020-Run | 2020-Run | 2021-Run | 2022-Run | 2023-Run
Access Controls | 2.7 | 23 | 10 | 16.5 | 7.5 | 6 | 23 | 13 | 4
FSD | 5.5 | 5 | 1.7 | 10.5 | 0 | 0.5 | 20 | 9 | 0
Ion Chambers | 6.2 | 0 | 0 | 0 | 8 | 2.5 | 6 | 0 | 0
BLA | 5 | 2 | 0 | 0 | 3.5 | 0 | 0 | 0 | 0
Beam Stoppers | 0 | 5 | 3.5 | 1 | 0 | 0 | 7 | 0 | 12
Chart: Overall Safety Systems
| 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023
Safety Systems | 99.6 | 99.8 | 99.7 | 99.8 | 99.6 | 99.8 | 99.5 | 99.6857

## Slide 9: Annual Availability for Magnet Systems
Chart: Overall Magnet Systems
| 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023
Magnets | 96.9 | 99.7 | 99.7 | 99.1 | 99.3 | 98.8 | 99.5
Chart: DT - Magnet Systems
| 2017-Run | 2018-Run | 2018-Run | 2019-Run | 2020-Run | 2020-Run | 2021-Run | 2022-Run | 2023-Run
Box Power Supplies | 105 | 14 | 7 | 35 | 14 | 15 | 82 | 42 | 3
Dipoles | 3 | 1.6 | 3.2 | 5 | 15 | 6 | 47 | 150 | 17
Quads | 8 | 9 | 8.5 | 15 | 5 | 11 | 20 | 9 | 2
Trim Racks | 2 | 2.2 | 2.5 | 30 | 3.5 | 1 | 3 | 19 | 2
Correctors | 1 | 1 | 2.5 | 4 | 1 | 2 | 3 | 10 | 3

## Slide 10: Annual Availability for Facilities
Chart: Overall Facilities
| 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023
Facilities | 100 | 99.7 | 99.6 | 98.8 | 99 | 99.8 | 99.2
Chart: DT - Facilities
| 2017-Run | 2018-Run | 2018-Run | 2019-Run | 2020-Run | 2020-Run | 2021-Run | 2022-Run | 2023-Run
AC Distribution | 0 | 23 | 3.5 | 11 | 0 | 4.5 | 91 | 16 | 18
LCW | 0 | 0 | 0 | 27 | 0 | 0 | 18 | 7.7 | 0
Chiller System | 0 | 0 | 0 | 0 | 0 | 0 | 10 | 9 | 4.5
Site Fire Protection | 0 | 0 | 0.3 | 0 | 0 | 0 | 1 | 1 | 0

## Slide 11: DT – Operations – Info Systems – Cryogenics - Diagnostics
Chart: DT - Operations
| 2018-Run | 2019-Run | 2020-Run | 2020-Run | 2021-Run | 2022-Run | 2023-Run
Operator Error | 2.6 | 10.5 | 10 | 1.8 | 1.8 | 0.5
Operator Staffing | 0.5 | 1.7
Operator Training | 0.3 | 0.8 | 0.3
Chart: DT - Diagnostics
| 2017-Run | 2018-Run | 2018-Run | 2019-Run | 2020-Run | 2020-Run | 2021-Run | 2022-Run | 2023-Run
BPM nAmps | 7.2 | 0 | 0 | 3.9 | 0 | 0 | 0 | 0 | 0
30Hz Modulation | 4.2 | 0 | 0 | 1.2 | 0 | 0 | 0 | 0 | 0
Harps | 0.5 | 0 | 0 | 1.2 | 1.2 | 0 | 0 | 0 | 0
Viewers | 0.5 | 0 | 0 | 9 | 2.6 | 0 | 0 | 0 | 0
30Hz Sync | 0 | 0 | 0 | 0.5 | 0 | 0 | 0 | 0 | 0
BPMs - SEE | 0 | 0 | 0.8 | 0 | 0 | 0 | 0 | 22.4 | 1.6
Fast Feedback | 0 | 0 | 0 | 0 | 5 | 0 | 0 | 0 | 0
Chart: DT - Information Sytems
| 2017-Run | 2018-Run | 2018-Run | 2019-Run | 2020-Run | 2020-Run | 2021-Run | 2022-Run | 2023-Run
IOC LL Apps | 20 | 1.5 | 2.6 | 6 | 1.1
Network | 11 | 0.2
Unix Apps | 1.5 | 0.7 | 0 | 2 | 11 | 0.6 | 2.2 | 1.3
SRVC Bldg. UPS | 6
File Servers | 0.5
Chart: DT - Cryogenic Systems
| 2017-Run | 2018-Run | 2018-Run | 2019-Run | 2020-Run | 2020-Run | 2021-Run | 2022-Run | 2023-Run
CHL1 | 3.5 | 4.6 | 0 | 55 | 0 | 9.1 | 17 | 6.6 | 7.2
CHL2 | 2.5 | 1.2 | 0 | 0 | 0 | 6.2 | 9 | 5.2 | 0
Linacs | 0 | 0 | 3.2 | 1 | 0 | 0 | 0 | 1.2 | 2.2
ESR | 0 | 0 | 0 | 0 | 2.2 | 0 | 0 | 0 | 0

## Slide 12: DT - Other
Chart: DT- Other
| 2017-Run | 2018-Run | 2018-Run | 2019-Run | 2020-Run | 2020-Run | 2021-Run | 2022-Run | 2023-Run
Weather | 0 | 0 | 4.6 | 7 | 0 | 72 | 0.5 | 56 | 0
Unknown/Missing | 2.7 | 1 | 6.1 | 19 | 3.2 | 0 | 1.9 | 11 | 5.2
Hall Downtime | 0 | 0 | 0 | 1.5 | 1.8 | 1 | 0 | 4 | 1.2

## Slide 13: DT – Trip Durations Per Cryomodule
The data used for the figure above was retrieved from the Downtime Manager’s FSD Trip Summary tool. All trips greater than ten minutes were excluded. Ideally, any trips longer than five minutes are taken into consideration in the downtime manager. In addition, all trips that occurred when all four Hall statuses were set to OFF (i.e. maintenance days) were excluded. The C25/C50s are the quickest to recover, on average, at about 40s per FSD trip, C100s (non-SELAP) around 110s per FSD trip, and C100s (SELAP) around 45s per FSD trip.

## Slide 14: Energy Reach vs. True Arc Faults
We use the energy reach here as some quantification of the amount of headroom that we have in each linac. It’s pretty easy to see that as headroom decreases the number of true arc faults also increases, leading to an increase in time lost due to FSD trips.
The figures for Energy Reach vs True Arc Faults were created with data taken from the RF Dashboard and the RF Fault Viewer. Values were recorded for energy reach and true arc faults for each linac on a daily basis for the entirety of last run and superimposed on two graphs, one for the north linac and one for the south linac.

## Slide 15: DT- Average Ramp Times
Average ramp times associated with Hall A and Hall C are as follows:
Hall A was limited to a 0.7uA/s ramp time due to sensitive targets
  The average production current into Hall A was about 33.2uA
  This gives us an average ramp time of between 46.2 and 48.2 seconds for Hall A
Hall C’s ramp time and production current varied throughout their run
  Utilizing a similar ramp time for Hall C’s average production current resulted in an average ramp time of 33.7 seconds for Hall C
Details and guidelines for determining these parameters will be provided, in depth, in the follow-up technical note.
*A special thanks to Eric Deir for researching and crunching these numbers!

## Slide 16: Questions???
Authors:
O. Garza
E. Deir
Improving Reliability
Using good design practices
Using high-quality components
Operating and maintaining the systems properly
Protecting the system from environmental hazards
Conduct regular inspections and maintenance to identify and fix potential problems.
Improve system monitoring and alarms to identify problems early on
Have a well-trained staff
Keep systems up-to-date.
Do not exceed design parameters – know your systems limits