## Slide 1: The MOLLER Experiment Caryn Palatchi Indiana University JLUO Meeting June 28, 2023

## Slide 3: Parity-Violating Electron Scattering
unpolarized target
e
e
e
e
Z0
Incident beam is longitudinally polarized
Change sign of longitudinal polarization
Measure fractional rate difference
New physics: measure fundamental coupling constants to test completeness of standard model
σ ∝ |Mγ + Mweak|2
~ |Mγ|2 + 2Mγ(Mweak)* +…
PVES measures Apv
MOLLER: measure fundamental constant Cee in electron-electron scattering

## Slide 4: Next-generation Experiments will provide precise BSM probe
MOLLER@JLab
P2@MESA
SOLID@JLab
 | APV | δ(APV) | δ(APV)/APV
MOLLER | 35 ppb | 0.8 ppb | 2.2%
Broad program studying the structure of protons and nuclei, and searching for new (beyond Standard Model) physics
Searches for New Neutral Currents
Experiments measure increasingly smaller Apv

## Slide 5
Moller Experiment Overview
APV 35.6ppb to 0.72ppb precision
4kW LH2 cryotarget
134 GHz Møller rate
Downstream
65uA
APV = 35.6 ppb
δ(QeW) = ± 2.1 % (stat) ± 1.0 % (syst)
δ(APV) = 0.72 parts per billion
signal rate: 135 GHz
run time: 8200 hours
~3x1018 electrons detected

## Slide 6
Measure the weak charge of the electron to extremely high precision
Constrains coupling coefficient Cee
Extend the reach of new physics beyond the Standard Model
which relates directly to the electron weak charge, weak mixing angle, and ee coupling coefficient
Interference term between the electro-magnetic and weak amplitudes gives rise to parity-violating asymmetry,
MOLLER
Ultra-precise measurement sensitive to new parity-violating interactions
MOLLER Purpose
sin2θW :±0.00026(stat) ±0.00013(syst)
δ(QeW) = ± 2.1 % (stat) ± 1.0 % (syst)
=

## Slide 7
Theory: Standard Model prediction is tight and MOLLER measurement will constrain BSM theories
Radiative Corrections
The Standard Model Prediction: Remarkably Well-Known
MOLLER: δ(QeW) = ± 2.1 % (stat.) ± 1.1 % (syst.)
SM:
2-loop Calculations

## Slide 8: Quantifying Discovery Potential: Mass Reach
Zo
Low energy WNC interactions (Q2<<MZ2)
Heavy mediators = contact interactions
mass scale Λ, coupling g
for each fermion and handedness combination
Eichten, Lane and Peskin, PRL50 (1983)
Consider or
Mass Reach scale ~ 38TeV
Measurements test for small deviations from precisely calculated SM processes ⟶ new possible couplings
Erler et al., Ann.Rev.Nucl.Part.Sci. 64 (2014)
= 2π Λ = up to 47 TeV
New
Physics
δ(QeW) = 2.3%

## Slide 9: Quantifying Discovery Potential: Weak mixing angle precision
BSM: The Dark Z
Interpreting each result as an independent measure of sin2θW provides a quick way to put these all one one plot, but:
  interference in precision PVES measurements away from the Z resonance enhances new physics sensitivity
  Room for 10sigma discovery potential
  But additionally…

## Slide 10: Quantifying Discovery Potential : Coupling coefficients phase space
MOLLER
Qweak, P2
SoLID
,
Standard model PV e-q or e-e couplings
ee and ep elastic and e-D DIS are all unique phase space - the precision on sin2θW is not the story
Constraining the space of BSM physics is the story

## Slide 11: Constraining the space of BSM physics: Complimentary Measurements
Allowed region: R-Parity-violating Supersymmetry
R-Parity-conserving Supersymmetry
Future constraints:
MOLLER & P2
Ramsey-Musolf and Su, Phys. Rep. 456 (2008)
Erler and Su,
arXiv:1303.5522
Includes
LHC
constraints
SOLID: 100-200 GeV range
Buckley and Ramsey-Musolf Phys.Lett. B712 (2012) 261-265
Heavy Z’s and neutrinos, technicolor, compositeness, extra dimensions, SUSY…
Many new physics models give rise to new neutral current interactions
Coupling Coefficients Space
SUSY: – RPV and RPC
SOLID: Leptophobic Z’

## Slide 12
MOLLER: BSM and Sensitivity to New Physics
Complimentary Measurement with LHC
LHC observes an anomaly
LHC agrees with the Standard Model to 14TeV
MOLLER: provide access to hidden weak scale BSM physics scenarios that could escape LHC detection
ex) MeV-scale “Dark” Z0d
MOLLER will help provide constraints to choose between various BSM theories
ex) TeV scale 𝑍′bosons

## Slide 13: MOLLER: BSM and Sensitivity to New Physics
Λ > 5 TeV Doubly-Charged Scalars
Significant reach beyond LEP-200
Lepton Number Violation
MOLLER: e-e- scattering
dark Z: mass mixing with Z0
Davoudiasl, Lee, Marciano
PRD89 (2014), 095006
PRD92 (2015) 055005
Susan Gardner and Xinshuai Yan†,PHYSICAL REVIEW D (2020)
Heavy Z’s and neutrinos, technicolor, compositeness, extra dimensions, SUSY, dark Z…
Many new physics models give rise to new neutral current interactions
Dark Z
Doubly Charged Scalars

## Slide 14: MOLLER Apparatus
inelastic
ep elastic
Møller elastic
r [cm]
rate
Unique, 7-sector design, to optimize acceptance for identical particles
Acceptance-defining collimator
Accepted particles spread over full azimuth at the detector
Focal plane instrumented with array of thin quartz detectors
Five separate toroids, no iron
4kW LH2 cryotarget
high power, high stability
Møller scattered electrons localized at a radial distance, separated from ep elastic, photons
θlab ~ 5-18 mrad, E’ = 2-8 GeV
134 GHz Møller rate
Low noise beam with 1nm control of average beam position on target

## Slide 15
Moller Uncertainty Requirements
35ppb Apv
65uA, ~90% polarization, 344 PAC days
Stringent Uncertainty Goals
Statistical goal is <1ppb !
Total Systematic <0.5ppb!
Each indiv. systematic is <1% of Apv
Minimal Beam Asymmetries
Well measured & controlled polarization
Minimal and well characterized backgrounds

## Slide 16: Measuring this small asymmetry
Rapid (2kHz) helicity reversals
Analog integrate detector current
Place a detector where it sees the Møller scattered electron
Form an asymmetry over the helicity reversal
Measure to 0.01% at 1 kHz, repeat for a year straight
Specialized experimental techniques
Precise spectrometer to separate signal
Low noise electronics
Precise beam control and measurement
…
Target Boiling
4kW LH2 cryotarget
high power – Bubbles!
RTP Pockels Cell (Rubidium Titanyle Phosphate) currently in operation in Cebaf capable of fast ~10us switching for 2kHz

## Slide 17: Full Azimuthal Coverage: Identical Particles
  Unique concept allows for full azimuthal acceptance (effectively) even leaving space for coils but makes for a challenging design
CM angles 60o -120o
11 GeV in: 2.75 to 8.25 GeV out
Lab angles ~5 mrad - 17 mrad
Since you only need either the forward or the backward scatter, accept forward+backward for half the azimuth
highly boosted laboratory frame
Asymmetry (ppb)
Center of Mass Angle
Highest figure of merit at θCM = 90o
APV
dσ/dΩ
Identical particles.
Measure either forward or backward scattering.
Center of mass
Lab
boost

## Slide 18
Types of HCBA that contribute to PVES systematics
  Achieving HCBA goals all depends on the laser and Pockels Cell
Polarized Beam Source
RTP Cell fast switching for 2kHz
(Rubidium Titanyle Phosphate)
Any change in the polarized beam, correlated to helicity reversal, can be a potential source for a false asymmetry
 | Error
Systematic | 0.2ppb
Intensity | 0.1ppb
Position, E, angle | 0.1ppb
Spot-size | 0.12ppb
HCBA contributions

## Slide 19: Magnet Concept
19
cm
rad
cm
leaving USTorus
leaving DSTorus
at Detector
0.5 x 2m
0.9 x 6.5m
long and skinny
Bend scattered particles, separate ee from ep and photons
Small angles and high beam power
Large energy range (3-8 GeV)
Focus both back & forward scattered electrons
Two toroidal magnets (Upstream and Downstream)

## Slide 20: Main Detector
open
closed
transition
ee
ep
ep
ee
Illustration with each septant a different fundamental background
Segmented detector plane deconvolutes signal from backgrounds

## Slide 21: Collimation & More Detectors
SAMs
pion detectors
Pb absorber
GEMS
Walls, collars, and lintels supplement the collimation
Collimator 1: long snout, collimates primary beam so what remains can go to the dump. ~3200 W
Collimator 2: wedges define the acceptance of the 7 septants

## Slide 22: MOLLER status
MOLLER MIE Project Schedule
MOLLER Collaboration
~ 160 authors, 37 institutions, 6 countries
Includes experience from E158, PREX, Qweak, PVDIS, HAPPEX, G-Zero
K. Kumar: Contact
J. Fast: Project Manager
Prototyping/construction/installation (2022-25)
  Final Design Reviews now complete
  Plan for Fall 2023 CD-2/3 review followed by approval
  Technically driven schedule is then ~15 months construction and ~18 months installation
  Now fully funded!
  Project currently on track to be ready to start installation as early as Fall 2024/Q1 2025 or when the hall becomes available
  (*details beyond that depend on performance of CEBAF and delivery of luminosity to SBS program)
  Project itself currently on track to be ready to start commissioning as early as Spring 2026 subject to scheduling/installation start date

## Slide 23: Summary
Thank you collaboration, Jlab staff, engineers, project team!
MOLLER represents an outstanding opportunity to take advantage of the unique instrument (11 GeV CEBAF beam) enabled by the 12 GeV upgrade
Electroweak physics with PVES are a powerful component of the low energy fundamental symmetries program
The science case remains compelling and the plan is to run physics at about the time that precision results from high luminosity phases of 14 TeV LHC are becoming available
MOLLER will search for new interactions with reach into new physics phase space that cannot otherwise be accessed
Now we just have to do is build it and do it (construction and execution of MOLLER)

## Slide 24: Backup

## Slide 25: Outline
Collaboration
PVES measure Apv
Next-generation Experiments will provide precise BSM probe – experiments measure increasingly smaller Apv
MOLLER experiment Design
MOLLER is precise and measures Qwe and constrains Cee
Theory: Standard Model prediction is tight and MOLLER measurement will constrain BSM theories
Quantifying Discovery Potential: Mass Reach Scale
Quantifying Discovery Potential : sin2thetaW precision
Quantifying Discovery Potential : Coupling coefficients phase space
New Physics Complementarity
MOLLER Apparatus
MOLLER measuring the asymmetry – integration at 2kHz
MOLLER full azimuthal coverage
MOLLER complex magnets/collimation
MOLLER Main detector: segmented for backgrounds
MOLLER Beam Control??
MOLLER Uncertainty Requirements
MOLLER Status
Conclusion

## Slide 26: MOLLER status
DOE MIE (Office of Nuclear Physics)
MOLLER MIE Project Schedule
Prototyping/construction/installation (2022-25)
  Final Design Reviews now complete
  Plan for Fall 2023 CD-2/3 approval
  Technically driven schedule is then ~15 months construction and ~18 months installation
  Now fully funded!
  Project currently on track to be ready to start installation as early as Fall 2024/Q1 2025 or when the hall becomes available
  (*details beyond that depend on performance of CEBAF and delivery of luminosity to SBS program)
  Project on track to be ready to start commissioning as early as Spring 2026 subject to scheduling
MOLLER Collaboration
~ 160 authors, 37 institutions, 6 countries
Includes experience from E158, PREX, Qweak, PVDIS, HAPPEX, G-Zero
K. Kumar: Contact
J. Fast: Project Manager

## Slide 27: MOLLER schedule – CD-3a and beyond
Working on completing final procurement packages for CD-3a scope
  Intent is to have all requisitions in motion by July
Completing planning (Performance Measurement Baseline) for CD-2/3
  Data freeze in May – no changes until we set baseline at end of CY2023
Plan remains to complete fabrication/assembly/test outside Hall A by end of Q1 FY25
  Details beyond that depend on performance of CEBAF and delivery of luminosity to SBS program

## Slide 28: Figure of Merit
Kent Paschke - UVa
Simulation Workship - Experiment Overview
Asymmetry (ppb)
Center of Mass Angle
Highest figure of merit at θCM = 90o
APV
dσ/dΩ
highly boosted laboratory frame
Identical particles.
Measure either forward or backward scattering.
CM angles 90o-120o
11 GeV in: 2.75 to 5.5 GeV out
Lab angles ~9 mrad - 17 mrad
Center of mass
Lab
boost

## Slide 29: Identical Particles
Kent Paschke - UVa
Simulation Workship - Experiment Overview
  Unique concept allows for full azimuthal acceptance (effectively) even leaving space for coils but makes for a challenging design
CM angles 60o -120o
11 GeV in: 2.75 to 8.25 GeV out
Lab angles ~5 mrad - 17 mrad
Since you only need either the forward or the backward scatter, accept forward+backward for half the azimuth

## Slide 30: MOLLER

## Slide 32: PV-DIS at EIC
Measurement of modeled with ECCE detector
Proton or deuterium, PDF uncertainty is under control
Average over nuclear polarization
1% precision of e-beam polarimetry competes with statistics
Int. Lumi. ~100 fb-1 (~1yr@1035)

## Slide 34: Electroweak Structure Functions
polarized electron, unpolarized hadron
unpolarized electron, polarized hadron
proton
deuteron
e-
1H, 2H, 3He
“Non-small x”
few % on
10% on
Assuming integrated luminosity ~500 fb-1
Simulations from Yuxiang Zhao, SBU

## Slide 36: Spectrometer Concept
Kent Paschke - UVa
Simulation Workship - Experiment Overview
Bend scattered particles, separate ee from ep and photons
Small angles and high beam power
Large energy range (3-8 GeV)
Long target
Two toroidal magnets (Upstream and Downstream)
Collimation + “shields” or “blockers”
vacuum pipe to take beam to dump
26.5 m target to detector

## Slide 37: Switching faster – Use New Crystal
KD*P Cell
RTP Cell
Suffers from piezoelectric ringing
At 2kHz helicity switching,
70-100μs deadtime is 20% loss of data
No piezoelectric ringing up to 100kHz
At 2kHz helicity switching, 12μs transition,
Deadtime reduced by ~10x
ZOOMED IN
transition + ringing ~ 100μs
transition ~ 12μs
(Potassium Dideuterium Phosphate)
(Rubidium Titanyle Phosphate)

## Slide 39
Improve E158 by a factor of 5
At 11GeV, Jlab high luminosity and stability make large improvement possible
Matches best collider (Z-pole) measurement!
Design for Moller experiment
Mass Reach is ~600X the mass of the W mediator, ~400X the Higgs Mass
APV 35.6ppb to 0.72ppb precision
sin2θW :±0.00026(stat) ±0.00013(syst)
Mass Reach scales up to 47TeV
 | Error
Systematic | 0.39ppb
Intensity | 0.1ppb
Position | 0.14ppb
Spot-size | 0.14ppb
HCBA contributions

## Slide 41: MOLLER at JLab
Search for new flavor diagonal
neutral currents
Improve by a factor of 5
Only existing ee measurement:
Unique (purely leptonic) new physics reach
best contact interaction reach for leptons at low OR high energy
To do better for a 4-lepton contact interaction would require:
Giga-Z factory, linear collider, neutrino factory or muon collider
MOLLER Reach
δ(sin2θW) = ± 0.00024 (stat.) ± 0.00013 (syst.)
~ 0.1%
Matches best collider (Z-pole) measurement!
δ(QeW) = ± 2.1 % (stat.) ± 1.1 % (syst.)
δ(APV) ~ 0.8 ppb
APV ~ 32 ppb
Elastic ee (Møller) scattering

## Slide 43
Target Boiling
Fast helicity flipping = high speed camera
Moller is designed around a flip rate of at least 2 kHz
Target boiling is a noise source that can’t be filtered out using correlations with beam monitors, it must be suppressed by taking data faster than the bubbles form
Qweak
data
The electron beam must switch back and forth very quickly between helicity states