## Slide 1: Compact Liquid-Nitrogen-Cooled High-Gradient Linacs
Emilio Nanni
2024 International Topical Meeting on Nuclear Applications of Accelerators
3/20/2024
Notes: Compact Liquid-Nitrogen-Cooled High-Gradient Linacs
Mar 20, 2024, 10:20 AM
30m
4th Floor - Claremont (Sheraton Waterside Hotel)
Invited Talk Design and Technology Accelerators Design and Technology - 4
Speaker
Emilio Nanni (SLAC National Accelerator Laboratory / Stanford University)
Description
Achieving high accelerating gradient and the benefit of compactness, improved transport, and high brightness beams is limited by the onset of rf induced breakdown and reduced rf to beam efficiency. The operation of normal conducting accelerators at cryogenic temperatures provides a pathway to addressing both of these principle challenges by increasing material strength, reducing susceptibility to breakdown, improving rf to beam efficiency and reducing pulsed/average thermal effects in the accelerating structure. The benefits of cryogenic operation can be achieved with a closed-cycle cryocooler or immersion in cryogenic fluids. Operation in a liquid nitrogen environment provides access to commercial solutions, while capturing the majority of the benefits of cryogenic operation. In this talk, we will provide an overview of the underlying mechanisms and benefits of cryogenic operation and highlight recent results in the development of compact liquid-nitrogen-cooled high-gradient linacs.

## Slide 2: Acknowledgements
Muhammad Shumail
Xueying Lu
Greg Le Sage
Mitchell Schneider
Emma Snively
Sami Tantawi
Valery Dolgashev
Zenghai Li
Dennis Palmer
Garrett Mathesen
Charlotte Wehner
Julian Merrick
Bradley Shirley
Mamdouh Nasr
Ankur Dhar
SLAC
Evgenya Simakov
Muhammed Zuboraj
Ryan Fleming
Dmitry Gorelov
Mark Middendorf
LANL
Ronald Agustsson
Robert Berry
Amirari Diego
Alex Murokh
Radiabeam
Supported by:
RF Accelerator Technology Team

## Slide 3: Acknowledgements – C3 Enthusiasts
AccelApp'24
Community Events
More Details Here (Follow, Collaborate):
https://web.slac.stanford.edu/c3/
https://sites.google.com/view/ec4c3
Fermilab, SLAC, LANL, Cornell & Snowmass Session in Seattle
Next Meeting LCWS 2024:
https://agenda.linearcollider.org/event/10134/overview
2023 PRX Energy 2, 04700 - Sustainability Strategy for the Cool Copper Collider
2023 JINST 18 P09040 - R&Datus and future plans for C 3 R&D
2023 JINST 18 P07053 - A "Cool" route to the Higgs boson and beyond. The Cool Copper Collider
2307.07981 - The alignment of the C3 Accelerator Structures with the Rasnik alignment system

## Slide 4: Accelerator Technology Drives Scientific Discovery
AccelApp’24
Coherent X-rays from LCLS (2009)
How do we develop the next generation of accelerators and what new science does this enable?
Ultrafast Electron Diffraction (2015)

## Slide 5: Limits of High Gradient Performance – Power and Heat
AccelApp'24
Pritzkau, et al., Phys. Rev. STAB 2002
Laurent, et al. PRSTAB 14.4 (2011): 041001
Frequency | 3 GHz | 
Stored Energy [mJ] | 8450 | 
Temp [K] | 300 | 77
Q-value [x1000] | 18 | 50
Shunt Impedance [MOhm/m] | 55 | 150
Max. Mag. Field [MA/m] | 0.3 | 
Max. Electric Field [MV/m] | 210 | 
Loss in 1 meter [MW] | 181 | 67
Parameters for 100 MeV/m Gradient
Damage from RF Induced Heating
5 cm
Over-Coupled Designs for Fast Fill and High Beam Loading
C-Band 1 m Struc.

## Slide 6: Cryo-Copper: Enabling Efficient High-Gradient Operation
AccelApp'24
Cryogenic temperature elevates performance in gradient
Material strength is key factor
Impact of high fields for a high brightness injector may eliminate need for one damping ring
Operation at 77 K with liquid nitrogen is simple and practical
Large-scale production, large heat capacity, simple handling
Small impact on electrical efficiency
Cahill, A. D., et al. PRAB 21.10 (2018): 102002.
Cryogenic temperature elevates performance in gradient
Increased material strength is key factor
Increase electrical conductivity reduces pulsed heating in the material

## Slide 7: Breakthrough in the Performance of RF Accelerators
AccelApp'24
RF power coupled to each cell – no on-axis coupling
Full system design requires modern virtual prototyping
Electric field magnitude produced when RF manifold feeds alternating cells equally
Optimization of cell for efficiency (shunt impedance)
Control peak surface electric and magnetic fields
Key to high gradient operation
Tantawi, Sami, et al. PRAB 23.9 (2020): 092001.

## Slide 8: Cold-Copper High Gradient Testing

## Slide 9: Split Structure Accelerator Topology Accelerates Beam and Operates at High Gradient at X-band
AccelApp'24
Confirmation of gradient by measuring 24 MeV energy gain
Operating with ~100 MeV/m gradient with 16.5 MW of input power and 300 ns pulse length
Wakefield measurement matches expected RF structures performance
Structure processed to 160 MeV/m
87.5MeV
85.6MeV
89.4MeV
Forward and Reflected Power
Measured Charge with Faraday Cup and Calculated from Induced Wakefield
Tantawi, et al. PRAB 23.9 (2020): 092001.
26 cm structure installed at XTA
Beam Energy
Power in Wakefield

## Slide 10: Cryogenic-Copper Accelerating Structures: New Frontier for Beam Brightness, Efficiency and Cost-Capability
AccelApp'24
Increased conductivity and hardness enables higher gradients
Dramatic reduction in cost of system including cryogenics at 77K
2.5X less power establishing gradient allows for heavy beam loading even at high gradient – improving system efficiency
T decrease
Increase in by a factor of 2.5
Bane et al., ArXiv 1807.10195 (2018)
Cryostat w/ Structure

## Slide 11: Cryogenic X-band Structure in High Power Test to Confirm RF Performance and Measure Breakdown Statistics
AccelApp'24
Best fit parameters
Expected parameters
Reflected RF Power Matched Molded Cavity Performance
Modeled Structure Gradient Confirmed with Dark Current
Energy Gain=28MeV
Gradient=107MV/m
Dark current
Forward Power (MW)
Gradient (MV/m)
120 MV/m
Arbitrary Units
Nasr, et al. PRAB 24.9 (2021): 093201.
40X Improvement in Breakdown Rate

## Slide 12: What’s the Optimal Frequency for High Charge Beams?
C3 2024
Linear collider: high beam power
1 nC per bunch, 0.3 A during rf pulse
Most challenging design parameters
Pursue broad array of applications
Medical, x-ray sources, gamma-ray sources,….
1 nC, 150 micron, 25 deg.
arXiv:1807.10195 (2018)

## Slide 13: Scaled Design of Low-Beta or Reduced Phase Adv. Struc.
AccelApp'24
Original design was for low-beta protons – efficient with relativistic electrons and appropriate cell to cell phase advance
RF power coupled to each cell can lead to a local hot spot in H-field
Tailoring coupler profile limits enhancement to 15-20% (vs. 230%)
Schneider, Mitchell, et al. "High gradient off-axis coupled C-band Cu and CuAg accelerating structures." Applied Physics Letters 121.25 (2022).

## Slide 14: High Gradient Performance of Cu and CuAg Cavities
AccelApp'24
Utilized C-band test stand at LANL
Each structure processed for O(100M) pulses
How does this behavior extend to cryogenic temperatures?

## Slide 15: Characterization at 77K
AccelApp'24
Improvement of 2.5 X for Cu and 2.9X for CuAg(!)
2.9 is consistent of Cu sample measurements at UCLA (may be material batch specific)
Parameter​ | CuAg​ | Cu​
Temp​ | 77K​ | 
Frequency​ | 5.71455 GHz​ | 
Length | 1.58 cm​ | 
 | 2.97​ | 2.683​
Q0​ | 29,695​ | 25,697​
Rs​ () | 352 | 305 ​
Ea MeV/m/​ | 141 | 131
Parameter​ | CuAg​ | Cu​
Temp​ | 77K​ | 
Frequency​ | 5.71455 GHz​ | 
Length | 1.58 cm​ | 
 | 2.97​ | 2.683​
Q0​ | 29,695​ | 25,697​
 | 352 | 305 ​
 | 141 | 131
Preliminary
Cu
CuAg

## Slide 16: Two Cell Assembly for High Power Test
AccelApp'24

## Slide 17: Two Cell Assembly for High Power Test
AccelApp'24
SLAC
Radiabeam

## Slide 18: Typical High Gradient Performance
AccelApp'24
Measured and modeled response for CuAg Cavity
C3 - 250
C3 - 550

## Slide 19: Structure Processing
C3 2024
~20M Pulses (two weeks)
Increased pulse length – 400 ns, 700 ns, 1 microsecond
Preliminary
A. Diego, M. Schneider, M. Boyce and A. Dhar

## Slide 20: 40 Cell Pi-Mode Distributed Coupling Structure
AccelApp'24
Scaling fabrication techniques in length and including controlled gap
Incorporate the two key technical advances: Distributed Coupling and Cryo-Copper RF
Main linac utilizes meter-scale accelerating structures, technology demonstration underway
Implement optimized rf cavity designs to control peak surface fields

## Slide 21: High Power Test of Meter-Scale Distributed Coupling Structure
AccelApp'24
Tested at Radiabeam
Up to 15 MW, 1 microsecond delivered to structure, no measurable breakdowns after reaching max power
Structure Destroyed in Tuning Attempt for Cryogenic Operation
Structure for Cryogenic Operation in Production

## Slide 22: Outlook

## Slide 23: C3 Cool Copper Collider
Snowmass
C3 is based on a new rf technology
Dramatically improving efficiency and breakdown rate
Distributed power to each cavity from a common RF manifold
Operation at cryogenic temperatures (LN2 ~80-K)
Robust operations at high gradient: 120 MeV/m
Scalable to multi-TeV operation
High Gradient Operation at 150 MV/m
Cryogenic Operation at X-band
C3 Prototype One Meter Structure
High power Test at Radiabeam
Nasr, et al., PRAB 24.9 (2021): 093201.

## Slide 24: Accelerator Complex
Snowmass
8 km footprint for 250/550 GeV CoM ⟹ 70/120 MeV/m
Large portions of accelerator complex compatible between LC technologies
Beam delivery / IP modified from ILC (1.5 km for 550 GeV CoM), compatible w/ ILC-like detector
Damping rings and injectors to be optimized with CLIC as baseline
C3 Parameters
C3 - 8 km Footprint for 250/550 GeV (to scale)
C3 Main Linac Cryomodule
9 m (600 MeV/ 1 GeV)

## Slide 25: The Complete C3 Demonstrator
AccelApp'24
Demonstrate fully engineered cryomodule
~50 m scale facility
3 GeV energy reach
Answer technical questions needed for CDR

## Slide 26: Power Consumption and Sustainability
250 GeV CoM - Luminosity - 1.3x1034
Parameter | Units | Value
Reliquification Plant Cost | M$/MW | 18
Single Beam Power (125 GeV linac) | MW | 2
Total Beam Power | MW | 4
Total RF Power | MW | 18
Heat Load at Cryogenic Temperature | MW | 9
Electrical Power for RF | MW | 40
Cryoplant Electrical Power | MW | 60
Accelerator Complex Power | MW | ~50
Site Power | MW | ~150
Surface-Site Mockup
Precision-Weighted Carbon Footprint
Compact footprint <8 km for both underground and surface sites
  Underground – less constraints on energy upgrade
  Surface – lower cost and faster to first physics
Sustainability - construction + operations CO2 emissions per % sensitivity on couplings
  Polarization and high energy to improve sensitivity
  Construction CO2 emissions → minimize excavation and concrete
  Operations → limit power, decarbonization of the grid and dedicated renewable sources
Accepted PRX Energy, https://arxiv.org/abs/2307.04084
Notes: Sustainability lcws talk and paper

## Slide 27: Synergies with Future Colliders
RF Accelerator Technology Essential for All Near-Term Collider Concepts
C3 Demo is positioned to contribute synergistically or directly to all near-term collider concepts
CLIC - components, damping, fabrication techniques
ILC - options for electron driven positron source based C3 technology
Muon Collider - high gradient cryogenic copper cavities in cooling channel, alternative linac for acceleration after cooling
AAC - C3 Demo utilized for staging, C3 facility multi-TeV energy upgrade reutilizing tunnel, 𝛾𝛾 colliders
FCC-ee - common electron and positron injector linac from 6 to 20 GeV
  reduce length 3.5X OR reduce rf power 3.5X
AccelApp'24
90% seeds < 8 um-rad with lattice errors
Planned test at Argonne
Tracking with Lucretia includes longitudinal and transverse wakes, chromatic effects etc
Error study is 100 seeds, 100 μm element offsets, 300 μrad element rolls (rms)
  No corrections applied
Vibrant International Community for Future Colliders is Essential

## Slide 28: Cornell
AccelApp'24

## Slide 29: UCLA
AccelApp'24
Rosenzweig et al., https://www.mdpi.com/2410-390X/8/1/19

## Slide 30: Conclusions
AccelApp'24
Cold-copper’s achievable gradient, breakdown rate and pulse length at C-band have transformative potential
How do we incorporate damping?
How improve manufacturing of structures?
How do meter scale structures perform?
What is the optimal aperture and phase advance?
How do we support and align structures in cryogenic environment?
H. Xu + LANL
Damped Cavities
Cryogenic Pi-Mode
A. Dhar
M. Shumail
Wide-Aperture Reduced Phase Adv.
S-Band
Large Aperture

## Slide 31: Questions?

## Slide 32: Optimized RF Feed for Distributed Coupling Structure
C3 2024
RF power coupled to each cell can lead to a local hot spot in H-field
Tailoring coupler profile limits enhancement to 15-20% (vs. 230%)
Built and tested on an S-band structure
Lu, et al., Review of Scientific Instruments 92.2 (2021).

## Slide 33: Ongoing Technological Development
C3 2024
Modern Manufacturing
Prototype One Meter Structure
Preliminary Alignment and Positioning
High Accelerating Gradients
Cryogenic Operation
Integrated Damping with NiChrome Coating
C3 Main Linac Cryomodule
9 m (600 MeV/ 1 GeV)

## Slide 34: Implementation of Slot Damping
ILC Update
Need to extend to 40 GHz / Optimize coupling / Modes below 104 V/pC/mm/m
NiCr coated damping slots in development
Tapered Slot
Kick Factor
Vacuum Space Model
Kick Factor * Q
Two Cell Prototype
H. Xu, NCRF W 17th May 13:30
NiCr Tested at 80K

## Slide 35: Additively Manufactured Spiral Load
AccelApp'24
Tested at Radiabeam
3D printed in stainless steel (inspired by CERN)
First version is only air cooled
Tested to 8 MW, 20Hz, 700ns
Water Cooled Design for V2 (now in use)

## Slide 36: Structure Processing
AccelApp'24
~10M Pulses to Date
Operating with human supervision
Chart: C-Freeze Run 10/17/2023
| 0.47152777777777777 | 0.47847222222222219 | 0.48055555555555557 | 0.48402777777777778 | 0.48749999999999999 | 0.4909722222222222 | 0.49236111111111108 | 0.49374999999999997 | 0.49722222222222223 | 0.50069444444444444 | 0.50763888888888886 | 0.51111111111111118 | 0.51458333333333328 | 0.52152777777777781 | 0.52500000000000002 | 0.52777777777777779 | 0.52916666666666667 | 0.53055555555555556 | 0.53402777777777777 | 0.53749999999999998 | 0.54097222222222219 | 0.54236111111111118 | 0.54583333333333328 | 0.5493055555555556 | 0.55625000000000002 | 0.55972222222222223 | 0.56319444444444444 | 0.56388888888888888 | 0.56736111111111109 | 0.5708333333333333 | 0.57430555555555551 | 0.57777777777777783 | 0.58124999999999993 | 0.58472222222222225 | 0.58819444444444502 | 0.59166666666666701 | 0.59513888888888899 | 0.59861111111111098 | 0.60069444444444442 | 0.60416666666666663 | 0.60763888888888895 | 0.61111111111111105 | 0.61458333333333304 | 0.61805555555555503 | 0.62152777777777779 | 0.625000000000001 | 0.62847222222222299 | 0.63194444444444442 | 0.63541666666666596 | 0.63888888888888695 | 0.64236111111110805 | 0.64583333333332904 | 0.65277777777777779 | 0.65972222222222221 | 0.66319444444444442 | 0.66319444444444442 | 0.66666666666666663 | 0.67013888888888884 | 0.67361111111111116
CuAg | 0 | 36 | 0 | 1020 | 168 | 24 | 0 | 1416 | 1080 | 864 | 2838 | 792 | 420 | 240 | 72 | 0 | 3132 | 0 | 636 | 444 | 120 | 408 | 348 | 408 | 228 | 108 | 60 | 0 | 204 | 300 | 192 | 156 | 264 | 60 | 204 | 168 | 48 | 612 | 60 | 108 | 48 | 48 | 144 | 36 | 420 | 192 | 3180 | 348 | 156 | 396 | 120 | 264 | 972 | 486 | 84 | 0 | 804 | 204 | 252
Cu | 0 | 48 | 0 | 204 | 96 | 108 | 0 | 4608 | 804 | 120 | 678 | 192 | 48 | 78 | 12 | 0 | 3576 | 0 | 360 | 204 | 168 | 5208 | 1176 | 732 | 102 | 72 | 36 | 0 | 84 | 84 | 156 | 72 | 432 | 36 | 288 | 48 | 36 | 3840 | 84 | 240 | 84 | 492 | 204 | 96 | 144 | 288 | 1188 | 60 | 60 | 180 | 48 | 156 | 684 | 270 | 36 | 0 | 2196 | 180 | 96
Max Power End of Day
Cavities: Max 3.37 MW into Cu Cavity
Pulse Width: 700 ns
Rep Rate: 80 Hz
Freq: 5714.3 MHz
Preliminary

## Slide 37: What’s Next for the Energy Frontier?
AccelApp'24
The Energy Frontier 2021 Snowmass Report
Physics goals beyond HL-LHC:
1. Establish Yukawa couplings to light flavor ⟹ precision & lumi
2. Search for invisible/exotic decays and new Higgs ⟹ precision & lumi
3. Establish self-coupling ⟹ > 500 GeV e+e- operations

## Slide 38: Linear vs. Circular
AccelApp'24
Linear e+e- colliders: ILC, C3, CLIC
Reach higher energies (~TeV), and can use polarized beams
Relatively low radiation
Collisions in bunch trains
Circular e+e- colliders: FCC-ee, CEPC
Highest luminosity collider at Z/WW/ZH
limited by synchrotron radiation above 350 – 400 GeV
Beam continues to circulate after collision

## Slide 39: Alignment and Vibrations
System level optimization essential for achieving performance
AccelApp'24
RF Structure Optimization
Main Linac Beam Dynamics
Vibration Measurements and Analysis
Two-Phase Fluid Simulations
Precision Short and Long Range Alignment
3.55 mm iris radius
2.0=Emax/Eacc
1.23=Hcoup/Hwall
White (C3), Schulte (CLIC)
Alignment Parameters | Units | Value
Raft Components | μm | 5
Short Range (~10m) | μm | 30
Long Range (>200m) | μm | 1000
Structure Vert. Vibration | μm | 9
Quad Vert. Vibration | nm | 15
BPM Resolution | μm | 0.1
BPM-Quad Alignment | μm | 2
Electric Field
Magnetic Field
M. Shumail, Z. Li
K. Shoele
H. Van Der Graaf
Z. George, V. Borzenets, A. Dhar, D. Palmer
100 nm resolution
Approved effort to test cold
https://arxiv.org/pdf/2307.07981.pdf

## Slide 40: Table of Parameters
AccelApp'24

## Slide 41: Full Parameters
AccelApp'24

## Slide 42: Further Cavity Optimization Possible
AccelApp'24
Dipole
with symmetrization 100X reduction
V1-simple-stub
(not ideal cancellation)
V2-symm-stub
(good cancellation)
Single side coupling iris induces dipole and quad fields
Coupling hole symmetrization and racetrack shape incorporated to minimize dipole and quad fields
Dipole
Quad
Quad
w/o symmetrization
✅
dipole, quad calculated at 50MV/m
Zenghai Li

## Slide 43: Distributed Coupling Structures Provide Natural Path to Implement Detuning and Damping of Higher Order Modes
AccelApp'24
Individual cell feeds necessitate adoption of split-block assembly
Perturbation due to joint does not couple to accelerating mode
Exploring gaps in quadrature to damp higher order mode
Detuned Cavity Designs
Quadrant Structure