## Slide 1: The ARIEL e-Linac and its technical development for user operation
Stephanie Diana Rädel

## Slide 2: Outline
TRIUMF – an introduction
ARIEL and its e-Linac (– a love story)
The e-Linac – a new multi-user facility
  ARIEL
  FLASH
  DarkLight
  THz

## Slide 3: TRIUMF: Canada’s particle accelerator center
University of Alberta University of British Columbia University of Calgary Carleton University
University of Guelph University of Manitoba
McGill University McMaster University
Université de Montréal
University of Northern
British Columbia
Our multidisciplinary community drives leading-edge research that delivers impact in science, medicine, and industry, positioning Canada as a world leader.
Queen's University
University of Regina
Saint Mary's University
Université de Sherbrooke Simon Fraser University University of Toronto University of Victoria
University of Waterloo
Western University
University of Winnipeg York University

## Slide 5: TRIUMF: Canada’s particle accelerator centre
Primary beam driver: cyclotron
  500 MeV H– cyclotron
  Produces rare isotopes, neutrons and muons
Other Cyclotrons
  TR13
  IAMI
  BWXT
Separator Accelerator facility (ISAC)
  Isotope Separator Online (ISOL) facility
  ISAC-I: Normal conducting-linac
  ISAC-II: Superconducting-linac
e-Linac
Advanced Rare Isotope Laboratory (ARIEL)
D. Castaneda

## Slide 6: ARIEL: one of the world’s most powerful ISOL complexes
Massively expand our rare isotope research program
  Providing more exotic isotope species with very high intensities
  Adding two production targets in parallel to existing ISAC target stations
Three simultaneous isotope production stations
  Fully exploit numerous existing experimental facilities at ISAC
https://www.flickr.com/photos/triumflab/15148509948/in/photostream/

## Slide 7: An independent driver for TRIUMF’s Rare Isotope Program
35 MeV x 10 mA electrons [1/s]
500 MeV x 10 µA protons [1/s]
Pure neutron-rich products from photo fission
Production cross section reduced in comparison to hadrons
production intensity from 238UCx
A. Gottberg

## Slide 8: ARIEL target hall location – at TRIUMFs heart
D. Castaneda

## Slide 9: The ARIEL Target Hall
module storage
target exchange point
spent target storage
protons
electrons
AETE
APTW
driver beam tunnel
RIB
Electron beam and
proton beam transport
Hot cell facilities (target handling, PIE, waste processing, medical isotope extraction repair and maintenance)
Remote-controlled crane
Target pit shielding
RIB
A. Gottberg

## Slide 10: e-Linac location
D. Castaneda

## Slide 11: The e-Linac in its hall
EGUN
tuning dump

## Slide 12: e-Linac overview
ARIEL
Electron Beam
Total beam energy | 30 MeV
Maximum beam current | 10 mA
Normalized emittance | 5 μm
Bunch charge | 15.4 pC
Bunch repetition rate | 650 MHz
Power rating of high energy dump | 10 kW
High-energy section
Medium-energy section
Low-energy section
High-energy tuning dump
Cryomodules

## Slide 13: 300 kV thermionic electron gun
The electron source is housed inside a pressurized SF6 vessel to avoid breakdown of the 300 kV voltage
RF is fed into the e-gun using a ceramic waveguide to form bunches at 650 MHz
Allows CW mode

## Slide 14: 300 kV thermionic electron gun
Cathode has grid with suppressing voltage and RF modulation
F. Ames et al., “The TRIUMF ARIEL RF modulated thermionic electron source”, 2016
SF6 vessel
e- beam
300 kV bias power supply
RF
Beam pipe
Grid
Cathode

## Slide 15: First cryomodule to accelerate beam to 10 MeV
9-cell elliptical superconducting niobium cavity at 1.3 GHz, operating at 2 K
2 power couplers capable of delivering 50 kW each
EINJ
D. Yosifov et al., “ARIEL’s E-linac and beam transport line vacuum systems”, 2012
Heat exchanger
4 K separator
Cavity
Tuner
2 K separator
strongback
Power coupler

## Slide 16: Second cryomodule to accelerate beam to 30 MeV
Two 9-cell elliptical superconducting niobium cavity at 1.3 GHz, operating at 2 K
4 power couplers capable of delivering 50 kW each
Y. Ma et al., “First RF results of two-cavities accelerating cryomodule for ARIEL E-Linac at TRIUMF”, 2018
EACA
Heat exchanger
4 K phase separator
WPM bracket
Power coupler
4 K - 2 K Cryoinsert
Strong- back
Support Post

## Slide 17: 10 kW tuning dump
High energy beam dump
To ARIEL

## Slide 18: e-Linac commissioning timeline
Dec. 2019
Feb. 2020
Dec. 2020
Jul. 2018
Sep. 2014
Sep. 2021
31 MeV at low beam power
complete
1 kW at 7 MeV
26 MeV at 1 kW
25 MeV at low beam power
First high-energy beam (20 MeV)

## Slide 19: The e-linac commissioning was completed
ARIEL electron target will be ready to receive beam in 2026
After multiple years of commissioning, we achieved a 10 kW beam at 30 MeV for the first time
Next milestone: Reliable beam delivery
https://web.accel.triumf.ca/Elog_Attachments/elinac_elog/2021-09/2021-09-13-14:23:14.grab.h6pRsk.png

## Slide 20
Entering a new era: The e-linac as an upcoming multi-user facility

## Slide 21: 300 keV Converter Test Stand: validated target materials for ARIEL
Ta-Al Expl. Weld
Au-Al E.D.
Au-Al Expl. Weld
Au-Al E.D. + Ni
L. Egoriti et al., “Material development towards a solid 100 kW electron-gamma converter for TRIUMF-ARIEL”, 2020
A. Gottberg
Beam
Notes: 300 keV–3kW test stand that simulate the sort of power density encountered in the future 30MeV–100kW ARIEL targets.
Outcome gold on aluminum:
Temperature increase during irradiation
Radiation-enhanced Au-Al diffusion
Formation of brittle intermetallic
Outcome tantalum on aluminum
Temperature stable over 500 h of irradiation
No change of surface morphology
No major evolution of interface
No-radiation enhanced diffusion

## Slide 22
FLASH

## Slide 23: FLASH – Radio Therapy Research
FLASH dose rates allow for sub-second treatments to reduce normal tissue toxicity compared to low dose rate (conventional) treatments
Objective: build e– to photon converter
t < 1 s , > 40 Gy/s (ultra-high dose-rate)
Energy ≤ 10 MeV (world first)
Dose ~ 40 Gy
Dose ~ 40 Gy
0
minutes
~ 0.05 Gy/s
t
1 sec
~ 40 Gy/s
Dose rate
FLASH
Conventional
L. Egoriti (2022)

## Slide 24: E-Linac medium energy dump modification
ARIEL-inspired converter
N. Esplen et al., “Design optimization of an electron-to-photon conversion target for ultra-high dose rate x-ray (FLASH) experiments at TRIUMF”, 2022

## Slide 25: Dosimetry with dosimetry films and water-filled tubes
It is safe to touch this
Notes: Dosimetric films
Water phantom is the medical term for those water-filled tubes

## Slide 26: FLASH – a challenging user
Limited time window (1 hr) to accommodate safe animal handling procedures
Key: develop lockup procedure
Lock up e-Hall
Establish all HV connections
Enable all safety stages
Ramp up all devices
Get beam ready
Deliver beam
close
open

## Slide 27: FLASH beamtime
12 in-vivo irradiation in total
  6 FLASH and 6 CONV
8 samples of fruit fly larvae

## Slide 28
Dark Light

## Slide 29: DarkLight – an upcoming experiment
Looking for dark bosons that could interact with dark matter with a thin-target scattering experiment
ATOMKI experiment
  Observed possible boson with mass circa 17 MeV/c2 (“X17”)
Incoming electron interacts with target and created γ rays … and X17?
Measure energy spectrum of electron-positron pairs created by γ or X17
What can TRIUMF offer for this collaboration?
Electron Beam
K. Pachal: “The DarkLight experiment at TRIUMF and the hunt for a new boson”
High intensity electron beam in CW
Notes: Some anomalies in e+e- invariant mass spectra in 8Be

## Slide 30: Relocating the DarkLight experiment
Now: test chamber downstream of second cryomodule (@ 30 MeV)
2024: directly upstream high energy dump
T. Planche, “New Scientific Opportunities with the TRIUMF ARIEL e-linac”, 2022
Relocation and design experimental chamber for initial round of data taking

## Slide 31: DarkLight and desired beam properties
Expected beam to be delivered:
  30 MeV
  300 μA
  10 kW
  Minimum of 1000 hours beam delivery
https://www.dropbox.com/scl/fo/iuufqqevskmgk00kz6sc2/h?rlkey=7repp8r3kv7f4os79vaiuxzs5&e=2&dl=0 - DARKLIGHT ARIEL EXPERIMENT LAYOUT_01_31_2024 v1

## Slide 32: DarkLight integration
Current machine optics
Machine optics with DarkLight chamber
https://www.dropbox.com/scl/fo/iuufqqevskmgk00kz6sc2/h?rlkey=7repp8r3kv7f4os79vaiuxzs5&e=2&dl=0 - DARKLIGHT ARIEL EXPERIMENT LAYOUT_01_31_2024 v1
beam
beam
To integrate DarkLight the machine needs adaptation to compensate emittance growth

## Slide 33
THz

## Slide 34: High-Brightness THz/IR Photon Source
Producing THz light requires sub-mm high-charge electron bunches and a THz production station
CFI funded project with objective: demonstrate production of high intensity (~MV/cm) broadband radiation and establish a user community within material science
S. D. Rädel, “Status and Future Perspective of the TRIUMF E-Linac”, 2019
S. D. Rädel, “On space charge driven microbunching instability in bERLinPro”, 2017
Join our team: JR101115
https://www.nicepng.com/ourpic/u2e6e6o0e6a9w7r5_we-want-you-developer-clipart-youtube-uncle-sam/

## Slide 35: Summary
Overview of electron linac
Initially e-Linac designed with only ARIEL in mind
The electron linac commissioning was completed in 2021
  Next step reliability
  ARIEL ready for electron beam in 2026
Converter Test Stand (experiment for ARIEL electron target) in low energy section was our first user
FLASH:
  12 in-vivo irradiation in total
    6 FLASH and 6 CONV
  8 samples of fruit fly larvae irradiated
DarkLight introduction and its impact on delivering electron beam
CFI project: e-Linac becoming a THz source

## Slide 36
Thank you
Merci
Stephanie Diana Rädel
sradel@triumf.ca
www.triumf.ca

## Slide 37
BACKUP SLIDES

## Slide 38: ARIEL e-γ Converter Test Stand (TRIUMF, UBC, UVic, SLAC)
Existing irradiation capability: 300 keV to 35 MeV, up to 1023 electrons/cm2/day
High-Z / aluminum interface at risk:
  Thermal stresses (100 kW beam, thermal cycles)
  Radiation damage / radiochemistry
  Irradiations of up to 3 weeks
Experimental setup:
  Water-cooled sample holder
  Several high-Z materials tested
  Beam power density matching online value
  300 keV beam to avoid activation (online 35 MeV)
e-
AETE
A. Gottberg

## Slide 39: ARIEL Hermetic Target Vessel
Increased development space for new ion source and transfer line concepts (cold transfer line, variable temperature transfer line, quartz transfer line, improved FEBIAD, low work function cavity, IG-LIS2)
Hermetic enclosure allows for the use of air-sensitive target materials
Service connections with provisions for future ion source and target concepts
Converter integrated into target vessel lid allows for routing additional cooling for high power target operation
Vessel volume increased for new target concepts (liquid targets, new converters, etc.)
A. Gottberg

## Slide 40: The ARIEL Target Hall
module storage
target exchange point
spent target storage
protons
electrons
AETE
APTW
drivers beam tunnel (existing)
Hall with two floor levels (existing)
RIB
ASTM
Electron beam and proton beam transport
Hot cell facilities (target handling, PIE, waste processing, medical isotope extraction repair and maintenance)
Remote-controlled crane
Target pit shielding
Storage of expired targets for 3 years before shipment to CNL
Symbiotic medical target
RIB
A. Gottberg

## Slide 41: Cryo
ALAT LL Cold Box, KAESER (FSD571SFC) main compressor (112 g/s), Cryotherm - distribution
4 Bush combi DS3010-He pumping units specified and installed (1.4 g/s @ 24mBar each)
T. Planche, “New Scientific Opportunities with the TRIUMF ARIEL e-linac”, 2022

## Slide 42: FLASH – a challenging user
Limited time window (1 hr) to accommodate safe animal handling procedures
Key: develop lockup procedure
In accordance with animal care protocol
ethics approval #AUP#21-0060

## Slide 43: DarkLight – Experimental apparatus
K. Pachal: “The DarkLight experiment at TRIUMF and the hunt for a new boson”

## Slide 44: DarkLight chamber and desired beam properties
Expected beam to be delivered:
  30 MeV
  300 μA
  10 kW
  Minimum of 1000 hours beam delivery
https://www.dropbox.com/scl/fo/iuufqqevskmgk00kz6sc2/h?rlkey=7repp8r3kv7f4os79vaiuxzs5&e=2&dl=0 - DARKLIGHT ARIEL EXPERIMENT LAYOUT_01_31_2024 v1