## Slide 1: MYRRHA and its driver accelerator
Adrian Fabich
19.03.2024

## Slide 2: Fission generates high-level radioactive waste
U235
n
Pu
Np
Am
Cm
Actinides
Minor Actinides
Neutron
Uranium
Fission
Fuel
U238
n
n
n
U235
U238
Plutonium
Neptunium
Americium
Curium
Source: SCK•CEN MYRRHA Project Team
FP
FP
After 4,5 years the spent nuclear fuel contains:
  94,7% of resources we can recycle (U+Pu)
  5,1% of nuclear waste with low radiotoxicity (FP’s)
  0,2% of high radiotoxicity nuclear waste
1 ton of nuclear fuel used 4,5 year in commercial PWR reactor produces electricity for 100,000 families per year (3500 kWh/y per family)


## Slide 3: Advanced treatment of nuclear waste Recycling of high level radioactive waste by P&T
Partitioning (P)
Transmutation (T)
VS
Separate the ingredients of the spent fuel in “similar” categories we can treat in a similar way
VS
Use intense neutron field to transmute isotopes into others, less “nasty” and producing energy (circular economy)

## Slide 4
Natural Uranium
1
Spent
Nuclear
Fuel
1000
Recycling
(PUREX*)
No recycling
Radiotoxicity
Advanced Recycling
(P&TMYRRHA)
+10 000 years
300 years
+300 000 years
* PUREX = plutonium uranium reduction extraction
4
Reducing the radiotoxicity

## Slide 5
Fast neutrons for transmutation
Fission of minor actinides
Resulting in radio-isotopes of lower radiotoxicity
Cross-section for fission requires fast neutrons

## Slide 6: Three options for Minor Actinide (MA) transmutation
Core safety parameters limit the amount of MA that can be loaded in the critical core for transmutation, leading to transmutation rates of:
  FR = 2 to 4 kg/TWh
  ADS = 35 kg/TWh (based on a 400 MWth EFIT design)
EFIT = European Facility on Industrial scale Transmuter
FR
heterogeneous
FR homogeneous
ADS
Driver fuel
Blanket with MA
Fuel with MA
Blanket
Fuel with MA
Fission Reactor

## Slide 7
Reactor
(Sub-critical, Lead-Bismuth cooled)
Accelerator Driven System (ADS) MYRRHA
Linear accelerator
(600 MeV)
42 m
≈360 m
Main Objectives
Transmutation demonstration
ADS at pre-industrial scale
Flexible irradiation facility

## Slide 8: MYRRHA ADS : inherently safety
Nuclear chain reaction sustained by the accelerator beam power
In case of issues, turning off the accelerator immediately puts the reactor in a safe state as the nuclear chain reaction dies out.
Based on natural circulation of the coolant by gravity between the cold Heat Exchanger (HX) and the hot core
 MYRRHA is inherently safe!

## Slide 9
Purpose:
  ADS technology demonstrator at pre-industrial scale
  Flexible irradiation facility (Radio isotope production, reactor fuel research, …)
At SCK CEN – the Belgian nuclear research center
Pre-studies since decades
SUBCRITICAL REACTOR (~70MWth)
600 MeV Protons
4mA - CW
MTBF > 250h for beam trips over 3s
3 types of SC-cavities

## Slide 10
MYRRHA
7 September 2018
The Belgian Federal Government announce its decision to:
Build MYRRHA, a new large research infrastructure in Mol
Establish governmental support for promoting MYRRHA international partnership
Establish the MYRRHA international not-for-profit organization (Founded in 2022)
  Responsible for construction, development and operation of MYRRHA infrastructure
  Legal entity to welcome international Countries and Organizations in MYRRHA Consortiums

## Slide 11
Less (toxic) nuclear waste
Transmutation reduces the final residual waste volume by a factor 100 and natural radiation level is reached after 300 years
Production of medical radio-isotopes
Therapeutic radio-isotopes can fight cancer cells in a more targeted way with significant reduction of side effects for patient
New reactor concepts
A wide range of material testing by fast neutrons for development of fusion reactors as well as used in current fission reactors
Fundamental research
Deepening understandings in Nuclear physics, atomic physics, fundamental interactions, solid state physics & nuclear medicine
MYRRHA’s versatility

## Slide 12: MYRRHA, a phased approach
Phase 3 - Reactor
Phase 1 - 100 MeV
“MINERVA”
Application Centers
Phase 2 - 600 MeV

## Slide 13: MYRRHA reactor
To be operational by 2040
Sub-critical operation (keff < 0.97)
Inherently safe
  Proton driver determines neutron flux (no chain-reaction)
  Passive decay heat removal - by natural convection

## Slide 14: Resulting accelerator requirements
600 MeV protons
4mA CW
Reliability: <10 beam trips of >3 s per 90 day run
  Minimize the mechanical stresses to the reactor structure
  Maximize the uptime

## Slide 15: Accelerator key design decisions
17 MeV normal conducting injector
  Parallel redundancy
Superconducting linac
  3 types of SC cavities
  Significant RF-power overhead for serial redundancy
Use of solid state amplifiers

## Slide 16
MINERVA = MYRRHA phase 1 implementation
100 MeV
  1 injector
  1 SC cavity type
Test the reliability concepts (RF-fault tolerance)
Two target stations:
  ISOL system (PTF): reduced duty factor (50kW)
  Full power Facility (FPF): Fusion material research, 400 kW

## Slide 17
Normal conducting CH-cavities up to 17MeV, 176MHz
Experimentally validated up to exit RFQ in R&D manner
  ECR ion source, 4-rod RFQ with up to 160 kW
  Emittance measurement done
Full Beam characterization including collimation (also in stand-by inj.)
Injector
CH-linac
Diagnostic & Collimation
Dogleg
SC-linac
Injector test stand currently being dismantled
Emittance | Horizontal ( | Vertical (
Simulation | 0.114 | 0.113
Scan | 0.080(7) | 0.093(5)
Emittance |  | 
Simulation | 0.114 | 0.113
Scan | 0.080(7) | 0.093(5)

## Slide 18: Injector Teststand
Pantechnik Monogan1000
LEBT
  2 solenoids optics
  gas injection for SCC
  2 Allison emittancemeters
  electrostatic chopper
  ACCT
4 rod RFQ
up to 160kW
Rebunching section

## Slide 19: Injector Teststand
RFQ commissioned with 95% transmission in nominal conditions
Nominal energy : 1.494 ± 0.003 MeV

## Slide 20
Optics & layout “classic high-power SC-linac-style”:
  30 cryo modules with each 2 single spoke cavities (352.2 MHz, β = 0.352)
  Warm section with doublet & diagnostic
  BPM & correctors integrated into quadrupoles
Last doublet used to match into “HEBT”
Significant RF-overhead for serial fault tolerance
Matching optimization still ongoing
SC-linac

## Slide 21: Series production of SC cavities (CAV)
cavity welded successfully
Integrated into He tank
  Leak test OK
  RF frequency after welding within tolerance
First series cavities successfully tested for Eacc (January/February 2024)
tested at 11 MeV/m exceeding nominal 9 MeV/m

## Slide 22
Design choices
  Linear accelerator
  Injector: parallel redundancy
  SC linac: serial redundancy
    installing RF overhead
    Fast de-tuning of SC cavities
Reliability model
  in collaboration with CERN
  using AvailSim4
Reliability

## Slide 23
Reliability requirement: # beam trips > 3s: Max 10 per 90 days
Reliability model done together with CERN as part of the EU-funded PATRICIA collaboration
Reliability approach
MYRRHA reliability requirements
Fault budget for individual systems, based on existing reliability data from other facilities
Identify critical sub-systems and develop fault compensation schemes

## Slide 24
Top down model
MYRRHA accelerator (10)
Injectors (1)
Injector 1 (5.5){8}
Injector 2 (5.5){8}
Main LINAC (5)
[152] SRF (9.5)
Infrastructure and Services (3.6)
[58] SRF Cryo-module (0.5)
[59] Quad- doublets (5)
BI (0.25)
Electrical network (1)
Cooling plant & ventilation (0.25)
Cryo plant & distribution (0.75)
Pressurized air (0.1)
IT services (0.5)
[58] Valve box (0.2)
[58] Cryostat (0.3)
[152] Powering (2.5)
[152] Feeder, circulator, coupler (2)
[152] Cavity & tuning (2.5)
[152] LLRF (2.5)
[59] Converters (3)
Cabling and connectors (1.8)
[59] Doublet Magnets (0.2)
Controls and Timing (1)
LEBT (1)
RFQ (1)
Vacuum (0.25)
Operation & maintenance (0.2)
Non-redundant kickers and magnets (0.1)
Kickers 100 MeV (0.001)
Dipole 600 MeV (0.099)
Source (0.75)
Injector switching (0.95) < 92% >
Dynamic compensation (3.3) < 66% >
Quad – Matrix / Compensation <80%> (1)
Switching magnet (0.05)
Vacuum (0.25)
Non-redundant RF & Cryo (0.1)
[1] Rebuncher 100 MeV (0.1)
Source (0.75)
MEBT (1)
CH (1.5)
LEBT (1)
RFQ (1)
MEBT (1)
CH (1.5)
Vacuum (0.25)
BDS to reactor (0.2)
MYRRHA Top-Down model with fault-tolerance strategies. Numbers in brackets are fault count per 90 days (worst case to reach requirements). Numbers in square brackets are the system count. Numbers in arrow-brackets indicate the effectiveness of the respective fault-tolerance mechanism (i.e. what percentage of faults in the systems below the fault-tolerance method will be visible to operation).

## Slide 25
Injector reliability - AVAILSIM4 simulations
Availability of the linac simulated with Monte Carlo code (AVAILSIM4)
AVAILSIM4 result for the redundant injector strategy:
target failure rate per hour for the injector deduced from breakdown of estimated individual failure rates for all components
Failure rate/h simulated for
  different Mean Time Between Failures (MTBF)
  different Mean Time To Repair (MTTR)

## Slide 26
Dynamic RF-compensation
 Ideal from beam dynamics
 With fault compensation
 With minimal margins for fault compensation
MINERVA
60 single spoke cavities
30 cryo modules
17  100 MeV
(*) 18 double spoke cavities
9 cryo modules
100  172 MeV
(**) 72 elliptical cavities
18 cryo modules
172  600 MeV
(*)
(**)
The plot shows power requirements for all cavities from a pure beam dynamics point of view, when 4 neighboring cavities compensate 1 faulty cavity

## Slide 27: International R&D network (1)
Universities
Source: SCK CEN MYRRHA Project Team
* Acquired by Veolia
Research

## Slide 28: International R&D network (2)
Source: SCK CEN MYRRHA Project Team
* Acquired by Veolia
Private Sector
Beyond EU
*

## Slide 29
Nuclear licensing: approval received from authorities
2024
2020
2026
Construction
2016
2028
Beam Commissioning
Design
11/2022
Timeline – phase 1

## Slide 30
MYRRHA Phase 1 is funded and currently implemented
International not-for-profit organization established since 2022
Inviting interested parties (countries, organizations, companies) to join MYRRHA
Design consolidation of accelerator optics & components being finalized
Summary
First series components in production
Heavily relying on collaborations & industry

## Slide 31
Copyright © SCK CEN
All property rights and copyright are reserved.
This presentation contains data, information and formats for dedicated use only and may not be communicated, copied, reproduced, distributed or cited without the explicit written permission of SCK CEN.
If this explicit written permission has been obtained, please reference the author, followed by ‘by courtesy of SCK CEN’.
Any infringement to this rule is illegal and entitles to claim damages from the infringer, without prejudice to any other right in case of granting a patent or registration in the field of intellectual property.
SCK CEN
Belgian Nuclear Research Centre
Studiecentrum voor Kernenergie
Centre d'Etude de l'Energie Nucléaire
Foundation of Public Utility
Stichting van Openbaar Nut
Fondation d'Utilité Publique
Registered Office:
Avenue Herrmann-Debrouxlaan 40 - 1160 BRUSSELS - Belgium
Research Centres:
Boeretang 200 - 2400 MOL - Belgium
Chemin du Cyclotron 6 - 1348 Ottignies-Louvain-la-Neuve - Belgium