## Slide 1: Status of the Second Target Station Project with Target Systems Highlight
Peter Rosenblad
with Michael Allitt, Gary Bloom, Leighton Coates, Steve Hartman, and Ken Herwig
ANS AccelApp ‘24 Conference, Norfolk, VA

## Slide 2: Topics
Neutrons at ORNL
SNS Overview and Upgrades
Second Target Station (STS) Project
STS Target Systems

## Slide 3: ORNL has an 80-year history of developing neutron sources and neutron sciences
1943
Courtesy Erik Iverson
ORNL (Clinton Laboratories) in 1943
The Clinton X-10 Pile was the world’s first continuously operated nuclear reactor
1994 Nobel Prize in Physics awarded to Shull and Brockhouse for development of neutron scattering
Wollan (seated) and Shull at 1950 diffractometer
Ernie Wollan requested beam access at “the pile” in 1944, just after the reactor started operation
Notes: Source limiting technologies – removal of waste heat, target robustness

## Slide 4: Today ORNL operates two of the brightest neutron sources
High Flux Isotope Reactor (HFIR)
Highest continuous neutron flux
Spallation Neutron Source (SNS)
Highest peak neutron brightness
Hg
26 n/proton (1 GeV)
25 MeV/useful n
Pulsed
2.5 n/fission
190 MeV/useful n
Continuous
33 instruments
600 publications/year
1200 experiments/year
1200 unique users/year

## Slide 5: SNS upgrades will accelerate scientific progress and deliver wholly new capabilities
STS instruments see 4x more and 100x faster than today’s similar instruments
STS project: Build the second target station with initial suite of beam lines
Optimized for cold neutrons
World-leading peak brightness
Provide new science capabilities for measurements across broader ranges of temporal and length scales, real-time, and smaller samples
PPU project: Double the power of the existing accelerator structure
First Target Station (FTS) is optimized for thermal neutrons
Increases the brightness of beams of pulsed neutrons
Provides new science capabilities for atomic resolution and fast dynamics
Provides a platform for STS
Notes: SNS was planned from its outset to be upgraded to operate at higher power and to share this power with a second target station.
The Proton Power Upgrade, or PPU, project, which is a totally separate project from STS, will double the power of the SNS accelerator.
PPU is well underway and they are already assembling cryomodules and building infrastructure
I should also mention that the First Target Station is optimized for thermal neutrons and with the PPU power increase it will be among the brightest sources of thermal neutrons in the world
The STS Project, which is outlined in yellow on this artists concept of the SNS site, is the subject of this review. STS will be optimized for cold neutrons, in-line with its Mission Need.
In fact, as I will show in a later slide, STS will achieve the highest brightness of cold neutrons in the world, which will provide scientists the capability to make measurements across a broader range of length and time scales and to examine smaller samples

## Slide 6: STS will make optimal use of the PPU-upgraded SNS accelerator capability
3 out of 4 proton pulses
45 pulses/sec
2 MW
1 out of 4 proton pulses
15 Hz
700 kW
*animation courtesy of Matt Stone
Accumulator Ring
Ion Source
Linac
60 Hz accelerator
46.7 kJ/proton pulse
2.8 MW capable
First Target Station (FTS)
Second Target Station (STS)
Short pulses at 15 Hz enables simultaneous measurement across broad wavelength range (=13.2 Å at 20 m from source)
Complementarity with FTS – uses all available accelerator capability provided by PPU
Flexibility will be provided to operate both FTS and STS at the same time or separately if either is shutdown
Notes: Both the first and second target station make use of the same accelerator infrastructure of the SNS. Negatively ionized hydrogen atoms are accelerated along the linear accelerator up to about 90% of the speed of light. The particles pass through a foil which strips them of their electrons, leaving just a positively charged proton. The protons are injected into a storage ring and further accelerated and bunched together into pulses. These pulses then are sent to the liquid mercury target of the first target station to produce neutrons. The second target station will use the same accelerator, but operate at a rate of 15 Hz. So one in four of the first target stations pulses will be sent to the second target station. To compensate for this loss of neutrons at the first target station, the linear accelerator is currently going through a power upgrade to operate at up to 2 MW peak power compared to the current 1.4 MW.
Both of these target stations can operate independently If the first target station is under a maintenance outage, the second target station can continue to operate.

## Slide 12: STS uniquely combines advanced technologies to deliver new science capabilities needed to understand more complex materials, processes, and devices
PPU upgraded SNS
46.7 kJ/proton pulse
60 Hz, 2.8 MW capable
Start with the world’s most powerful hadron accelerator – the SNS
Use the accumulator ring to compress the proton pulse
1 msec linac production compressed to < 1 msec
Add optics & transport to produce uniform proton spot size on the target
STS proton area = 60 cm2
FTS proton area = 140 cm2
Add rotating, segmented solid-tungsten target
Spreads heat load over larger volume with longer lifetime
Add low dimensional moderators, tightly-coupled to neutron production zone
Two high-brightness, geometrically-optimized moderators (cylinder & tube)
Add science-driven, optimized instrument designs
8 initial STS instrument, latest technologies, integrated controls, scientific software, proposed by and selected with the user community
Next generation neutron facility with science capabilities needed for materials innovation: materials discovery & materials in-action.

## Slide 13: World class performance for 8 initial instruments
ST01
EXPANSE
ST02
QIKR
ST03
CUPI2D
ST04
BWAVES
ST05
CHESS
ST06
Future
ST07
VERDI
ST08
PIONEER
ST09
CENTAUR
 = 5 Å
SNS-STS
ESS (5 MW)
ESS (2 MW)
J-PARC
SNS-FTS (2 MW)
CSNS
SNS-FTS
ISIS TS2
ISIS TS1
HFIR
ILL
FRM-II
NIST
SONATE (est.)
PSI
ORPHEE
LUJAN
short-pulse
long-pulse
steady-state
USA
Asia
Europe
Planned
Existing

## Slide 14: Major Projects Take Time
1996 – A DOE advisory committee recommended that SNS proceed and include additional target station capability.
1999 - Environmental Impact Statement for SNS included a Second Target Station (STS).
2009 – DOE approved Critical Decision-0 (CD-0)
2013 – A DOE advisory committee noted STS is “absolutely central” to US leadership in science.
2016, January – Initiated STS conceptual design activities.
2017, April –Selection of major STS technical alternatives: 15 Hz pulse repetition rate, 700 kW proton beam power, short pulse options.
2019, October – Dedicated STS Project Office established.
2020, November – DOE approved the project’s CD-1 status
2010
1996
2000
2024

## Slide 15: Significant progress has been made across the project over the past 4 years
Independent Control
700 kW proton beam power
Peak Brightness
≥ 8 neutron instruments
Lasagna
Target Concept
Selected
Preliminary Moderator Optimization Complete
MRA/Inst. Sys. Interface Sheet issued
Preliminary neutronic heating, structural & CFD analysis completed
Second critical device workshop for FTS target cart out of position
PDR Timing System, Run Permit System, & Linac LLRF controls
ICDs & ICSs with AS & SNS issued
TS/AS beam parameter IS Rev 2 issued
8 STS Project Neutron Instruments selected
Technical review of initial designs for 4 instruments complete
Two beam flavors workshop report issued
Requirements documents issued for all 8 instruments
PDR for CHESS, PIONEER, & QIKR optics
Segment
Target Concept
Selected
PDR proton beam optics
New proton transport lattice
Site plan established
RTST & CSB design begins
T & I bldg. design begins
2021 IPR
2021
2022
2023
QIKR Instrument
Segmented Target

## Slide 16: Notional Execution Strategy
Subproject 1 – Conventional Facilities
CD-2/3
Early Finish
CD-4
FY24
FY25
FY26
FY27
FY28
FY29
FY30
FY31
FY32
FY33
FY34
FY35
FY36
FY37
FY38
FY39
FY40
Subproject 2 – Accelerator, Target, 3 Instruments
CD-2
CD-3
Early Science
Early Finish
CD-4
Subproject 3 – 5 remaining Instruments
CD-2
CD-3
Early Finish
CD-4
CD-3A
All CD dates represent ESAAB Approval dates

## Slide 17: STS Target Systems key parameters / features
1.3 GeV, 700 kW, 15 Hz, 46.7 kJ/pulse
Rotating tungsten target 1.1 m diameter x 60 mm tall
Small (3 cm) 20 kelvin supercritical hydrogen moderators
  Coupled and not poisoned
  2 cm light water pre-moderator
Be reflector, no heavy water
Aluminum proton beam window
Core Vessel with flexibility for helium or rough vacuum operation
Vertical only maintenance

## Slide 18: Target Systems challenge: to provide world’s brightest neutron source
Small beam footprint – started at 30 cm2, grown to a range of 60 – 90 cm2
Time – pulses are less than 1 micro-second
Energy – each pulse = 2.5 times the energy of a .50 caliber round
Small moderators (3 cm) closely coupled
Alignment – laser, not flood light
Cost effectiveness
Reliability
Maintainability
Notes: The hart of the STS is the rotating tungsten target, surrounded by the two moderators.
On the top we have cylindrical moderator.
On the bottom is the so-called “tube” moderator.
Both use para-hydrogen at 20 degrees Kelvin for the moderator material.
A catalytic converter is included in the hydrogen loop to control the ortho-para content. Para-hydrogen is surrounded by the water pre-moderator and the beryllium reflector. All vessels are made from aluminum. The gap between the moderators and the target will be ~ 10 mm.

## Slide 19: Target Systems in the Building
Monolith
Gas liquid separator and delay tank cavity
Hot process vault
Cryogenic Moderator System rooms
Service cell
Mock-up test stand
Target drive room

## Slide 20: Monolith – “Core” of STS
Bulk steel shielding,
(Ø8.7 m)
Core Vessel
Target assembly, drive, shaft segments
Proton beam window
Target Viewing Periscope
Core vessel shielding
Target disk (Ø1.2 m)
Proton beam tube assembly
Moderator Reflector Assembly
Nozzle Extension
Instrument Optics Insert

## Slide 21: Key Target Systems decisions taken, and challenges overcome
Segmented Target – maintenance, availability, and flexibility
Target Block Design – eliminate water to tungsten or tantalum contact
Moderator configuration and manufacturability – See J. Janney Poster
Compact moderator alignment
Single hydrogen loop for both moderators – facility simplification and cost savings
Cost effective future PIE capability included
Target Viewing Periscope included
Core Vessel Nozzle Extension manufacturability
Simplified water cooling – one loop for target and one loop for all remaining components

## Slide 22: Remaining Target Systems key challenges
Target block manufacturability
Core Vessel Beltline manufacturability
Design coordination, particularly with conventional facilities and integrated controls
Execution!

## Slide 23: Conclusion and Discussion!
ORNL and DOE Basic Energy Sciences seek to strengthen long term leadership is material science with neutrons
STS will provide world leading peak brightness by stealing 1 out of 4 pulses from the upgraded existing Spallation Neutron Source
To reach peak brightness, STS Target Systems employ a novel combination of designs and material systems, but design features are based on previously proven technologies