## Slide 1
A compact medical cyclotron
for research into
medical and multi-disciplinary applications
Saverio Braccini
Albert Einstein Center for Fundamental Physics (AEC),
Laboratory of High Energy Physics (LHEP),
University of Bern, Switzerland

## Slide 2: Outline
The Bern medical cyclotron laboratory
  GMP industrial production of radiopharmaceuticals and academic research under the same roof
Multi-disciplinary research based on tools and methods from high-energy physics
  Radioisotopes for theranostics in nuclear medicine
  Targets, beam monitoring detectors and irradiation systems
  Radiation hardness
  Proton induced neutron beams
  Cell irradiation in both conventional and FLASH regime

## Slide 3: The cyclotron at the Bern University Hospital (Inselspital)
In operation since 2013

## Slide 4: The Bern medical cyclotron and its research Beam Transport Line (BTL)
IBA 18 MeV high current cyclotron (up to 150 mA) – 2 H- ion sources
2 18F liquid targets: daily GMP industrial production (up to 1 TBq per run)
External Beam Transfer Line (BTL) in a separate bunker: research
Solid target Station (STS): research
Specific method to produce currents down to 1 pA

## Slide 5: The hot labs
3 GMP production labs (SWAN Isotopen AG – 18F, 68Ga, 177Lu radiopharmaceuticals)
1 GMP clinical research lab (Nuclear Medicine, Inselspital)

## Slide 6: The BTL
Beam from cyclotron
Beam from BTL
S. Braccini, AIP Conf. Proc. vol. 1525, p. 144, 2013

## Slide 7: Theranostics in nuclear medicine
  Promising pairs:
    68Ga/177Lu and 68Ga/225Ac
    43Sc/47Sc and 44Sc/47Sc
    61Cu/67Cu and 64Cu/67Cu
    155Tb/149Tb and 155Tb/161Tb
  Radiometals

## Slide 8: Our starting point: commercial solid target station
  IBA Nirta “COSTIS”
  Target:
    24 mm diameter 2 mm thick disk
    electro-plated materials
  Manual insertion and recovery of the disk
  Cooling: water in the back, helium in the front
Radiometals
Target material:
~10 mg
~ 5 mm diameter
Powder
Target: ?
Beam: ?
Radioprotection: ?

## Slide 9: Our strategy
Accurate knowledge of the beam (position, shape, energy)
  Beam monitoring detectors
Novel targets + transfer systems
Nuclear data
  Production cross sections (also for impurities!)
Novel irradiation systems

## Slide 10: The UniBEaM detector
  2D beam profiler based on (doped) optical fibres passed through the beam
  On-line, minimal interference with the beam
  Developed by LHEP and commercialized by D-Pace (Canada)
M. Auger et al., J. Instrum. 2016, 11, P03027001
D. Potkins et al., Phys. Procedia 2017, 90, 215–222

## Slide 11: On-line monitoring with UniBEaM

## Slide 12: The Pi2 detecor
S. Braccini et al., Appl. Sci. 2023, 13, 3657

## Slide 13: The Collar detector
C. Hoehr et al., Proc. IPAC’23, Venice, Italy
Scintillating fibres located around the beam pipe in front of the target
In collaboration with TRIUMF and D-Pace

## Slide 14: The target coin
High-purity aluminum
Two halves kept together by permanent magnets
  SmCo, 350oC Curie temperature
O-ring (viton) to avoid radioactive degassing
Variable thickness of the front (entry energy variation)
Target material pellet

## Slide 15: Cross section measurements with a novel method
T. Carzaniga et al., Appl. Radiat. Isot. 129 (2017) 96–102

## Slide 16: The target station for cross section measurements
Studied radionuclides of medical interest:
43Sc, 44Sc, 47Sc, 48V, 61Cu, 64Cu, 67Cu, 66Ga, 67Ga, 68Ga,
155Tb, 165Er, 165Tm, 167Tm

## Slide 17: Cross sections and radio-nuclidic purity: the case of 68Ga
S. Braccini at al., Appl. Radiat. Isot., 186 (2022) 110252
Use of two different enriched materials: the (p,n) and (p,2n) 67Ga nuclear reactions can be measured!

## Slide 18: Yield, purity and production tests
68Ga

## Slide 19: Some produced radioisotopes
Contributions to fundamental physics:
High Efficiency Cyclotron Trap Assisted Positron Moderator, Instruments 2 (2018) 10.
High-resolution laser resonance ionization spectroscopy of 143−147Pm, Eur. Phys. J. A (2020) 56:69
G. Dellepiane et al, Appl Rad Isot 189 (2022): 110428 (scandium)
G. Dellepiane et al, Appl Rad Isot 191 (2023): 110518 (copper)
S. Braccini et al., Appl Rad Isot 186 (2022): 110252 (gallium)
G. Dellepiane et al, Appl Rad Isot 184 (2022): 110175 (terbium)

## Slide 20: 44Sc is ready for clinical applications
IBA Award 2020
In collaboration with PSI
15 GBq in 5 h irradiation!

## Slide 21: The Automatic Focusing System (AFS)
STS
2D Beam monitor
MiniBeamLine
Cyclotron
Beam line
MBL Magnets
Feedback beam monitor
STS
Control system
before
P. Haffner et al., Appl. Sci. 11.6 (2021): 2452
after

## Slide 22: Radiation hardness studies
Applications in space (Juice mission), HEP (ATLAS at CERN), material science
J. Anders at al., 2022 JINST 17 P04021
Example: Twinax cable for ATLAS pixel detector

## Slide 23: Proton induced neutron beams
Several materials for the target (Al, Cu, Li, 18O-water)
DIAMON neutron spectrometer
In collaborator with
S. Braccini et al., Sci Rep 12, 16886 (2022).

## Slide 24: Cell irradiation
The cells are plated on a flask
PRELIMINARY
Cell survival of B16-F10
mouse melanoma
https://zenodo.org/records/10478639
In collaboration with the
Institute of Anatomy of the Univesity of Bern
Protons vs photons
Ionization
chamber

## Slide 25: Exploring the FLASH regime
High currents are an advantage!
PRecision dOsimetry in
FLASH radiotherapy with Optical Fibers (PROOF)
P. Casolaro et al., 11th Int. Beam Instrum. Conf. (2022)

## Slide 26: Conclusions and Outlook
Medical cyclotrons:
  Tools of choice for radioisotope production in a hospital-based environment
  Have a high scientific potential
  Excellent for the training of young scientists
  Production and research can run in parallel
Several multi-disciplinary research programs at the Bern medical cyclotron in the last 10 years
… we are open to collaborations!

## Slide 27: Acknowledgements
https://www.lhep.unibe.ch/research/medical_applications/index_eng.html
Seniors and PostDocs: P. Scampoli, I. Mateu, L. Mercolli, P. Casolaro, L. Franconi, C. Belver Aguilar, E. Kasanda
PhD students: A. Gottstein, A. Oliveira, G. Dellepiane (2023), P. Häffner (2021), T. Carzaniga (2019), K. Nesteruk (2017)
Master and Bachelor Students (last 5 years):
  L. Eggimann, D. Wermelinger, T. Stammbach, M. V. Rossi (2024), R. Zehnder (2024), M. Schmid (2021), E. Zyaee (2021), N. Voeten (2022), D. Wüthrich (2019), J. Askew (2022), D. Wermelinger (2023), M. Wenger (2022), N. Kämpfer (2020), A. Gaschen (2023), N. Gaschen (2023), A. Andrey (2023), Andreas Gsponer (2019), Melina Lüthi (2019)
LHEP mechanics and electronics workshop; SWAN Team