## Slide 1
Eduard Pozdeyev
Director of Accelerator Operations
Presented to:
CLAS Collaboration Meeting
November 7, 2023
Accelerator Operations Update

## Slide 2: Outline
Priorities of CEBAF Operations
Status of Accelerator Operations
Beam availability and downtime mitigation
CEBAF Performance Plan (CPP)
Accelerator Improvement Projects (AIPs) and R&D portfolio
Accelerator Division reorganization
Conclusions

## Slide 3: Mission of Accelerator Operations
Operate CEBAF for Nuclear Physics for >30 week/yr. for >1800 users
Ensure CEBAF ready for upcoming 12 GeV experimental program (MOLLER, SoLID, K-Long)
Support future upgrades providing new experimental capabilities (22 GeV and e+)
Adapted from S. Henderson’s
all-hands presentation 07/2023

## Slide 4: Priorities of CEBAF Operations
Deliver beam (up) to four halls for nuclear physics program safely and reliably
Increase beam availability, reduce unscheduled downtime and frequency of trips
Improve CEBAF multi-hall performance with a high intensity beam.
Prepare for upcoming experiments to meet users’ requirements
Execute CEBAF Performance Plan
  Extend CEBAF energy reach up to 12 GeV after 5.5 passes with margin
  Improve hardware reliability through acquisition of critical components and spares
  Address hardware obsolescence
Enhance CEBAF capabilities through AIPs, upgrades, and R&D
Maintain strong operations team capable of meeting operational challenges

## Slide 5: FY24 and FY25 Operations
 | FY23 |  |  | FY24 |  |  |  | FY25 | 
 | Q2 | Q3 | Q4 | Q1 | Q2 | Q3 | Q4 | Q1 | Q2
Hall A |  |  |  |  |  |  |  |  | 
Hall B |  |  |  |  |  |  |  |  | 
Hall C |  |  |  |  |  |  |  |  | 
Hall D |  |  |  |  |  |  |  |  | 
SAD |  |  |  |  |  |  |  |  | 
Energy/linac |  |  |  |  |  |  |  |  | 
FY24 Run
34 weeks of beam operations, ~31 weeks physics
Expected challenges
  Increasing reliability and beam availability
Scheduled Accelerator Down starts on May 20th
FY25 Run
33 weeks of beam operations, ~31 weeks physics
Expected challenges
  Physics requests CEBAF to operate at full design energy (12 GeV) and high beam power (1.1 MW)
Increasing CEBAF energy reach will be critical
1047 MeV
1047 MeV
1100 MeV
Now

## Slide 6: FY23 Scheduled Accelerator Downtime (SAD) Completed
New injector will reduce helicity correlated asymmetries for MOLLER.
Installed cryomodules and plasma processing increased the energy reach.
Upgrade of Personnel Safety System in South Linac. Certification once per year is considered.
C100-10R
98 MV
C100-05R
98 MV
1L26
Drift tube
2L26
C100
76 MeV
2L22
C100
90 MeV
2L23
C100
82 MeV
2L25
C100
84 MeV
2L24
C100
80 MeV
Booster
Plasma processing
North linac
energy gain +72 MV
South linac
energy gain +65-70 MV
0L02
New Injector Phase 2
Installed
PSS Upgrade in South Linac
Lost 1L09
helium leak

## Slide 7: Status of CEBAF Beam Operations
Beam parameters on target
  Hall A: ~40 uA, 4 pass
  Hall B: 5 – 100 nA, 5 pass
  Hall C: 10 – 30 uA, 5 pass
More stable beam than last year
  Reduced number of RF trips
  Longer uninterrupted runs
  Likely, due to increased energy reach, smaller number of Halls

## Slide 8: Status of CEBAF Beam Operations: Beam Availability
Average beam availability for this run is 81%
81% - This Run Average
72% - Previous Run Average
As of 11/05/2023
Data shows average
beam availability over a week
ending on the shown date

## Slide 9: Beam Availability and Reliability, This Run (08/26/2023 – now)

## Slide 10: Main Sources of Downtime and Their Mitigation
RF/SRF failures are the largest contribution to downtime
  CEBAF Performance Plan (see following slides)
  CEBAF Gradient Team formed to address immediate SRF/RF performance issues and identify opportunities for improvement
  SRF/RF/Operations meeting to address to issues common for SRF/RF/Ops
  Qext reduced 3e7 to 1.6e7 due to lower field and higher microphonics
Beam losses and unscheduled tuning is a consistently high contribution
  Improve and automate beam measurement and tuning procedures
  Ongoing effort to Re-calibrate most offending beam loss monitors
  Conduct a mini-workshop to develop path forward with BLM system upgrade
Number of MPS fast trips caused by BLMs
60% of all trips are caused
by four BLMs

## Slide 11: Improving Reliability Is High Priority
Last run beam availability was 72%. DOE wants to see 80% at least.
Accelerator Ops are hiring Operability Deputy with a focus on reliability.
Need a cultural change to shift from reactive approach to proactive/preventive maintenance.
  Identify immediate opportunities to improve reliability
  Long term planning to address aging CEBAF systems
SMEs must be fully engaged in the process, understand failure modes of their systems, proactively think how to improve reliability, and plan for upgrades
CEBAF Performance Plan addresses critical spares and obsolescence
  Procurement of critical spares and maintaining spares inventory
  Replacement of obsolete systems

## Slide 12: Probing CEBAF Performance Limits Increased Intensity Run in 10/2023
High intensity run to identify CEBAF limitations in anticipation of the high-power run in FY 2025 (1.1 MW).
850 kW (395 uA)
RF Klystron Power Distribution
Absolutely needed 10 kW RF power output
Klystrons are specified at 11 kW linear regime.
Beam power as function of time

## Slide 13: CEBAF Performance Plan (CPP)
Goal: ensure CEBAF reaches 12 GeV in 5.5 passes and sustains reliable operations to meet physics program requirements
Energy Reach Project, manager – Tony Reilly
Reliability Project, manager – Randy Michaud
 | Cryomodules Installed | Cryomodules Removed | Energy Gain (NL/SL), MV
FY23 | C100, C100 | C100 | 98 / 22
FY24 | C100, C75, C75 | F100, C20, C20 | 24 / 97
FY25 | C100, C75 | C100, C20 | 75 / 0
FY26 | C100, C75 | C100, C20 | 0 / 75
FY27 | C100, C75 | C100, C20 | 75 / 0
FY28 | C100, C75 | C100, C20 | 0 / 75
FY29 | C100, C75 | C100, C20 | 75 / 0
FY30 | C100, C75 | C100, C20 | 0 / 75
Cryomodule Installation Plan

## Slide 14: CPP: Energy Reach Projection
Energy reach is the energy gain per linac corresponding to 10 RF trips/hour
Available RF power and beam current can dictate linac voltage profile and frequency of RF trips
FY23
FY24
FY25
FY26
FY27
FY28
FY29
FY30
1090 (12 GeV)
1090+100
✽
CEBAF
energy reach
in 03/2023
Requested Physics
Energy (per linac)

## Slide 15: Successful In-Situ Plasma Processing Of CEBAF CMs
Four cryomodules, 2L22 - 2L25 (all cavities), were plasma-processed in the tunnel during last SAD
Path Forward
  Process 3 to 4 C100 and C75 cryomodules during accelerator shutdowns.
  Extend plasma processing to C75 cavities.

## Slide 16: In-Situ Plasma Processing Increased Gradient by 2.7 MV/m
Field emission free operation was improved by 59.1 MeV (24%).
An average improvement of 2.7 MV/m.
5 cavities were field emission free after processing.
Average Increase
is 2.7 MV/m
Success of plasma processing supports more aggressive curve for CEBAF energy reach

## Slide 17: Accelerator Improvement Projects
AIPs are used to upgrade existing system and bring new functionality
AIP | Status
Full Energy Injector - Integration | Completed
LLRF Digital Upgrades - C75 LLRF | On-going
Next Gen BPM Upgrade | Prototyping
Global Timing System | Not started
Spare CEBAF Booster | Not started
Waveguide Stub Tuners | Not started
BLM system upgrade (New) | Not started
RF one zone upgrade (New) | Not started

## Slide 18: AIPs: Injector Upgrade Completed
The injector upgrade reduces helicity correlated asymmetries for the Parity Quality program (MOLLER).
Scope
  Increased gun voltage from 130 to 180 keV.
  Upgraded Wien filters.
  Solenoids with a larger aperture.
  New SRF Booster cryomodule with reduced deflection and coupling.
Injector is successfully used for this beam run
Beam tests to quantify beam Parity Quality and fully evaluate the injector are on-going
180 kV photogun
booster
New injector and Booster CM
In the CEBAF tunnel
Beam in the injector

## Slide 19: Portfolio of R&D and SBIR-Funded Projects
Three AI/ML DOE funded projects (FOA-LAB-20-2261)
  Automate identification of unstable SRF cavities.
  C100 Cavity Fault Prediction.
  CEBAF cavity field emission management using neutron detectors and surrogate models (ML)
    Reduce field emission, increase lifetime of components
He flowmeter (SBIR, Hyperboloid LLC)
  Allows for fast and accurate measurement of cavity heat and Q0
1497 MHz Magnetron RF source (SBIR, Muon Inc)
  Demonstrate feasibility of magnetron as alternative, efficient RF source for CEBAF
Detection of anomalies in cavity field
First L-Band tube at
Richardson Electronics
Helium Mass
Flow Monitor​

## Slide 20: Accelerator Division Reorganization
Effective October 1, 2023, DC Power, RF, I&C, Safety Systems, Support Services, Vacuum Technicians, Specific Mechanical Engineering personnel moved from Engineering Division to Accelerator Division
Goal: align resources, responsibility and accountability for CEBAF operations, maintenance and improvements within a single organization

## Slide 21: FY24 SAD Planning Started
Dates (preliminary) 5/19/2024 – 9/5/2024
SRF
  Install 2xC75 CM and swap one C100 CM
  Plasma-process 3-4 C100 and C75 CMs
  Change gate valves around these CMs, girders?
RF
  Keep installing LLRF 3.0
  Install fiber links for Master Oscillator to North and South Linacs to reduce EMI induced trips
…

## Slide 22: How Do CEBAF Operations Compare To Other Facilities
The Good
  Close interaction with experimental halls
  Strong CEBAF operator group and training
  Work release system (ATLis)
The Bad
  Culture of reactive approach to hardware maintenance results in low reliability
  In-consistent use of best engineering practices and processes and lack of ownership
And we really need to think about it…
  How are we going to upgrade aging infrastructure under present funding and schedule boundary conditions
  Succession planning

## Slide 23: Conclusions
Beam run in CEBAF is in full progress. Average reliability for the run is 81%.
Focus on improvement of communication between Ops and SMEs and performance and reliability issues
Energy reach will meet 12 GeV requirements with the required margin in FY 25-27. Successful demonstration of in-situ plasma processing will speed up growth of the CEBAF energy.
Accelerator Division reorganization will align resources with CEBAF operations
Looking forward to another successful year of delivering beam to NP users.

## Slide 24: Thank you!