## Slide 1: HKS Target Design and Status
David Meekins
22 March 2024

## Slide 2: Design Status
Design is in concept stage and will be for some time
  Target group does not have resources to develop a comprehensive design at this time.
  Solid target concept complete
  Gas target concept is complete as well
  Concepts will need to include backward angle acceptance requirements which have yet to be addressed.
Best to design and fabricate one system
  System with both solid and fluid targets
  This is more work to install but could be done in two phases if needed
Both systems require cryogenic cooling
  Pb and Li both need this to meet beam current requirements
  He and Hydrogen gas cells will need it to reach proposed densities
Fluid systems are designed to appropriate Codes and Standards
  Somewhat limiting for the cell design (wall thickness)

## Slide 3: Concept Design
There has been no real progress here
Base motion system and top end design on PREX/CREX target
  Plenty of range for all targets needed for
Custom chamber will be needed
Long transfer lines will be needed.
  Base this design on existing design for PREX
Cooled solid target ladder/heat exchanger
Cooled cells (not shown)
  Fed gas from gas panels in Hall C
Chamber
Solid targets
Motion system
Cryo/gas interface

## Slide 4: “Original” Proposal (circa 2022)
Solid targets
  Some basic solid targets (these targets are relatively easy)
    C, Al, B4C etc.
  More Challenging (these targets require special handling/cooling)
    Lead, Ca40,48, Li6, Pb etc.
Gas Cells
  H2, He3 and He4
  Tuna can with vertical axis perpendicular to the beam
  Diameter is 20 cm
  Total Al thickness 162 mg/cm^2
  Gas pressures low

## Slide 5: Optimization of the Cells
Assumptions for improvement
  Thinner cells walls
  Higher fluid densities
  Smaller diameter
Plan to use actively filled cells
  This is contrast to the tritium target were the cells were filled with a static pressure
  Two gas isotopes can be used concurrently
  One gas species at a time (e.g., H2 and D2 OR He3 and He4)
Requires gas handling system
  This might need to be in a second phase as schedule permits

## Slide 6: Solid Targets
Lead and calcium will present challenges
  Lead will need to be cryogenically cooled with good thermal conductivity
    Realistic thickness will need to be at least 0.1 mm
  Ca and Li targets will need special handling
    Ca48 stock at Jefferson Lab is highly compromised
    Recommend purchasing new Ca48 foil ($50K to $100K)
Other solid targets are relatively simple to work with
  Proposed thickness are OK
  Multi-foil: reduce to +/- 5 cm to closer match cell length
Design path:
  Combine latest Hall C solid target ladder with PREX/CREX motion system and T2 target style heat sink.

## Slide 7: Solid Target Ladder
Solid target design concept
All components are aluminum 7075
Target material is clamped into the frame with sufficient force to ensure good Kc
  Threaded clamp screws into heat sink
  Nuclear grade anti-seize is used to enhance Kc and prevent galling
  Clamp ring prevents spinning of the target foil
Proven to work will all targets except lead
  Preliminary calcs show design is acceptable for lead as well
This design does not meet the backward angle acceptance requirement and will have to be adjusted.
Clamp
Clamp ring
Heat sink
/mount
Target material

## Slide 8: Time Line
Currently the Target Group is over committed
  We are working to increase our staff but this will likely not have a positive near term affect
It MAY be possible for some Target Group design team members to work with Hall C designers to develop SOME designs.
  Possibilities include scattering chamber and support structures
Cannot give any firm estimates at this time

## Slide 9: Summary
A completely new cryogenic target will be required to be located ~11 m downstream from the nominal pivot.
  Current gas handling panels should be sufficient for HKS target
  New electrical installations will be required
  New gas lines will be needed
The cryogenic distribution system will require some new transfer lines in excess of 40 ft. These will need to be fabricated somewhere (JLAB or ???)
We will need to work with Hall engineers/designers to layout target services and design the scattering chamber.
  Hall C design team has already reached out.
At the moment the target group does not have the resources to complete a final design or substantially develop the concept
  It is not clear when the resources will be available either although some design resources may be available near the end of 2024.