## Slide 1: Polarized Ion Sources
Deepak Raparia

## Slide 2: Outlines
Introduction
Polarization techniques
Electron polarization
Nuclear polarization
Ionization
Polarized Sources H, D, 3He, 6Li
Conclusion

## Slide 3
The Spin of the Proton
Proton is composed of three “valence quarks”
Each quark carries spin ½
Proton carries spin ½ - two quarks with spin “up” and one with spin “down” would yield a net “up” spin of ½
However, experiments in the 1980’s revealed that the three valence quarks only contribute a few percent of the proton spin!
Some Fundamental Physics Questions
The Proton
in 1975
The Proton
in 2015
Proton in a nucleus

## Slide 4: Only Polarized Proton Collider
EBIS

## Slide 5: Electron Ion Collider

## Slide 6: Ion Polarization Techniques
Three-step process
First electron spin polarization
-Spin filter
- Optically pumped cell
(2) Electron spin transfer to nucleus
-RF transition
-Sona Transition
(3) Ionization to positive ot negative ions
-Electron beam, ECR ionizer
-Cs cell, Cs Beam
-Plasma ionizer
-Alkali vapor
-He cell

## Slide 7: Polarization: Nuclear Scattering
All the proton have spin with randomly distributed
To collect proton with same spin in a group > Polarized proton
E M. Hafner 1958
Unpolarized P 220 MeV, 0.3 𝝻A , scattered with Carbon 12
Highly polarized >90% 4 106 P /s,
higher momentum spread
and angular spread
Ref: E. M. Hafner, Physical Review, 111(1) , 1958

## Slide 8: Spin filter
Electron has much larger Magnetic moment than proton
In H atom proton feel very strong magnetic filed (~20T) due to electro
Thermal H-atom passed in an inhomogeneous magnetic field (4-pole or 6-pole)
atoms with spin up are driven towards the axis of magnet, atoms with spin down are defocused. The acceptance angle ⍺ only depends on atomic beam energy and pol-tip B-filed, and is independent of radius and length
Homogeneous dipole
Guide filed
Since the direction of the field pointing
in all direction , at the exit of magnet ,
average polarization od the beam is zero
Ifa homogeneous dipole filed
after the multipole magnet: adiabatic
change if the angular velocity of the
field seen by H-atom is low compered to
the Larmor Precession of the atom in
that filed
W. Haeberly . PSTP 2007, AIP Conf. Proc. 980,15, (2008)

## Slide 9: Optical Pumping
Absorption of polarized photon and subsequent spontaneous emission of unpolarized photon (optical pumping) Angular momentum of atom electron shell is changed during the process and atom takes on electron polarization
Direct optical pumping of H atom need 121.5 nm laser, unavailable
Polarized 3He atoms are obtained by exciting transitions 23 S1 → 23P0 by 1083 nm laser
Colegrove, Schearer
And Walters 1963

## Slide 10: Optically pump polarized ion source (OPPIS)
For optical pumping of rubidium atoms laser radiation with wavelength of 795 nm is used to excite transitions: 5S1/2 → 5P1/2
spontaneous decay 5S1/2 100% polarization Rb atom
Charge exchange collision Polarized electron transfer to H
Rb
H+
H0
Proton
source
Laser-795 nm
Optical pumping
Rb: NL(Rb) ~1014 cm-2
Rb+
Charge-exchange collisions: ~1014 cm2
Superconducting solenoid 2.5T
A. Zelenski, AIP Conf. Proc. 570, 179, (2000)

## Slide 11: Nuclear polarization
Week guide field
Strong guide field with RF (BNL pulse source)
Sona transition (BNL OPPIS)
(1) Pure spin state (↑↑), maxed state (↑↓)
Use week guide filed ( weak compared to the hyperfine interaction filed B=50.7 mT)
pure state remain completely polarized P=1
Mix state atoms preces one about other (↑↓+↓↑) P=0
Net polarization p=0.5 ,

## Slide 12: Nuclear Polarization: RF Transitions
Strong guide field changing slowly in space with RF Transition can achieve =1 or p=-1
Magnetic Moment M= *I , = gyromagnetic ratio, I angular moment
Torque =dI/dt= M x B0
𝞈0= - B0
Applied RF with frequency 𝞈0 and amplitude 2B1
(1) Such that B1 << 𝝳0 ;
2 𝝳0 Change in magnetic filed in traversal time
(2) Angular velocity of Beff smaller then Lamber precession
Beff.=B1
W. Haeberli, Ann. Rev. Nucl. Sci. 17, 1967

## Slide 13: Nuclear polarization: Sona transition
Change the quantization axis of an external magnetic field faster than the electron spin could follow its redirection through Larmor precision. This would lead to an inversion of occupation numbers in the pure states of the hyperfine splitting in which both, proton and electron spin, are aligned in the same direction, Example H atom
B>dB/dz
Off axis filed rotation as seen by atoms
Larmor Precision
Sona condition:
Ref: A. Kponou, etal, AIP Vol. 980, 2008
W. Haeberli, Ann. Rev. Nucl. Sci. 17, 1967
Karl Engels
New Insights into Sona Transitions

## Slide 14: Ionization
(1) By electron, Less efficient, ( 2e-4)
electron beam with solenoid filed improve ionization (1e-3)
Example : Preposed polarized H3-3 source at BNL
(2) Charge exchange ,
Example: BNL source 1982’s
(3) Resonant Charge Exchange
Example : INR Mosco ,D+ source
(4) Alkali Vapor
Example : OPPIS at BNL

## Slide 15: BNL pulse polarized H- source (1982)
Atomic Beam
Pulse Ground state atomic beam line with an RF Disassociator (pulse), Nozzle thermalized at 100 K
Sextupole for electron polarized beam
RF transition for polarization transfer to Nuclear Pulse to pulse basis
Density of H0 beam 2-3 1011 atoms /cm3
Charge Exchange
Surface ionization of cesium on a hot porous
Tungsten button , 30KeV 15 mA Cs+
Neutralized by cesium vapor (pulse)
6-10 particle mA,30 cm long
Charge exchange ionization
H↑ +Cs0 -> H- ↑+ Cs+
H- ↑ , 25 uA, 75% polarization,
emittance 0.065 pi cm mrad
500 𝜇s
J. Alessi , etal, “ A 25 uA Pulsed Polarized H- ion source, 6th internation Symp. On high energy Spin Physics, France, 9/12-19, 1984

## Slide 16: INR Polarized H/D Source Resonant Plasma Ionizer
Atomic beam:
RF Dissociator , cooled 20-80 K
Electron polarization: Sextupole Spin filter
Nuclear polarization: RF Transition Unit
Ref:A. Belov, AIP Conf. Proc. 980,209 (2008)
INR Moscow achieved 4 mA of polarized H- with > 90% polarization and D- current
up to 60 mA
Plasma guided by axial (plasma coil) and transverse (electromagnet) toward to neutralizer surface Plasma interact with neutralizer surface and reflect as neutral hot atom towards molybdenum converter surface. At converter hot atoms are converted to partially negative ion and injected into ionization region

## Slide 17: Polarized source for NICA ion collider (JINR)
Atomic beam,
RF dissociator pulse length 3 ms, 2 mm Pyrex channel , cool to 80K
For Hydrogen WFT and SET. +1 and -1
Deuterium MFT, WFT, and SET +1, _1, Tensor polarization +1, -2,
Charge exchange storage cell
Polarized D0 ↑ injected in storage cell and Hydrogen plasma Jet
generated by a plasma arc-discharge source
Charge exchange collision
D0↑ H+ -> D+ ↑ + D0
And proton
H0 ↑. + D+. -> H+ ↑ +D0
2016-2017: 6 mA D+ , 88% polarization

## Slide 18: Optically pumped Polarized Ions Source (OPPIS)
A. Zelenski, etal, AIP Conf. Proc. 980, 221 (2008)
OPPIS produces Polarized H- ion pulse current. 0.6 mA
81-85% polarization @200 MeV
Electron polarization : optical pumping
Nuclear polarization: Sona transition
Ionization:: Na vapor

## Slide 19: OPPIS Layout
D. Raparia, CAD Seminar 24/09/13
95%
60%
70%
8%
OPPIS: Six steps: (1) Atomic beam, FABS, (2) Ionization of atomic beam, He-Cell, (3) Rb-electron polarization, Rb-Cell, (4) Rb-electron transfer to H, Rb-cell (5) nuclear polarization, Sona Transition and (6) ionization, Na cell

## Slide 20: Optically –Pumped Rb- vapor Cell
Polarization Vs Rb-vapor thickness
Polarization vs. Magnetic field in Rb cell

## Slide 21: Sodium –Jet Ionizer Cell

## Slide 22: H- Current at 200 MeV
Operation of the OPPIS H- ion Source during the RHIC Run-2024
A. Cannovo

## Slide 23: Requirements to the 3He++ Source at BNL
Intensity ~ 2.5∙1011 3He++ ions in 20 us pulse ~5.0 mA-peak current
Maximum polarization > 80%
Compatibility with the operational EBIS for heavy ion physics.
Spin flip for every source pulse in the beam transport line.
3He polarization by optical pumping and metastability-exchange technique inside the EBIS in high (5.0T) magnetic field. No polarization losses in 3He+ state.
EBIS is used for efficient ionization and accumulation of polarized 3He++ ions to the full capacity of about (2.5-5.0)∙1011 , 3He++ ions.
J. Alessi, G. Atoian, E. Beebe, S. Ikeda, S. Kondrashev, J. Maxwell, M. Musgrave, R. Milner, M. Okamura, A. Poblaguev, D. Raparia, J. Ritter, A. Sukhanov, S. Trabocchi, N. B. Wuerfel, A. Zelenski,
Polarized 3He++ source is a part of the EBIS. The development of the polarized 3He ion source is being done as a collaboration between BNL and Massachusetts Institute of Technology (MIT).

## Slide 24
Principle of EBIS Operation
Radial trapping of ions by the space charge of the electron beam.
Axial trapping by applied electrostatic potentials at ends of trap.
The total charge of ions extracted per pulse is ~ (0.5 – 0.8) x ( number electrons in the trap ~1.0∙1012 )
Ion output per pulse is proportional to the trap length and electron current.
Ion charge state increases with increasing confinement time.
Output current pulse is independent of species or charge state!
10A, 10-20 keV
Notes: 24

## Slide 25: EEBIS
In the test Lab
At the site

## Slide 26: Optical Pumping and Probe Lasers Layout
Pumping laser
Probe laser, Toptica, DL-100, diode laser
Detector
WS6-200
wavemeter
Pumping laser-Keopsys 10 W 1083 nm- fiber laser

## Slide 27
Circular polarized
Laser light at 1083 nm

## Slide 28
3He-cell with filling and injection valves inside the EBIS SC Solenoid-1
Prepare the 3He gas for polarization by the purification system; Valve1-open/ Valve2-close
Polarize the 3He gas inside the glass-cell by a MEOP technique; Valve1-close/ Valve2-close
Continually control the polarization of the injected 3He gas by using the Optical Probe polarimeter
Inject a polarized 3He portions into drift tube (beam line) through the pulsed valve ( ~2-3*1012 atoms/pulse); Valve1-close/ Valve2-open
Ionize the polarized atoms of 3He by electron beam (~10 A).
3He-cell
3He Filling Valve1
3He Injection pulse Valve2
HV isolator
Drift tube (20-40 kV)
e-beam ~10A
To the purification system
Rf –discharge

## Slide 29: 3He-gas purification and filling system
Modified Cryo-pump for 3He
purification and storage
Vessel filled with charcoal granules
The pump also absorbs quite a significant amount of 3He gas (of about 100 scc).
The absorbed gas is released by the pump vessel heating ~20K.
This provides gas storage and supply for 3He-cell operation at the optimal pressure value (3-5 Torr).
The hydrogen Balmer-alpha line intesty at 656 nm is strongly reduced <0.4%. Relative to the 668 nm 3He line after 10 hours of RF discharge with the solation valve closed

## Slide 30
Polarization Measurements by the Probe Laser Absorption
Closed cell
Open cell
89% polarization in. sealed
3He cell at 3 Torr pressure
Polarization build-up time .
0-4 min: Valve open
5-27 min: valve closed
29 min: laser off and valve opened
(3 Torr valve closed)

## Slide 31: Gas Cell Testing at EBIS Test Lab
Progress On a Polarized 3He++ ion source at BNL
Noah Wuerfel 09/23

## Slide 32: Development of Polarized Lithium ion Source for EIC
This topic will be discussed on Monday 09/23 , 11:40 AM
By Chao Peng

## Slide 33: Polarized Ion Source 09/23 10:40 – 11:00
Karl Engels
New Insights into Sona Transitions
11:00 - 11:20
Antonino Cannavo
Operation of the OPPIS H⁻ Ion Source during the RHIC Run-2024
11:20 - 11:40
Noah Wuerfel
Progress on a Polarized 3He++ Ion Source at BNL
11:40 - 12:00
Chao Peng
Development of Polarized Lithium Sources for EIC

## Slide 34
Summary
Polarize ion source three steps
Electron polarization: Spin filtering, optical pumping
(2) Transfer to nucleus polarization : RF transition, Sona transition
(3) Ionization: electron collision , charge exchange, resonance plasma charge exchange, alkali vapor
BNL Polarized H- source(1982): 25 𝝻A, 75%
INR Polarized H- source with Resonant Plasma Ionizer: 4mA, 90%
NICA Polarized H+/D+ Source: 6mA D+, 88 %
BNL OPPIS (Pol. H-): 1.6 mA, P=85 % Reliable. Run unattended
BNL Polarized 3He: High polarization of He was achieved in the "open" cell in the high magnetic field. Final test for Cell cell is underway.
Will be world highest intensity pol. 3He source

## Slide 36: Relativistic Heavy Ion Collider (RHIC) world’s only polarized proton collider
Two superconducting storage rings
3.8km circumference
Energy up to 255GeV protons, or 100GeV/n gold
110 bunches/beam
Ion species from protons to uranium
60% proton polarization
Exceeded design luminosity by factor 44
6 interaction regions, 2 detectors
First high energy e-cooling
Very successful stochastic cooling for
In operation since 2001
EIC is based on existing RHIC facility

## Slide 37: Fast Atomic Beam Source

## Slide 38: He-Ionizer Cell with 3-grid Energy Separation System
Two functions of the new He-cell with pulsed valve:
Ionization of the injected neutral beam
Deceleration of the ionized part of the beam to separate from the no-ionized part
He-valve
Operating in high magnetic field ~1-3T
He-pulsed
valve
3-grid beam
Deceleration system
He-cell

## Slide 39: Extended EBIS for 3He++
The polarized 3He ion source will be mounted on the Solenoid-1.
The atoms of the 3He gas will be polarized by Metastability Exchange Optical Pumping (MEOP) technique and
After injected through a fast pulse valve in the ion trap region of the EBIS.
There the 3He ions will be trapped and bred to the 3He++ state.

## Slide 40: P/D Polarization Techniques
Three step Process: (1) electron polarization, (2) polarization transfer E-P,
(3) ionization positive or negative
A. Zelenski