## Slide 1
PSPT2024
Precision Moller Polarimetry in Hall A at Jefferson Lab
Donald Jones
for the Hall A Moller polarimetry team
Sept. 2024

## Slide 2: History of Moller polarimetry in Hall A
The Moller polarimeter in Hall A was installed in the late 1990s using polarized ferromagnetic foils (max polarization ~8%)
For the first decade tilted foil target was used
  Polarization measured with pickup coils.
  Early measurements having systematic errors >3% due to target polarization uncertainty
  With lots of effort systematics reduced to 1.7% for HAPPEX-III but still dominated by target polarization
~0.024T

## Slide 3: History of Moller polarimetry in Hall A
The Moller polarimeter in Hall A was installed in the late 1990s using polarized ferromagnetic foils (max polarization ~8%)
For the first decade tilted foil target was used
  Polarization measured with pickup coils.
  Early measurements having systematic errors >3% due to target polarization uncertainty
  With lots of effort systematics reduced to 1.7% for HAPPEX-III but still dominated by target polarization
In 2009 new 4T magnet installed to polarize Fe foils out of plane along beam direction
  Can achieve (in theory) full saturation
  Polarization for pure Fe foils out of plane known to 0.24% at saturation magnetization
  Reached 1.2% relative uncertainty during PREX-1
~0.24T

## Slide 4: History of Moller polarimetry in Hall A
The Moller polarimeter in Hall A was installed in the late 1990s using polarized ferromagnetic foils (max polarization ~8%)
For the first decade tilted foil target was used
  Polarization measured with pickup coils.
  Early measurements having systematic errors >3% due to target polarization uncertainty
  With lots of effort systematics reduced to 1.7% for HAPPEX-III but still dominated by target polarization
In 2009 new 4T magnet installed to polarize Fe foils out of plane along beam direction
  Now can achieve (in theory) full saturation
  Polarization for pure Fe foils out of plane known to 0.24% at saturation magnetization
  Reached 1.2% relative uncertainty during PREX-1
In 2016 a new 5T self-contained superconducting Helmholtz coil magnet installed with a rotatable target ladder
  Reached 0.85% systematic uncertainty for CREX

## Slide 5: History of Moller polarimetry in Hall A
The Moller polarimeter in Hall A was installed in the late 1990s using polarized ferromagnetic foils (max polarization ~8%)
For the first decade tilted foil target was used
  Polarization measured with pickup coils.
  Early measurements having systematic errors >3% due to target polarization uncertainty
  With lots of effort systematics reduced to 1.7% for HAPPEX-III but still dominated by target polarization
In 2009 new 4T magnet installed to polarize Fe foils out of plane along beam direction
  Now can achieve (in theory) full saturation
  Polarization for pure Fe foils out of plane known to 0.24% at saturation magnetization
  Reached 1.2% relative uncertainty during PREX-1
In 2016 a new 5T self-contained superconducting Helmholtz coil magnet installed with a rotatable target ladder
  Reached 0.85% systematic uncertainty for CREX
I will focus on efforts in Hall A to reach this level of accuracy.
Continuing on this trajectory:
MOLLER experiment (2025) and the SoLID (future) both in Hall A experimental program require polarimetry at the 0.4% level of accuracy

## Slide 6: Moller polarimetry in Hall A
Elastic ee scattering from a Fe foil polarized || beam
Low current dedicated measurement (~1 μA) experiments run at tens of μA
Parity conserving Moller asymmetry
Measured asymmetry
Learned a lot from PREX2/CREX (2019-2020) and GEn (2022-2023)
Key
systematics
(Foil)
(Foil)
Beam time measurements needed to reduce/constrain these

## Slide 7: Moller Azz + Levchuk
Azz is a function of center of mass scattering angle
Must be averaged across the detector acceptance i.e. comes from simulation
typical acceptance
Simulated event
distribution for
CREX experiment
Levchuk effect
Kinematic change to scattering angle (and thus Azz) from intrinsic motion of bound atomic target electrons
Inner unpolarized atomic electrons have higher intrinsic momenta  greater transverse momenta preferentially modify the trajectories of these unpolarized electrons modifying their acceptance probability
arXiv 2207.02150

## Slide 8: Moller Azz: two useful discoveries
Coincidence Rate
Simulated Azz
Levchuk Corr Azz
1. Our knowledge of spectrometer optics (field maps) is limited to several percent uncertainty, BUT simulation shows if we calibrate our settings relative to the rate maximum, we are highly insensitive to absolute knowledge of optics.
2. Limiting the vertical detector acceptance allows one to tune the Levchuk correction to nearly 0 AND create a large flat region of Azz.

## Slide 9: Levchuk correction improvement
Levchuk correction requires a model of the momentum distributions for polarized and unpolarized electrons in Fe
For past two decades this correction has been done using distributions from modified hydrogen wavefunctions (MH)
Data from CREX showed that this calculation predicted a 30% smaller “peak” than measured
Colleagues at Temple University suggested using a Hartree-Fock (HF) model (and provided the momentum distributions).
Exciting agreement!
arXiv 2207.02150

## Slide 10: Fe foil target polarization
In a recent publication we demonstrate using world data on saturation magnetization and on the fraction of magnetization from spin that electron polarization in Fe foils is known to 0.24%.
Difficult to improve.
Degree of saturation: two key things prevent reaching full saturation magnetization
Magnetic field not strong enough
  Difficult to magnetize out of plane
  Crystal imperfections and stresses/strains create stubborn domain walls (ideal crystal fully saturated at 2.2T)
Imperfect alignment of foil (not taut, wrinkles, not precisely normal to magnetic field)
Stoner-Wohlfarth model of magnetization vs field
arXiv 2203.11238
arXiv 2203.11238

## Slide 11: Fe foil target polarization
Ideal: demonstrate saturation precisely using an asymmetry vs. field scan
Previous scans/data have demonstrated
Apparent agreement with Stoner-Wohlfarth model and ability to align foils to within a fraction of a degree of normal using asymmetry vs foil angle scans
Results with two foils apparently aligned to within agree at 1.24σ on saturation polarization.
Wrinkle in foil during PREX2 showed 1% lower polarization
Also, loosely mounted foils may contribute to interpretation difficulties as the foil angle is not completely correlated with the ladder angle
Working on techniques to ensure foils mounted taut and flat and perpendicular to field

## Slide 12: Compton/Moller comparison during CREX
Compton average:
Moller measurements on average percentage points) higher than Compton (0.85% relative error)
Polarization with Compton and Moller combined: (0.33% relative uncertainty!)

## Slide 13: Current dependence
There is a class of uncertainties which I call “extrapolation uncertainties” which arise not from imprecision in the polarization measurements but instead from the fact that the Moller measurements are taken at different conditions (beam current, energy, source laser polarization and phase, photocathode QE etc.) and time from the main experiment.
The dominant extrapolation uncertainty is the current dependence: does the polarization measured at 1uA match that of the main experiment at 50uA or greater.
This was 0.42% during PREX-2 and 0.5% during CREX. Needs to be <0.1% during MOLLER.
Uncertainty bounded via studies using “beat frequency technique” from 2007 will likely be resurrected.
  Laser frequency set just off the 499MHz of the accelerator cavities such that it beats on 499 MHz so only Nth bunch actually goes through
https://journals.aps.org/prab/pdf/10.1103/PhysRevSTAB.10.053502

## Slide 14: Improvements before MOLLER
Adding GEM tracking planes in drift region between dipole and detector to verify models for multiple scattering, radiative corrections and Levchuk effect
New FADC-based DAQ under development with ability to count events, integrate yields and produce energy spectra
New tungsten collimator in front of detector will limit acceptance and virtually eliminate sensitivity to the Levchuk correction
Utilizing a new CAEN detector emulator to directly measure dead time and understand accidentals in the DAQ
No showstoppers at this point keeping us from reaching proposed 0.4% uncertainty

## Slide 15: Recent esoteric issues: accidentals (too many events)
Accidentals (keep at or below 1%)
Measure accidentals using a copy of the left detector signal delayed by 120 ns which we use to form a coincidence with the un-delayed right detector
Left events
time
coinc
left
single
Right events
  True accidentals happen when uncorrelated right and left detector events happen at nearly the same time such that they lie inside the coincidence time window. True accidentals add extraneous events.
  Measured accidentals between a single uncorrelated right electron and a left coincidence electron (or vice versa) should not be counted unless this class could spuriously add coincidence events to the un-delayed signals. NOTE. This would mean that a right or left electron would have to be counted twice: once with an uncorrelated electron and once with its true coincidence electron.
  Utilizing a detector emulator that can produce coincidence and singles events Poisson-distributed in time to help us understand. Ongoing studies to figure out correct way of doing this correction.
  Because we keep accidental rates and corrections small, we expect our past quoted uncertainties to cover this: (Eg. Acc. correction CREX 0.21+/-0.04% PREX-2 0.12+/-0.02%)
Recently we have realized this is incorrect
  Delayed line includes singles with no left/right correlated pair and true Moller coincident events
accid
Left delayed
accid

## Slide 16: Recent esoteric issues: dead time (too few events)
Dead time: coincidence events lost because they occur too close in time for the DAQ to measure them both as
discrete events
We currently measure dead time using LEDs that flash simultaneously in right and left operating during beam on data taking. Measure fraction of LED flashes lost.
Dead time measurements with detector emulator show much higher dead time with LED measurements. Working to understand how to determine this correction accurately
Dead time corrections have typically been small with 100% uncertainty quoted on the corrections (Eg CREX 0.15+/-015%) so not expected to significantly affect past measurements.
Cartoon of dead time with parameters of existing Moller DAQ in Hall A

## Slide 17: Conclusions
  Stringent requirements from future experiments MOLLER and SoLID in Hall A at Jefferson Lab are pushing us towards a new level of accuracy in electron beam polarimetry with both Compton and Moller polarimeters aiming to attain 0.4% uncertainty
  Significant progress has been made in understanding the Moller polarimetry and while only 0.85% uncertainty has been reached thus far, that is in large part due to the fact greater precision wasn’t required. Significant reductions can be achieved with a measurement program with beam time allocation.
  Each source of systematic error is being studied and minimized or eliminated.
Thank you