## Slide 1: Compton polarimetry for SuperKEKB
D. Charlet1, T. Ishibashi2, H. Kaji2, A. Martens1, M. Masuzawa2, F. Mawas1*, Y. Peinaud1, D. Zhou2, F. Zomer1
1: IJCLab; 2: KEK; *: PhD student

## Slide 2: SuperKEKB polarization upgrade
Only for electrons
Beam transport of polarized beam
Top-up injection at nominal energy
Spin rotators (combined function magnets from BNL)
Preservation of polarization
See Belle II upgrade framework CDR arXiv:2406.19421; M. Roney talk at ICJHEP 2024
Compton polarimeter

## Slide 3: Compton scattering
Berestskii & Lfshitz QED textbook
The Compton cross-section averaged over scattered particles spins:
Differential cross-section
Electron beam polarization independent
Electron beam polarization dependent
Linear laser polarisation: nuisance parameter to minimize and keep under control
Transverse electron beam polarisation: intervenes as an asymmetry in the transverse plane
⚠️ But small opening angle of scattered particles:
  Transverse polarimetry is more difficult to implement wrt longitudinal polarimetry
What we want to measure
Expected polarization orientation at Compton IP longitudinal and parallel to that of Belle II IP !

## Slide 4: Compton polarimetry
Polarization dependent term generates a left-right asymmetry function of
Landau-Lifshitz QED book paragaphs 86 and 87
Use green (~515nm) laser
Concentrate on measurement of scattered photon
Electron measurement difficult (integration, quads in the beam line)

## Slide 5: Mechanical system integration
450 mm
910 mm
Crossing Angle Horizontal : 8 deg
Crossing Angle Vertical : 4 deg
+ some neutron + lead shielding around electronics to be located below the table
+ some lead shielding around the table to protect the laser
D. Charlet et al., 2023 JINST 18 P10014

## Slide 6: Beam impedance (longitudinal)
Zhou, Ishibashi

## Slide 7: Beam impedance (vertical)
Zhou, Ishibashi

## Slide 8: Laser system
Box with rough temperature control
Box with rough temperature control
design based on past experience
Elliptic beam can be delivered with cylindrical lenses/mirrors (not planned for a first step)
Possibility to synchronize the laser on the RF clock of the accelerator using the WhiteRabbit+IDROGEN technology under experimental investigation at IJCLab
Key aspect: remote operation of the system that will be located in the tunnel
250MHz
Possibility to insert mirror for laser polarization calibration
D. Charlet et al., 2023 JINST 18 P10014

## Slide 9: WhiteRabbit/IDROGEN synchronisation
RMS time jitter <500fs above 30Hz
Demo with laser expected soon
4km optical link does not affect noise performance
 Possible low impact/cost integration of laser frequency control
Master Oscillator (510MHz/51)
4km fibre link
IDROGEN, high speed DAQ
Low noise WR node
WhiteRabbit
Sept’24
June’24
D. Charlet et al., https://cds.cern.ch/record/2893372?ln=en
H. Kaji, D. Charlet

## Slide 10: Photon detector integration
‘minor’ modifications of beam pipe modification (validated for impedance)
BreadBoard 450x450 mm2
Xray out : 210 µrad
≈ Ø6 mm at 14,5 meters
Beam pipe at ~1m from ground
Electronics can be located and shielded on ground below scintillator +PMT

## Slide 11: Single channel photon detector
Basic elements
  a VERY FAST radhard scintillating crystal  BaF2
    Need to filter out the slow component  UV optical filters
  a PMT with low transit time dispersion  commercially available (hamamatsu for instance)
  Bunch/bunch measurement
Energy measurement
Currently ‘waiting’ for funding
External collaborators welcome
…
2500 histograms

## Slide 12: Conceptual acquisition chain
BaF2
PMT
Optical filter
FPGA
IDROGEN board
White Rabbit node
Analog Front-end
+ ADC (>=10bits)
Every 4ns
2500 histograms
Fast treatment: fit
Accelerator RF
1rst Bunch identifier
To remote storage (10MB/min)
Reduced data
To online monitoring
clock
Update program, constants

## Slide 13: Expected performance
Statistical precision: 1%/bunch every 5min
NB: fit can be performed in 1min for the 2500 bunches assuming few nuisance parameters known and fixed (calibration can occur from time to time)
Fast simulation
D. Charlet et al., 2023 JINST 18 P10014

## Slide 14: Expected performance
Systematic uncertainty related to beam transport from Compton IP to Belle 2 IP need to be evaluated  misalignements in beam transport
D. Charlet et al., 2023 JINST 18 P10014

## Slide 15: Conclusion & Prospects
SuperKEKB upgrade with electron beam polarization is a challenging project
  Existing machine  minimize modifications
  Goal for ‘transparency’ of upgrade
Longitudinal Compton polarimeter can be inserted in the existing lattice with no impact on impedance
  Bunch/bunch
  1% precision /bunch every 5min
Design of laser system, pipe modifications and detector concept available
Synchronization tests ongoing (use of WhiteRabbit technology)
Detector development will start as soon as funding is available
Open to new collaborators

## Slide 16: Expected beam polarization at Compton polarimeter
Snowmass document: arXiv:2205.12847
Location of Compton IP
Spin orientation longitudinal
And // to that of Belle II IP !
Elliptical beam size

## Slide 17: Integration
BLA2LE
Laser/e-beam interaction point
Photon detection
Spin rotators planned to be installed far away from Belle II IP
 a nice place before BLA2LE where polarization is longitudinal and enough free space
 polarimeter data is representative of polarization at Belle II IP (up to magnet mislalignments)

## Slide 18: Conceptual design
A summary of the conceptual studies performed for the laser system and the scattered photon detector has been published recently
A summary of the results is inserted in the current CDR draft

## Slide 19: Beam sizes and spin projection in z
BLA2LE
BLX2LE.2
BLY1LE.1/2
55% of the IP Sz
99% of the IP Sz
85% of the IP Sz
Using Y. Peng data, https://indico.belle2.org/event/5306/

## Slide 20: Transverse polarimetry at HERA
Exactly the operation that was done at HERA TPOL a long time ago.
Notoriously a difficult task but ‘do-able’
Eased by implementing a nicely vertically segmented electron detector.
Requires detailed simulations
Requires some transverse sampling (not easy for photons)
https://indico.cern.ch/event/1181966/contributions/5046178/attachments/2512013/4318517/220905_tpol.pdf

## Slide 21: Choice of scintillating material
Basic elements
  a VERY FAST radhard scintillating crystal  BaF2, the only solution ?
  Filter for the slow component
  a PMT with low transit time dispersion (AND solar blind ?)  commercially available ?
  Associated electronics

## Slide 22: Slow component filtering
From Saint-Gobain datasheet.
Stefan Diehl et al 2015 J. Phys.: Conf. Ser. 587 012044
Solar blind photocathodes (CsTe) only reduce the. Slow component such that is amounts about 50% of the final light yield
Long tail  pile-up
Requires subtraction (in average), but fluctuations remain  spoil resolution
Use UV optical filters insteadcommercial products exist for instace at 185nm +- 20nm (FWHM)
Y doped BaF2 being investigated

## Slide 23: PMT
Main requirements: fast (low rise time, low transfer time spread) and not blind to UV.