## Slide 1: Polarized Positrons at Ce+BAF
Concept of Ce+BAF injector
Development of high-power targets
Design of CW NC capture cavity
Beam and spin tracking simulations
Andriy Ushakov (Jefferson Lab)
on behalf of the Ce+BAF Working Group
Work supported by the U.S. Department of Energy Office of Nuclear Physics under contract DE-AC05-06OR23177 and Office of High Energy Physics US-Japan Science & Technology Cooperative Program

## Slide 2: Acknowledgments
We would like to acknowledge members of the Ce+BAF Working Group, the Jefferson Lab Positron Working Group, the DOE industry partner Xelera, members of the DOE US-Japan HEP Collaboration, and collaborators at Universities and National Labs which contribute to the positron R&D effort.
T. Abe, J. Benesch, A. Bogacz, L. Cardman, J. Conway, S. Covrig, P. Degtiarenko, Y. Enomoto, S. Gessner, P. Ghoshal, S. Gopinath, J. Grames, J. Gubeli, C. Gulliford, S. Habet, C. Hernandez-Garcia, D. Higinbotham,
A. Hofler, R. Kazimi, M. Kostin, F. Lin, V. Kostroun, V. Lizarraga-Rubio, K. Mahler, Y. Morikawa, S. Nagaitsev,
E. Nanni, S. Ogur, M. Poelker, N. Raut, B. Rimmer, Y. Roblin, A. Seryi, K. Smolenski, M. Spata, R. Suleiman,
A. Sy, N. Taylor, D. Turner, C. Valerio-Lizarraga, E. Voutier, M. Yamamoto, S. Zhang

## Slide 3: 12 GeV Ce+BAF : Polarized Electron or Polarized Positron Beams
Machine Parameter | Electrons | Positrons
Hall Multiplicity | 4 | 1 or 2
Energy (ABC/D) | 11/12 GeV | 11/12 GeV
Beam Repetition | 249.5/499 MHz | 249.5/499 MHz
Duty Factor | 100% cw | 100% cw
Unpolarized Intensity | 170 µA | > 1 µA
Polarized Intensity | 170 µA | > 50 nA
Beam Polarization | > 85% | > 60%
Fast/Slow Helicity Reversal | 1920 Hz/Yes | 1920 Hz/Yes

## Slide 4: Positron Experiments Approved by JLab Program Advisory Committee (PAC)
NUMBER | TITLE | CONTACT PERSON | HALL | DAYS REQUESTED | DAYS AWARDED | SCIENTIFIC RATING | PAC DECISION
PR12+23-002 | Beam charge asymmetries for deeply virtual Compton scattering on the proton at CLAS12 | Eric Voutier IJCLab, Orsay, France | B | 100 | 100 | A- | C1
PR12+23-003 | Measurement of deep inelastic scattering from nuclei with electron and positron beams to constrain the impact of Coulomb corrections in DIS | Dave Gaskell Jefferson Lab | C | 9.3 | 9.3 | A- | C1
PR12+24-005 | A dark photon search with a JLab positron beam | Bogdan Wojtsekhowski Jefferson Lab | B | 55 | 55 | A- | C1
PR12+23-006 | Deeply virtual Compton scattering using a positron beam in Hall C | Carlos Munoz Camacho IJCLab, Orsay, France | C | 137 | 137 | A- | C1
PR12+23-008 | A direct measurement of hard two-photon exchange with electrons and positrons at CLAS12 | Axel Schmidt George Washington University | B | 55 | 55 | A | C1
PR12+23-012 | A measurement of two-photon exchange in unpolarized elastic positron-proton and electron-proton scattering | Michael Nycz University of Virginia | C | 56 | 56 | A- | C1
C1 = Conditionally Approved with Technical Review by the Lab
Approved 210 days Hall B & 202 days in Hall C for 357 total PAC days
(PAC day = two calendar day)

## Slide 5: Selection of e+ Energy at Exit of 4 mm W Target for 120 MeV e‒ and Pz = 1
e+ Yield [e+/ e-] and Figure-of-Merit (FoM) vs Energy
, where is e+ yield and is e+ long. polarization
For 120 MeV drive e‒ beam, if e+ captured with energy spread < 0.05 and opening (divergence) angle < 5°:
Max is for and
Captured e+ yield is relatively low (~5·10-5-10-3 e+/e‒) → high current polarized e‒ source is required (1 mA, up to 90% pol.)
e+ Long. Polarization vs Energy at Target Exit
Calculations results of e+ yield, polarization and FOM for different thicknesses of tungsten targets and liquid metal targets (GaInSn, PbBi) and at different energies of drive e ‒ beams:
V. Lizarraga-Rubio et al., PSTP24 presentation
Notes: S. Habet et al., “Characterization and optimization of polarized and unpolarized positron production”, Tech. Rep. JLAB-ACC-23-3794, Feb. 2023. doi:10.48550/arXiv.2401.04484

## Slide 6: Positron Injector and Transport Line at CEBAF
New Beamline to CEBAF Tunnel
New e+ Injector at LERF
123 MeV e+ Beam Injected to NL
New Transport Line along SL and West Arc
CEBAF Polarized Electron Injector
123 MeV e+
LERF
LERF – Low Energy Recirculation Facility
J. Grames et al., IPAC’23, MOPL152
East Arc
West Arc
North Linac
South Linac

## Slide 7: Pol. e+ Injector Critical Risk Areas mA e‒ Source, High Power Targets, Capture Cavity
Conceptual Development
Improve design of e+ injector
Develop pCDR
High current e‒ source (<10 mA @ 10 MeV)
Up to 90% polarization
Long life time
Liquid Metal Target Test Area
Liquid Metal Targets are developed by
Xelera Research LLC DOE SBIR Phase2, Oct 2024 – Sep 2026
Prototype of GaInSn Test Stand
GaInSn Jet
N. Taylor et al., IPAC’24, TUPC83
GaInSn target will be tested at JLab with up to 10 mA @ 10 MeV e‒ beam
Development of liquid PbBi target and test with 1mA @ 120 MeV e‒ is planned
Two target concepts are considered
1) Solid high-Z target (i.e. tungsten)  next slide 2) Liquid metal targets

## Slide 8: Concept of Tungsten Target, CFD Simulations, Prototype Testing (S. Covrig)
Focused on assessing with CFD solid high-Z targets, mostly W, for e+ production at CEBAF:
A rotating target (<10 Hz, >30 cm diameter) could take 20 kW beam power with Tmax < 1000 K
e- beam has a Gaussian profile with σ ~ 1 ÷ 3 mm
The beam hits the W target on a circle with radius 18 cm
The W target rotates at 2 Hz and the water flow is 0.3 kg/s, water pressure loss is 1.5 psi
Full time-dependent CFD simulations implemented
No studies on target material lifetime
Started looking at the target engineering, radiological issues, shielding
Max T of Tungsten vs Time
Max T of Cooling Water vs Time
Tungsten Target Test
DOE HEP Advanced Positron Concepts, U.S.-Japan Collaboration (SLAC/JLab/KEK)
DOE FY2024 R&D for Next Generation Nuclear Physics Accelerator Facilities

## Slide 9: Conceptual Development and Design of CW NC Capture Cavity (S. Wang)
Working plan
Year 1:
Define solenoid and cavity specifications
Generate preliminary cavity fields
Integrate with target geometry
Perform radiation simulations
Thermal analysis
Preliminary e+ and e- beam tracking
Year 2:
Iterate and optimize magnet and cavity design
Explore beam loading and magnetization effects
Find optimal parameters of capture system with an adjustable energy selection band
At the early design stage, the goal is not to produce a single design but to provide a range of options
Capture Cavity Design Strategy
Balance and Tradeoff
Large cavity iris radius is expected, >15mm, to accommodate more e+ transversely → lowers the shunt impedance
As high as possible E field gradient is desired to manipulate the incoming e+ beam longitudinally → requires high shunt impedance
Type A: simpler structure, larger cell-to-cell coupling
Type B: typically higher shunt impedance
Capture cavity set for CW Ce+BAF was obtained for further capture section design
Studied influence of solenoid magnetic field to the e+ transportation before entering cavity
Performed initial studies of the action of cavity field on 20, 60 MeV positrons
S. Wang et al., IPAC’24, MOPC51

## Slide 10: Ce+BAF: Simulations of CW Positron Beam Generation, Capture and Acceleration
Main Solenoid
Absorbers
Target
Cavity
Bucking Solenoid
Target and Capture Magnets
Cu Coil
W10Cu
W10Cu
TZM
Target
Cu Cavity*
Steel
Cu Coil
Compensation
Solenoid
Power Deposited by 1 mA e‒ Beam @ 120 MeV
e+ Energy Spectrum at Target Exit and Captured e+
Scheme of Positron Generation, Capture, Selection of e+ Energy Band and Acceleration to 123 MeV
1 mA 120 MeV
A. Ushakov et al., IPAC’24, MOPC54

## Slide 11: Spin Tracking in Geant4 and General Particle Tracer (GPT)
At Exit of C100
At Exit of Col. #1
At Exit of Capture Cavity
At Target Exit

## Slide 12: Design of Low-Dispersion e+ Transfer Line from LERF to North Linac
Z [m]
SL to ARC Twiss matchings
ARC to NL Transfer needs Twiss matching and Low D and Beta optics
Polished DBA Arc low dispersion and low beta optics, fitting layout
LERF matched to the new SL
The new SL with the half # quads
Needs fine-tuning according to the crossover
X [m]
LERF Transfer Line
(LTL)
South Transfer Line
(STL)
West Transfer Line
(WTL)
The Crossover
LERF
S. Ogur, J. Benesch, Y. Roblin, D. Turner
Tunnel Walls

## Slide 13: Measurement of CEBAF Acceptance with Degraded e‒ Beam (A. Sy)
Measurement of CEBAF Acceptance is a JLab Laboratory Directed Research & Development (LDRD) project
Goal: determine acceptance of CEBAF by increasing beam emittance and energy spread through multiple scattering in thin carbon foils and using two apertures to define the maximum transverse emittance. The energy spread can be additionally increased by adjusting field phase of accelerator cavities.
Degrader location: downstream injector booster, 6.24 MeV e‒
Targets: carbon foils with thicknesses of 1 µm, 5 µm and 10 µm
Degrader apertures:
  1st aperture: 2 mm and 6 mm diameter
  2nd aperture: 8 mm and 16 mm diameter
  14.9 cm distance from target to 1st aperture and 27.3 cm between apertures
Degrader components have been built and installed in CEBAF injector
Experiments will be performed soon
Target Ladder
Aperture 1
Aperture 2
Corrector
Corrector
Solenoid
Helicity Coil
A. Sy et al., IPAC’24, MOPC53
Aperture 1

## Slide 14: Summary
Continue working on design of Ce+BAF injector and critical risk areas:
  Optimization of positron capture system
  Beam/spin tracking simulations for Ce+BAF injector at LERF and beam tracking from LERF to North Linac (and later to the experimental halls)
  mA polarized electron source
  High power solid and liquid targets
  CW capture cavities