## Slide 1: Developments of polarized 7LiD target system for spin-dependent EMC effect experiments at CLAS12
D. Akers, J. Brock, C. Carlin, G. Dezern,
C. Flanagan, D. Griffith, M. Hoegerl,
P. Hood, C. Keith, J. Maxwell, S. Madlock,
D. Meekins (JLab Target Group)
P. Dobrenz, X. Wei (Jlab Hall B)
J. Creel, B. Mastracci (JLab Engineering
Division)
P. Dobrenz, M. Poelker, E. Pozdeyev
(JLab Accelerator Division)
Tsuneo Kageya
Thomas Jefferson National Accelerator Facility (JLab)
Related talks: J. Brock, “A Solid Polarized Target Development Facility at Jefferson Lab.” (Tue.)
X. Wei, “Preparation at Jefferson Lab. for Spin Polarized Fusion Program” (Thurs.)

## Slide 2
Quark’s momentum distributions accessed by DIS: different for light and heavy nuclei ➾ Not anticipated results
From
U. Landgraf (NMC Collaboration.),
Nucl. Phys. A527, 123C (1991)
Compare for F2(A) with F2(D) ( A: Fe, Ca and Cu, D: deuteron )
F2: unpolarized
structure function
F2 (A)
F2 (D)
XBj
If NO EMC effects
EMC effects
(European Muon
Collaboration)

## Slide 3
(J. Arrington (Hall C),
Phys. Rev. C 104, 065203 (2021))
7LI : between 3He and 9Be
EMC effects observed
for light nuclei
3He
D
9Be
D

## Slide 4
Polarized (Spin-Dependent) EMC effects
Proposed experiments (Hall B, (PR12-14-001)) for Spin dependent EMC effects:
- measure and compare spin dependent structure function g1
from bound proton (p in 7) with free proton (three H in N3)
at same experimental setup
Polarized EMC effect could be
more enhanced than
unpolarized Theoretical
predictions
An example of theoretical prediction for polarized EMC for 7Li
(I. C. Clo ̈et etal. ADP-06-05/T636)
x

## Slide 5
Side view of the polarized target installed in Hall B. A few elements of the CLAS12
spectrometer are shown.
1. Longitudinally Polarized Solid Target for Spin dependent EMC effect at Hall B
Use the same setup of target system as Run Group C (Run in 2022-23).
DNP at 5 Tesla (Solenoid) and 1 K (4He evaporation cryostat)
Use Longitudinally polarized e- beams (11 GeV)
(P. Pandey etal, Proc. of 25th Int.
Symposium of Spin Physics. 2023, 211)

## Slide 6
2. Advantages of using polarized solid 7LiD and NH3 targets
for Spin dependent EMC effects
No so much data for 7LiD; use data from 7LiH, 6LiD and 6LiH
Solid 6LiD has been used as polarized targets in the past experiments:
its performances are rather well known, 7LiD is supposed to perform similarly.
a. Low mass nuclei like 7Li; detailed structure of nuclei is well known
b. 7LiD and NH3 can be highly polarized with DNP
c. 7LiD and NH3 are highly radiation resistant on electron beams
d. Reasonable Dilution Factor

## Slide 7
a. Low mass nuclei like 7Li; detailed structure of nuclei is well known
Structure of 7Li in a simple shell model picture
Neutrons
Protons
7Li: p (∽ 87 % of Li spin)1,2 + n + n (0.04 %)1,2 + 4He (zero pol.)
(From proposal
PR12-14-001)
( 1 : Shell model; S. Cohen, D. Kurath, Nucl. Phys. 73 (1965) 1.
2: Quantum Monte Carlo calculations; B.S. Pudliner etal., Phys. Rev. C 56 (1997) 1720)

## Slide 8
b. 7LiD and NH3 can be highly polarized with DNP
Polarization past records; as high as (at 5 Tesla and 1K on beam line)
* 7Li (in 7LiH) : 60 %
(S. Bueltzmann etal. Nucl. Instr. and Meth. A 425 (1999) 23)
* H (in NH3) : 90 %
(from past experiments at JLab)

## Slide 9
c. Radiation resistance for 6LiD (No data for 7LiD nor 7LiH)
Irradiation (180 K) dose of 2.0x1017 e-/cm2
During E155 experiments at SLAC, 50 GeV e beam
Max pol. at 5x1015 e-/cm2. : about 5 times larger than ND3
Expect similar radiation resistance for 7LiD

## Slide 10
d. Acceptable dilution factor for 7LiD and NH3
Ratio (7LiD)
Ratio (NH3)
Other nuclei candidates with a single valence polarized proton;
11B (5p, 6n), 15N (7p, 8n), 19F(9p, 10n) and 27Al (13p, 14n), for example.
Heavier nuclei: smaller dilution factor.
Number of polarizable bound proton
Total number of nucleons
=
1
9
Number of polarizable free protons
Total number of nucleons
=
3
17
= 0.11
= 0.18

## Slide 11
3. Three processes of producing and testing polarized target
materials of 7LiD
I. Fabrications of a disc from 7LiD powder
II. Irradiation of 7LiD on CEBAF injector beam line
III. Polarization measurements at 5 Tesla and 1 K

## Slide 12
I. Fabrications of a disc from 7LiD powder
* 7LiD powder is commercially available on the following conditions
- Isotopic purity of Lithium, 7Li : ∽ 93 % and 6Li : ∽ 7 %
- Isotopic purity of Deuterium, D : ∽ 98 % and H : ∽ 2 %
- Chemical purity, 5 % of impurities (LiOD, LiOD-H2O, Li2CO2 …)
(Analysis of 7LiH powder (from a commercial company) by a group
of LLNL (C.G. Bustillos etal., Annals of Nuclear Energy 185 (2023) 109709 ))
* Requesting service work to Y12 to fabricate disc (2 cm diameter and 2 mm thick)

## Slide 13
II. Irradiation of 7LiD on CEBAF injector beam line (JLab) : New
e- beam
10 MeV and uA
of electron beams
Beam dump
Faraday Cup
(Dose
measurements)
NH3 and ND3 had been irradiated at NIST with collaboration of UVA target group in the past
Irradiation
Cryostat
BPM
Raster Magnet

## Slide 14
II. Irradiation Cryostat (detail)
Veritically
Rastered e- beam
Variable Temperature Irradiation cryostat (under design & construction)
3 K He coolant from Central He Liquefier
Temperature controlled by heater
Irradiate 7LiD and NH3 at different
temperatures
Target materials
inserted and uninserted vertically
Solid 7LiD/NH3
Rotating 1 turn/min

## Slide 15
II. Irradiation conditions for 7LiD (higher polarization and shorter polarization building Time)
Group | Tirrad (K) | Ee- (MeV) | Dose ( X 1017 e/cm2 ) | PLi(%) | TBuild | T(K) | B(Tesla) | Year & note
Bonn1 | 180 | 20 | 1 |  | 50 min | 1 | 2.5 | 1995 (7LiH)
 |  |  |  | 15 | 8 min |  |  | Ad. Irad. 1K 1015 e-
Group | Tirrad (K) | Ee- (MeV) | Dose ( X 1017 e/cm2 ) | PLi(%) | TBuild | T(K) | B(Tesla) | Year & note
Bonn1 | 180 | 20 | 1 |  | 50 min | 1 | 2.5 | 1995 (7LiH)
 |  |  |  | 15 | 8 min |  |  | Ad. Irad. 1K 1015 e-
Bochum3 | 190 | 20 | 0.1 | -17.8 | 220 min | 1 | 2.5 | 2001 (6LiD)
 | 140 |  | 1 | -17.9 | 60 min | 1 | 2.5 | Warm RT
(3) 6LiD at room temperature for 10 min; as od as on standard and may shorten Tbuild
∗ Irradiate NH3 at 80 K (standard irradiation temperature) and 3 K (low temperature as (1)) in prior to 11 GeV beam.
NH3 materials will be supplied by Univ. New Hampshire group.
Standard
Additional irradiations at Lower Temperature (3K): can increase Pmax and shorten Tbuild
Some noteworthy past records for 7LiH & 6LiD (different irradiation temperatures and option)
SLAC2 | 183 | 30 | 1.3 – 4.5 | 60 |  | 1 | 5 | 1999 (7LiH)
SLAC2 |  | 30 | 1.3 – 4.5 |  |  | 1 | 5 | 1999 (7LiH)
(2) 7Li in 7LiD is expected to polarize as high as 60 % at 5 Tesla (may optimize dose)
(1)
(2)
(3)

## Slide 16
1. S. Goertz etal., Nuclear Instruments and Methods in Physics Research A 356 (1995) 20
2. S. Bueltmann etal. Nuclear Instruments and Methods in Physics Research A 425 (1999) 23
3. A. Meier, 6LiD for the polarized target of the COMPASS experiment, PhD. Thesis, Ruhr-University Bochum 2001

## Slide 17
III. DNP cryostat with 5 Tesla and 1 Kelvin (under design and construction)
Vertical 1 K cryostat
(Refer J. Brock’s presentation)
Cryomagnetics Cryo-Free 5 T Warm Bore Magnet

## Slide 18
Summary
We are developing polarized 7LiD target system for Spin dependent EMC effect experiments at Hall B.
2. For this purpose, designing and constructing irradiation and polarizing
cryostats.
Plan to irradiate and polarize 7LiD target materials in the middle of 2025.
Test materials and optimize parameters to obtain higher polarization
and shorter building up time of polarization on the beamline.

## Slide 19
Backup Slides

## Slide 20
II. Irradiation of 7LiD (higher polarization and shorter polarization building Time)
Summary of some past records; Tirrad, PolMax, TimeBuild and polarizing conditions for 7LiH
Group | Tirrad(K) | Ee- (MeV) | Dose (e/cm2 ) | PLi(%) | PH(%) | BuildT | T(K) | B(Tesla) | Year
Abragam1 | 77 | 3 | 2 x 10 17 | 80 | 95 | 50 h | 0.2 | 6.5 | 1978
Saclay2 | 183 | 300-650 | 1 | 50 | 70 | 24 h | 0.2 – 0.4 | 5 | 1985-87
 | 183 | 300-650 | 2 | 47 | 56 | 6 h | 0.2 - 0.4 | 2.5 | 1985-87
PSI3 | 180 | 3 | 2 | 90 |  |  | 0.2 - 0.4 | 2.5 | 1990
Saclay4 | 184 | 30 | 0.5 | 31 | 42 | 3 h | 0.2 – 0.4 | 2.5 | 1992
Bonn5 | 180 | 20 | 1 |  |  | 50 min | 1 | 2.5 | 1995
 |  |  |  | 15 |  | 8 min |  |  | Ad. Irad. 1K 1015 e-
SLAC6 | 183 | 30 | 1.3 – 4.5 | 60 |  |  | 1 | 5 | 1999
Group | Tirrad(K) | Ee- (MeV) | Dose (e/cm2 ) | PLi(%) | PH(%) | BuildT | T(K) | B(Tesla) | Year
Abragam1 | 77 | 3 | 2 x 10 17 | 80 | 95 | 50 h | 0.2 | 6.5 | 1978
Saclay2 | 183 | 300-650 | 1 | 50 | 70 | 24 h | 0.2 – 0.4 | 5 | 1985-87
 | 183 | 300-650 | 2 | 47 | 56 | 6 h | 0.2 - 0.4 | 2.5 | 1985-87
PSI3 | 180 | 3 | 2 | 90 |  |  | 0.2 - 0.4 | 2.5 | 1990
Saclay4 |  | 30 | 0.5 | 31 | 42 | 3 h | 0.2 – 0.4 | 2.5 | 1992
Bonn5 | 180 | 20 | 1 |  |  | 50 min | 1 | 2.5 | 1995
 |  |  |  | 15 |  | 8 min |  |  | Ad. Irad. 1K 1015 e-
SLAC6 |  | 30 | 1.3 – 4.5 |  |  |  | 1 | 5 | 1999
Bochum7 | 190 |  | 0.1 | -17.8 | -18.6 | 220 min | 1 | 2.5 | 2001
 | 140 |  | 1 | -17.9 | -18.7 | 60 min | 1 | 2.5 | Warm RT
Optional procedure: after irradiation keep 6LiD at room temperature for 10 min.

## Slide 21
1. A. Abragam etal., J. Physique Let. 41 (1980) L-309
2. P. Chaumette etal. Proc. of 8th Int. Symposium of High Energy Spin Physics. 1988, 1275
3. S. Mango etal. Proc. of 9th Int. Symposium of High Energy Spin Physics, 1990, 320
4. J.J. Jarmer etal., Proc. Of 10th International Symposium on High Energy Spin Physics, 1992, 363
5. S. Goertz etal., Nuclear Instruments and Methods in Physics Research A 356 (1995) 20
6. S. Bueltmann etal. Nuclear Instruments and Methods in Physics Research A 425 (1999) 23
7. A.Meier, 6LiD for the polarized target of the COMPASS experiment, PhD. Thesis, Ruhr-University Bochum 2001