## Slide 1: Preparations at JLab for a Spin Polarized Fusion Program The Polarized 7LiD Program for Polarized Fusion Experiments at the DIII-D Tokamak
Xiangdong Wei
9/26/2024

## Slide 2: Jefferson Lab Fusion Program Motivations
Power!
Clean Power!!
Sustainable Clean Power!!!
(with least environmental impact)
Fossil Fuels, Fission, Hydroelectric, Wind Turbine, Solar, Geothermal, Ocean Current, ……
and finally
Fusion!!!
DOE core mission objectives:
… to promote innovative research in clean energy sources, …
Ignition Approaches:
ICF (inertial), MCF (magnetic)...

## Slide 3: Jefferson Lab Fusion Program Channels and Facilities
The intended fuel:
    D + T  + n
    and
Most research Tokamaks ever built (~30 in operation today) have focused on D+D reactions.
Jump in scale towards a fusion power reactor: the International Thermonuclear Experimental Reactor (ITER) will pave the way to fusion power.
Polarized fuels could enhance the cross section by up to 50%, & the power and Q by 75%, without changing the plasma conditions.
The cost is ~V-plasma x B2.
20~40 billion dollars.
DIII-D (USA)
Best instrumented most diagnostics
20m3, 2.1T, Q<<1
JET (UK)
Only one runs tritium
90m3, 3.8T, Q~2/3
ITER (France)
½ GW reactor
700m3, 5.3T, Q>10
(under construction)
Q ≡ Pout/Pin

## Slide 4: Jefferson Lab Fusion Program SPF Collaboration
Jefferson Lab
(Polarized D Fuel)
X. Wei, P. Dobrenz, D. Williams,…
plus 2 incoming postdocs from UVA
University of Virginia
(Polarized 3He Fuel)
G. W. Miller, A. M. Sandorfi, X. Zheng,…
Oak Ridge National Lab
(Polarized Fuels Delivery) L. Baylor, S. Meitner, …
University of California, Irvine
(Run Preparations and Diagnostics)
W. Heidbrink, …
Ultimate Goal:
Run D + 3He   + at DIII-D in FY28-29
First phase, Spin Polarized Nuclei for Injection into DIII-D, has been funded by DOE FES.

## Slide 5: Jefferson Lab Fusion Program Polarized D Fuel at JLab
Fabrication
Irradiation
Polarization
Extraction
Commission
D + 3He   + p
The life cycle of a polarized 7LiD pellet
Shape, size, density…
DF, pol chamber, pellet loader,
Wave & NMR
Pellet extractor, (integrated with DF and injection gun)
Final installation at DIII-D tokamak
DIII-D,
Particles detection,
Data analysis
beamline, cryostat
Wave
Funded for FY24 & FY25
Subsequent
renewals
(for FY26-29)
Storage
LN2 cryostat
Integration
Integrate pellet polarizer with (ORNL built) injection gun)

## Slide 6: Jefferson Lab Fusion Program The Program
  Ultimate Goal:
  Running D + 3He   + p in DIII-D tokamak with polarized fuels to test polarization survivability.
  Approach:
  FY24-25 Equipment preparation, Fuel pellet production, 7LiD Polarizer designs, Prototype, …
  FY26-27 Equipment production, System integration, Polarized fuel production, …
  FY28-29 Commissioning, Running spin-polarized fusion at DIII-D.
  JLab’s Short Term focus:
    Preparing 7LiD pellets.
    Irradiating 7LiD pellets with eBeams to create paramagnetic centers for DNP process.
    Preparing mWave and NMR systems for polarization production and monitoring.
    Designing a (commercial dilution refrigerator based) DNP polarizer.
    Building a prototype Polarization Chamber with pellet handling system.

## Slide 7: Jefferson Lab Fusion Program The Unique Challenges
The advantages:
JLab Target Group operates DNP polarized targets routinely.
Polarized LiD targets have been used successfully – eg. CERN COMPASS exp.
JLab PAC approved experiments require polarized 7LiD targets.
The challenges:
Precision engineering----Uniform shape and r to deliver ~1020 deuterons/pellet.
Cold transporting----Pellet dispensed into 4K tokamak injector with holding field.
Impact resistance----Survives ~20m subsonic injection journey.
Requirements for the polarizer--High cooling-power commercial DF with ~7T magnet.
    A pellet manipulation mechanism for loading/dispensing.
    A polarizing chamber with NMR coils (V~0.06cc) and tuned waveguide.
    Properly anchor components to achieve low operating temp (~100mK with mWave ON).
    A 77K entrance interface and a 4K exit interface.

## Slide 8: Jefferson Lab Fusion Program Pellets Design
To consistently deliver ~1020 deuterons/shot, the shape, density and edges of the pellet must be well controlled and smoothly fit inside injection gun, for achieving high injection speed.
7LiD is chemically unstable, and caustic; must be handled in an inert gas environment.
7LiD pellets can be:
  fused from powder;
  casted;
  machined from a solid chunk;
  purchased from a vender – preferred; discussions in progress
7LiD Pellet size: cylindrical, =1.5mm, L=3.0mm.
Totally ~200 7LiD pellets will be used for developing, testing and running the SPF experiment.

## Slide 9: Jefferson Lab Fusion Program Doping 7LiD Pellets
Beamline
The 7LiD pellets must be irradiated with electron beams to create paramagnetic centers for the DNP process.
The pellets will be irradiated at ~185K with ~10mA electron beams (~9MeV) for several hours and stored/transported under 77K.
CEBAF Injector will be used for the irradiations.
The irradiation beamline has been built by Injector Group and is currently under vacuum.

## Slide 10: Jefferson Lab Fusion Program Dosing 7LiD Pellets
Irradiation Cryostat
The 7LiD pellets will be irradiated at ~185K with ~10mA electron beams (~9MeV) for several hours to create ~2x1017 e- /cm2 for the DNP process and stored/transported under 77K. (See Kageya’s talk tomorrow)
The Irradiation Cryostat has been designed by the Target Group and the Fusion Group. Together, we will build it in FY25.
The irradiation results will be validated by measuring achievable polarization with DNP at the onsite Polarized Target Development Lab. (See Brock’s talk on Tuesday)

## Slide 11: Jefferson Lab Fusion Program Beamline Simulation
Beamline Simulations (samples, UITF runs)
Goals of the Beamline Simulation:
Guide the beamline commissioning;
Guide the target material irradiation runs by predicting the missing electrons with the dump current and viewers data.

## Slide 12: Jefferson Lab Fusion Program NMR coils & Polarizing Chamber
Sized for 7LiD pellet
Sized for NP target
As an example, a standard Commercial Dilution Refrigerator with a 7.5T Magnet can be purchased.
Credit: Bluefors
Designing the Polarization Chamber to fit in a commercial DF
(for phase-II funding)

## Slide 13: Jefferson Lab Fusion Program Other Places
  While JLab is preparing the polarized D fuel:
  UVA will build the 3He polarizer.
  ORNL will design/build the cold pellet injection gun with continuous magnetic field.
  UC-I will study fusion product detection and plasma diagnostics.
  All components will be shipped to DIII-D in 2027.
3He
7LiD
4K Injector
77K Injector
• Simulations follow secondary reactions to
estimate background yields:
3He + D a α + p (Q = +18.3 MeV) E(p) ~ 15 MeV
9 D + D a 3He+n (Q = + 3.3 MeV)
9 D + D a T + p (Q = + 4.0 MeV) E(p) ~ 3 MeV
9 D + T a α + n (Q = +17.6 MeV)
15 MeV proton orbits are unconfined
Measure at wall to infer polarization.
parallel spins  large
anti-parallel spins  large

## Slide 14: Jefferson Lab Fusion Program The Ultimate Goal
Run D + 3He --> a + p in FY28

## Slide 15: Jefferson Lab Fusion Program Schedule
Expecting to run the D + 3He test within 5-6 years. ​
​
Work at JLab for the current funding cycle:​
FY24: Preparing 7LiD pellets, designing/Building Irradiation Cryostat and Beamline.​
FY25: Testing Irradiation Cryostat, Producing Irradiated 7LiD pellets.​
In subsequent funding cycles:​
FY26-27: Finishing subsystem constructions and then production test.​
FY28-29: System integration and final assembly.​
  Polarized D + 3He fusion at DIII-D!!!