## Slide 1: A Possible Spin Rotator for Ce+BAF
Fanglei Lin
Jlab Positron Working Group Meeting
2024.01.31

## Slide 2: A Spin Rotator for Ce+BAF
In 2021
  Explored a combination of low energy spin rotator and high energy spin rotator
    Low energy spin rotator for rotation from longitudinal to vertical spin direction in the energy range of 10-123 MeV
    High energy spin rotator for rotation from vertical to longitudinal spin direction before the experimental halls
  Pros:
    Suppress polarization diffusion due to the beam energy spread with vertical spin direction in CEBAF
    Provide both transverse and longitudinal polarizations in an energy range for all experimental halls
  Cons:
    More instruments
    Layout changes
    Costly
Work done by Amy Sy
Detail in the backup slides

## Slide 3: A Spin Rotator for Ce+BAF
In 2022, we realized that :
  High energy rotators are complicated additions to the end stations
  Prefer low energy spin rotator with "Wien-like" functionality
  Space should be constrained by LERF
  Cost should be minimized
=> Lead us to explore other options

## Slide 4: Conditions
Positron polarization needs to be in the horizontal plan (longitudinal or/and radial directions)
Positron spin precession in the CEBAF is same as electron spin precession
Spin manipulation will only be in the low energies of 123 MeV
  Solenoid is preferable, considering its effective spin rotation () at energies and negligible effect on the orbit excursion
  Dipole is needed to help to produce a desired spin rotation axis

## Slide 5: Layout and Spin Rotation
Spin rotation: ~50.20
Spin rotation: 50.20
Spin rotation from the rotator

## Slide 6: One Possible Solution
Yu.N. Filatov et al., Eur. Phys. J.C, 81:986 (2021)
Side view
vertical
longitudinal
: spin rotation around the radial axis ( due to a radial dipole field )
: spin rotation around the longitudinal axis ( due to a longitudinal solenoid field)

## Slide 7: Background
Two-component spinor is used
Spinor matrix (2x2):
for solenoids
for radial dipole fields (bending beams vertically)
for vertical dipole fields (bending beams horizontally)
Pauli matrices:

## Slide 8: Matrices
vertical
longitudinal
Spin rotation angle:
Spin rotation axis:

## Slide 9: Rotation Angle and Axis
Spin rotation angle:
Spin rotation axis
In our case, we would like to have , therefore it is MUST
    Spin rotation
    Spin rotation
    and
: radial
: vertical
: longitudinal

## Slide 10: Possible Solutions
Spin rotation from 1st dipole
  at 123 MeV
Spin rotation from 1st solenoid
  at 123 MeV
 | (spin rotation) | (dipole bending) | (spin rotation) |  | 
Solenoid | 900 |  |  |  | 
Dipole |  | 50 | 1.40 | 5.60 | 1
 |  | 100 | 2.80 | 11.20 | 1
 |  | 450 | 12.60 | 50.30 | 1
 |  | 80.60 | 22.50 | 900 | 1
Solenoid | 900 |  |  |  | 
Dipole |  | 50 | 1.40 | 5.60 | 1
 |  | 100 | 2.80 | 11.20 | 1
 |  | 450 | 12.60 | 50.30 | 1
 |  | 80.60 | 22.50 | 900 | 1
Orbit is NOT fixed

## Slide 11
 |  | BL (T.m) for | (spin rot. from ) | (total spin rot. from the rotator)
Dipole | 50 | 0.036 | 1.40 | 5.60
 | 100 | 0.072 | 2.80 | 11.20
 | 450 | 0.322 | 12.60 | 50.30
 | 80.60 | 0.577 | 22.50 | 900
Dipole | 50 | 0.036 | 1.40 | 5.60
 | 100 | 0.072 | 2.80 | 11.20
 | 450 | 0.322 | 12.60 | 50.30
 | 80.60 | 0.577 | 22.50 | 900

## Slide 12: Possible R&D for Development of Spin Rotator in Ce+BAF
FY24
  Explore a spin rotator design suitable for 123 MeV e-/e+ beams.
  Integrate the spin rotator into the injection lattice.
  Perform particle tracking simulations to verify the desired spin rotation in the injector.
  Optimize and finalize the spin rotator design.
FY25
  Extend the spin rotator design for a beam energy of 5 to 10 MeV (apply to e- beam).
  Define the magnet specifications through tracking simulations.
  Set up the prototype test at LERF or CEBAF.
  Demonstrate the spin rotation experimentally and publish a paper.

## Slide 13
Back Up

## Slide 14
x

## Slide 15
x

## Slide 16: eRHIC-like Spin Rotator for low energy
It is a ring !
spin
solenoid
spin
spin
dipole
Top view
eRHIC
Solenoid and dipole fields
Works for one energy

## Slide 17: JLEIC-like Spin Rotator for high energy
Decoupling sessions may not be needed in Ce+BAF
Needed length ~30 m
Interleaved solenoid and dipole fields
Works for an energy range with

## Slide 18
End of Hall A lattice
8 dipoles bending 34.3/8 = 4.2875 degrees each
Each dipole 3 m in length
Quads 0.3 m in length
10s of m from last dipole to Hall A target
*Try constructing spin rotator with last three dipoles, and 5 and 10 m long solenoids

## Slide 19: Spin Rotations from
Solenoid
Dipole
Solenoids are preferable at low beam energies due to their negligible effect on the orbit excursion, while dipoles are effective at high beam energies from their energy-independent spin precession.

## Slide 20: Low energy positron spin rotator
= 90 degrees, = 90 degrees
Energies lower than ~ 110 MeV need dipole bends > 360 degrees for complete spin rotation, i.e. a ring
Solenoid integral field strengths are reasonable
Energy [MeV] | 10 | 125 | 220
 | 0.023 | 0.284 | 0.499
[deg] | 3965.9 | 317.3 | 180.3
[T-m] | 0.052 | 0.656 | 1.154
Energy [MeV] | 10 | 125 | 220
 | 0.023 | 0.284 | 0.499
 | 3965.9 | 317.3 | 180.3
 | 0.052 | 0.656 | 1.154

## Slide 21: Low energy positron spin rotator – some options
A small ring could be built to let positrons circulate for the right spin precession for complete spin rotation
  Ring geometry will dictate which positron energies can be injected with vertical polarization
180 degree arc from LERF to SL could be used for the dipole component of the spin rotator for 220 MeV positrons
  Complete the spin rotation with a solenoid
  Decelerate to desired positron energy

## Slide 22: Spin Rotation Along the Beam Lines
Spin rotation: 20.40 – 28.60 at 50 – 70 MeV
Spin rotation: 50.20
Spin rotation: 50.20
Spin rotation: 50.20
Total spin rotation angles: 171.20 - 179.30 before NL.
It seems not much additional spin rotation is needed to have longitudinal e+ before NL, unless spin dancing and radial polarization are expected.