## Slide 1: Continuous Electron Beam Accelerator Facility Overview
Yves Roblin
Center for Advanced Studies of Accelerator

## Slide 2: Jefferson Lab Overview
Core Competencies
  Nuclear Physics Research
  SRF Technology Leadership
  Polarized Electron Sources
  Cryogenics Research and Development
  Accelerator Physics and Diagnostics Development

## Slide 3: Jefferson Lab Overview
Quick Facts
  180 M$ annual operating budget
  759 Full Time Employees
  >1600 Active Users
  Produces ~1/3 of US PhDs in Nuclear Physics
  169 acres and 80 buildings and trailers

## Slide 4: Cut and Cover Construction
East Arc Tunnel
LINAC Tunnel
CEBAF Tunnel ~30 feet underground
Sits on an ancient Sea Floor called the Yorktown Formation
Composed largely of over-consolidated sand, clay and sea shells

## Slide 5: CEBAF Overview
1213 MeV
3393 MeV
5573 MeV
7747 MeV
9922 MeV
2303 MeV
12051MeV
4483 MeV
6660 MeV
8836 MeV
11006 MeV
11006 MeV

## Slide 6: CEBAF Injector
Source provides ~90% polarized electrons with variable bunch charge
Interleaved micro-bunch structure at 499 MHz or 249.5 MHz depending on physics program
Bunching cavities to control longitudinal size of beam
Faraday cups to measure beam current
Aperture A1 and A2 to collimate the beam and minimize transverse phase space extent
Chopper system to independently control beam intensity for each experiment
Capture RF system to transition to relativistic energy
18 SRF cavities accelerate beam to 123 MeV beam for injection into the North Linac
Spectrometers to measure energy of the electron beam
~150 m

## Slide 7: Why using a CW beam system ?
SRF technology allows for more efficient acceleration (higher gradients,not limited by resistive effects)
Better control of energy spread and stability. CEBAF is world leader in producing near chromatic beam (<2e-4 de/e at lower energy) perfect for hypernuclear experiments (tens of KeV resolution in the spectrometers)
Low bunch charge with high rep rate reduces pile up (one event per bunch or less), yet still enable measuring very small cross-sections
Narrow coincidence windows reduce accidentals.

## Slide 8: CEBAF Beam Structure
Accelerator tuning is always done using low average power beam.
The 250 ms pulse width at 60 Hz provides a 1.5% duty cycle.
Nominal pulse height is 4 mA.
Beam power is 720 W for a 12 GeV beam at this duty factor.
The 4 ms trailing pulse is for measuring linac BPM orbits and linac arrival time.
3 interleaved 499 MHz bunch trains injected into 1497 MHz Linacs
4-Hall operations uses 249.5 MHz bunch trains

## Slide 9: Chopping System
Chopper #1 RF Cavity (499 MHz)
Chopper #2 RF Cavity (499 MHz)
Lens
Lens
B
C
A/D
Master Slit
Beam
Beam
Beam
Beam
Beam
Beam
Beam
Beam
Beam
Beam
Beam
Beam
Beam
Beam
Beam
Beam
Beam
Beam
Beam
Beam
Beam
Beam
Beam

## Slide 10: North and South Linacs
North and South Linac Optics:
  9.6 m FODO channel with cryomodules between quadrupoles.
  Beam injected with large spot size and damps as the beam is accelerated.
  Skew quads in lattice around C20 and C50 cryomodules to correct for skew moment in cavity fields.
  C100s have no skew moment.
  Designed to provide 1090 MeV for a 12 GeV CEBAF

## Slide 11: Average Cavity Gradient
There are 418 SRF cavities in CEBAF

## Slide 12: Spreaders and Recombiners
Spreader/Recombiner layout:
  Vertically achromatic system designed to accept broad range of multi-pass input parameters for recirculation transport.
  Final step heights in ½ meter increments above lowest pass.
  Quads in step control the vertical dispersion.
  Recombiner is mirror-symmetric to the Spreader.
West Recombiner
West Spreader

## Slide 13: CEBAF Recirculation Arcs
Arc layout:
  Sixteen dipoles for Arc 1 and Arc 2 and thirty-two dipoles for Arc 3-10.
  The recirculating Pi bends are at a radius of 80 m.
  Each Arc has 32 quadrupole girders grouped in 4 families to control achromaticity, momentum compaction and the betatron tune.
  Beam Position Monitors at the entrance of quadrupoles.
  Horizontal and vertical correctors throughout to control the beam orbit.
West Arc Dipoles
Arc Quadrupole Girders

## Slide 14: 1st and 2nd Recirculation Arcs
Arc 1/2 Optics:
  Segment begins at start of the Spreader and ends at the exit of the Recombiner.
  Matching section in Spreader for matching the beam to the Arc.
  Matching section in Recombiner for matching to the Linac.
  Quads in vertical steps are used to null the vertical dispersion.
  Quads near peaks of dispersion function within the Arc are used to null the horizontal dispersion and control M56.
  Enhanced horizontal dispersion in Arcs 1/2 provide better resolution for energy monitoring.
Matching Section
Matching Section
Vertical Dispersion Knobs
Vertical Dispersion Knobs
Horizontal
Dispersion Knobs

## Slide 15: Higher Energy Arcs
Arc 3-10 Optics
  The design optics for the upper Arcs is represented below.
  Matching section in Spreader for matching the beam to the Arc.
  Matching section in Recombiner for matching to the Linac.
  Quads in vertical steps are used to null the vertical dispersion.
  Quads near peaks of dispersion function within the Arc are used to null the horizontal dispersion and control M56.
  Amplitude of vertical dispersion peaks go down with pass count due to the smaller elevation change.
Matching Section
Matching Section
Vertical Dispersion Knobs
Vertical Dispersion Knobs
Horizontal
Dispersion Knobs
Insertable
Dump

## Slide 16: Extraction Region
1213 MeV
3393 MeV
5573 MeV
7747 MeV
9922 MeV
2303 MeV
12051MeV
4483 MeV
6660 MeV
8836 MeV
11006 MeV
11006 MeV

## Slide 17: Extraction System
  Overall configuration:
    Horizontal extraction systems at 500 MHz for 1st through 4th pass
    Vertical extraction system at 500 MHz for 5th pass
    New horizontal extraction system at 750 MHz for 5th pass
Extraction Elevation View
Pass 1
Pass 2
Pass 4
Pass 3
Pass 5
West Arc Beamlines

## Slide 18
B
C
B
A
A
B
A
C
B
A
C
B
A
C
B
A
C
B
A
C
B
A
C
B
A
C
B
A
C
B
A
C
C
B
A
C
B
A
C
C
B
A
C
B
A
C
B
A
C
B
A
C
B
A
C
C
B
A
C
B
A
C
B
A
C
B
A
C
B
A
C
C
B
A
C
B
A
C
B
A
C
B
A
C
B
A
C
C
B
A
C
B
A
C
B
A
C
B
A
C
B
A
C
C
B
A
C
B
A
C
B
A
C
B
A
C
B
A
C
C
B
A
C
B
A
C
B
A
C
B
A
C
B
A
C
C
B
A
C
B
A
C
B
A
C
B
A
C
B
A
C
C
B
A
C
B
A
C
B
A
C
B
A
C
B
A
C
C
B
A
C
B
A
C
B
A
C
B
A
C
B
A
C
B
A
C
B
A
C
B
A
C
C
B
A
C
B
A
C
C
B
A
C
B
A
C
B
A
C
B
A
C
B
A
C
Accelerator
Frequency
1500 MHz
RF Separator Cavity
500 MHz
Beam to Halls
Recirculated
Beams
Separator frequency is 1/3 of the fundamental frequency
Beam
Turn on RF separator
RF Separation – 1st through 4th Pass
Beams begin to separate
B
B
B
B
B
B
B
A
A
A
A
A
A
A
C
C
C
C
C
C
C
Hall Lasers
Hall A: 500 MHz
Hall C: 500 MHz
Hall B: 500 MHz

## Slide 19
Accelerator
Frequency
1500 MHz
RF Separator Cavity
500 MHz
To Halls A,B,C
Beam
Halls A,B,C 5th Pass Vertical Separation
A
B
C
B
C
A
B
A
B
C
A
B
C
A
C
A
B
B
A
C
A

## Slide 20: 12 GeV Beam at CEBAF vs. Ce+BAF
Machine Parameter | Electrons | Positrons
Hall Multiplicity | 4 | 1 or more
Max. Energy (ABC/D) | 11/12 GeV | 11/12 GeV
Beam Repetition | 249.5/499 MHz | 249.5/499/1497 MHz
Duty Factor | 100% cw | 100% cw
Unpolarized Intensity | 170 mA** | > 1 mA
Polarized Intensity | 170 mA** | > 50 nA
Beam Polarization | > 85% | > 60%
** Total beam power at Jefferson Lab is limited to 1.1 MW with a max. of 0.9 MW to individual high power dumps.
Notes: Slides 4 and 5 are basically what we told pac51 (and the users proposing to pac51) we were aiming for.
The key point is we are not going to get to very high currents. And polarization is even lower.
Hall B clearly rocks as they basically get polarized positions at their nominal current.
> Signs are ~ signs
One hall is easy. Multiple halls will be a challenge. Right now it is a three year program of single hall running.
1499 is one hall get best CW

## Slide 21
The FFA@CEBAF Collaboration
R. M. Bodenstein, S.A. Bogacz, A.M. Coxe, K.E. Deitrick, B.R. Gamage, R. Kazimi, D. Khan, E.A. Nissen, K.E. Price, Y.R. Roblin, R. Ruber, T. Satogata, A. Seryi, Jefferson Lab
J.S. Berg, S.J. Brooks, D. Trbojevic, Brookhaven National Lab
V.S. Morozov, Oak Ridge National Lab
G.H. Hoffstaetter, Cornell University

## Slide 22: CEBAF FFA Upgrade – Baseline under Study
  While last energy upgrade was achieved by adding additional cavities, there is no more room for cavities in existing footprint (stay with 1.1 GeV per linac)
  So, increasing number of recirculation passes has been considered, keeping in mind very limited room in the arcs for additional passes
  Remove the highest recirculation pass (Arc 9 & A) and replace them with two compact FFA arcs including time-of-flight chicanes (TOF)
  New 650 MeV recirculating injector
  Recirculate 4 + 6.5 times to get to 22 GeV
Pass Arithmetic: 5 -1 + 6.5 = 10.5
TOF
TOF
650 MeV
Enabling Technology:
Novel permanent magnets, -like used for power and cost savings

## Slide 23: Overview
Current baseline: 650 MeV inj + 4-pass CEBAF + 6.5-pass FFA
FFA Arc Architecture – -style
  Non-scaling FFA based on high-gradient permanent magnets
  Compact merger to control orbits, beta functions and dispersion at arc ends
Multi-pass linac optics
  650 MeV injector upgrade
  Strongly focusing triplet lattice periodic optics for lower passes
Modified CEBAF ‘switchyard’, Arcs 1-8 and TOF correction ‘splitters’
Synchrotron radiation impact on beam quality, mitigations
Summary, Outlook

## Slide 24: Non Scaling FFA Arc - Compact FODO Cell
Large momentum acceptance FFA cell, configured with combined function magnets capable of transporting six beams with energies spanning a factor of two
Arc composed of 75 cells, Lcell = 3.15 m
Closely spaced orbits for all six beams (~ 4 cm)
Low betas (~ a few m)
Extremally low dispersions (a few cm) - Virtue of combined function FFA magnets
orbits
dispersions
beta functions

## Slide 25: Permanent Magnet Design
Very compact compared to conventional electro magnets
Allows for accommodating 6 additional passes in CEBAF tunnel
Provides power and cost savings
Concept successfully tested at
Open mid-plane geometry
13 cm
12 cm
Focusing Magnet BF
GF= -41.13 T/m
LQF= 1.67 m
BF= -0.812 T
Defocusing Magnet BD
GD= 43.44 T/m
LBD= 1.24 m
BD= -0.593 T
13 cm
12 cm

## Slide 26: Prototype Magnet
Prototype open-midplane BF magnet successfully built and evaluated for mechanical integrity
>1.5 Tesla measured in good field region
Field accuracy of
Testing magnetic materials for radiation resilience at CEBAF - LDRD project started Oct. 1, 2023

## Slide 27
Stephen Brooks

## Slide 28: FFA Arc to Straight – Compact Merger
Breaking cell symmetry by altering (length, bend) of a few magnets to merge different energy orbits at arc ends.
Simultaneously, the dispersion and its derivative are suppressed at arc ends.
Furthermore, small beta functions (~5 m) need to be matched to higher-bets of the linacs (~90 m).
This simplifies switchyard and reduces its functionality to pathlength and momentum compaction adjustment.

## Slide 29
Injector Upgrade - 650 MeV Recirculating Injector
With the present 123 MeV injector, the difference in the first and final pass energies in the North Linac is too large (1:175) to effectively control the beam.
650 MeV recirculating injector (3-pass) based on LERF will allow a manageable difference in energies (1:33)

## Slide 30
Recirculating Injector Based on LERF (3-pass)
C-75
C-75
C-75
436 MeV
10 MeV + 3 × 3 × 71 MeV = 650 MeV
10 MeV

## Slide 31
Recirculating Injector Based on LERF (3-pass)
C-75
C-75
C-75
436 MeV
10 MeV + 3 × 3 × 71 MeV = 650 MeV
10 MeV
C-75
C-75
C-75
10 MeV + 3 × 3 × 71 MeV = 650 MeV
New arc
New arc
650 MeV

## Slide 32
243.507
0
60
0
0
BETA_X&Y[m]
BETA_X
BETA_Y
DISP_X
DISP_Y
243.507
0
30
0
0
BETA_X&Y[m]
BETA_X
BETA_Y
DISP_X
DISP_Y
pass 4
pass 1
7.25 GeV
0.65 GeV
Triplet Cells, phase advance: 1500 per cell
Multi-pass Linac Optics (11 passes, 1:33 Energy Ratio)
Present FODO linac offers periodic optics only for the lowest energy pass with large beta beating for higher passes (beta ~1000 m), which is not compatible with small betas (~5 m) in the FFA arcs.
Replacing FODO (alternating singlets) with alternating triplets – more uniform beam envelope

## Slide 33
284.877
0
240
0
5
0
BETA_X&Y[m]
BETA_X
BETA_Y
DISP_X
DISP_Y
pass 10
20.5 GeV
Transition to weakly focusing ‘Beta Beat’ Linac Optics for FFA Passes
.
.
.
11.6 GeV
pass 6
Deviate from optics periodicity  Induce and optimize beat in linacs  Reasonably small ’s at both ends of each linac at the expense of increase in maximum inside the linacs, ’s adjusted to nearly zero as favored by FFA matching  Greatly relaxed matching requirements
284.877
0
180
0
5
0
BETA_X&Y[m]
BETA_X
BETA_Y
DISP_X
DISP_Y

## Slide 34: Modified Switchyard to Accommodate Six FFA Passes
pass 1
pass 2
pass 3
pass 4
FFA passes 5-10
FFA passes 5-10

## Slide 35: Energy loss, Emittance dilution and Energy spread
  Doubling the energy, while staying within current CEBAF footprint, makes the synchrotron radiation effects of paramount importance.
  Quantum nature of a ‘recoil’ effect on electrons due to photon emission makes significant impact on both the transverse and longitudinal beam dynamics, leading to cumulative emittance growth (transverse and longitudinal).
Energy loss
Emittance dilution
Natural energy spread
  Cumulative emittance dilution (transverse and longitudinal) at 22 GeV (4 CEBAF + 6 FFA passes)
Projected value from the Spr/Rec contribution
Maximize , minimize H

## Slide 36: Summary
Present Baseline (1.1 GeV per linac):
  650 MeV Recirculating Injector (additional three C-75 cryomodules)
  Recirculate 4 passes with the current CEBAF
  Plus Additional 6 passes via a single FFA: 10 – 22 GeV
Non Scaling FFA Arc Architecture configured with compact FODO cells
  Beta and dispersion matching to the linacs through cell-by-cell variation (length, bend)
  Open mid-plane permanent magnet design: B-field ≤ 1 T, Gradient ≤ 50 T/m
Synchrotron Radiation impact on beam quality:
  Net transverse normalized emittance:
  Net natural energy spread: 1.5×10-3
  Net synchrotron radiated energy: 1 GeV
at 22 GeV, b = 20 m → s = 175 microns
at 22 GeV → DE = 33 MeV

## Slide 37
Thanks for your attention!
22 GeV CEBAF FFA Energy Upgrade