## Slide 1: Particle identification performance studies with pfRICH simulations
Youqi Song (youqi.song@yale.edu)
EIC User Group Early Career Workshop
Bethelehem, PA
07/22/2024

## Slide 2
Overview of pfRICH
pfRICH
“electromagnetic shock wave”
Competing species | Separation range [GeV]
vs hadrons () | ~0.2 to ~2.5
vs | ~2.0 to ~7.0
Competing species | Separation range [GeV]
 | ~0.2 to ~2.5
 | ~2.0 to ~7.0
pfRICH (proximity-focusing Ring Imaging CHerenkov)
  Crucial for PID in e-going direction in
    Excellent separation power up to 7 GeV:
    Cherenkov radiation angle , is related to particle’s speed and medium’s refractive index
  pfRICH also has potential application for global timing
Notes: Mention what is omega
Cherenkov bullet point

## Slide 3
Path of a Cherenkov photon
Aerogel
  “Radiator”: Cherenkov photons produced here
  2.5 cm thick, 42 tiles
    Optimize angle resolution & number of photons
Acrylic layer
  Filters out photons with wavelength < 300 nm
    Minimize dependency on
Vessel
  Encloses a 40 cm long “expansion volume”: Photons travel through here
    Large gap improves angle resolution
Sensor plane
  Detects the photons and amplifies the signals
  68 HRPPD (High Rate Picosecond Photo Detector) sensors
Multiple sources of Cherenkov photons. Aerogel photons are used for PID (today’s focus)
from HRPPD window
from expansion volume
[Fig 7.3 (a), CDR]
[Fig 1.3, CDR]
Notes: Preet’s talk on mirrors: https://indico.jlab.org/event/855/contributions/14991/
Don’t talk too much about sub-bullets
N for aerogel, careful with what is said
Schematic
overall

## Slide 4
Study pfRICH performance with standalone software https://github.com/eic/pfRICH
E.g., “imaging” part of the HRPPD sensor plane
“Imaging” sensor plane
1000 single-particle events, GeV,
Notes: Look at extremely low p LUT. Do particles reach them or radiate

## Slide 5
Study pfRICH performance with standalone software https://github.com/eic/pfRICH
“Imaging” sensor plane
Check other features of setup
  “Pyramid” mirrors help reconstruct photons lost in gaps between HRPPD tiles
Missing half ring due to gap in aerogel wall

## Slide 6
Mean ~ 12
1000 single-particle events for each value,
Mean higher for higher
  Expected from
  , where is a constant dependent on detector geometry
Number of tracks
Periodic efficiency drops due to aerogel support structure
Efficiency vs azimuthal angle

## Slide 7
From Cherenkov angle to PID
Theoretical expectation
Reconstruction result from simulation
[Fig 4.8 (a), CDR]
→ Systematically determine particle type through a analysis, with framework integrated in standalone software
Roughly, for single-particle events…
Step 1. Determine if a photon hit is associated with the track, or is “background”
Step 2. For each track, calculate for each PID hypothesis,
  is the expected angle for the given PID hypothesis
  is the single photon Cherenkov angle resolution
Step 3. Find the PID hypothesis that minimizes

## Slide 8
Quantifying PID performance: Look-up tables
For a given kinematic selection, what is the probability of correctly identifying PID?
Probability that it is reconstructed as…
e
K
p
unidentified
E.g., GeV, , degrees
For a truth level …
Note:
Unidentified column for , mostly from detector geometry
GeV, worse e/ separation
→ next step: have separate tables for e/h and /K/p
e
K
p
Probability
Number of tracks
0.51
0.31
0.36
0.47
0.16
0.14
0.15
0.15
0.84
0.82

## Slide 9
Quantifying PID performance: Look-up tables
For a given kinematic selection, what is the probability of correctly identifying PID?
E.g., GeV, , degrees
Probability
Probability that it is reconstructed as…
e
K
p
unidentified
For a truth level …
e
K
p
0.97
0.87
0.15
0.85
1.00
0.11
We created 37x20x120 = 88800 histograms, covering
  GeV
  degrees
400M single-particle events (100M e, , K, p each)
The latest tables: https://github.com/eic/epic-data/blob/main/pfrich.lut , made with the latest magnetic field map MARCO_v.7.6.2.2.11_1.7T, 2024_05_02
Highly differential!
Large statistics!
Notes: Mention effect of field map is not different

## Slide 10
Conclusions
pfRICH is crucial for PID in the e-going direction at ePIC
  through detection and measurement of Cherenkov photons emitted by charged particles
Standalone software offers flexibility for examining detector features and enables detailed studies of detector performance
Look-up table with fine binnings and large statistics is available
Looking forward to feedback on the table from analysis teams!

## Slide 11: Backup

## Slide 12
Efficiency vs azimuthal angle
1000 single- events for each range

## Slide 13
Efficiency vs azimuthal angle

## Slide 14
Talk by Alexander Kiselev at HADRON 2023
QE vs wavelength