## Slide 1
Simulation Study of W-ScFi Calorimeter for Pair Spectrometer Luminosity Detector at ePIC
Aranya Giri
Relativistic Heavy Ion Lab
Department of Physics, University of Houston
Advisor – Prof. Rene Bellwied
Date - 22nd June, 2024
Early Career Day – EICUG 2024 – Lehigh University

## Slide 2
Brookhaven National Laboratory ( BNL ), New York is the host site for the future Electron-Ion Collider (EIC).
arXiv.2103.05419
Variable e-p COM energy range from ∼ 20 to 100 GeV, upgradable to ∼140 GeV.
High electron-nucleon luminosity.
The Electron Ion Collider
1
First detector (experiment) is @ IP6, the electron Proton-Ion Collider (ePIC) experiment.
The collider and experiment is expected to commission at 2032.

## Slide 3
Luminosity
https://www.lhc-closer.es/taking_a_closer_look_at_lhc/0.luminosity
Luminosity is the maximum no. of collisions that can be produced in the collider
L = f N2 / 4 πr2
Rate of any event during collision (R) = L · cross-section (σ) of the associated process
Precise measurement of L = Precise measurement of σ
Higher Luminosity = Higher rate to observe any physics processes
At EIC, precision ~ 1% & High Luminosity ~ 1033-34 cm-2 s-1
2

## Slide 4
Luminosity Detector – Past to Future
The Forerunner ( precision of ~ 2% )
The Future !
[1] https://www.rhichome.bnl.gov/RHIC/Runs/
3

## Slide 5
Luminosity Detector – Bremsstrahlung Process
HERA ( Forerunner of EIC ) measured luminosity via Bremsstrahlung (BH) radiation produced during collisions.
Radiation due to elastic scattering of electron near strong electric field ( p / Nu ).
[1] https://arxiv.org/pdf/2106.08993.pdf
[2] http://www-library.desy.de/preparch/desy/1992/desy92-066.kek.pdf
θγ
Ee : Incoming e- energy
Ep : Incoming p energy
Ee’ : Outgoing e- energy
Ep’ : Outgoing p energy
Bremsstrahlung
Photons
1. High Rate ~ 4.7 MHz [2]
2. Precisely calculable cross-section from QED, Bethe-Heilter equation
3. Almost all produced BH γs are along e- beam direction, θγ ~ me / Ee
4

## Slide 6
Interaction Region of ePIC at EIC
https://arxiv.org/abs/2103.05419
Measurement of bremsstrahlung photons
e- beam
p or A beam
Fig: Schematic Diagram of ePIC interaction region
far-backward
far-forward
5

## Slide 7
Interaction Region of ePIC at EIC
https://arxiv.org/abs/2103.05419
Measurement of bremsstrahlung photons
e- beam
p or A beam
Fig: Schematic Diagram of ePIC interaction region
far-backward
far-forward
5
Low energy synchrotron radiation as major background

## Slide 8
Pair Spectrometer Luminosity Detector
y-axis
z-axis
e-
e+
Fig. The base model of ePIC Pair Spectrometer Luminosity Detector
6
L = R / σBH
To measure LUMINOSITY !

## Slide 9
Pair Spectrometer Luminosity Detector
https://arxiv.org/pdf/2106.08993.pdf
Fig. Current ePIC Luminosity Detector design with e- and p beam pipes and magnets built by Dhevan G., Aranya G.
& Justin C. in DD4hep. The placement of different component not fixed, changes according to experimental needs.
Interaction
Point
7

## Slide 10
Calorimeter
Fig. Shower generation by photon in EM CAL
Calorimeters completely absorbs the incident particle and measure its energy and position.
The incident particle initiates a particle shower. Each secondary particle deposits energy and produces further particles until the full energy is absorbed.
The composition and the dimensions of these showers depend on the type and energy of the primary particle (e±, photons or hadrons ) .
8

## Slide 11
Requirements
  Fairly good energy and position resolution.
  Radiation Hard for compact size.
  Low integration time (< 10 ns bunch spacing).
  Track shower profile for improved pile-up
  (multiple e- hits) treatment.
A Electromagnetic Sampling Calorimeter
  Passive “hard” material – Tungsten (W)
  Active Absorber – Plastic Scintillating Fibers
The Volumetric Ratio of W : ScFi is 4:1
Layered Structure – Alternate layers have fiber
running parallel along X or Y direction.
Brass holders are used to keep the fibers uniform.
W-ScFi Calorimeter
9

## Slide 12
Requirements
  Fairly good energy and position resolution.
  Radiation Hard for compact size.
  Low integration time (< 10 ns bunch spacing).
  Track shower profile for improved pile-up
  (multiple e- hits) treatment.
A Electromagnetic Sampling Calorimeter
  Passive “hard” material – Tungsten (W)
  Active Absorber – Plastic Scintillating Fibers
The Volumetric Ratio of W : ScFi is 4:1
Layered Structure – Alternate layers have fiber
running parallel along X or Y direction.
Brass holders are used to keep the fibers uniform.
W-ScFi Calorimeter
Fig. X|| layer in CAL
Fig. W-SciFi calorimeter built in DD4hep
y-axis
x-axis
z-axis

## Slide 13
W-ScFi Calorimeter
e-
e-
Y-Z shower profile from X|| layer
X-Z shower profile from Y|| layer
Fig. X|| layer in CAL
Fig. W-SciFi calorimeter built in DD4hep
y-axis
x-axis
z-axis

## Slide 14
Simulation Results – Sampling Fraction
σ2/E2 = a2/E2 + b2/E + c2
σ2/E2 = a2/E2 + b2/E + c2
σ2/E2 = a2/E2 + b2/E + c2
Sampling Fraction is ~ 3% and independent of incident particle energy
12

## Slide 15
Simulation Results – Energy Resolution
σ2/E2 = a2/E2 + b2/E + c2
σ2/E2 = a2/E2 + b2/E + c2
σ2/E2 = a2/E2 + b2/E + c2
e-
Electron Gun Parameters:
Vx = Uniform(-1.0, 1.0)
Vy = Uniform(14.9, 15.9)
Vz = -6388 cm
θ = Uniform(-.25º, 2.5º)
φ = Uniform(-.25º, 2.5º)
Z = -6400 cm
Egen = 11.5 GeV
Egen = 3.5 GeV
For each generated energy (0.5, 18.0) GeV, the reconstructed energy distribution is fitted with Gaussian distribution.
The fit parameters, mean (Erec) and sigma is used to calculate energy resolution.
13

## Slide 16
σ2/E2 = a2/E + b2/E2 + c2
Simulation Results – Energy Resolution

## Slide 17
σ2/E2 = a2/E + b2/E2 + c2
Energy resolution of a calorimeter is determined by fluctuations in the processes by which energy is deposited and measured.
Respective terms in the equation :
Stochastic (a): Includes the event-by-event fluctuations of shower development in calorimeter. ( 8.8%/√E(GeV) )
Noise (b): From the electronic noise of the readout chain and depends on the detector technique and on the features of the readout circuit. ( 20 MeV )
Constant (c): From non-uniformity, like from imperfections in the detector mechanical structure and readout system, from temperature gradients, from the detector aging, from radiation damage, etc. ( ~ 0 )
Simulation Results – Energy Resolution

## Slide 18
Simulation Results – Position resolution
σ2/E2 = a2/E2 + b2/E + c2
σ2/E2 = a2/E2 + b2/E + c2
σ2/E2 = a2/E2 + b2/E + c2
Egen = 3.5 GeV
Egen = 11.5 GeV
For each generated energy (1.0, 18.0) GeV, the (reconstructed – generated ) vertex distribution is fitted with Gaussian distribution.
The fit parameters,
  sigma is used to calculate position resolution.
  Mean ideally should be equal to zero but deviations was observed.
*Position measurements are in centimeters
17
Egen = 11.5 GeV
Egen = 3.5 GeV

## Slide 19
Simulation Results – Position Resolution
σ2/E2 = a2/E2 + b2/E + c2
σ2/E2 = a2/E2 + b2/E + c2
σ2/E2 = a2/E2 + b2/E + c2
Both x or y resolution is inversely proportional to energy of incident particle.
Position resolution increases as the energy increases.
*Position measurements are in centimeters
The mean should ideally be 0 but for both x & y shows max deviation of about 0.06 cm.
18

## Slide 20
Simulation Results – Radiation Length
σ2/E2 = a2/E2 + b2/E + c2
σ2/E2 = a2/E2 + b2/E + c2
σ2/E2 = a2/E2 + b2/E + c2
Egen = 3.5 GeV
Egen = 11.5 GeV
X0
For each generated energy (1.0, 18.0) GeV, the deposited energy distribution along longitudinal direction (z) is fitted with Gamma distribution.
Radiation length (X0) of a calorimeter is the longitudinal distance where energy of shower becomes 1/e times the incident energy.
  Depends on material of calorimeter.
19

## Slide 21
Simulation Results – Radiation Length & Shower Depth
σ2/E2 = a2/E2 + b2/E + c2
σ2/E2 = a2/E2 + b2/E + c2
σ2/E2 = a2/E2 + b2/E + c2
The fit parameters, alpha and beta is used to calculate zmax = (ɑ -1)/β, the location where maximum energy is deposited.
zmax = X0 ( log(Egen) + c) , X0 = 0.8248 cm
Shower Depth – Longitudinal depth of calorimeter in terms of X0 : ( 18 cm / 0.8248 cm ) = 22X0
20

## Slide 22
Energy 3.5 GeV
Energy 11.5 GeV
Simulation Results – Moliere Radius
rm
rm ~ 1.4 cm
Moliere radius (rm) is the radius of a cylinder containing on average 90% of the shower's energy deposition.
  Depends on the material of calorimeter.
20

## Slide 23
Conclusion
Design of W-ScFi calorimeter of Pair Spectrometer Luminosity Detector at EIC for ePIC experiment.
  It has been successfully implemented DD4hep for simulation.
  Characteristics of calorimeter like energy resolution, position resolution, radiation length
  & Moliere radius is studied.
Future Work
To study effect of radiation damage in the calorimeter.
Study optical parameters of scintillating fiber.
Beam test with first prototype build with collaborators at York University, UK
21

## Slide 24
Thank You

## Slide 25
Simulation Results – Position Resolution
e-
Electron Gun Parameters:
Vx = Uniform(-1.0, 1.0)
Vy = Uniform(14.9, 15.9)
Vz = -6388 cm
θ = Uniform(-.25º, 2.5º)
φ = Uniform(-.25º, 2.5º)
15

## Slide 26
Energy deposition (Edep_i) in 9 fibers of each SiPM is associated with a position, pos_i where i = {SiPMs}
The center of SiPM is the associated position , Pos_i = { x_center or y_center } depending on layer.
For a slice say j, in Suppose X|| layers, the mean y_j is
Simulation Results – Position Resolution
SiPM from X|| layers
SiPM from Y|| layers
y_center
x_center
x-axis
y-axis
o o o o o o o o o o
Find the mean position in each slice
16