## Slide 1
Alex Bogacz
Accelerator Physics Group Leader
The 22 GeV Upgrade of CEBAF
Developing a pre-conceptual design for additional FFA* racetrack in the existing CEBAF tunnel to reach the top energy of about 22 GeV
*FFA (Fixed Field Alternating-Gradient)
JLUO Meeting
June 12, 2024
  Recirculate 4 + 6.5 times to get to 22 GeV
  Alternative staging scenario:
    4 + 5.5 passes with 1.1 GeV/linac to get to 20 GeV
    Upgrade linac energy to 1.21 GeV/linac to get to 22 GeV

## Slide 2: Non Scaling FFA Arc - Compact FODO Cell
Large momentum acceptance FFA cell, configured with combined function magnets capable of transporting six beams with energies spanning a factor of two
Arc composed of 75 cells, Lcell = 3.15 m
Closely spaced orbits for all six beams (~ 4 cm)
Low betas (~ a few m)
Extremally low dispersions (a few cm) - Virtue of combined function FFA magnets
orbits
dispersions
beta functions

## Slide 3: Non Scaling FFA Arc - Compact FODO Cell
Stephen Brooks
Imported a vendor's magnet mechanical design and overlaid it on the beam orbits to make sure there is clearance

## Slide 4: Permanent Magnet Design
Very compact compared to conventional electro magnets
Allows for accommodating 6 additional passes in CEBAF tunnel
Provides power and cost savings
Concept successfully tested at
Open mid-plane geometry
13 cm
12 cm
Focusing Magnet BF
GF= -41.13 T/m
LQF= 1.67 m
BF= -0.812 T
Defocusing Magnet BD
GD= 43.44 T/m
LBD= 1.24 m
BD= -0.593 T
13 cm
12 cm

## Slide 5: Prototype Magnet
Prototype open-midplane BF magnet successfully built and evaluated for mechanical integrity
>1.5 Tesla measured in good field region
Field accuracy of
Testing magnetic materials for radiation resilience at CEBAF - LDRD project started Oct. 1, 2023

## Slide 6
Stephen Brooks

## Slide 7
Stephen Brooks
Stephen Brooks

## Slide 8: FFA Arc Error Sensitivity Studies
Machine Errors (misalignments and field errors)
Error studies, diagnostics, correction schemes
6-pass Orbit Excursions in FFA Arcs
12
Orbit Excursion (m)
0.016
0
-0.016
0
12
s (m)
Survey (positioning) errors were taken from a normal distribution but capped at a misalignment magnitude of 0.1 mm
Field and gradient errors were capped at 1% of the intended field.

## Slide 9: Panofsky Quad Window Corrector
Jay Benesch
Correction studies are underway (PhD Thesis project of Alex Coxe)
Stability of the beam dynamics not too demanding to error tolerances…
Currently under study…
  Requirements for beam position and Twiss at the transition to the recombiner
  Understanding of beam quality tolerances at the arc’s exit
Corrections and Error Resilience

## Slide 10
Injector Upgrade - 650 MeV Recirculating Injector
With the present 123 MeV injector, the difference in the first and final pass energies in the North Linac is too large (1:175) to effectively control the beam.
650 MeV recirculating injector (3-pass) based on LERF will allow a manageable difference in energies (1:33)

## Slide 11
243.507
0
60
0
0
BETA_X&Y[m]
BETA_X
BETA_Y
DISP_X
DISP_Y
243.507
0
30
0
0
BETA_X&Y[m]
BETA_X
BETA_Y
DISP_X
DISP_Y
pass 4
pass 1
7.25 GeV
0.65 GeV
Triplet Cells, phase advance: 1500 per cell
Multi-pass Linac Optics (11 passes, 1:33 Energy Ratio)
Present FODO linac offers periodic optics only for the lowest energy pass with large beta beating for higher passes (beta ~1000 m), which is not compatible with small betas (~5 m) in the FFA arcs.
Replacing FODO (alternating singlets) with alternating triplets – more uniform beam envelope

## Slide 12
284.877
0
240
0
5
0
BETA_X&Y[m]
BETA_X
BETA_Y
DISP_X
DISP_Y
pass 10
20.5 GeV
Transition to weakly focusing ‘Beta Beat’ Linac Optics for FFA Passes
.
.
.
11.6 GeV
pass 6
Deviate from optics periodicity  Induce and optimize beat in linacs  Reasonably small ’s at both ends of each linac at the expense of increase in maximum inside the linacs, ’s adjusted to nearly zero as favored by FFA matching  Greatly relaxed matching requirements
284.877
0
180
0
5
0
BETA_X&Y[m]
BETA_X
BETA_Y
DISP_X
DISP_Y

## Slide 13: Energy loss, Emittance dilution and Energy spread
  Doubling the energy, while staying within current CEBAF footprint, makes the synchrotron radiation effects of paramount importance.
  Quantum nature of a ‘recoil’ effect on electrons due to photon emission makes significant impact on both the transverse and longitudinal beam dynamics, leading to cumulative emittance growth (transverse and longitudinal).
Energy loss
Emittance dilution
Natural energy spread
  Cumulative emittance dilution (transverse and longitudinal) at 22 GeV (4 CEBAF + 6 FFA passes)
Projected value from the Spr/Rec contribution
Maximize , minimize H

## Slide 14: Hall Lines (A and C) – Beam Occupancy at 21 GeV
Challenge: Transporting beam of through a 22 mm ID beam tube
The 22 GeV Upgrade of CEBAF
150
0
120
0
5
-5
BETA_X&Y[m]
DISP_X&Y[m]
BETA_X
BETA_Y
DISP_X
DISP_Y
Dmax = 4 m
= 1.2×10-3
‘beam stay clear’:
=
=
=
39.9
0
90
0
2
-2
BETA_X&Y[m]
DISP_X&Y[m]
BETA_X
BETA_Y
DISP_X
DISP_Y
Dmax = 0.7 m
=
8 × 3.8 m bends
16 × 1.8 m bends
12 × 2.4 m bends?
SLI
150
0
120
0
5
-5
BETA_X&Y[m]
DISP_X&Y[m]
BETA_X
BETA_Y
DISP_X
DISP_Y
Dmax = 1.8 m
=
Jay Benesch

## Slide 15: Increasing Linac Energy Flexibility, DE/E - Alternative Staging
19.4
11.6
E [GeV]
2.2
19.4
11.6
E [GeV]
2.2
    Changing the linac energy by more than 1%, either the top or bottom pass will fall out of the range
    This would not allow for flexibility to reduce energy (e.g. cavities de-rated, or one of the cryomodules bypassed)
    Adding a sextupole component to permanent magnets extends the energy acceptance (currently under study)
  Assuming only 5 FFA passes (to about 20 GeV) the linac energy flexibility is greatly enhanced
  Increasing linac energy from 1.1 to 1.21 GeV boosts the lowest pass energy by 1.1 GeV (5×0.22 GeV) and brings the final energy back to about 22 GeV with adequate linac energy flexibility
11.6
21.7
E [GeV]
2.2
12.7
E [GeV]
2.42
21.7
  FFA permanent magnets, as presently designed, are at limit of their aperture and strength, to accommodate 6 orbits of different energy within energy acceptance from about 11 GeV to 22 GeV

## Slide 16: Adding Sextupole Component to Permanent Magnets

## Slide 17: Summary
Present Baseline (1.1 GeV per linac):
  650 MeV Recirculating Injector (additional three C-75 cryomodules)
  Recirculate 4 passes with the current CEBAF
  Plus Additional 6 passes via a single FFA: 10 – 22 GeV
Non Scaling FFA Arc Architecture configured with compact FODO cells
  Beta and dispersion matching to the linacs through cell-by-cell variation (length, bend)
  Open mid-plane permanent magnet design: B-field ≤ 1 T, Gradient ≤ 50 T/m
Synchrotron Radiation impact on beam quality:
  Net transverse normalized emittance:
  Net natural energy spread: 1.5×10-3
  Net synchrotron radiated energy: 1 GeV
at 22 GeV, b = 20 m → s = 175 microns
at 22 GeV → DE = 33 MeV

## Slide 18
The FFA@CEBAF Collaboration
R. M. Bodenstein, S.A. Bogacz, A.M. Coxe, K.E. Deitrick, B.R. Gamage, R. Kazimi, D. Khan, E.A. Nissen, S. Ogur, K.E. Price, Y.R. Roblin, R. Ruber, T. Satogata, A. Seryi, Jefferson Lab
J.S. Berg, S.J. Brooks, D. Trbojevic, Brookhaven National Lab
V.S. Morozov, Oak Ridge National Lab
G.H. Hoffstaetter, Cornell University

## Slide 19
Thanks for your attention!
The 22 GeV Upgrade of CEBAF

## Slide 20
Backup Slides

## Slide 21: CEBAF Energy Upgrade 10.55 → 23.75 GeV
Injector at 650 MeV
1.1 GeV
1.1 GeV
#1-10.55 GeV
#2-12.75 GeV
#3-14.95 GeV
#4-17.15 GeV
#5-19.35 GeV
#6-21.55 GeV
#1-11.65 GeV
#2-13.85 GeV
#3-16.05 GeV
#4-18.25 GeV
#5-20.45 GeV
#6-22.65 GeV
9.45
9.45 GeV
8.35
7.25 GeV
7.25
6.15 GeV
5.05 GeV
1.75 GeV
2.85 GeV
6.15
3.95 GeV
3.95
1.75
8.35 GeV
2.85 GeV
12 GeV
5.05 GeV
WEST FFA
EAST FFA
23.75 GeV
0.650
80.6 m
80.6 m
4 existing lines + 6 FFA turns
1.75 GeV
22.65 GeV
23.75 GeV
0.65 GeV
Energy range
Energy range
21
The 22 GeV Upgrade of CEBAF

## Slide 22: Modified Switchyard to Accommodate Six FFA Passes
pass 1
pass 2
pass 3
pass 4
FFA passes 5-10
FFA passes 5-10

## Slide 23: FFA Arc to Straight – Compact Merger
Breaking cell symmetry by altering (length, bend) of a few magnets to merge different energy orbits at arc ends.
Simultaneously, the dispersion and its derivative are suppressed at arc ends.
Furthermore, small beta functions (~5 m) need to be matched to higher-bets of the linacs (~90 m).
This simplifies switchyard and reduces its functionality to pathlength and momentum compaction adjustment.

## Slide 24
Synergy Between the Positron Source and 650 MeV Injector
Positron program ends prior to 22 GeV FFA, so LERF can be repurposed for 650 MeV electrons.
SRF to accelerate e+ to 123 MeV
SRF to accelerate e- to 120 MeV
Compact 10 mA P-Gun, Wien filter, 10 MeV e- injector
Joe Grames

## Slide 25: Distinguishing multi-pass beams - BPM multiplexing scheme at CEBAF
The 22 GeV Upgrade of CEBAF
25
Measuring distinct energy orbits in the FFA arcs by employing beam time structure to multiplex BPMs (currently used in our linacs - 5 beams).
To measure orbits for different linac passes we use ‘tune beam’ with the following time structure (repeating at 60 Hz):
  250 micro sec of continuous beam
  followed by a 100 micro sec gap
  and then 4 micro sec ‘trail’ of continuous beam.
The transit time around the machine is 4.2 micro sec, so appropriately gated electronics can distinguish, from which pass the 4 micro sec ‘trailing’ pulse is coming from. The same, or similar scheme could be extended to the FFA arcs.
at 60 Hz

## Slide 26: Distinguishing multi-pass beams - BPM multiplexing scheme at CEBAF
The 22 GeV Upgrade of CEBAF
26
1.1 GeV/linac
1.1 GeV/linac
650 MeV
650 MeV