## Slide 1: Overview and Use of SIMC
Dave Gaskell
NPS Collaboration Meeting
July 17-18, 2022
SIMC overview
Basics of using SIMC

## Slide 2: What is SIMC?
SIMC is the standard Hall C Monte Carlo for coincidence reactions (similar to MCEEP)  written in FORTRAN (now gfortran compatible …)
Features:
 Optics (COSY) and “aperture checking” Monte Carlos of spectrometers
[HMS, SOS, SHMS, HRS’s, BigCal,…]
 Includes radiative effects, multiple scattering, ionization energy loss, particle decay
 Simple prescriptions available for FSIs, Coulomb Corrections, etc.
Reactions implemented:
  Elastic and quasielastic  H(e,e’p), A(e,e’p)
  Exclusive pion production
     H(e,e’p+)n, A(e,e’p+/-) [quasifree or coherent]
  Kaon electroproduction  H(e,e’K+)L,S, A(e,e’K+/-)
  H(e,e’p+/-)X, D(e,e’p+/-)X [semi-inclusive]
  H(e,e’K+/-)X, D(e,e’K+/-)X [semi-inclusive]
  H(e,e’rp+p-)p, D(e,e’rp+p-) [diffractive r]
  H(e,e’p0)p, D(e,e’p0)p/n, (e,e’p0)X
Peter’s updates underway

## Slide 3: What SIMC is NOT…
SIMC is NOT a full detector response simulation a la GEANT
SIMC does NOT simulate a large class of processes simultaneously to generate backgrounds (like Pythia for example)
SIMC is not a generic event generator  processes are generated over a limited phase space with the specific purpose of being “thrown” into a spectrometer
SIMC is not hard to modify  if you want it to do something else (different cross section model, add new spectrometer, etc.) it is pretty easy to update + I can help

## Slide 4: Overview
Initialization
  Choose reaction, final state (if appropriate)
  Disable/enable implementation of (or correction for) raster, eloss …
Event generation
  Select vertex based on target size, position, raster size, beam spot size
  Determine energy, angle generation that will populate 100% of the acceptance (accounting for radiation, energy loss, …)
Physics Processes
  Event-by-event multiple scattering, radiative corrections, particle decay, coulomb corrections
Acceptance
  Can apply geometric cuts or spectrometer model. Default spec. models include target/spec. offsets, model of magnetic elements, apertures at front, back, middle of magnets, collimators, detector active area
Event Reconstruction
  Tracks are fitted in the focal plane and reconstructed to the target. Apply (average) energy loss, fast raster corrections. Calculate physics quantities for Ntuple/Root tree

## Slide 5: Example: Exclusive Pion Electroproduction
Initialize limits:
Generate vertex:
Generate scattering kinematics:
H(e,e’p): Generate qe, fe, qp, fp, pe – calculate pp
D(e,e’p): Generate qe, fe, qp, fp, pe, qN fN, pN  calculate pp
Modifications to kinematics:
Follow particles:
Apply cross section weighting (use model for free proton/neutron in g-N center of mass)
Simulate particle decay
 Decay the meson and follow the decay product(s)
Calculate Normalization Factors:
Bound nucleon momentum/direction

## Slide 6: Spectrometer Models (HMS, SHMS, HRS ...)
Magnetic elements simulated using COSY
Real apertures
  collimators, vacuum pipes
  magnet apertures (front, middle, and back)
Fiducial cuts for detectors (depends on analysis, trigger)
Sequential transformations for magnetic elements, continuous drift for field free regions (important for decay)
Reconstruct track
  Use smeared position at drift chamber
  Fit track at focal plane
  Reconstruct to target using matrix elements fit from MC data
Can easily disable spectrometer, apply geometric cuts, add new spectrometer/detector (for example, NPS)

## Slide 7: Getting SIMC
https://github.com/JeffersonLab/simc_gfortran

## Slide 8: SIMC Basics
Compiling: just type “make” in the main directory
Important directories
  infiles  where the input files for your simulation live
  worksim  SIMC event-by-event output (root trees)
  outfiles  where the *.hist file lives  need this for normfac
  util  “helper” applications to generate output
Helper applications
  SIMC default output is a FORTRAN binary file
  Helper applications in util directory convert to root trees or paw ntuple
  util/ntuple and util/root_tree  must be compiled separately
  Choose appropriate Makefile (Makefile.rhel9 or Makefile.rhel7)

## Slide 9: SIMC: structures  derived types
Long ago – had to convert from “structures” to ”derived types”
structure /double_arm/
structure /arm/ e
real*8 delta, yptar, xptar, z
end structure
structure /arm2/ p
real*8 delta, yptar, xptar, z
end structure
end structure
Use as variables, like:
recon.e.delta
vertex.p.xptar
type arm
sequence
real*8 delta, yptar, xptar, z
end type
type arm2
sequence
real*8 delta, yptar, xptar, z
end type
type double_arm
sequence
type(arm)::e
type(arm2)::p
end type
Use as variables, like:
recon%e%delta
vertex%p%xptar

## Slide 10: SIMC RHEL9/Alma9 updates: derived types in modules
First try to transition to Alma9 – all the derived types were broken
After lots of googling found a helpful web page that described the problem
Compilers can handle derived types in 2 different ways
  Name equivalence: two types are equal if they have the same name
  Index equivalence: each time a type is declared/defined, it’s given a unique index, even if they have the same name!
  Old compiler used first option, new gfortran uses second
How to fix/deal with this?
  Put the derived types in a module and load the module in each relevant subroutine
  All the derived types that were in “structures.inc” are now in “modules.f”
MODULE structureModule
! Define some BASIC record structures and associated parameters
! ... generic cut --> initialized with MAX large and MIN small
type cutstype
sequence
real*8 min, max
end type cutstype
…
…
…
In each relevant subroutine, added this statement:
USE structureModule

## Slide 11: SIMC Input File

## Slide 12: SIMC Input File
These parameters should not change much in general
”using_Eloss” should always be on to simulate ionization energy loss, but “correct_Eloss” should be off since hcana does not apply a correction
Don’t change the radiation flags, except maybe “one_tail”  might want to turn off proton radiation for neutral particles

## Slide 13: Input File Notes
Kinematics
  Units are in MeV
  No need to account for ionization energy loss – that’s in simulation
  Include synchrotron energy loss in beam energy (if relevant)
  If you find offsets to nominal kinematics in your analysis – apply those to the SIMC kinematics  will impact the model cross section calculation
Make sure to include contraction of target cell at low temperatures in target information
Target info mixes units, density in g/cm3, but thickness in mg/cm2
Generation volume: must be larger than nominal acceptance to get correct yield and cross sections. You can easily check in the *.hist file if the “found” values are too close to the generation limits
Despite the names, “targ%yoffset” and “targ%xoffset” are beam position offsets

## Slide 14: Running SIMC and Generating Output
Create your input file: eep_example.inp
run SIMC

## Slide 15: Running SIMC and Generating Output
Go to util/root_tree directory
./make_root_tree

## Slide 16: Make some plots and get some yields
Normalized yield by applying “Weight” from tree
Includes cross section, radiative corrections, small jacobian
What’s this 0.161960E+07 thing?
  “normfac” from eep_example.hist file
  Includes target thickness, simulated charge, generation volume
Also need to divide by number of events in tree
Result from this simulation (with these cuts) was:
Yield = 542.9 counts/mC

## Slide 17: Reconstructed Quantities in SIMC
Calculation of reconstructed quantities (W, x, Q2, etc.) may not match how these quantities are calculated in hcana
  Reconstruction was originally intended to match calculations in Hall C 6 GeV fortran analyzer
Found to be a problem for H(e,e’p) analysis for KaonLT/PionLT  definitions of missing momentum components weren’t even consistent
Ideally, we should make calculations in simc match hcana
  In the short term, should use stand-alone scripts to make comparable output
  Richard Trotta has done this for H(e,e’p) and exclusive Kaon production:
  https://github.com/trottar/simc_gfortran/tree/fall_2023_kaon_xsects/recon_hcana

## Slide 18: Updates for NPS
Peter B. has done most of the work needed to make SIMC work for NPS
Adding event generation for exclusive and semi-inclusive p0 is straightforward  same as p+ and p-
  Additional complication is decay of p0 into 2 photons (extra subroutine)
DVCS event generation same as exclusive mesons, just changing mass to zero!
Physics models needed for cross sections:
  SIDIS p0  average of p+ and p-
  Exclusive p0
    Large W (>2 GeV): Average of p+ and p-, removing pion pole contributions
    Low W (<2 GeV): MAID model
NPS calorimeter can just be an aperture for checking acceptance. Simple resolution smearing can be added later if desired
I’m working on incorporating Peter’s updates into the main branch on version on github

## Slide 19: SIMC Summary
SIMC is a pretty simple tool in many ways, but powerful
If full GEANT4 simulations are needed (e.g. for NPS) SIMC can be combined with those simulations
  SBS is doing this for d(e,e’N) simulations
Main drawback is that it’s fortran
  Modern cross section models are usually in C++, etc.
  Easy work-around is to use look-up tables  Peter has done this for the MAID model of pion electroproduction for example
Peter has already implemented many of the needed updates, integration underway