## Slide 1: HMS Calibrations for NPS: Optics
Optics Optimization at high momentum for the NPS Experiment
Christine Ploen
NPS Collaboration Meeting July 17-18, 2024

## Slide 2: Experimental Setup – top view
Sweeper Magnet
NPS Calorimeter on SHMS carriage
Target
HMS
NPS Collaboration Meeting July 17-18, 2024

## Slide 3: Experimental Setup
Coordinates rotated to mimic the orientation of the CAD rendering
e beam
NPS Collaboration Meeting July 17-18, 2024

## Slide 4: HMS Magnets and Parameters
6 mSr acceptance
25 deg vertical bend
Delta = (P-P0)/P0 better than 0.1%
Momentum range 0.5 to 7.5 GeV
Rotates from 12.5 to 90 deg
Saturation effects in both quads and dipole>4.8 GeV
NPS Collaboration Meeting July 17-18, 2024

## Slide 5: HMS saturation in dipole and quadrupoles
1.5 3.3 4.8 6.1 6.9 7.5
Approximate Central P (GeV)
Field to momentum relationship must be clear to set the dipole.
Dipole and quad saturation over 4.8 GeV, or ~1500 A
This effect also reflected in LH2 data (Szumila-Vance)
B/I versus set current
NPS Collaboration Meeting July 17-18, 2024

## Slide 6: Experimental Setup – NPS and HMS at small angles
Sweeper magnet field = 0.3 T*m
NPS fringe field may be relevant before HMS Q1, near the HMS vacuum snout
Schematic from Paulos Medieros
NPS Sweeper Magnet
Target
Collimator/Sieve
NPS Collaboration Meeting July 17-18, 2024

## Slide 7: Schematic of sieve slit array
NPS Collaboration Meeting July 17-18, 2024

## Slide 8: Preliminary Look at Effect of Sweeper Magnet
Simulations from R. Ent indicated any effects from the fringe field will be small vertical offset
Can be corrected within matrix optimization
X and Y sieve plots for the -6.117 GeV setting, comparing sweep magnet on and off
NPS Collaboration Meeting July 17-18, 2024

## Slide 9: Matrix optimization with sieve slit measurements
4 basic parts:
Event reconstruction with existing matrix
Determining “True” initial values
Setting up the Singular Value Decomposition (SVD) problem
Calculating the new matrix
NPS Collaboration Meeting July 17-18, 2024

## Slide 10: Matrix optimization and sieve slit measurements
Sieve slit measurements are taken with extended carbon foil targets:
1/ Carbon foil at z = 0 cm
2/ Carbon foil at z = +/- 3 cm
3/ Carbon Foil at z = +/- 8 cm
X, Y sieve reconstruction with unoptimized matrix from 2018
Schematic of sieve slit array
NPS Collaboration Meeting July 17-18, 2024

## Slide 11: NPS Momentum Settings to Optimize
Lower rates in March runs  the statistics of the +/-3 cm target setting set the limit on the others
P = -6.667 GeV/c: x50_2
  +/-3 cm carbon foil/ sweeper mag ON
  +/- 8 cm carbon foil /sweeper mag ON and OFF
  Carbon 0.5% at z=0/ sweeper mag ON
P = -6.117 GeV/c: x36_3
  +/-3 cm carbon foil/ sweeper mag ON
  +/- 8 cm carbon foil/ sweeper mag ON
  Carbon 0.5% at z=0/ sweeper mag ON
P = -5.878 GeV/c: x60_3
  +/-3 cm carbon foil/ sweeper mag ON
  +/- 8 cm carbon foil/ sweeper mag ON
  Carbon 0.5% at z=0/ sweeper mag ON
P = -5.639 GeV/c: x25_3’
  +/-3 cm carbon foil/ sweeper mag ON
  +/- 8 cm carbon foil/ sweeper mag ON
  Carbon 0.5% at z=0/ sweeper mag ON and OFF
Christine Ploen
Josh Crafts
Julio Gil Gutierrez & Abhyuday Sharda (XEM)
TBD
Josh/Christine

## Slide 12: NPS Momentum Settings Status
P = -6.667 GeV/c: x50_2
  1st pass angular opt (ang. matrix elements) DONE
  Delta Optimization In Progress
  Sweeper Magnet studies TBD
P = -6.117 GeV/c: x36_3
  Angular optimization in progress
  Delta Opt TBD
  Sweeper Magnet studies TBD
P = -5.878 GeV/c: x60_3
  Angular optimization in progress
  Delta Opt TBD
  Sweeper Magnet studies TBD
P = -5.639 GeV/c: x25_3’
  Onboarding with NPS Software
  Angular optimization TBD
  Delta Opt TBD
  Sweeper Magnet studies TBD
Christine Ploen
Josh Crafts
Julio Gil Gutierrez & Abhyuday Sharda (XEM)
TBD
Josh/Christine

## Slide 13: Sieve Slit Calibration Runs at -6.667 GeV for angular optimization
Run | HMS Angle (deg) | Sweeper Magnet | Target
1537,1538 | 12.490 | OFF | Carbon 0.5%
1543, 1544 | 12.490 | ON | Carbon 0.5%
1539 | 12.490 | OFF | Carbon +/-8 cm
1540 | 12.490 | ON | Carbon +/-8 cm
5162 | 15.195 | ON | Carbon 0.5%
5156-5160 | 15.195 | ON | Carbon +/-3 cm
5161,5163 | 15.195 | ON | Carbon +/-8 cm
5164 | 15.195 | OFF | Carbon +/-8 cm

## Slide 14: Step 1: event reconstruction within HallC analysis software, nps_replay
Matrix elements are specified in a parameter file at runtime which contains the angular and delta coefficients up to sixth order
i + j + k +l + m ≤ 6

## Slide 15: Step 2: Calculating true initial values on +/- 8 cm target
Cutting event on foils, along with foil and beam positions, gives us the central y target position
Ztar = target foil position
Xbeam = beam horizontal position from the fast raster
Ymis = horizontal mis-pointing from survey data

## Slide 16: Step 2: Calculating true initial values
Graphical cuts in the focal plane correlate events to each sieve hole (red polygons)
Cuts in delta assist in resolving the sieve pattern
Cuts here are labeled by their midpoints, and are delineated at delta = (-10%, -8%, -5 %, 0%, 5%, 10%)

## Slide 17: Results of angular optimization Yptar
Previous (optimized for -6.59 GeV)
New Optimized Matrix for -6.667 GeV

## Slide 18: Results of angular optimization in ytar

## Slide 19: Results of angular optimization in xptar

## Slide 20: Results of angular optimization in xptar, del2.5

## Slide 21: Results of angular optimization in xptar, del -2.5

## Slide 22: Results – sieve slit plots for 2018 matrix and 6.667
Low P Matrix
-6.667 GeV NEW Matrix
(only angular optimization)
Using the replay’s current matrix!!

## Slide 23: Next steps –
Immediate
Delta Optimization – x50_2 (-6.667 GeV/c) and upload fully optimized matrix to replay
1st Pass angular elements for 3 other settings, then delta optimization
  - This means at least one run for each optics target for one angle per high-mom kinematic
1st Pass sweeper magnet studies at 4.64 GeV/c
(would be nice?) Afterburner script for existing replays
Fine Tune
Utilize all possible runs for angular optimization, fine-tune cuts
2nd look at delta optimization
Sweeper magnet studies at other P, theta

## Slide 24: Location in nps_replay:
g_ctp_parm_filename = "DBASE/NPS/general_coin.param"
g_ctp_kinematics_filename = "DBASE/NPS/standard_coin.kinematics"
g_ctp_det_calib_filename = "DBASE/HMS/default_det_calib_nps23.param"
g_ctp_bcm_calib_filename = "PARAM/GEN/gscalers.param"
g_ctp_optics_filename = "PARAM/HMS/GEN/hcana_fa22.param"
g_ctp_map_filename = "MAPS/HMS/DETEC/STACK/hms_stack_nps.map"
g_ctp_trig_config_filename = "PARAM/TRIG/thms_nps23.param"

## Slide 25: Questions?

## Slide 26: Next Steps – Delta Optimization of Elastic Calibration Runs at -6.667 GeV
Run | HMS Angle (deg) | Sweeper Magnet | Target
1534 | 19.145 | OFF | LH2
1547 | 19.150 | ON | LH2
1548 | 19.150 | ON | LH2
1535 | 17.995 | OFF | 
1546 | 18.005 | ON | LH2
1536 | 16.850 | OFF | 
1545 | 16.850 | ON |