## Slide 1: Combined Analysis Status Report From all GEn-II Students
Hunter Presley (& Arun)
Faraz Chahili, Kate Evans, Vimukthi Gamage, Jack Jackson, Sean Jeffas, Jacob Koenemann, Braian Mederos, Gary Penman
SBS Collaboration Meeting 09/2024
Notes: Currently under production or commissioning?

## Slide 2
Presley
SBS Collab Meeting, Sep 2024
GEn-II Students
Kate Evans
Jack Jackson
Gary Penman
Faraz Chahili
Me
Vimukthi Gamage
Jacob Koenemann
Braian Mederos
Sean Jeffas
Graduated July 2024
Moller
GEMS
Target and BBCAL
Target and GRINCH
Target and Hodo
Target and HCAL
Target UVA
Target UVA
GEMS
Notes: Bullet 2: at highq2 more than just spatial distr.

## Slide 3
Presley
SBS Collab Meeting, Sep 2024
Outline
GEn-II experimental measurement
Flow chart and stages of analysis
Progress and status
Challenges moving forward
Notes: Bullet 2: at highq2 more than just spatial distr.

## Slide 7
Presley
SBS Collab Meeting, Sep 2024
SBS Form Factor Program
GMn : measure GMn/GMp up to Q2 = 13.5 GeV2 LD2 target - Complete
GEn-II : measure GEn/GMn up to Q2 = 10 GeV2 3He target - Complete
GEn-RP : measure GEn/GMn up to Q2 = 4.5 GeV2 LD2 target - Complete
GEp : measure GEp/GMp up to Q2 =12 GeV2 LH2 target - March 2025?
Goal of SBS Form Factor Program - Determine Sachs Electric and Magnetic Form Factors at unprecedentedly high Q2 values with higher statistical uncertainty
Notes: Bullet 2: at highq2 more than just spatial distr.

## Slide 8
Presley
SBS Collab Meeting, Sep 2024
8
2022-23 data taken
GMp - published
2022 data taken
2025
Q2 [GeV]2
SBS
SBS Form Factor Program

## Slide 9
Presley
SBS Collab Meeting, Sep 2024
GEn-II and Elastic Nucleon Form Factors
Fundamental properties of a nucleon
Encodes information on the spatial distribution of charge and magnetization
Purpose: extract GEn at very high Q2
Asymmetry measurement with polarized electron beam and polarized 3He target - effective polarized neutron target
Notes: Bullet 2: at highq2 more than just spatial distr.

## Slide 10
Presley
SBS Collab Meeting, Sep 2024
Experimental Measurement
Unpolarized Cross Section
Polarized Cross Section
Notes: Bullet 2: at highq2 more than just spatial distr.

## Slide 11
Presley
SBS Collab Meeting, Sep 2024
Experimental Measurement
Choose polarization transverse to Q2
Asymmetry proportional to the ratio of GnE/GnM
Notes: Bullet 2: at highq2 more than just spatial distr.

## Slide 12
Employ all QE cuts
Count events with + and - helicity for each run
Run by run required due to varying polarizations
Presley
SBS Collab Meeting, Sep 2024
Experimental Measurement - Raw

## Slide 13
Presley
SBS Collab Meeting, Sep 2024
Corrections to Raw Asymmetry
For the following list must determine 2 things:
f - fraction of quasielastic sample the component occupies
A - asymmetry of said component
Accidentals, Inelastics, Pions, FSI, Protons
The nitrogen fraction must also be calculated using target measurements
Notes: Bullet 2: at highq2 more than just spatial distr.

## Slide 14
Presley
SBS Collab Meeting, Sep 2024
Analysis Flowchart
Raw Data
Detector
Calibrations - 1
Data Selection - 3
Polarimetry - 6a
Physics
Asymmetry - 6
Red - To do
Green - In Progress
GEn
Data Quality Checks - 2
Raw Asymmetry - 5
Physics Corrections - 6b
Other Corrections - 6c
Error Analysis
Statistical - 7a
Systematic - 7b
Pass 2 / 3 calibration - 4
Notes: Bullet 2: at highq2 more than just spatial distr.

## Slide 15
Presley
SBS Collab Meeting, Sep 2024
Stages of Analysis
Detector Calibration procedure
Data Selection
Asymmetry Corrections
Target and Beam Polarimetry Application
Sensitivity Study and Results
Notes: Compare to seamus and freddies thesis

## Slide 16
Presley
SBS Collab Meeting, Sep 2024
Detector Calibration
BBCal - Kate Evans
GEMs - Vimukthi Gamage and Sean Jeffas
GRINCH - Jack Jackson
HCal - Hunter Presley
Hodoscope - Gary Penman
BB Optics - Sean Jeffas
SBS Optics - Vimukthi Gamage
List of Subsystems
*Guidance from Andrew Puckett, Todd Averett, Gordon Cates, Bogdan Wojtsekhowski and other experienced GMn students, postdocs and senior collaborators!
Notes: Pic of sbs detectors

## Slide 17: BBCAL (Shower + Preshower)
Purpose
  Measures the scattered 𝑒! energy and crudely determines the track position.
  Provides handle for pion background rejection (PS energy deposit is used for this purpose)
  Provides trigger for the BigBite spectrometer
  Gives constraint for the track search region
General principles
  Collect Cherenkov light from relativistically charged particles including primaries and secondary e+/e- shower in electromagnetic cascades
  Long axis of preshower perpendicular to e- or pion
  Long axis of shower parallel to e- or pion

## Slide 18
Presley
SBS Collab Meeting, Sep 2024
Detector Calibration
Calibration Concept
ꭓ2 minimization of cluster energy compared to reconstructed electron energy
  Generate new ADC gain coefficients
Align ADC time of each block with respect to the hodoscope* cluster mean time
  Generate new ADC time offsets
BBCAL
Current Status
Energy calibrations are done and look good for all kinematics
Timing alignment was NOT done for the pass-1 mass replay and is being worked on for pass 2
Notes: Bullet 2: at highq2 more than just spatial distr.

## Slide 19
Presley
SBS Collab Meeting, Sep 2024
Detector Calibration
BBCal
Results
GEN2 using H2 data
GEN4-a using He3 data
Notes: Bullet 2: at highq2 more than just spatial distr.

## Slide 20: Timing Hodoscopes
Consists of 89 plastic scintillator paddles with a PMT on each side (178 channels)
Each PMT read out by dedicated 1190 TDC channel for precision timing
Designed to measure precision timing and position
Timing resolution: ~600 ps
  Can resolve e’ time-of-flight differences
Position resolution: ~5 cm
  Segmentation provides dispersive (vertical) resolution
  𝛥t = tleft - tright and e’ track matching provides transverse (horizontal) resolution
Slide credit: Sebastian Seeds

## Slide 21
Presley
SBS Collab Meeting, Sep 2024
Detector Calibration
Calibration Concept
The hodoscope requires a timewalk and absolute timing offset calibration for each PMT (x178), as well as calibration of the scintillation speed of each plastic bar (x89).
Timing Hodoscope
Current Status
In Pass1 of the GEn data, these were performed separately. More recently a formalism was initialised (A. Puckett) to perform a more consistent global fit, and this is under further development. This includes correcting the timing of all systems (HCal, Hodo, RF) simultaneously in order to extract nucleon TOF.
Notes: Bullet 2: at highq2 more than just spatial distr.

## Slide 22: GEN Pass 2 (Working Towards)
Still figuring out how to treat the trigger and RF times, for example. The “rf structure” is misaligned across the 89 bars
Initial run of “TOFcal” calibration script including some HCal parameters and the existing hodoscope global fit, begins to yield improvement in the TDC coincidence time
1.4ns
Hodoscope

## Slide 23: GEMs (GAS ELECTRON MULTIPLIER)
e’ causes ionization of gas within cells with potential, accelerating them to segmented readout planes for tracking
Very high segmentation enables excellent position resolution (~7000 channels per layer!)
  5 layers in electron arm
Measures position and timing
  Position resolution: ~70 µm
  Timing resolution: ~10 ns
Position resolution enables precision tracking in the electron arm.
Primary detector subsystem responsible for tracking!
Constraint Region
Typical event: many strips are firing at once!
GEMs Single Event Display
Constraint reduces search region to 2-3% of active GEM area
Due to high luminosity, without constraints, combinatorics can regularly reach to > 1M competing tracks per event!

## Slide 24
Presley
SBS Collab Meeting, Sep 2024
Calibration Concept
Alignment - difference between the absolute hit position and the track position for each module is minimized to arrive at the accurate alignment
Gain Match - adc asymmetry due to u, v cluster APVs are minimized
ADC threshold - ADC thresholds are chosen such that the lowest 0.3% of ADC values are removed
Timing Calibration - U/V and Δt timing distributions are fitted with gaussians, 4.5σ and 5σ cut are used respectively
GEMs
Current Status
Electron arm (BigBite) GEMs are calibrated for all kinematic points by Sean Jeffas
Hadron arm (SuperBigBite) GEMs are a working progress with the aim of Hcal energy calibration
Notes: Bullet 2: at highq2 more than just spatial distr.

## Slide 25
HCal is a sampling, segmented hadron calorimeter
  12 col x 24 row (288 channels)
  fADC250 flash analog to digital and f1TDC time to digital converters (all channels)
HCal measures hadron energy, position, and precision timing
Energy: Hadrons interact with iron absorbers to create showers of many particles, shower energy is converted to light via scintillator, and light is converted to analog signal via PMT. PMT signals are read out by analog-to-digital converters (ADC) and time-to-digital converters (TDC).
  A portion of the initial hadron energy is sampled: the sampling fraction
  Simulated/observed energy sampling fraction: ~10%
  Simulated/observed energy resolution: ~40%
Position: Shower deposits energy in localized set of modules (a cluster). Hadron position in HCal reconstructed via energy-weighted cluster centroid
  Simulated/observed position resolution: ~7cm
Timing: Difference in time between signal in HCal and hodoscope corrected trigger
  Observed single-channel timing resolution: ~1.3 ns
Primary detector responsible for measuring scattered hadrons and associated yields
Single module
1/288 Single Modules in HCal
HCAL

## Slide 26
Presley
SBS Collab Meeting, Sep 2024
Calibration Concept
Identify timing and energy of detected recoiled nucleon
Align fADC and TDC times
Set fADC gain coefficients
HCAL
Current Status
First pass of calibrations completed
Timing and energy calibration procedure needs to be optimized before pass 2
  New timing calibration procedure
  SBS GEMs being implemented for energy calibration
Notes: Bullet 2: at highq2 more than just spatial distr.

## Slide 27
The Gas Ring ImagiNg CHerenkov, GRINCH
  Heavy gas (C4F8) filled light-tight “coffin” box promotes cherenkov reactions with charged electrons and pions
  510 PMTs in a honeycomb array designed to resolve electron rings
Measures timing with unique properties
  Each PMT is read out by a single time to digital converter (TDC) channel
  Timing resolution ~4.5 ns
Designed to mitigate pion contamination for better quasi-elastic e’ selection
  Much heavier pions with similar momentum as e’ move more slowly and produce smaller rings
  Pion threshold ~2.7 GeV/c
Provides efficient pion rejection over all kinematics.
GRINCH (Gas RINg imaging CHerenkov)

## Slide 28
Presley
SBS Collab Meeting, Sep 2024
Detector Calibration
Calibration Concept
Check time over threshold (ToT) for the 510 photomultiplier tubes (PMTs)
  ToT vs. PMT should be centered ~12.5ns
Align and set timing offsets for the leading edge (LE) for each PMT
GRINCH
Current Status
LE calibrations ready for pass2 (all kinematics)
First looks at GRINCH efficiency
Cut studies
  ToT, # of (GRINCH) Clusters, PS Energy, W2, etc.
Notes: Bullet 2: at highq2 more than just spatial distr.

## Slide 29
Presley
SBS Collab Meeting, Sep 2024
Identifying Protons and Neutrons
Calculate expected recoiled nucleon location with BBCal
This calculation doesn’t consider SBS magnet
  Expected location should have larger discrepancy with actual location for protons in the dispersive direction
dX - Difference between expected and actual in dispersive direction
dY - Difference between expected and actual in non-dispersive direction
Data Selection
Notes: Bullet 2: at highq2 more than just spatial distr.

## Slide 30
Presley
SBS Collab Meeting, Sep 2024
Quasi Elastic Cuts
dX
dY
W2
Coincidence
Data Selection
Notes: Bullet 2: at highq2 more than just spatial distr.

## Slide 31
Presley
SBS Collab Meeting, Sep 2024
dX and dY
Data Selection
Notes: Bullet 2: at highq2 more than just spatial distr.

## Slide 32
Presley
SBS Collab Meeting, Sep 2024
W2
Data Selection
Notes: Bullet 2: at highq2 more than just spatial distr.

## Slide 33
HCal.adc.t - BBCal.adc.t
Rough cuts on dxdy -> clear coincidence
Presley
SBS Collab Meeting, Sep 2024
Coincidence cut
Data Selection
Notes: Bullet 2: at highq2 more than just spatial distr.

## Slide 34
Irreducible Background at large
Efforts underway to understand and integrate the inelastic generator into the mainstream analysis framework
Presley
SBS Collab Meeting, Sep 2024
34
Event selection
Plot credit: Sean Jeffas

## Slide 35
Presley
SBS Collab Meeting, Sep 2024
GEn-II successfully completed data taking with a high luminosity polarized 3He target!
Highly motivated group that meets weekly for analysis meetings
Major analysis efforts are underway in terms of timing, calibrations, energy reconstruction, simulations and beam and target polarimetries
1 graduated, 8 to go!
Summary
Notes: Bullet 2: at highq2 more than just spatial distr.

## Slide 36
Presley
SBS Collab Meeting, Sep 2024
GEn-II Students
Kate Evans
Jack Jackson
Gary Penman
Faraz Chahili
Me
Vimukthi Gamage
Jacob Koenemann
Braiain Mederos
Sean Jeffas
Graduated July 2024
Moller
GEMS
Target and BBCAL
Target and GRINCH
Target and Hodo
Target and HCAL
Target UVA
Target UVA
GEMS
Notes: Bullet 2: at highq2 more than just spatial distr.

## Slide 37
Presley
SBS Collab Meeting, Sep 2024
Extras
Notes: Bullet 2: at highq2 more than just spatial distr.

## Slide 38: GEN Pass 1
Post TW correction alignment check (Bar 44)
Timewalk observed in TDC Leading Edge vs TOT (Bar 44)
Position alignment relative to GEMs in dispersive plane after vscint calibration
HCal TDC - Hodo TDC Coincidence Time resolution after Pass1
Hodoscope

## Slide 39
Hodoscope

## Slide 40: GEN Pass 2 (Working Towards)
Still figuring out how to treat the trigger and RF times, for example. The “rf structure” is misaligned across the 89 bars
Initial run of “TOFcal” calibration script including some HCal parameters and the existing hodoscope global fit, begins to yield improvement in the TDC coincidence time
1.4ns
Hodoscope